Source	Marketwire
Date	08/24/2015
Time	05:03:46 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Results from Exploration Drilling at the Northwest 
Drinkwater and Chieftan Targets, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

August 24, 2015

Scorpio Gold Reports Results from Exploration Drilling at the Northwest 
Drinkwater and Chieftan Targets, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 24, 2015) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports results 
from exploration drilling at the Northwest Drinkwater and Chieftan targets at 
its 70% owned Mineral Ridge project, located in Nevada.

The Northwest Drinkwater and Chieftan targets are located immediately northwest 
and 500 meters west-northwest, respectively, of the Drinkwater pit. Both target 
areas lie outside of currently defined resources for the Mineral Ridge project. 
First pass drilling at Chieftan returned significant results in 10 of 12 holes 
drilled (Table 1). Significant results were also returned from three holes 
drilled at the Northwest Drinkwater target (Table 2), where previous drilling 
(2011-13) outlined a mineralized trend that extends approximately 300 meters 
northwest of the Drinkwater deposit. Scorpio Gold's management considers the 
results from drilling on both targets to be encouraging. No follow-up drilling 
is planned on either target at this time but may be considered at a future date.

A drill hole location map is available at: DH Plan

/T/



Table 1. Chieftan Target - Significant Drill Results

----------------------------------------------------------------------------
Hole       Azm   Dip   From     To  Width   From     To  Width   Gold   Gold
No.      (deg) (deg)   (ft)   (ft)   (ft)    (m)    (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR14930      0   -90     20     30     10   6.10   9.14   3.05  0.024   0.84
----------------------------------------------------------------------------
90    100     10  27.43  30.48   3.05  0.029   1.00
----------------------------------------------------------------------------
MR14940    210   -60     50     55      5  15.24  16.76   1.52  0.010   0.34
----------------------------------------------------------------------------
MR14961      0   -90      5     15     10   1.52   4.57   3.05  0.048   1.66
----------------------------------------------------------------------------
55     60      5  16.76  18.29   1.52  0.019   0.65
----------------------------------------------------------------------------
MR14963      0   -90    175    180      5  53.34  54.86   1.52  0.027   0.93
----------------------------------------------------------------------------
1-95    200      5  59.44  60.96   1.52  0.023   0.79
----------------------------------------------------------------------------
235    240      5  71.63  73.15   1.52  0.017   0.59
----------------------------------------------------------------------------
330    335      5 100.58 102.11   1.52  0.278   9.53
----------------------------------------------------------------------------
MR14964      0   -90    220    225      5  67.06  68.58   1.52  0.023   0.79
----------------------------------------------------------------------------
240    245      5  73.15  74.68   1.52  0.027   0.93
----------------------------------------------------------------------------
270    275      5  82.30  83.82   1.52  0.025   0.86
----------------------------------------------------------------------------
MR14965      0   -90    115    130     15  35.05  39.62   4.57  0.039   1.33
----------------------------------------------------------------------------
MR14967      0   -90                  No Significant Results
----------------------------------------------------------------------------
MR14995    261   -45    0.0   11.8   11.8   0.00   3.60   3.60  0.032   1.10
----------------------------------------------------------------------------
36.0   37.0    1.0  10.97  11.28   0.30  0.017   0.57
----------------------------------------------------------------------------
112.4  115.5    3.1  34.26  35.20   0.94  0.016   0.53
----------------------------------------------------------------------------
312.1  322.0    9.9  95.13  98.15   3.02  0.106   3.65
----------------------------------------------------------------------------
391.2  392.6    1.4 119.24 119.66   0.43  0.016   0.55
----------------------------------------------------------------------------
MR141031   210   -55   88.0   92.7    4.7  26.82  28.25   1.43  0.023   0.79
----------------------------------------------------------------------------
MR141033    94   -45  212.0  214.5    2.5  64.62  65.38   0.76  0.095   3.25
----------------------------------------------------------------------------
232.5  237.5      5  70.87  72.39   1.52  0.018   0.60
----------------------------------------------------------------------------
286.0  311.0     25  87.17  94.79   7.62  0.022   0.74
----------------------------------------------------------------------------
MR141034   218   -50  186.0  190.0      4  56.69  57.91   1.22  0.022   0.74
----------------------------------------------------------------------------
MR141048     0   -90                  No Significant Results
----------------------------------------------------------------------------




Table 2. Northwest Drinkwater Target - Significant Drill Results

----------------------------------------------------------------------------
Hole       Azm   Dip   From     To  Width   From     To  Width   Gold   Gold
No.      (deg) (deg)   (ft)   (ft)   (ft)    (m)    (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR14989    205   -65  316.3  333.6   17.3  96.41 101.68   5.27  0.018   0.62
----------------------------------------------------------------------------
444.0  448.0    4.0 135.33 136.55   1.22  0.026   0.89
----------------------------------------------------------------------------
MR14990      0   -85  155.5  160.3    4.8  47.40  48.86   1.46  0.034   1.17
----------------------------------------------------------------------------
164.0  167.0    3.0  49.99  50.90   0.91  0.022   0.75
----------------------------------------------------------------------------
216.6  221.4    4.8  66.02  67.48   1.46  0.033   1.13
----------------------------------------------------------------------------
245.0  249.7    4.7  74.68  76.11   1.43  0.016   0.55
----------------------------------------------------------------------------
598.7  600.0    1.3 182.48 182.88   0.40  0.036   1.23
----------------------------------------------------------------------------
MR141011   225   -65  548.9  553.5    4.6 167.30 168.71   1.40  0.026   0.88
----------------------------------------------------------------------------
619.9    624    4.1 188.95 190.20   1.25  0.022   0.75
----------------------------------------------------------------------------



/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling with the exception of 7 core holes MR14995, MR141031, 33 and 34, 
MR14989, 90 and MR141011. True width is estimated at 80-100% of downhole width. 
Analytical results were performed by American Assay Laboratory Inc. in Sparks, 
Nevada, an ISO/IEC 17025:2005 accredited facility. External check assays to 
verify lab accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 
certified and ISO/IEC 17025:2005 accredited facility. Further details are 
presented in the Company's quality assurance and quality control program for 
the Mineral Ridge project available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Waterton Global Value L.P. (30%). Mineral Ridge is a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property in Manhattan, Nevada, with a fully 
permitted underground mine and 400 ton per day mill facility.

Scorpio Gold's President & CEO, Peter J. Hawley, PGeo,, is a Qualified Person 
as defined by National Instrument 43-101 and has reviewed and approved the 
content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project. Such forward-looking statements involve known and 
unknown risks, uncertainties and other factors that could cause actual events 
or results to differ materially from estimated or anticipated events or results 
implied or expressed in such forward-looking statements, including risks 
involved in mineral exploration and development programs and those risk factors 
outlined in the Company's Management Discussion and Analysis as filed on SEDAR. 
Any forward-looking statement speaks only as of the date on which it is made 
and, except as may be required by applicable securities laws, the Company 
disclaims any intent or obligation to update any forward-looking statement, 
whether as a result of new information, future events or results or otherwise. 
Forward-looking statements are not guarantees of future performance and 
accordingly undue reliance should not be put on such statements due to the 
inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Peter J. Hawley
President & CEO
(819) 825-7618
phawley@scorpiogold.com
www.scorpiogold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=540040809