Source	MARKET NEWS
Date	08/24/2015
Time	05:56:14 AM

Company	 Scorpio Gold Corporation
Title	Results From 
Exploration Drilling At The Northwe





    CDNX Symbol: SGN











Press Release	





SCORPIO GOLD CORP ("SGN-V;SRCRF-0")
- Results From Exploration Drilling At The Northwest Drinkwater
- And Chieftan Targets, Mineral Ridge Project, Nevada

Scorpio Gold Corporation ("Scorpio Gold" or the "Company") reports
results from exploration drilling at the Northwest Drinkwater and
Chieftan targets at its 70% owned Mineral Ridge project, located in
Nevada.

The Northwest Drinkwater and Chieftan targets are located
immediately northwest and 500 meters west-northwest, respectively, of
the Drinkwater pit. Both target areas lie outside of currently defined
resources for the Mineral Ridge project. First pass drilling at
Chieftan returned significant results in 10 of 12 holes drilled (Table
1). Significant results were also returned from three holes drilled at
the Northwest Drinkwater target (Table 2), where previous drilling
(2011-13) outlined a mineralized trend that extends approximately 300
meters northwest of the Drinkwater deposit. Scorpio Gold's management
considers the results from drilling on both targets to be encouraging.
No follow-up drilling is planned on either target at this time but may
be considered at a future date.

A drill hole location map is available at: DH Plan

//st
Table 1. Chieftan Target - Significant Drill Results

---------------------------------------------------------------------------
-
Hole       Azm   Dip   From     To  Width   From     To  Width   Gold
Gold
No.      (deg) (deg)   (ft)   (ft)   (ft)    (m)    (m)    (m)  (OPT)
(g/t)
---------------------------------------------------------------------------
-
MR14930      0   -90     20     30     10   6.10   9.14   3.05  0.024
0.84
---------------------------------------------------------------------------
-
90    100     10  27.43  30.48   3.05  0.029
1.00
---------------------------------------------------------------------------
-
MR14940    210   -60     50     55      5  15.24  16.76   1.52  0.010
0.34
---------------------------------------------------------------------------
-
MR14961      0   -90      5     15     10   1.52   4.57   3.05  0.048
1.66
---------------------------------------------------------------------------
-
55     60      5  16.76  18.29   1.52  0.019
0.65
---------------------------------------------------------------------------
-
MR14963      0   -90    175    180      5  53.34  54.86   1.52  0.027
0.93
---------------------------------------------------------------------------
-
1-95    200      5  59.44  60.96   1.52  0.023
0.79
---------------------------------------------------------------------------
-
235    240      5  71.63  73.15   1.52  0.017
0.59
---------------------------------------------------------------------------
-
330    335      5 100.58 102.11   1.52  0.278
9.53
---------------------------------------------------------------------------
-
MR14964      0   -90    220    225      5  67.06  68.58   1.52  0.023
0.79
---------------------------------------------------------------------------
-
240    245      5  73.15  74.68   1.52  0.027
0.93
---------------------------------------------------------------------------
-
270    275      5  82.30  83.82   1.52  0.025
0.86
---------------------------------------------------------------------------
-
MR14965      0   -90    115    130     15  35.05  39.62   4.57  0.039
1.33
---------------------------------------------------------------------------
-
MR14967      0   -90                  No Significant Results
---------------------------------------------------------------------------
-
MR14995    261   -45    0.0   11.8   11.8   0.00   3.60   3.60  0.032
1.10
---------------------------------------------------------------------------
-
36.0   37.0    1.0  10.97  11.28   0.30  0.017
0.57
---------------------------------------------------------------------------
-
112.4  115.5    3.1  34.26  35.20   0.94  0.016
0.53
---------------------------------------------------------------------------
-
312.1  322.0    9.9  95.13  98.15   3.02  0.106
3.65
---------------------------------------------------------------------------
-
391.2  392.6    1.4 119.24 119.66   0.43  0.016
0.55
---------------------------------------------------------------------------
-
MR141031   210   -55   88.0   92.7    4.7  26.82  28.25   1.43  0.023
0.79
---------------------------------------------------------------------------
-
MR141033    94   -45  212.0  214.5    2.5  64.62  65.38   0.76  0.095
3.25
---------------------------------------------------------------------------
-
232.5  237.5      5  70.87  72.39   1.52  0.018
0.60
---------------------------------------------------------------------------
-
286.0  311.0     25  87.17  94.79   7.62  0.022
0.74
---------------------------------------------------------------------------
-
MR141034   218   -50  186.0  190.0      4  56.69  57.91   1.22  0.022
0.74
---------------------------------------------------------------------------
-
MR141048     0   -90                  No Significant Results
---------------------------------------------------------------------------
-





Table 2. Northwest Drinkwater Target - Significant Drill Results

---------------------------------------------------------------------------
-
Hole       Azm   Dip   From     To  Width   From     To  Width   Gold
Gold
No.      (deg) (deg)   (ft)   (ft)   (ft)    (m)    (m)    (m)  (OPT)
(g/t)
---------------------------------------------------------------------------
-
MR14989    205   -65  316.3  333.6   17.3  96.41 101.68   5.27  0.018
0.62
---------------------------------------------------------------------------
-
444.0  448.0    4.0 135.33 136.55   1.22  0.026
0.89
---------------------------------------------------------------------------
-
MR14990      0   -85  155.5  160.3    4.8  47.40  48.86   1.46  0.034
1.17
---------------------------------------------------------------------------
-
164.0  167.0    3.0  49.99  50.90   0.91  0.022
0.75
---------------------------------------------------------------------------
-
216.6  221.4    4.8  66.02  67.48   1.46  0.033
1.13
---------------------------------------------------------------------------
-
245.0  249.7    4.7  74.68  76.11   1.43  0.016
0.55
---------------------------------------------------------------------------
-
598.7  600.0    1.3 182.48 182.88   0.40  0.036
1.23
---------------------------------------------------------------------------
-
MR141011   225   -65  548.9  553.5    4.6 167.30 168.71   1.40  0.026
0.88
---------------------------------------------------------------------------
-
619.9    624    4.1 188.95 190.20   1.25  0.022
0.75
---------------------------------------------------------------------------
-



//et

All holes presented in Table 1 were completed by reverse
circulation (RC) drilling with the exception of 7 core holes MR14995,
MR141031, 33 and 34, MR14989, 90 and MR141011. True width is estimated
at 80-100% of downhole width. Analytical results were performed by
American Assay Laboratory Inc. in Sparks, Nevada, an ISO/IEC 17025:2005
accredited facility. External check assays to verify lab accuracy are
routinely completed by ALS Chemex, an ISO 9001:2000 certified and
ISO/IEC 17025:2005 accredited facility. Further details are presented
in the Company's quality assurance and quality control program for the
Mineral Ridge project available at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge
gold mining operation located in Esmeralda County, Nevada with joint
venture partner Waterton Global Value L.P. (30%). Mineral Ridge is a
conventional open pit mining and heap leach operation. The Mineral
Ridge property is host to multiple gold-bearing structures, veins and
lenses at exploration, development and production stages. Scorpio Gold
also holds a 100% interest in the advanced exploration-stage Goldwedge
property in Manhattan, Nevada, with a fully permitted underground mine
and 400 ton per day mill facility.
Scorpio Gold's President & CEO, Peter J. Hawley, PGeo,, is a
Qualified Person as defined by National Instrument 43-101 and has
reviewed and approved the content of this release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, President & CEO

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking
statements. This news release contains forward-looking statements that
are based on the Company's current expectations and estimates.
Forward-looking statements are frequently characterized by words such
as "plan", "expect", "project", "intend", "believe", "anticipate",
"estimate", "suggest", "indicate" and other similar words or statements
that certain events or conditions "may" or "will" occur, and include,
without limitation, statements regarding the Company's plans with
respect to the exploration, development and exploitation of its Mineral
Ridge project. Such forward-looking statements involve known and
unknown risks, uncertainties and other factors that could cause actual
events or results to differ materially from estimated or anticipated
events or results implied or expressed in such forward-looking
statements, including risks involved in mineral exploration and
development programs and those risk factors outlined in the Company's
Management Discussion and Analysis as filed on SEDAR. Any
forward-looking statement speaks only as of the date on which it is
made and, except as may be required by applicable securities laws, the
Company disclaims any intent or obligation to update any
forward-looking statement, whether as a result of new information,
future events or results or otherwise. Forward-looking statements are
not guarantees of future performance and accordingly undue reliance
should not be put on such statements due to the inherent uncertainty
thereof.

Peter J. Hawley
President & CEO
(819) 825-7618
phawley@scorpiogold.com
www.scorpiogold.com
______________________________________
_______________________________________________
TSX Venture closing price for SGN-V
Date: 2015/08/21
Closing Price: 0.10
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1523500005TS11523500453-05532820150824