Source	MARKET NEWS
Date	08/11/2015
Time	06:23:13 AM

Company	 International Lithium Corp.
Title	Continuing Work in Argentina and Ireland





    CDNX Symbol: ILC











Press Release	





Continuing Work in Argentina and Ireland --->@NEWS RELEASE
INTERNATIONAL LITHIUM CORP ("ILC-V;ILHMF-0")
- Continuing Work in  Argentina and Ireland

International Lithium Corp. (the "Company" or "ILC") (@
http://ca.finance.yahoo.com/q?s=ilc.v) is pleased to provide an update
on the Mariana Project in Argentina and the Avalonia Project in
Ireland.

The Mariana lithium brine project in Salta province, Argentina and
the Avalonia lithium pegmatite project in Counties Carlow and Wicklow
in Ireland are joint ventures with strategic partner Ganfeng Lithium
Co. Ltd., ("GFL"). GFL is a leading China based lithium products
manufacturer working to vertically integrate their lithium business and
secure supplies of lithium raw materials. The work summarized here is
the result of the 2014/2015 exploration budget for both projects,
estimated at CAN $2,645,000.

Programs on both projects were completed within the allocated
budget. The Company is currently in discussions with GFL over budgets
proposed for exploration programs on both projects.

Mariana Project - Salta, Argentina

As announced on June 1, 2015 a 171-metre core recovery drill hole
("DHMA15-09PW") was completed near the centre of Salar de Llullaillaco
approximately 20 metres from drill hole DHMA12-07, a reverse
circulation ("RC") drill hole. Drill hole DHMA15-09PW confirmed the
presence of two aquifers. One aquifer is from surface to 30 metres
while the other is from 53 to 119 metres.

Analytical results from the 2015 drill hole are similar to those
from the 2012 drill program, for example the interval from 6.3 to 111.5
metres averages 318 mg/L lithium, 9,255 mg/L potassium and 605 mg/L
boron. Table 1 compares the lithium results from drill hole DHMA15-09PW
with those of DHMA12-07.

Analytical results from samples collected at DHMA10-01 and -02
(located 890 metres to the east and 950 metres to the west,
respectively) are also consistent with the results from DHMA15-09 and
DHMA12-07 indicating a uniform concentration of metals and metal ratios
over a large surface area as well as throughout the two aquifers.

Analytical results taken during the pump tests remained consistent
even after long periods of pumping further supporting the concept that
metal concentrations within Salar de Llullaillaco may be homogenous
over a large area.

Table 1: 2015 Brine Sample Results compared with 2012 results for
drill hole DHMA12-07.

//st

-------------------------------------------------------
|Drill      |Li    |K     |B     |Mg    |Mg / |Charge |
|Hole       |(mg/L)|(mg/L)|(mg/L)|(mg/L)|Li   |Balance|
|No.        |      |      |      |      |ratio|(%)    |
|-----------------------------------------------------|
|DHMA12-07  |      |      |      |      |     |       |
|-----------------------------------------------------|
|Avg        |300   |9774  |656   |4534  |15.12|-0.5   |
|-----------------------------------------------------|
|Max        |327   |10655 |770   |4947  |16.28|2.5    |
|-----------------------------------------------------|
|Min        |271   |9168  |610   |4323  |14.54|-6.9   |
|-----------------------------------------------------|
|           |      |      |      |      |     |       |
|-----------------------------------------------------|
|DHMA15-09PW|      |      |      |      |     |       |
|-----------------------------------------------------|
|Avg        |318   |9255  |605   |4478  |14.09|-2.8   |
|-----------------------------------------------------|
|Max        |341   |9818  |636   |4776  |14.71|-0.5   |
|-----------------------------------------------------|
|Min        |300   |8739  |554   |4355  |13.72|-6.0   |
|-----------------------------------------------------|
|           |      |      |      |      |     |       |
|-----------------------------------------------------|
|DHMA10-01  |311   |9789  |570   |4334  |13.94|-0.3   |
|-----------------------------------------------------|
|DHMA10-02  |320   |9942  |629   |4451  |13.91|-0.6   |
|-----------------------------------------------------|
|           |      |      |      |      |     |       |
-------------------------------------------------------

//et

The uniformity of the brine chemistry is an important property of
the aquifer as it will simplify the development of a robust process
path.

A series of three pumping tests were carried out on the well
battery centred on DHMA15-09. These tests were:

1.An initial two-hour constant rate test at the maximum pumping
capacity of 9.5 L/sec to test equipment function, ensure proper well
development and test the aquifers.

2.Step tests at 4.4, 5.9, 7.2 and 8 L/sec to test flow rate and
brine level draw down as well as efficiency of the pumping well.

3.24 hour constant rate test at 8 L/sec followed by a 12-hour
recovery test to test aquifer storability and transmissivity.

The results of the pumping tests report:

-Well design performs at a high level of efficiency, 88%.

-Well can support a very high pumping rate up to 350m3/hr (97
L/sec).

-Brine level achieves a steady state within minutes of the
cessation of pumping indicating that the aquifer transmits brine
rapidly and does not rely on storage capacity.

-Both aquifers have a high transmissivity averaging 5,544m3/day.

The results continue to confirm that Salar de Llullaillaco (a
halite dominant, mature salar) bears a significant stratigraphic and
hydrogeological resemblance to prominent salars in the region including
Atacama, Rincon and Uyuni.

Avalonia Project - Ireland

As announced on June 1, 2015 a programme of mapping, prospecting
and geochemical sampling over the 30 kilometre strike length of the
lithium-pegmatite belt has been completed and a preliminary
interpretation of the results concluded.

Twelve (12) new targets were identified through geochemical
surveys and prospecting, bringing the total to 21 targets now
identified within the belt as having a high probability of containing
spodumene bearing pegmatite. Only 7 of these targets have had any drill
testing with three showing significant spodumene intersections and
elevated lithium concentrations.

The pegmatite belt is buried under soil cover with very little
outcrop making exploration difficult. Targets are considered blind and
historically, lithium pegmatites were located by prospecting for
spodumene bearing boulders - often observed in field walls. The
regional and detailed geochemical surveys were designed to test the
belt in areas between the lithium bearing boulder trains. The surveys
have successfully outlined the main lithologies through cover and
subsequent drill testing confirms that pegmatites can be traced by soil
geochemistry.

A small 680 metre drill program of fifteen (15) holes was
conducted over two target areas more than three kilometres apart. Each
area had a line of short holes drilled across the target. At the first
target several pegmatite bodies were intersected but none with
significant spodumene. At the second target area spodumene bearing
pegmatite grading 1.29% Li2O over 1.60 metres was intersected at
shallow depth, adjacent to subcrop containing spodumene (MON15-09). In
addition, part of the secong target area successfully tested below a
lithium soil anomaly for a blind bedrock source. MON15-14 intersected
pegmatite grading 2.24% Li2O over 0.71 metres. All widths are reported
in core length and do not reflect true width. Both tests in the second
area confirm the viability of the exploration methods used for
advancing exploration targets to the delineation drilling stage.

Oriented core technology was used at both targets to maximize
collection of structural data and confirm the orientation of the
pegmatite bodies to better target future drilling campaigns. Previous
pegmatite drilling experience indicates that granitic pegmatites can
occur in proximity to spodumene and rare metal bearing pegmatites.
Further work is planned at both target areas.

Work reports, as required by the Energy and Mines Division,
Republic of Ireland, are now submitted for the eight prospecting
licenses.

The goal for future exploration programs will be to 1) identify
the contact zone between the pegmatites and the country rocks with
greater accuracy using detailed magnetic surveys and if warranted other
geophysical methods, 2) continue detailed geochemical surveys and
trenching to refine drill targets, 3) drill test new targets for
bedrock sources and 4) conduct delineation drilling on established
lithium pegmatites.

Future exploration plans call for a significant increase in the
budget to effectively test high priority target areas.

Mr. Kirill Klip, President, International Lithium Corp. comments,
"Our projects are advancing in tandem with rising lithium prices. The
lithium supply chain is being stressed even before the commissioning of
the Tesla Gigafactory and other megafactories from BYD, Foxconn, Boston
Power and LG Chem. Our joint ventures with Ganfeng Lithium demonstrate
that cooperation between companies with varying expertise in the raw
materials supply chain can work to secure a supply of strategic
commodities. In this case, lithium which is necessary for the clean
energy initiatives announced by the U.S. and China. These two countries
alone will provide mass markets for electric cars and home energy
storage units increasing the demand for lithium batteries."

John Harrop, P.Geo, FGS, is the Company's Qualified Person on the
project as defined under NI 43-101 and has reviewed the technical
information contained in this press release.

About International Lithium Corp.

International Lithium Corp. is an exploration company with an
outstanding portfolio of projects, strong management ownership, robust
financial support and a strategic partner and keystone investor GFL
International, a fully owned subsidiary of Ganfeng Lithium Co. Ltd., a
leading China based lithium product manufacturer.

The Company's primary focus is the Mariana lithium-potash brine
project, within the renowned South American "Lithium Belt" that is the
host to the vast majority of global lithium resources, reserves and
production. The 160 square kilometre Mariana project strategically
encompasses an entire mineral rich evaporate basin that ranks as one of
the more prospective salars or 'salt lakes' in the region.

Complementing the Company's lithium brine project are rare metals
pegmatite properties in Canada and Ireland. These projects reported
highly encouraging lithium mineralization in drill holes targeting
pegmatites that are unexposed at surface (news releases dated April
3,2013 and June 25, 2013).

With the increasing demand for high tech rechargeable batteries
used in vehicle propulsion technologies and portable electronics,
lithium is paramount to tomorrow's "green-tech" economy. By positioning
itself with solid development partners and acquiring high quality grass
roots projects at an early stage of exploration, ILC aims to be the
green tech resource explorer of choice for investors and build value
for its shareholders.

On behalf of the Board of Directors,

Kirill Klip

President, International Lithium Corp.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release. Statements in this press release other than purely historical
information, historical estimates should not be relied upon, including
statements relating to the Company's future plans and objectives or
expected results, are forward-looking statements. News release contains
certain "Forward-Looking Statements" within the meaning of Section 21E
of the United States Securities Exchange Act of 1934, as amended.
Forward-looking statements are based on numerous assumptions and are
subject to all of the risks and uncertainties inherent in the Company's
business, including risks inherent in resource exploration and
development. As a result, actual results may vary materially from those
described in the forward-looking statements.





__________________________________________________
_______________________________________________
TSX Venture closing price for ILC-V
Date: 2015/08/10
Closing Price: 0.04
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1522200012TS11522200901-06221520150811