Source	MARKET NEWS
Date	08/11/2015
Time	05:15:05 AM

Company	 Terrax Minerals Inc.
Title	Terrax 
Channel Samples 11.0 M @ 7.55 G/T Au Acro





    CDNX Symbol: TXR











Press Release	





TERRAX MINERALS INC ("TXR-V")
- Terrax Channel Samples 11.0 M @ 7.55 G/T Au Across Strike Of
- New Zone On Barney Deformation Corridor, Yellowknife City Gold
- Project

TerraX Minerals Inc. has received results from channel sampling of
a new zone of mineralization, the Hebert-Brent showing, on its
Yellowknife City Gold Project ("YCG"), immediately north of Yellowknife
in the Northwest Territories. Assays from cut channel sampling across
the strike of the zone returned 11.0 metres @ 7.55 g/t Au.This result
is highly significant, being 1 km south and on strike with the Barney
Zone drilled in 2014 (22.42 m @ 6.35 g/t Au in hole NB95-16W1 - see our
news release of August 25, 2014) on a newly mapped deformation zone
called the Barney Deformation Corridor ("BDC").

Joe Campbell, P. Geo, President of TerraX states "This high grade
sampling result reported today is illustrative of the prospectivity of
the YCG, where we have the ability to discover top quality virgin
mineralization on surface within an established major Canadian Gold
camp."

Importantly, the sericite-ankerite alteration sampled at the
Hebert-Brent showing is very similar to alteration zonation at the C-1
shaft area at the past producing Con Mine to the south on the same
structure. Sericite-ankerite altered schists have therefore become key
exploration criteria for identifying potential gold mineralization in
the YCG; numerous additional sericitic zones have been discovered in
reconnaissance mapping in the BDC this summer and assay results are
pending.

The channel sampling program returned gold assay results averaging
7.55 g/t over 11 metres of contiguous one (1) metre channel samples.
Maps and pictures of the sampled area in the Barney Deformation
Corridor are available under "Field Exploration 2015" on our web site
at www.terraxminerals.com.

//st
Sample ID           From (m)      To (m)      Interval (m)      Au (g/t)
R953442                 0.00        1.00              1.00          1.13
R953443                 1.00        2.00              1.00         24.70
R953444                 2.00        3.00              1.00         24.60
R953445                 3.00        4.00              1.00          1.68
R953446                 4.00        5.00              1.00          4.20
R953447                 5.00        6.00              1.00          2.76
R953651                 6.00        7.00              1.00          0.89
R953652                 7.00        8.00              1.00         11.35
R953653                 8.00        9.00              1.00          7.10
R953687                 9.00       10.00              1.00          2.15
R953688                10.00       11.00              1.00          2.45
//et

About the Barney Deformation Corridor

Geological mapping in June and July identified several areas of
extensive sericite alteration in the Core Gold area of the Northbelt
Property. This work resulted in the discovery of a new surface showing
associated with a mapped deformation zone called the Barney Deformation
Corridor ("BDC") approximately 1km south and on strike with the Barney
Zone drilled by TerraX in 2014 and winter 2015. The new zone, coined
the Hebert-Brent showing, had a hand dug trench completed in July 2015
to uncover fresh bedrock for channel sampling beneath the weathered
sericite of the showing. This work revealed an 11 m-wide sulphide
mineralized sericite-ankerite schist shear zone intersected by a 10-15
m wide felsic intrusive. The mineralization consists of:

i) 20% to 60 % semi-massive, fine-grained sulphide needles, clots
and 1-3 cm wide bands; and

ii) 1-3% fine grained stibnite associated with the sulphides
(stibnite was an accessory mineral in the Con deposit which had
historic production of 6.1 Moz Au).

The orientation of the felsic dyke rotates from an SSE strike into
the direction of the main NNE shear zone. The main shear zone offsets
the felsic dyke in a dextral sense (ie. west side has moved north).This
structural setting would be favorable for creation of dilational zones
and associated gold mineralization.

The BDC has several areas that support the style of mineralization
in the Hebert-Brent showing:

Historic drill hole NB94-1A was drilled west of Hebert-Brent to
test the "20 Shear" and intersected a 21.12 m wide zone grading 2.97
g/t Au, and containing sulphide mineralization that is similar in
character to the Hebert-Brent showing.

Surface sampling in 2014 prospecting discovered outcrops of
sheared and silicified felsic volcanics with a 3 m to 5 m wide NNE
trending shear zone containing no quartz veins but mineralized with
20%-30% disseminated to massive sulphides and needles, and 2-3%
stibnite, and returning 44 g/t Au in samples from the Brent showing
located east of Hebert-Brent. The 2015 detailed mapping of Brent
revealed it as sheared and silicified mafic volcanics with a felsic
dyke in contact with sheared sediments.

To the north of the Hebert-Brent showing, surface sampling in 2014
and 2015 returned values of 126 g/t Au and 129.5 g/t Au in sheared
volcanics with quartz veins. This is approximately 600 meters south of
the main Barney Zone (22.42 m @ 6.35 g/t Au in NB95-16W1, drilled in
summer 2014), and 300 meters north of the Hebert-Brent showing.

Numerous additional sericitic zones have been discovered in
reconnaissance mapping in the BDC; assays are pending.

Sampling included insertion of certified standards and blanks into
the stream of samples for chemical analysis. Samples were prepared at
ALS Chemex's laboratory in Yellowknife and shipped to their Vancouver
facility for gold analysis by fire assay and other elements by ICP
analysis. ALS is a certified and accredited laboratory service. It
should be noted that, due to their selective nature, assay results from
grab samples may not be indicative of the overall grade and extent of
mineralization on the subject area. The technical information contained
in this news release has been approved by Joseph Campbell, President of
TerraX, who is a Qualified Person as defined in "National Instrument
43-101, Standards of Disclosure for Mineral Projects."

About the Yellowknife City Gold Project

The Yellowknife City Gold Project now encompasses approximately
99.3 sq km of contiguous land immediately north of the City of
Yellowknife in the Northwest Territories. Through a series of
acquisitions, TerraX now controls one of the six major high-grade gold
camps in Canada - and the least explored.

The project lies on the prolific Yellowknife greenstone belt and
covers 15 km of strike length on the northern extension of the shear
system that hosts the high-grade Con and Giant gold mines. The project
area contains multiple shears that are the recognized hosts for gold
deposits in the Yellowknife gold district, with innumerable gold
showings and high grade drill results this past year that serve to
indicate the project's potential as a world-class gold district. Since
February 2013, TerraX has consolidated the project area by acquiring,
optioning and staking numerous properties, including: Northbelt,
Goodwin, Ryan Lake, Walsh Lake, and U-Breccia, as well as staking
additional contiguous lands. Being all-season road accessible and
within 15 km of the City of Yellowknife, the YCG is close to vital
infrastructure, including transportation, service providers,
hydro-electric power and skilled trades people.

For more information on the Yellowknife City Gold Project, please
visit our web site at www.terraxminerals.com.

On behalf of the Board of Directors
Joseph Campbell, President

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release contains forward-looking information, which
involves known and unknown risks, uncertainties and other factors that
may cause actual events to differ materially from current expectation.
Important factors - including the availability of funds, the results of
financing efforts, the completion of due diligence and the results of
exploration activities - that could cause actual results to differ
materially from the Company's expectations are disclosed in the
Company's documents filed from time to time on SEDAR (see
www.sedar.com). Readers are cautioned not to place undue reliance on
these forward-looking statements, which speak only as of the date of
this press release. The company disclaims any intention or obligation,
except to the extent required by law, to update or revise any
forward-looking statements, whether as a result of new information,
future events or otherwise.


TEL:  514-341-0408  Paradox Public Relations
TSX Venture closing price for TXR-V
Date: 2015/08/10
Closing Price: 0.27

TEL:  1-866-460-0408
EMAIL:  info@paradox-pr.ca
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1522200004TS11522200469-05135120150811