Source	Marketwire
Date	08/13/2015
Time	05:03:24 AM

Company	 KAMINAK GOLD CORPORATION
Title	Kaminak Reports 2015 Infill Drill Results from Coffee Gold Project





    CDNX Symbol: KAM











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

August 13, 2015

Kaminak Reports 2015 Infill Drill Results from Coffee Gold Project

Highlights Include: 4.0 g/t Au over 27m, 6.2 g/t Au over 16.8m, 10.5 g/t Au 
over 9.1m, 18.6 g/t Au over 5.0m and 2.8 g/t Au over 32.0m

VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 13, 2015) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) today announced results from the 2015 infill 
drilling program at Coffee, Kaminak's flagship development track gold project 
located 130km south of Dawson City, Yukon. Infill drilling is now complete on 
all Coffee deposits, demonstrating good agreement with the existing block model 
and expected to result in a high conversion rate of in-pit resources from 
Inferred to Indicated in the updated 2015 block model underpining the 
Feasibility Study (FS), which is scheduled for completion in Q1, 2016. The 
results reported herein are predominantly from the Supremo deposit, which 
consists of six gold bearing structures (referred to as T1 to T5 and T7) that 
are interconnected and are interpreted to be part of the same mineralized 
system. Supremo contributes approximately 70% of the total ounces in the mine 
plan defined in the 2014 Coffee NI 43-101 Preliminary Economic Assessment (PEA).

"Our infill drilling program, which consisted of 70,000 metres, was executed on 
schedule and on budget in less than one year," stated Eira Thomas, Kaminak 
President & CEO. "Upgrading the confidence level of the Coffee gold resources 
is a big step towards de-risking Coffee as we move it through feasibility 
towards production."

In 2015, approximately 31,000 metres of infill drilling was undertaken on the 
series of parallel, north-south striking gold bearing structures comprising the 
Supremo deposit. Based on the 2014 PEA, the Supremo deposit contributes 
approximately 1,272,000 ounces of gold (recoverable) at an average diluted 
grade of 1.13 g/t Au in Oxide resources, plus an additional 44,000 ounces of 
gold at 1.64 g/t Au as Transitional-oxide resources. Drilling completed at 
Supremo has firmed up the existing geological interpretation providing 
additional confidence in the location, geometry and continuity of the 
mineralized lodes.

The location and spacing of infill drilling was determined in consultation with 
independent Qualified Person Robert Sim, P.Geo of SIM Geological Inc., who 
completed the Coffee Gold Project Mineral Resource Estimates (announced 
December 13, 2012, and updated January 28, 2014). The Company is now in the 
process of updating the Coffee mineral resource estimate for inclusion in the 
final feasibility study.

All maps, sections and assay sheets associated with this news release can be 
viewed by clicking the following link: 
http://kaminak.com/news_releases/index.php?&content_id=634

Kona North Drill Results

Kaminak also announced today the results from step-out drilling at the Kona 
North prospect consisting of two holes, CFD0601 and CFD0602, drilled 40m east 
along strike from CFR0976, which was drilled earlier this year and returned 
2.43 g/t Au over 50.3m. Both step-out holes intersected gold mineralization 
with the best intercept returning 2.4 g/t Au over 19m in CFD0602, and extending 
the strike length of the Kona North deposit to 330m while still remaining open 
along strike and at depth.
The depth extent of Oxide and Transitional mineralization appears to be quite 
shallow at Kona North compared to other Coffee gold deposits resulting from 
localized erosion of the upper sections of the mineralized structure. However 
there remains good potential to test for extensions of the Oxide mineralization 
at shallower levels of the system along strike to the east and west within the 
1.8km long gold-in-soil anomaly.

Table 1 2015 Coffee Infill and Kona North Drilling Results

/T/

----------------------------------------------------------------------------
Weighted
Average
From          To       Width       Grade
Prospect        Drill Hole           (m)         (m)         (m)    (g/t Au)
----------------------------------------------------------------------------
2015 Coffee Infill Drilling
----------------------------------------------------------------------------
Supremo T3      CFD0500               90         100          10        2.76
----------------------------------------------------------------------------
Supremo T3      CFD0501             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFD0502               29          36           7        1.39
----------------------------------------------------------------------------
Supremo T3      CFD0503              116         119           3       22.12
----------------------------------------------------------------------------
Supremo T3      CFD0503              201         204           3        7.01
----------------------------------------------------------------------------
Supremo T3      CFD0504               82          89           7       10.28
----------------------------------------------------------------------------
Supremo T3      CFD0504               96         100           4        3.25
----------------------------------------------------------------------------
Supremo T3      CFD0505              177         183           6        3.33
----------------------------------------------------------------------------
Supremo T3      CFD0506              144         149           5        2.12
----------------------------------------------------------------------------
Supremo T3      CFD0506              154         160           6        2.15
----------------------------------------------------------------------------
Supremo T3      CFD0506              193         194           1        11.1
----------------------------------------------------------------------------
Supremo T3      CFD0507               35          38           3        4.51
----------------------------------------------------------------------------
Supremo T3      CFD0507              143         148           5         5.2
----------------------------------------------------------------------------
Supremo T3      CFD0509              224         229           5        2.15
----------------------------------------------------------------------------
Supremo T3      CFD0509              275         278           3        3.81
----------------------------------------------------------------------------
Supremo T3      CFD0510               15          27          12        2.77
----------------------------------------------------------------------------
Supremo T3      CFD0511               37          45           8        7.95
----------------------------------------------------------------------------
Supremo T3      CFD0511               58          65           7        3.36
----------------------------------------------------------------------------
Supremo T3      CFD0513              111         114           3        2.18
----------------------------------------------------------------------------
Supremo T5      CFD0514              112         122          10        4.03
----------------------------------------------------------------------------
Supremo T1-2    CFD0516               88          90           2         2.4
----------------------------------------------------------------------------
Supremo T5      CFD0517              152         155           3        3.16
----------------------------------------------------------------------------
Supremo T5      CFD0519               50          58           8        1.84
----------------------------------------------------------------------------
Supremo T1-2    CFD0520               33          39           6        2.32
----------------------------------------------------------------------------
Supremo T1-2    CFD0521              112         115           3        8.08
----------------------------------------------------------------------------
Supremo T1-2    CFD0521              134         138           4        2.97
----------------------------------------------------------------------------
Supremo T5      CFD0523              202         205           3        2.61
----------------------------------------------------------------------------
Supremo T1-2    CFD0524               58          62           4        2.77
----------------------------------------------------------------------------
Supremo T5      CFD0525                6           9           3        5.58
----------------------------------------------------------------------------
Supremo T5      CFD0525               19          23           4        5.97
----------------------------------------------------------------------------
Supremo T1-2    CFD0526               94          98           4        3.09
----------------------------------------------------------------------------
Supremo T5      CFD0527             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFD0528               53          55           2        0.96
----------------------------------------------------------------------------
Supremo T1-2    CFD0529               38          45           7        1.62
----------------------------------------------------------------------------
Supremo T5      CFD0531              138         145           7        1.77
----------------------------------------------------------------------------
Supremo T5      CFD0531              183         188           5        2.02
----------------------------------------------------------------------------
Supremo T5      CFD0531              204         210           6         4.9
----------------------------------------------------------------------------
Supremo T5      CFD0532              140         152          12        1.44
----------------------------------------------------------------------------
Supremo T1-2    CFD0533               27          28           1        4.23
----------------------------------------------------------------------------
Supremo T5      CFD0535              133         146          13        1.37
----------------------------------------------------------------------------
Supremo T5      CFD0535              160         165           5        3.98
----------------------------------------------------------------------------
Supremo T5      CFD0536               26          28           2        3.41
----------------------------------------------------------------------------
Supremo T5      CFD0537              130         133           3        1.89
----------------------------------------------------------------------------
Supremo T5      CFD0539               68          75           7        7.77
----------------------------------------------------------------------------
Supremo T5      CFD0540              212         220           8        1.63
----------------------------------------------------------------------------
Supremo T5      CFD0541               57          64           7        4.26
----------------------------------------------------------------------------
Supremo T1-2    CFD0542               51          53           2       35.35
----------------------------------------------------------------------------
Supremo T1-2    CFD0542              124         128           4        6.06
----------------------------------------------------------------------------
Supremo T1-2    CFD0542              139         149          10        4.09
----------------------------------------------------------------------------
Supremo T1-2    CFD0542              227         229           2        5.38
----------------------------------------------------------------------------
Supremo T5      CFD0543               42          43           1        1.32
----------------------------------------------------------------------------
Supremo T1-2    CFD0544             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFD0546               10          22          12        1.71
----------------------------------------------------------------------------
Supremo T1-2    CFD0546              179         185           6       10.36
----------------------------------------------------------------------------
Supremo T1-2    CFD0547               88          90           2        3.17
----------------------------------------------------------------------------
Supremo T5      CFD0548              173         188          15        2.19
----------------------------------------------------------------------------
Supremo T1-2    CFD0549              137         138           1        1.53
----------------------------------------------------------------------------
Supremo T1-2    CFD0551             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFD0552              171         179           8        1.68
----------------------------------------------------------------------------
Supremo T1-2    CFD0553               97         124          27        4.04
----------------------------------------------------------------------------
Supremo T1-2    CFD0554              102         106           4        2.82
----------------------------------------------------------------------------
Supremo T1-2    CFD0554              118         121           3        5.17
----------------------------------------------------------------------------
Supremo T1-2    CFD0554              188         204          16         2.6
----------------------------------------------------------------------------
Supremo T5      CFD0555              144         161          17        4.74
----------------------------------------------------------------------------
Supremo T1-2    CFD0556              186         187           1        1.57
----------------------------------------------------------------------------
Supremo T1-2    CFD0557              119         143          24        2.39
----------------------------------------------------------------------------
Supremo T1-2    CFD0557              189         194           5       10.58
----------------------------------------------------------------------------
Supremo T5      CFD0558              165         170           5        3.34
----------------------------------------------------------------------------
Supremo T3      CFD0559               69          71           2         6.9
----------------------------------------------------------------------------
Supremo T3      CFD0559               93          99           6        
6.72----------------------------------------------------------------------------
Supremo T1-2    CFD0561              109         114           5       18.62
----------------------------------------------------------------------------
Supremo T1-2    CFD0561              132         135           3        3.54
----------------------------------------------------------------------------
Supremo T1-2    CFD0562              210         214           4        1.35
----------------------------------------------------------------------------
Supremo T5      CFD0563               54          58           4        13.9
----------------------------------------------------------------------------
Supremo T7      CFD0564               45          51           6        2.22
----------------------------------------------------------------------------
Supremo T7      CFD0565               32          34           2        1.61
----------------------------------------------------------------------------
Supremo T5      CFD0566               54          58           4       14.44
----------------------------------------------------------------------------
Supremo T1-2    CFD0567              185         189           4         1.3
----------------------------------------------------------------------------
Supremo T7      CFD0568               77          81           4        2.06
----------------------------------------------------------------------------
Supremo T5      CFD0569               44          48           4        4.42
----------------------------------------------------------------------------
Supremo T7      CFD0570               81          90           9        1.84
----------------------------------------------------------------------------
Supremo T7      CFD0571               61          63           2        2.02
----------------------------------------------------------------------------
Supremo T5      CFD0572              113         122           9        2.21
----------------------------------------------------------------------------
Supremo T5      CFD0574               41          43           2        2.32
----------------------------------------------------------------------------
Supremo T4      CFD0575             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFD0576             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T5      CFD0577               98         100           2        4.24
----------------------------------------------------------------------------
Supremo T7      CFD0578               42          44           2        3.74
----------------------------------------------------------------------------
Supremo T5      CFD0579               60          65           5        9.54
----------------------------------------------------------------------------
Supremo T1-2    CFD0580              196         202           6        1.29
----------------------------------------------------------------------------
Supremo T4      CFD0581             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFD0582               84          86           2        3.48
----------------------------------------------------------------------------
Supremo T4      CFD0583             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFD0584              104         105           1        2.44
----------------------------------------------------------------------------
Supremo T3      CFD0585               93          98           5         0.9
----------------------------------------------------------------------------
Supremo T4-5    CFD0586              127         133           6        3.89
----------------------------------------------------------------------------
Supremo T4-5    CFD0586              201         207           6        2.04
----------------------------------------------------------------------------
Supremo T5-7    CFD0587               30          34           4        4.23
----------------------------------------------------------------------------
Supremo T5-7    CFD0588               55          58           3        6.46
----------------------------------------------------------------------------
Supremo T7      CFD0589               37          46           9        0.82
----------------------------------------------------------------------------
Supremo T5-7    CFD0590               51          53           2        1.87
----------------------------------------------------------------------------
Supremo T3      CFD0591              145         149           4        3.66
----------------------------------------------------------------------------
Supremo T3      CFD0592               99         105           6         2.7
----------------------------------------------------------------------------
Supremo T3      CFD0592              114         122           8        2.75
----------------------------------------------------------------------------
Supremo T3      CFD0592              219         224           5        2.16
----------------------------------------------------------------------------
Supremo T4-5    CFR0804           103.63      115.82       12.19        3.35
----------------------------------------------------------------------------
Supremo T3      CFR0805            67.06       79.25       12.19        4.05
----------------------------------------------------------------------------
Supremo T3      CFR0805            89.92      103.63       13.71        1.06
----------------------------------------------------------------------------
Supremo T3      CFR0805           123.44      129.54         6.1        3.66
----------------------------------------------------------------------------
Supremo T3      CFR0806            77.72       99.06       21.34        0.97
----------------------------------------------------------------------------
Supremo T3      CFR0807            21.34       25.91        4.57        1.72
----------------------------------------------------------------------------
Supremo T3      CFR0808            21.34       27.43        6.09        2.95
----------------------------------------------------------------------------
Supremo T3      CFR0809               32       36.58        4.58        1.79
----------------------------------------------------------------------------
Supremo T3      CFR0810            64.01       74.68       10.67        2.07
----------------------------------------------------------------------------
Supremo T3      CFR0810            91.44       108.2       16.76        1.05
----------------------------------------------------------------------------
Supremo T3      CFR0810           117.35       120.4        3.05        3.83
----------------------------------------------------------------------------
Supremo T3      CFR0811            114.3      132.59       18.29        2.33
----------------------------------------------------------------------------
Supremo T3      CFR0812           129.54      134.11        4.57        4.18
----------------------------------------------------------------------------
Supremo T3      CFR0813            50.29       60.96       10.67        1.79
----------------------------------------------------------------------------
Supremo T3      CFR0813           102.11      109.73        7.62        4.45
----------------------------------------------------------------------------
Supremo T3      CFR0814           143.26      147.83        4.57        3.02
----------------------------------------------------------------------------
Supremo T3      CFR0815            71.63       74.68        3.05       15.67
----------------------------------------------------------------------------
Supremo T3      CFR0816             9.14       21.34        12.2        3.86
----------------------------------------------------------------------------
Supremo T3      CFR0817             70.1       77.72        7.62        3.45
----------------------------------------------------------------------------
Supremo T3      CFR0818            59.44       64.01        4.57        2.94
----------------------------------------------------------------------------
Supremo T3      CFR0819            59.44       62.48        3.04        5.72
----------------------------------------------------------------------------
Supremo T3      CFR0819           112.78      121.92        9.14        1.32
----------------------------------------------------------------------------
Supremo T3      CFR0820             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFR0821            16.76       22.86         6.1        4.29
----------------------------------------------------------------------------
Supremo T3      CFR0822            88.39       91.44        3.05        3.79
----------------------------------------------------------------------------
Supremo T3      CFR0823             76.2       91.44       15.24         5.5
----------------------------------------------------------------------------
Supremo T3      CFR0823           150.88      153.92        3.04        7.98
----------------------------------------------------------------------------
Supremo T3      CFR0824             NSV or did not reach target depth
----------------------------------------------------------------------------
Double Double   CFR0825            12.19       16.76        4.57        4.75
----------------------------------------------------------------------------
Double Double   CFR0825               32       41.15        9.15       10.47
----------------------------------------------------------------------------
Supremo T3      CFR0826            25.91       35.05        9.14        1.06
----------------------------------------------------------------------------
Double Double   CFR0827            54.86       57.91        3.05        9.31
----------------------------------------------------------------------------
Double Double   CFR0829             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFR0830           111.25      115.82        4.57        4.55
----------------------------------------------------------------------------
Supremo T3      CFR0830           128.02      160.02          32        2.77
----------------------------------------------------------------------------
Supremo T5      CFR0831            36.58       41.15        4.57        5.07
----------------------------------------------------------------------------
Supremo T7      CFR0832            51.82       54.86        3.04        4.52
----------------------------------------------------------------------------
Supremo T5      CFR0833            41.15       47.24        6.09        3.83
----------------------------------------------------------------------------
Supremo T7      CFR0834             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFR0835            41.15        44.2        3.05        1.19
----------------------------------------------------------------------------
Double Double   CFR0836            35.05       36.58        1.53        1.48
----------------------------------------------------------------------------
Double Double   CFR0837            35.05       36.58        1.53        1.38
----------------------------------------------------------------------------
Supremo T7      CFR0838             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T5      CFR0839            47.24       50.29        3.05        6.22
----------------------------------------------------------------------------
Supremo T7      CFR0840           155.45       158.5        3.05        3.52
----------------------------------------------------------------------------
Supremo T5      CFR0841           103.63      109.73         6.1        0.65
----------------------------------------------------------------------------
Supremo T4-5    CFR0842            89.92       94.49        4.57        2.93
----------------------------------------------------------------------------
Supremo T5      CFR0843            16.76       27.43       10.67        1.88
----------------------------------------------------------------------------
Supremo T5      CFR0843           124.97      128.02        3.05        3.53
----------------------------------------------------------------------------
Supremo T5      CFR0844            47.24       57.91       10.67        1.89
----------------------------------------------------------------------------
Supremo T5      CFR0845            47.24       50.29        3.05        3.77
----------------------------------------------------------------------------
Supremo T7      CFR0846            99.06      103.63        4.57        1.54
----------------------------------------------------------------------------
Supremo T4-5    CFR0847            33.53       59.44       25.91        1.59
----------------------------------------------------------------------------
Supremo T5      CFR0848           135.64      138.68        3.04         2.7
----------------------------------------------------------------------------
Supremo T7      CFR0849             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T5      CFR0850            35.05        38.1        3.05        3.96
----------------------------------------------------------------------------
Supremo T4-5    CFR0851            114.3      128.02       13.72        1.27
----------------------------------------------------------------------------
Supremo T5      CFR0852            45.72       50.29        4.57        5.81
----------------------------------------------------------------------------
Supremo T5      CFR0852            60.96       67.06         6.1        5.04
----------------------------------------------------------------------------
Supremo T7      CFR0853            22.86       36.58       13.72        3.37
----------------------------------------------------------------------------
Supremo T5      CFR0854             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFR0855             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T4-5    CFR0856            54.86       60.96         6.1        
0.66----------------------------------------------------------------------------
Supremo T4-5    CFR0857             38.1       39.62        1.52        1.95
----------------------------------------------------------------------------
Supremo T4-5    CFR0858              6.1       13.72        7.62        1.98
----------------------------------------------------------------------------
Supremo T4-5    CFR0858            71.63        76.2        4.57        2.79
----------------------------------------------------------------------------
Supremo T4-5    CFR0859             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFR0860              6.1        7.62        1.52        4.73
----------------------------------------------------------------------------
Supremo T4-5    CFR0861            91.44      112.78       21.34        1.41
----------------------------------------------------------------------------
Supremo T4-5    CFR0861            146.3      161.54       15.24        1.78
----------------------------------------------------------------------------
Supremo T7      CFR0862           153.92       158.5        4.58        1.78
----------------------------------------------------------------------------
Supremo T4-5    CFR0863           103.63      111.25        7.62        0.71
----------------------------------------------------------------------------
Supremo T4-5    CFR0864            59.44       60.96        1.52        7.34


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Kaminak Gold Corporation

TSX VENTURE SYMBOL: KAM

August 13, 2015

Kaminak Reports 2015 Infill Drill Results from Coffee Gold Project

Highlights Include: 4.0 g/t Au over 27m, 6.2 g/t Au over 16.8m, 10.5 g/t Au 
over 9.1m, 18.6 g/t Au over 5.0m and 2.8 g/t Au over 32.0m

VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 13, 2015) - Kaminak Gold 
Corporation (TSX VENTURE:KAM) today announced results from the 2015 infill 
drilling program at Coffee, Kaminak's flagship development track gold project 
located 130km south of Dawson City, Yukon. Infill drilling is now complete on 
all Coffee deposits, demonstrating good agreement with the existing block model 
and expected to result in a high conversion rate of in-pit resources from 
Inferred to Indicated in the updated 2015 block model underpining the 
Feasibility Study (FS), which is scheduled for completion in Q1, 2016. The 
results reported herein are predominantly from the Supremo deposit, which 
consists of six gold bearing structures (referred to as T1 to T5 and T7) that 
are interconnected and are interpreted to be part of the same mineralized 
system. Supremo contributes approximately 70% of the total ounces in the mine 
plan defined in the 2014 Coffee NI 43-101 Preliminary Economic Assessment (PEA).

"Our infill drilling program, which consisted of 70,000 metres, was executed on 
schedule and on budget in less than one year," stated Eira Thomas, Kaminak 
President & CEO. "Upgrading the confidence level of the Coffee gold resources 
is a big step towards de-risking Coffee as we move it through feasibility 
towards production."

In 2015, approximately 31,000 metres of infill drilling was undertaken on the 
series of parallel, north-south striking gold bearing structures comprising the 
Supremo deposit. Based on the 2014 PEA, the Supremo deposit contributes 
approximately 1,272,000 ounces of gold (recoverable) at an average diluted 
grade of 1.13 g/t Au in Oxide resources, plus an additional 44,000 ounces of 
gold at 1.64 g/t Au as Transitional-oxide resources. Drilling completed at 
Supremo has firmed up the existing geological interpretation providing 
additional confidence in the location, geometry and continuity of the 
mineralized lodes.

The location and spacing of infill drilling was determined in consultation with 
independent Qualified Person Robert Sim, P.Geo of SIM Geological Inc., who 
completed the Coffee Gold Project Mineral Resource Estimates (announced 
December 13, 2012, and updated January 28, 2014). The Company is now in the 
process of updating the Coffee mineral resource estimate for inclusion in the 
final feasibility study.

All maps, sections and assay sheets associated with this news release can be 
viewed by clicking the following link: 
http://kaminak.com/news_releases/index.php?&content_id=634

Kona North Drill Results

Kaminak also announced today the results from step-out drilling at the Kona 
North prospect consisting of two holes, CFD0601 and CFD0602, drilled 40m east 
along strike from CFR0976, which was drilled earlier this year and returned 
2.43 g/t Au over 50.3m. Both step-out holes intersected gold mineralization 
with the best intercept returning 2.4 g/t Au over 19m in CFD0602, and extending 
the strike length of the Kona North deposit to 330m while still remaining open 
along strike and at depth.
The depth extent of Oxide and Transitional mineralization appears to be quite 
shallow at Kona North compared to other Coffee gold deposits resulting from 
localized erosion of the upper sections of the mineralized structure. However 
there remains good potential to test for extensions of the Oxide mineralization 
at shallower levels of the system along strike to the east and west within the 
1.8km long gold-in-soil anomaly.

Table 1 2015 Coffee Infill and Kona North Drilling Results

/T/

----------------------------------------------------------------------------
Weighted
Average
From          To       Width       Grade
Prospect        Drill Hole           (m)         (m)         (m)    (g/t Au)
----------------------------------------------------------------------------
2015 Coffee Infill Drilling
----------------------------------------------------------------------------
Supremo T3      CFD0500               90         100          10        2.76
----------------------------------------------------------------------------
Supremo T3      CFD0501             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFD0502               29          36           7        1.39
----------------------------------------------------------------------------
Supremo T3      CFD0503              116         119           3       22.12
----------------------------------------------------------------------------
Supremo T3      CFD0503              201         204           3        7.01
----------------------------------------------------------------------------
Supremo T3      CFD0504               82          89           7       10.28
----------------------------------------------------------------------------
Supremo T3      CFD0504               96         100           4        3.25
----------------------------------------------------------------------------
Supremo T3      CFD0505              177         183           6        3.33
----------------------------------------------------------------------------
Supremo T3      CFD0506              144         149           5        2.12
----------------------------------------------------------------------------
Supremo T3      CFD0506              154         160           6        2.15
----------------------------------------------------------------------------
Supremo T3      CFD0506              193         194           1        11.1
----------------------------------------------------------------------------
Supremo T3      CFD0507               35          38           3        4.51
----------------------------------------------------------------------------
Supremo T3      CFD0507              143         148           5         5.2
----------------------------------------------------------------------------
Supremo T3      CFD0509              224         229           5        2.15
----------------------------------------------------------------------------
Supremo T3      CFD0509              275         278           3        3.81
----------------------------------------------------------------------------
Supremo T3      CFD0510               15          27          12        2.77
----------------------------------------------------------------------------
Supremo T3      CFD0511               37          45           8        7.95
----------------------------------------------------------------------------
Supremo T3      CFD0511               58          65           7        3.36
----------------------------------------------------------------------------
Supremo T3      CFD0513              111         114           3        2.18
----------------------------------------------------------------------------
Supremo T5      CFD0514              112         122          10        4.03
----------------------------------------------------------------------------
Supremo T1-2    CFD0516               88          90           2         2.4
----------------------------------------------------------------------------
Supremo T5      CFD0517              152         155           3        3.16
----------------------------------------------------------------------------
Supremo T5      CFD0519               50          58           8        1.84
----------------------------------------------------------------------------
Supremo T1-2    CFD0520               33          39           6        2.32
----------------------------------------------------------------------------
Supremo T1-2    CFD0521              112         115           3        8.08
----------------------------------------------------------------------------
Supremo T1-2    CFD0521              134         138           4        2.97
----------------------------------------------------------------------------
Supremo T5      CFD0523              202         205           3        2.61
----------------------------------------------------------------------------
Supremo T1-2    CFD0524               58          62           4        2.77
----------------------------------------------------------------------------
Supremo T5      CFD0525                6           9           3        5.58
----------------------------------------------------------------------------
Supremo T5      CFD0525               19          23           4        5.97
----------------------------------------------------------------------------
Supremo T1-2    CFD0526               94          98           4        3.09
----------------------------------------------------------------------------
Supremo T5      CFD0527             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFD0528               53          55           2        0.96
----------------------------------------------------------------------------
Supremo T1-2    CFD0529               38          45           7        1.62
----------------------------------------------------------------------------
Supremo T5      CFD0531              138         145           7        1.77
----------------------------------------------------------------------------
Supremo T5      CFD0531              183         188           5        2.02
----------------------------------------------------------------------------
Supremo T5      CFD0531              204         210           6         4.9
----------------------------------------------------------------------------
Supremo T5      CFD0532              140         152          12        1.44
----------------------------------------------------------------------------
Supremo T1-2    CFD0533               27          28           1        4.23
----------------------------------------------------------------------------
Supremo T5      CFD0535              133         146          13        1.37
----------------------------------------------------------------------------
Supremo T5      CFD0535              160         165           5        3.98
----------------------------------------------------------------------------
Supremo T5      CFD0536               26          28           2        3.41
----------------------------------------------------------------------------
Supremo T5      CFD0537              130         133           3        1.89
----------------------------------------------------------------------------
Supremo T5      CFD0539               68          75           7        7.77
----------------------------------------------------------------------------
Supremo T5      CFD0540              212         220           8        1.63
----------------------------------------------------------------------------
Supremo T5      CFD0541               57          64           7        4.26
----------------------------------------------------------------------------
Supremo T1-2    CFD0542               51          53           2       35.35
----------------------------------------------------------------------------
Supremo T1-2    CFD0542              124         128           4        6.06
----------------------------------------------------------------------------
Supremo T1-2    CFD0542              139         149          10        4.09
----------------------------------------------------------------------------
Supremo T1-2    CFD0542              227         229           2        5.38
----------------------------------------------------------------------------
Supremo T5      CFD0543               42          43           1        1.32
----------------------------------------------------------------------------
Supremo T1-2    CFD0544             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFD0546               10          22          12        1.71
----------------------------------------------------------------------------
Supremo T1-2    CFD0546              179         185           6       10.36
----------------------------------------------------------------------------
Supremo T1-2    CFD0547               88          90           2        3.17
----------------------------------------------------------------------------
Supremo T5      CFD0548              173         188          15        2.19
----------------------------------------------------------------------------
Supremo T1-2    CFD0549              137         138           1        1.53
----------------------------------------------------------------------------
Supremo T1-2    CFD0551             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFD0552              171         179           8        1.68
----------------------------------------------------------------------------
Supremo T1-2    CFD0553               97         124          27        4.04
----------------------------------------------------------------------------
Supremo T1-2    CFD0554              102         106           4        2.82
----------------------------------------------------------------------------
Supremo T1-2    CFD0554              118         121           3        5.17
----------------------------------------------------------------------------
Supremo T1-2    CFD0554              188         204          16         2.6
----------------------------------------------------------------------------
Supremo T5      CFD0555              144         161          17        4.74
----------------------------------------------------------------------------
Supremo T1-2    CFD0556              186         187           1        1.57
----------------------------------------------------------------------------
Supremo T1-2    CFD0557              119         143          24        2.39
----------------------------------------------------------------------------
Supremo T1-2    CFD0557              189         194           5       10.58
----------------------------------------------------------------------------
Supremo T5      CFD0558              165         170           5        3.34
----------------------------------------------------------------------------
Supremo T3      CFD0559               69          71           2         6.9
----------------------------------------------------------------------------
Supremo T3      CFD0559               93          99           6        
6.72----------------------------------------------------------------------------
Supremo T1-2    CFD0561              109         114           5       18.62
----------------------------------------------------------------------------
Supremo T1-2    CFD0561              132         135           3        3.54
----------------------------------------------------------------------------
Supremo T1-2    CFD0562              210         214           4        1.35
----------------------------------------------------------------------------
Supremo T5      CFD0563               54          58           4        13.9
----------------------------------------------------------------------------
Supremo T7      CFD0564               45          51           6        2.22
----------------------------------------------------------------------------
Supremo T7      CFD0565               32          34           2        1.61
----------------------------------------------------------------------------
Supremo T5      CFD0566               54          58           4       14.44
----------------------------------------------------------------------------
Supremo T1-2    CFD0567              185         189           4         1.3
----------------------------------------------------------------------------
Supremo T7      CFD0568               77          81           4        2.06
----------------------------------------------------------------------------
Supremo T5      CFD0569               44          48           4        4.42
----------------------------------------------------------------------------
Supremo T7      CFD0570               81          90           9        1.84
----------------------------------------------------------------------------
Supremo T7      CFD0571               61          63           2        2.02
----------------------------------------------------------------------------
Supremo T5      CFD0572              113         122           9        2.21
----------------------------------------------------------------------------
Supremo T5      CFD0574               41          43           2        2.32
----------------------------------------------------------------------------
Supremo T4      CFD0575             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFD0576             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T5      CFD0577               98         100           2        4.24
----------------------------------------------------------------------------
Supremo T7      CFD0578               42          44           2        3.74
----------------------------------------------------------------------------
Supremo T5      CFD0579               60          65           5        9.54
----------------------------------------------------------------------------
Supremo T1-2    CFD0580              196         202           6        1.29
----------------------------------------------------------------------------
Supremo T4      CFD0581             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFD0582               84          86           2        3.48
----------------------------------------------------------------------------
Supremo T4      CFD0583             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFD0584              104         105           1        2.44
----------------------------------------------------------------------------
Supremo T3      CFD0585               93          98           5         0.9
----------------------------------------------------------------------------
Supremo T4-5    CFD0586              127         133           6        3.89
----------------------------------------------------------------------------
Supremo T4-5    CFD0586              201         207           6        2.04
----------------------------------------------------------------------------
Supremo T5-7    CFD0587               30          34           4        4.23
----------------------------------------------------------------------------
Supremo T5-7    CFD0588               55          58           3        6.46
----------------------------------------------------------------------------
Supremo T7      CFD0589               37          46           9        0.82
----------------------------------------------------------------------------
Supremo T5-7    CFD0590               51          53           2        1.87
----------------------------------------------------------------------------
Supremo T3      CFD0591              145         149           4        3.66
----------------------------------------------------------------------------
Supremo T3      CFD0592               99         105           6         2.7
----------------------------------------------------------------------------
Supremo T3      CFD0592              114         122           8        2.75
----------------------------------------------------------------------------
Supremo T3      CFD0592              219         224           5        2.16
----------------------------------------------------------------------------
Supremo T4-5    CFR0804           103.63      115.82       12.19        3.35
----------------------------------------------------------------------------
Supremo T3      CFR0805            67.06       79.25       12.19        4.05
----------------------------------------------------------------------------
Supremo T3      CFR0805            89.92      103.63       13.71        1.06
----------------------------------------------------------------------------
Supremo T3      CFR0805           123.44      129.54         6.1        3.66
----------------------------------------------------------------------------
Supremo T3      CFR0806            77.72       99.06       21.34        0.97
----------------------------------------------------------------------------
Supremo T3      CFR0807            21.34       25.91        4.57        1.72
----------------------------------------------------------------------------
Supremo T3      CFR0808            21.34       27.43        6.09        2.95
----------------------------------------------------------------------------
Supremo T3      CFR0809               32       36.58        4.58        1.79
----------------------------------------------------------------------------
Supremo T3      CFR0810            64.01       74.68       10.67        2.07
----------------------------------------------------------------------------
Supremo T3      CFR0810            91.44       108.2       16.76        1.05
----------------------------------------------------------------------------
Supremo T3      CFR0810           117.35       120.4        3.05        3.83
----------------------------------------------------------------------------
Supremo T3      CFR0811            114.3      132.59       18.29        2.33
----------------------------------------------------------------------------
Supremo T3      CFR0812           129.54      134.11        4.57        4.18
----------------------------------------------------------------------------
Supremo T3      CFR0813            50.29       60.96       10.67        1.79
----------------------------------------------------------------------------
Supremo T3      CFR0813           102.11      109.73        7.62        4.45
----------------------------------------------------------------------------
Supremo T3      CFR0814           143.26      147.83        4.57        3.02
----------------------------------------------------------------------------
Supremo T3      CFR0815            71.63       74.68        3.05       15.67
----------------------------------------------------------------------------
Supremo T3      CFR0816             9.14       21.34        12.2        3.86
----------------------------------------------------------------------------
Supremo T3      CFR0817             70.1       77.72        7.62        3.45
----------------------------------------------------------------------------
Supremo T3      CFR0818            59.44       64.01        4.57        2.94
----------------------------------------------------------------------------
Supremo T3      CFR0819            59.44       62.48        3.04        5.72
----------------------------------------------------------------------------
Supremo T3      CFR0819           112.78      121.92        9.14        1.32
----------------------------------------------------------------------------
Supremo T3      CFR0820             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFR0821            16.76       22.86         6.1        4.29
----------------------------------------------------------------------------
Supremo T3      CFR0822            88.39       91.44        3.05        3.79
----------------------------------------------------------------------------
Supremo T3      CFR0823             76.2       91.44       15.24         5.5
----------------------------------------------------------------------------
Supremo T3      CFR0823           150.88      153.92        3.04        7.98
----------------------------------------------------------------------------
Supremo T3      CFR0824             NSV or did not reach target depth
----------------------------------------------------------------------------
Double Double   CFR0825            12.19       16.76        4.57        4.75
----------------------------------------------------------------------------
Double Double   CFR0825               32       41.15        9.15       10.47
----------------------------------------------------------------------------
Supremo T3      CFR0826            25.91       35.05        9.14        1.06
----------------------------------------------------------------------------
Double Double   CFR0827            54.86       57.91        3.05        9.31
----------------------------------------------------------------------------
Double Double   CFR0829             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFR0830           111.25      115.82        4.57        4.55
----------------------------------------------------------------------------
Supremo T3      CFR0830           128.02      160.02          32        2.77
----------------------------------------------------------------------------
Supremo T5      CFR0831            36.58       41.15        4.57        5.07
----------------------------------------------------------------------------
Supremo T7      CFR0832            51.82       54.86        3.04        4.52
----------------------------------------------------------------------------
Supremo T5      CFR0833            41.15       47.24        6.09        3.83
----------------------------------------------------------------------------
Supremo T7      CFR0834             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFR0835            41.15        44.2        3.05        1.19
----------------------------------------------------------------------------
Double Double   CFR0836            35.05       36.58        1.53        1.48
----------------------------------------------------------------------------
Double Double   CFR0837            35.05       36.58        1.53        1.38
----------------------------------------------------------------------------
Supremo T7      CFR0838             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T5      CFR0839            47.24       50.29        3.05        6.22
----------------------------------------------------------------------------
Supremo T7      CFR0840           155.45       158.5        3.05        3.52
----------------------------------------------------------------------------
Supremo T5      CFR0841           103.63      109.73         6.1        0.65
----------------------------------------------------------------------------
Supremo T4-5    CFR0842            89.92       94.49        4.57        2.93
----------------------------------------------------------------------------
Supremo T5      CFR0843            16.76       27.43       10.67        1.88
----------------------------------------------------------------------------
Supremo T5      CFR0843           124.97      128.02        3.05        3.53
----------------------------------------------------------------------------
Supremo T5      CFR0844            47.24       57.91       10.67        1.89
----------------------------------------------------------------------------
Supremo T5      CFR0845            47.24       50.29        3.05        3.77
----------------------------------------------------------------------------
Supremo T7      CFR0846            99.06      103.63        4.57        1.54
----------------------------------------------------------------------------
Supremo T4-5    CFR0847            33.53       59.44       25.91        1.59
----------------------------------------------------------------------------
Supremo T5      CFR0848           135.64      138.68        3.04         2.7
----------------------------------------------------------------------------
Supremo T7      CFR0849             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T5      CFR0850            35.05        38.1        3.05        3.96
----------------------------------------------------------------------------
Supremo T4-5    CFR0851            114.3      128.02       13.72        1.27
----------------------------------------------------------------------------
Supremo T5      CFR0852            45.72       50.29        4.57        5.81
----------------------------------------------------------------------------
Supremo T5      CFR0852            60.96       67.06         6.1        5.04
----------------------------------------------------------------------------
Supremo T7      CFR0853            22.86       36.58       13.72        3.37
----------------------------------------------------------------------------
Supremo T5      CFR0854             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFR0855             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T4-5    CFR0856            54.86       60.96         6.1        
0.66----------------------------------------------------------------------------
Supremo T4-5    CFR0857             38.1       39.62        1.52        1.95
----------------------------------------------------------------------------
Supremo T4-5    CFR0858              6.1       13.72        7.62        1.98
----------------------------------------------------------------------------
Supremo T4-5    CFR0858            71.63        76.2        4.57        2.79
----------------------------------------------------------------------------
Supremo T4-5    CFR0859             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFR0860              6.1        7.62        1.52        4.73
----------------------------------------------------------------------------
Supremo T4-5    CFR0861            91.44      112.78       21.34        1.41
----------------------------------------------------------------------------
Supremo T4-5    CFR0861            146.3      161.54       15.24        1.78
----------------------------------------------------------------------------
Supremo T7      CFR0862           153.92       158.5        4.58        1.78
----------------------------------------------------------------------------
Supremo T4-5    CFR0863           103.63      111.25        7.62        0.71
----------------------------------------------------------------------------
Supremo T4-5    CFR0864            59.44       60.96        1.52        7.34
----------------------------------------------------------------------------
Supremo T4-5    CFR0864            120.4      132.59       12.19        2.96
----------------------------------------------------------------------------
Supremo T4-5    CFR0865           147.83      155.45        7.62        2.17
----------------------------------------------------------------------------
Supremo T4-5    CFR0865           166.12      193.55       27.43        1.31
----------------------------------------------------------------------------
Supremo T4-5    CFR0866            24.38        38.1       13.72        2.38
----------------------------------------------------------------------------
Supremo T4-5    CFR0866            79.25       85.34        6.09        1.67
----------------------------------------------------------------------------
Supremo T7      CFR0867             4.57        7.62        3.05        2.52
----------------------------------------------------------------------------
Supremo T4-5    CFR0868            28.96          32        3.04        1.07
----------------------------------------------------------------------------
Supremo T4-5    CFR0869            86.87       92.96        6.09        2.84
----------------------------------------------------------------------------
Supremo T4-5    CFR0870            48.77       50.29        1.52        0.93
----------------------------------------------------------------------------
Supremo T1-2    CFR0871            65.53       71.63         6.1        1.01
----------------------------------------------------------------------------
Supremo T1-2    CFR0872           100.58      102.11        1.53        31.3
----------------------------------------------------------------------------
Supremo T1-2    CFR0872           111.25       146.3       35.05         1.6
----------------------------------------------------------------------------
Supremo T1-2    CFR0872           173.74      179.83        6.09        2.56
----------------------------------------------------------------------------
Supremo T7      CFR0873             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFR0874           124.97      131.06        6.09        2.18
----------------------------------------------------------------------------
Supremo T7      CFR0875            97.54       99.06        1.52        3.23
----------------------------------------------------------------------------
Supremo T1-2    CFR0876           111.25       120.4        9.15        3.26
----------------------------------------------------------------------------
Supremo T1-2    CFR0877            62.48       65.53        3.05        4.76
----------------------------------------------------------------------------
Supremo T1-2    CFR0877           106.68      112.78         6.1        2.47
----------------------------------------------------------------------------
Supremo T7      CFR0878             44.2       47.24        3.04        3.45
----------------------------------------------------------------------------
Supremo T1-2    CFR0879           111.25      129.54       18.29        1.98
----------------------------------------------------------------------------
Supremo T7      CFR0880           118.87      126.49        7.62        1.26
----------------------------------------------------------------------------
Supremo T1-2    CFR0881             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFR0882           137.16       146.3        9.14        4.07
----------------------------------------------------------------------------
Supremo T1-2    CFR0883            86.87       92.96        6.09        1.96
----------------------------------------------------------------------------
Supremo T1-2    CFR0883            114.3      121.92        7.62        1.69
----------------------------------------------------------------------------
Supremo T1-2    CFR0884             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFR0885            74.68        82.3        7.62        3.22
----------------------------------------------------------------------------
Supremo T1-2    CFR0886                0        9.14        9.14           1
----------------------------------------------------------------------------
Supremo T1-2    CFR0887            57.91       62.48        4.57        1.35
----------------------------------------------------------------------------
Supremo T1-2    CFR0888               32       33.53        1.53        6.93
----------------------------------------------------------------------------
Supremo T1-2    CFR0889            12.19       15.24        3.05        0.91
----------------------------------------------------------------------------
Supremo T1-2    CFR0890             7.62       33.53       25.91        2.86
----------------------------------------------------------------------------
Supremo T1-2    CFR0890            59.44       60.96        1.52        7.55
----------------------------------------------------------------------------
Supremo T1-2    CFR0891            39.62       77.72        38.1        1.19
----------------------------------------------------------------------------
Supremo T1-2    CFR0892            80.77        82.3        1.53        5.02
----------------------------------------------------------------------------
Supremo T1-2    CFR0893            83.82       94.49       10.67        2.55
----------------------------------------------------------------------------
Supremo T1-2    CFR0893           160.02      164.59        4.57        4.17
----------------------------------------------------------------------------
Supremo T1-2    CFR0894             1.52        7.62         6.1        3.03
----------------------------------------------------------------------------
Supremo T1-2    CFR0895            18.29       19.81        1.52        4.24
----------------------------------------------------------------------------
Supremo T1-2    CFR0896            89.92       91.44        1.52        1.56
----------------------------------------------------------------------------
Supremo T1-2    CFR0897           117.35      118.87        1.52        3.02
----------------------------------------------------------------------------
Supremo T1-2    CFR0898             1.52       13.72        12.2        1.54
----------------------------------------------------------------------------
Supremo T1-2    CFR0899            48.77       50.29        1.52        2.71
----------------------------------------------------------------------------
Supremo T1-2    CFR0900            89.92       91.44        1.52        1.42
----------------------------------------------------------------------------
Supremo T1-2    CFR0901            24.38       25.91        1.53        2.16
----------------------------------------------------------------------------
Supremo T1-2    CFR0902            35.05       42.67        7.62        2.67
----------------------------------------------------------------------------
Supremo T1-2    CFR0903            92.96       96.01        3.05        2.79
----------------------------------------------------------------------------
Supremo T1-2    CFR0904           102.11      112.78       10.67        2.55
----------------------------------------------------------------------------
Supremo T1-2    CFR0905            59.44       60.96        1.52        5.01
----------------------------------------------------------------------------
Supremo T1-2    CFR0906            15.24       16.76        1.52        0.96
----------------------------------------------------------------------------
Supremo T1-2    CFR0907            59.44       64.01        4.57        1.85
----------------------------------------------------------------------------
Supremo T1-2    CFR0908           137.16      143.26         6.1        1.53
----------------------------------------------------------------------------
Supremo T1-2    CFR0909            114.3      118.87        4.57        1.91
----------------------------------------------------------------------------
Supremo T1-2    CFR0910            80.77       85.34        4.57        1.45
----------------------------------------------------------------------------
Supremo T1-2    CFR0911            97.54      103.63        6.09        1.64
----------------------------------------------------------------------------
Supremo T1-2    CFR0912            51.82       56.39        4.57        1.77
----------------------------------------------------------------------------
Supremo T1-2    CFR0913             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFR0914            21.34       22.86        1.52        1.88
----------------------------------------------------------------------------
Supremo T1-2    CFR0915            42.67       51.82        9.15        3.65
----------------------------------------------------------------------------
Supremo T1-2    CFR0915            80.77       89.92        9.15        2.99
----------------------------------------------------------------------------
Supremo T3      CFR0916            30.48          32        1.52        1.33
----------------------------------------------------------------------------
Supremo T1-2    CFR0917            36.58       39.62        3.04        3.66
----------------------------------------------------------------------------
Supremo T3      CFR0918             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T1-2    CFR0919            24.38       28.96        4.58        10.1
----------------------------------------------------------------------------
Supremo T3      CFR0920            24.38       27.43        3.05        1.41
----------------------------------------------------------------------------
Supremo T1-2    CFR0921            60.96        70.1        9.14        1.92
----------------------------------------------------------------------------
Supremo T3      CFR0922            99.06      103.63        4.57       14.26
----------------------------------------------------------------------------
Supremo T1-2    CFR0923             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFR0924            45.72       47.24        1.52        5.08
----------------------------------------------------------------------------
Supremo T1-2    CFR0926            36.58       39.62        3.04        5.47
----------------------------------------------------------------------------
Supremo T1-2    CFR0927            36.58       42.67        6.09        0.83
----------------------------------------------------------------------------
Supremo T1-2    CFR0928             82.3       85.34        3.04         4.9
----------------------------------------------------------------------------
Supremo T1-2    CFR0929            25.91          32        6.09        0.83
----------------------------------------------------------------------------
Supremo T7      CFR0930            22.86       25.91        3.05        1.51
----------------------------------------------------------------------------
Supremo T1-2    CFR0931            15.24       35.05       19.81        2.12
----------------------------------------------------------------------------
Supremo T1-2    CFR0932              6.1       10.67        4.57        1.06
----------------------------------------------------------------------------
Supremo T7      CFR0933            21.34          32       10.66        1.66
----------------------------------------------------------------------------
Supremo T7      CFR0933             44.2       54.86       10.66        1.49
----------------------------------------------------------------------------
Supremo T1-2    CFR0935            89.92       91.44        1.52        9.38
----------------------------------------------------------------------------
Supremo T3      CFR0940            36.58       39.62        3.04        1.48
----------------------------------------------------------------------------
Supremo T3      CFR0942           105.16      106.68        1.52        7.35
----------------------------------------------------------------------------
Supremo T1-2    CFR0943             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T3      CFR0944            68.58       73.15        4.57        6.97
----------------------------------------------------------------------------
Supremo T3      CFR0945            33.53       45.72       12.19        1.29
----------------------------------------------------------------------------
Supremo T3      CFR0946             NSV or did not reach target depth
----------------------------------------------------------------------------
Latte           CFR0947            22.86       65.53       42.67        1.99
----------------------------------------------------------------------------
Latte           CFR0949            85.34      102.11       16.77        
1.88----------------------------------------------------------------------------
Latte           CFR0950            22.86       28.96         6.1        2.09
----------------------------------------------------------------------------
Latte           CFR0950            35.05       48.77       13.72        1.07
----------------------------------------------------------------------------
Supremo T3      CFR0951             NSV or did not reach target depth
----------------------------------------------------------------------------
Latte           CFR0952            12.19       28.96       16.77        6.16
----------------------------------------------------------------------------
Latte           CFR0952            53.34        82.3       28.96        1.15
----------------------------------------------------------------------------
Latte           CFR0952            89.92       94.49        4.57        2.65
----------------------------------------------------------------------------
Supremo T3      CFR0953             38.1       42.67        4.57        2.41
----------------------------------------------------------------------------
Latte           CFR0954           103.63      109.73         6.1        0.65
----------------------------------------------------------------------------
Supremo T3      CFR0955           126.49      132.59         6.1        7.35
----------------------------------------------------------------------------
Latte           CFR0956            51.82       53.34        1.52        8.15
----------------------------------------------------------------------------
Supremo T3      CFR0957             NSV or did not reach target depth
----------------------------------------------------------------------------
Supremo T7      CFR0959            47.24       57.91       10.67        3.19
----------------------------------------------------------------------------
Supremo T7      CFR0959            74.68       91.44       16.76        0.83
----------------------------------------------------------------------------
Supremo T7      CFR0961            97.54      100.58        3.04        2.72
----------------------------------------------------------------------------

----------------------------------------------------------------------------
2015 Kona North Exploration Drilling
----------------------------------------------------------------------------
Kona North      CFD0601               57          58           1        1.75
----------------------------------------------------------------------------
Kona North      CFD0602               85         104          19        2.41
----------------------------------------------------------------------------
Kona North      CFD0602              112         119           7        1.88
----------------------------------------------------------------------------
(i) True width estimated at approximately 2/3 down-hole length.
Additional notes: 'CFD' drill hole prefixes equate to diamond core holes,
'CFR' equate to RC drill holes. RC drill holes are sampled on 5' drill rod
lengths then converted to metric for input into the drill database. NSV
equals 'No Significant Value'.

/T/

QA / QC

Kaminak's disclosure of a technical or scientific nature in this press release 
has been reviewed and approved by Tim Smith, P.Geo., Vice President Exploration 
of Kaminak Gold Corporation, who serves as a Qualified Person under the 
definition of National Instrument 43-101. Quality assurance and quality control 
procedures include the systematic insertion of blanks and standards into the 
drill sample string. Samples are placed in sealed bags and shipped directly to 
the ALS Minerals preparatory laboratory in Whitehorse prior to gold fire assay.

On behalf of the Board of Directors of Kaminak

Eira Thomas, President and CEO

Kaminak Gold Corporation

For further information about Kaminak Gold Corporation or this news release, 
please visit our website at www.kaminak.com.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

Caution Concerning Forward-Looking Statements

Certain disclosures in this release, including management's assessment of the 
future potential of the Coffee Project, costs and timings for completion of the 
Coffee Project feasibliity study and future exploration programs, constitute 
forward-looking statements that are subject to numerous risks, uncertainties 
and other factors relating to Kaminak's operations as a mineral exploration 
company that may cause future results to differ materially from those expressed 
or implied in such forward-looking statements, including risks as to the 
completion of the plans and projects. Readers are cautioned not to place undue 
reliance on forward-looking statements. Except as required by law, Kaminak 
expressly disclaims any intention or obligation to update or revise any 
forward-looking statements, whether as a result of new information, future 
event or otherwise.

The Company has not made a production decision, and the Company's strategic 
plan to develop a stand-alone heap leach operation is subject to the results of 
its Feasibility Study. Further, if and when the Company makes any production 
decision, it will disclose the basis of such decision in accordance with the 
requirements of National Instrument 43-101 Standards of Disclosure for Mineral 
Projects ("NI 43-101").

- 30 -

CONTACT INFO:

Kaminak Gold Corporation
Tony Reda
Vice President of Corporate Development
604.646.4534 or toll free 1.844.646.4520
info@kaminak.com.
www.kaminak.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=539174624