Source	Marketwire
Date	08/19/2015
Time	04:30:30 AM

Company	 SAVARY GOLD CORP.
Title	Savary Gold Continues to Obtain Encouraging Drill Results at the 
Karankasso JV Project, Burkina Faso





    CDNX Symbol: SCA











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Savary Gold Corp.

TSX VENTURE SYMBOL: SCA

August 19, 2015

Savary Gold Continues to Obtain Encouraging Drill Results at the Karankasso JV 
Project, Burkina Faso

Savary Drills 0.90 g/t Gold Over 40 Metres and 12.71 g/t Gold Over 2 Metres at 
End of Hole

Karangosso Zone Mineralization Open at Depth and Along Strike, Preliminary 
Metallurgical Work is Positive

TORONTO, ONTARIO--(Marketwired - Aug. 19, 2015) - Savary Gold Corp. (TSX 
VENTURE:SCA) ("Savary" or the "Company") is pleased to announce the 
intersection of additional wide zones of gold mineralization at its Karangosso 
Zone. The Karangosso Zone has returned the best intercepts to date at 3.33 g/t 
gold over 41 metres (Savary Gold new release June 15, 2015). The Karangosso 
Zone is one of several zones defined along an approximately 45 kilometre long 
corridor of gold enrichment (partially shown in Figure 1).

During the 2015 spring drill program Savary completed 26 reverse circulation 
holes totalling 3,504 metres over the Karangosso Zone at its Karankasso Joint 
Venture Project in Burkina Faso, owned 65% by Savary and 35% by Sarama 
Resources Ltd. ("Sarama"). This release presents the results of the remaining 
14 holes that were drilled, along with the results of the initial 12 holes that 
were released on June 15, 2015. Highlight intercepts, for the Karangosso Zone 
are presented below:

/T/

--  0.90 g/t gold over 44 metres in hole 15-110

--  12.71 g/t gold over 2 metres at end of hole 15-110

--  0.87 g/t gold over 30 metres in hole 15-96

--  0.88 g/t gold over 19 metres in hole 15-98

--  3.33 g/t gold over 41 metres in hole 15-43(i)

--  2.02 g/t gold over 11 metres in hole 15-44(i)

--  6.61 g/t gold over 10 metres in hole 15-50(i)

--  2.30 g/t gold over 9 metres in hole 15-50(i)

--  1.97 g/t gold over 8 metres in hole 15-51(i)

--  1.94 g/t gold over 11 metres in hole 15-51(i)

--  1.79 g/t gold over 10 metres in hole 15-76(i)

/T/

(i) Previously reported intercept

Don Dudek, Savary's President and CEO commented: "We continue to receive 
encouraging results from the Karangosso Zone which is still open in all 
directions. In management's opinion, the setting, style and potential for 
grades greater than 2 g/t gold, continue to support the belief that the 
Karangosso Zone could be a centre-of-gravity deposit for the Karankasso 
Project. Our southern-most modelled hole intersected 0.77 g/t gold over 26.1 
metres and our northern-most hole on the zone, 900 metres to the north, 
intersected 0.87 g/t gold over 30 metres. As well, drilling has returned 
intercepts of 6.61 g/t gold over 10 metres, within approximately 80 metres of 
surface, that we have tested below. In summary, the Karangosso Zone mineralized 
system appears to have a lot more room to grow."

The Karankasso Property (the "Property") is located approximately 300 
kilometres southwest of Ouagadougou, Burkina Faso's capital city, and 60 
kilometres east of Bobo Dioulasso, the second largest city in Burkina Faso. The 
Property can be accessed by a paved highway with both rail and grid power 
coming within approximately 65 kilometres of the Property.

During the period from April 21, 2015 to June 30, 2015, Savary and Sarama 
completed approximately 15,515 metres of drilling in 115 reverse circulation 
holes on the Property.

The Karangosso Zone was initially discovered in 2013 when a reverse circulation 
drill hole, testing a gold-in-soil anomaly, returned an intercept of 10.14 g/t 
gold over ten metres. Subsequent drilling in 2014 returned up to 2.97 g/t gold 
over 27 metres and extended the gold-bearing portion of the altered alkaline 
granite for 800 metres along strike. Drilling in 2015 was primarily designed to 
complete enough drilling to define a resource, as the previous holes were 
spaced on fences 200 metres apart. As well, holes were drilled along strike 
with a goal to extend the strike length of the zone. Mineralization has been 
intersected for a distance of approximately 1,400 metres along strike with zone 
modeling completed along 900 metres of strike (Figure 2) to a maximum depth of 
approximately 150 metres. The modeled zones, A through D, appear to be open 
along strike and to depth with width and mineralization grades, apparently 
increasing at depth in several areas. It is likely that the D zone extends to 
the north, just west of the collars of holes 15-113 and 15-114, since the only 
gold-bearing mineralization was only intersected at the top of the holes. 
Further, mapping indicates that the host intrusion likely extends for at least 
another 1,000 metres to the north-northeast.

The Karangosso Zone is hosted by a pinkish potassic granitic rock that when 
altered becomes grey in color, silicified, sericitic, carbonate-bearing and 
weakly to moderately pyritic. Gold values are related to pyritic quartz vein 
zones with traces of tourmaline. Left-lateral-sheared, silicified, well 
layered, sedimentary rocks, with a moderate north-northeast plunge, lie to the 
east of the host felsic intrusion, and well foliated to sheared intermediate 
volcanic rock lie immediately to the west of the host felsic intrusion. A 
silicified, manganese-enriched sedimentary unit located 500 metres to the east 
that can be traced for approximately 2.6 kilometres, provides a good regional 
marker horizon. For reference, Endeavour's Vindaloo Zone on the Hounde 
Property, is 300 metres west of a similar-character manganese-enriched marker 
horizon.

More drill testing is required along strike to the north and to the south, 
where the zone appears to be open. As well, some deeper, likely core holes, 
will be required as the good grades persist and locally increase to depth with 
one hole, 15-110 returning 12.71 g/t gold over 2 metres, at the end of the 
hole. During the recent program, the RC drill had difficulties, due to water, 
to drill below 100 metres vertically. Mapping and additional IP geophysical 
surveys should also be carried out over the inferred strike extent of the 
mineralized intrusion, especially to the north, where another larger artisanal 
mining area, 2,000 metres to the north, has not been examined.

Figure 1: Karankasso Project - Select 2015 Significant Intercepts: 
http://media3.marketwire.com/docs/1021877figure1.pdf

Figure 2: Karangosso Zone - Surface Plan and Assay Summary: 
http://media3.marketwire.com/docs/1021877figure2.pdf

A summary of all assay composites, using a cut-off of 0.5 g/t Au, from all of 
the 2015 holes is presented in Table 1.

Timed, bottle roll metallurgical tests were completed over two, 
gold-mineralized, fresh rock samples from the Karangosso Zone in 2014. This 
work indicated an average gold recovery, for the two samples, of 87.2% (see 
Savary news release August 21, 2014).

Results for drilling on the other targets that were drilled during this program 
will be presented over the next month.

QA/QC Comments

Savary's procedures for handling reverse circulation drill chips comprise 
initial riffle splitting of the rock chips from one metre drill length samples 
into approximately 2.5 kilogram samples, as well as description and logging 
into a database. A duplicate 2.5 kilogram sample, prepared at the same time as 
the assay sample, is kept as a reference for each sample. Assay standards, 
sample duplicates and assay blanks were inserted sequentially every 14 samples 
resulting in an assay standard inserted every 42 samples. This sampling 
procedure was periodically reviewed by Savary's President and CEO, and the 
Company QP, Don Dudek, P. Geo. All assay samples were collected at site by SGS 
Laboratory or Actlabs staff from Ouagadougou, Burkina Faso. Sample preparation 
and fire assays were performed by SGS Laboratories and Actlabs, both based in 
Ouagadougou. Each sample was dried, crushed to 85% passing 2mm and then split 
to 1.5 kg by riffle splitter. The 1.5 kg, 2 mm split was pulverized to 95% 
passing 106mm. Fifty grams of the pulverized material was analysed for gold via 
fire assay with an atomic absorption spectroscopy (AAS) finish. SGS Burkina 
Faso SA operates according to ISO 17025 standards and institutes a full Quality 
Assurance/Quality Control (QA/QC) program consisting of insertion of blanks, 
standard reference material, repeats and reject splits which in total account 
for up to 25% of all determinations conducted.

About Savary Gold

Savary Gold, a Canadian exploration company, along with partner, Sarama 
Resources Limited, are focused on exploring the 750 km2 Karankasso Property in 
Burkina Faso. The Properties is in the Birimian age Hounde Greenstone Belt, 
which hosts Semafo's Mana mine and additional gold deposits that are presently 
subject to extensive exploration efforts (including Endeavour Mining's Hounde 
Project, Roxgold's Yaramoko Project and Sarama's/Acacia's South Hounde JV 
Project, which is adjacent to the Karankasso JV property). For additional 
information please visit our website at www.savarygold.com and follow us on 
Facebook, LinkedIn and Twitter.

Qualified Person

Don Dudek, P.Geo., President and CEO of the Company and a qualified person 
under National Instrument 43-101, has reviewed and approved the scientific and 
technical information in this press release.

SAVARY GOLD CORP.

On behalf of the Board,

Don Dudek, President & Chief Executive Officer

Cautionary Notes

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These statements 
include statements regarding the details of the drill program, the company's 
exploration plans, the focus on existing drill targets and new targets. These 
statements are based on current expectations and assumptions that are subject 
to risks and uncertainties. Actual results could differ materially because of 
factors discussed in the management discussion and analysis section of our 
interim and most recent annual financial statements or other reports and 
filings with the TSX Venture Exchange and applicable Canadian securities 
regulations. We do not assume any obligation to update any forward-looking 
statements, except as required by applicable laws.

This news release does not constitute an offer to sell or a solicitation of an 
offer to buy any of the securities in the United States. The securities have 
not been and will not be registered under the United States Securities Act of 
1933, as amended (the "1933 Act"), or any state securities laws and may not be 
offered or sold within the United States or to, or for the account or benefit 
of U.S. persons (as defined in Regulation S under the 1933 Act) absent such 
registration or an applicable exemption from such registration requirements.

/T/


Table 1 - 2015 Results Summary - Karangosso Zone

----------------------------------------------------------------------------
Hole                          From                       Width
(m)        To (m)      (m)(iii)        Au g/t
----------------------------------------------------------------------------
HS-RC-15-79                                                          NSV(ii)
----------------------------------------------------------------------------
HS-RC-15-80                     76            77             1          0.86
----------------------------------------------------------------------------
HS-RC-15-81                     34            42             8          0.51
----------------------------------------------------------------------------
incl            35            37             2          1.49
----------------------------------------------------------------------------
HS-RC-15-82                                                          NSV(ii)
----------------------------------------------------------------------------
HS-RC-15-94                                                          NSV(ii)
----------------------------------------------------------------------------
HS-RC-15-95                      4            12             8          0.87
----------------------------------------------------------------------------
HS-RC-15-95                     14            15             1          0.88
----------------------------------------------------------------------------
HS-RC-15-95                    107           108             1          1.50
----------------------------------------------------------------------------
HS-RC-15-95                    115           118             3          1.03
----------------------------------------------------------------------------
HS-RC-15-95                    144           145             1          1.27
----------------------------------------------------------------------------
HS-RC-15-96                     31            32             1          0.62
----------------------------------------------------------------------------
HS-RC-15-96                     70           101            30          0.87
----------------------------------------------------------------------------
incl            75            88            12          1.58
----------------------------------------------------------------------------
incl            95           101             6          0.76
----------------------------------------------------------------------------
HS-RC-15-97                     29            30             1          0.94
----------------------------------------------------------------------------
HS-RC-15-97                     38            40             1          1.19
----------------------------------------------------------------------------
HS-RC-15-97                     50            63            13          0.38
----------------------------------------------------------------------------
incl            51            53             2          1.39
----------------------------------------------------------------------------
HS-RC-15-98                    139           158            19          0.88
----------------------------------------------------------------------------
incl           139           144             5          1.30
----------------------------------------------------------------------------
HS-RC-15-110                    85            86             1          0.76
----------------------------------------------------------------------------
HS-RC-15-110                   105           149            45          0.90
----------------------------------------------------------------------------
incl           105           108             3          1.71
----------------------------------------------------------------------------
incl           113           114             1          
1.15----------------------------------------------------------------------------
incl           128           138            11          1.71
----------------------------------------------------------------------------
incl           144           149             5          1.49
----------------------------------------------------------------------------
HS-RC-15-110                   155           157             2         12.71
----------------------------------------------------------------------------
HS-RC-15-111                    65            67             2          1.06
----------------------------------------------------------------------------
HS-RC-15-111                    85           100            15          0.46
----------------------------------------------------------------------------
HS-RC-15-111                   123           124             1          1.05
----------------------------------------------------------------------------
HS-RC-15-112                    14            15             1          0.61
----------------------------------------------------------------------------
HS-RC-15-112                    89            99            10          0.63
----------------------------------------------------------------------------
HS-RC-15-112                   105           106             1          0.71
----------------------------------------------------------------------------
HS-RC-15-113                     5             7             2          0.55
----------------------------------------------------------------------------
HS-RC-15-114                     8             9             1          0.35
----------------------------------------------------------------------------
HS-RC-15-115                     2            10             8          0.17
----------------------------------------------------------------------------
HS-RC-15-115                    51            53             2          3.99
----------------------------------------------------------------------------
HS-RC-15-115                    65            67             2          0.73
----------------------------------------------------------------------------
HS-RC-15-43(i)                  33            34             1          0.98
----------------------------------------------------------------------------
HS-RC-15-43(i)                  40            81            41          3.33
----------------------------------------------------------------------------
HS-RC-15-43(i)                  94            95             1          1.30
----------------------------------------------------------------------------
HS-RC-15-44(i)                   1            12            11          2.02
----------------------------------------------------------------------------
HS-RC-15-44(i)                  27            29             2          1.42
----------------------------------------------------------------------------
HS-RC-15-44(i)                  74            76             2          0.65
----------------------------------------------------------------------------
HS-RC-15-45(i)                                                       NSV(ii)
----------------------------------------------------------------------------
HS-RC-15-46(i)                  54            55             1          0.87
----------------------------------------------------------------------------
HS-RC-15-46(i)                  61            62             1          1.89
----------------------------------------------------------------------------
HS-RC-15-46(i)                 115           116             1          0.75
----------------------------------------------------------------------------
HS-RC-15-47(i)                 112           114             2          1.54
----------------------------------------------------------------------------
HS-RC-15-47(i)                 135           136             1          0.70
----------------------------------------------------------------------------
HS-RC-15-48(i)                                                       NSV(ii)
----------------------------------------------------------------------------
HS-RC-15-49(i)                 146           147             1          0.61
----------------------------------------------------------------------------
HS-RC-15-50(i)                  76            78             2          0.49
----------------------------------------------------------------------------
HS-RC-15-50(i)                  91            96             5          1.72
----------------------------------------------------------------------------
HS-RC-15-50(i)                 100           110            10          6.61
----------------------------------------------------------------------------
HS-RC-15-50(i)                 112           113             1          1.05
----------------------------------------------------------------------------
HS-RC-15-50(i)                 127           129             2          2.39
----------------------------------------------------------------------------
HS-RC-15-50(i)                 137           139             2          0.60
----------------------------------------------------------------------------
HS-RC-15-50(i)                 144           153             9          2.30
----------------------------------------------------------------------------
HS-RC-15-50(i)                 158           160             2          0.70
----------------------------------------------------------------------------
HS-RC-15-51(i)                   2            10             8          1.97
----------------------------------------------------------------------------
HS-RC-15-51(i)                  17            28            11          1.94
----------------------------------------------------------------------------
HS-RC-15-51(i)                  30            31             1          1.09
----------------------------------------------------------------------------
HS-RC-15-51(i)                  94            95             1          2.09
----------------------------------------------------------------------------
HS-RC-15-51(i)                 111           112             1          0.65
----------------------------------------------------------------------------
HS-RC-15-51(i)                 129           131             2          1.63
----------------------------------------------------------------------------
HS-RC-15-76(i)                  39            49            10          1.79
----------------------------------------------------------------------------
HS-RC-15-76(i)                  77            80             3          1.81
----------------------------------------------------------------------------
HS-RC-15-76(i)                 119           120             1          1.42
----------------------------------------------------------------------------
HS-RC-15-77(i)                  18            23             5          1.04
----------------------------------------------------------------------------
HS-RC-15-77(i)                  60            62             2          1.69
----------------------------------------------------------------------------
HS-RC-15-77(i)                 102           103             1          1.26
----------------------------------------------------------------------------
HS-RC-15-78(i)                  51            52             1          0.98
----------------------------------------------------------------------------
HS-RC-15-78(i)                 112           115             3          0.84
----------------------------------------------------------------------------
HS-RC-15-78(i)                 124           126             2          0.98
----------------------------------------------------------------------------
HS-RC-15-78(i)                 128           130             2          2.94
----------------------------------------------------------------------------
HS-RC-15-78(i)                 136           138             2          1.53
----------------------------------------------------------------------------
(i) Previously released drill intercepts
(ii) No Significant Values
(iii) True widths are estimated at 70% of drilled length for the Karangosso
Zone Tables presents all composite assays values returning greater than 0.5
g/t gold over 1 metre and those holes where no assays greater than 0.5 g/t
gold over 1 metre were received

/T/

- 30 -

CONTACT INFO:

Savary Gold Corp.
Rob Hopkins
Manager, Investor Relations
416-861-5899
info@savarygold.com
www.savarygold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=539705836