Source	Marketwire
Date	08/31/2015
Time	06:30:28 AM

Company	 AMEX EXPLORATION INC.
Title	Amex Starts New Drilling Phase at its Cameron Gold Project Abitibi





    CDNX Symbol: AMX











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Amex Exploration Inc.

TSX VENTURE SYMBOL: AMX

August 31, 2015

Amex Starts New Drilling Phase at its Cameron Gold Project Abitibi


MONTREAL, QUEBEC--(Marketwired - Aug. 31, 2015) - Amex Exploration Inc. (TSX 
VENTURE:AMX) is pleased to announce that it has just started a new phase of 
drilling on its 100% owned Cameron gold property.

This new phase of drilling is in fact a follow up of the previous drilling 
completed in late 2013 (see PR of November 26, 2013) and in early 2011 where a 
gold-bearing shear zone, located in a mylonitic intermediate volcanic unit, is 
intersected returning high grade values, for example, up to 7,37 g/t Au over 
1.4 meters located within a broader lower grade zone that returned an average 
value of 1,27 g/t Au over 9,5 meters, in hole CA2013s04 (see PR2014-04-09).

Following a detailed review and interpretation of all of the previous phases of 
work, including detailed geophysics and two phase of drilling, this new 
campaign is prepared by Jacques Marchand, P. Eng., an independent consulting 
geological engineer. This work has lead to a 3D structural model interpretation 
of the mineralized high grade gold structure that will be tested by 6 holes 
totalling about 1,000 meters of drilling that should be completed by October.

The Cameron property is located at about 25 kilometres to the NE of 
Lebel-sur-Quevillon in the north-western part of Quebec, and consists of 93 
claims for a total area of 5231 hectares. Geologically, it is covered by 
volcano sedimentary rocks of the Abitibi Sub province which consists mostly of 
basaltic to andesitic rocks with several sheared / mylonitic intermediate 
volcanic sections in the drilling trench area. The property is strategically 
located near the intersection of the Cameron and Chieftain regional deformation 
corridors and is cut by the regional NE trending Franquet and Wedding faults. 
To the northwest, shear-related gold mineralization has been discovered along 
the NW Cameron deformation corridor at the Flordin deposit with 1997 estimated 
reserves of 815 500T @ 5.1 g/t Au and at the Cartwright deposit with 83 000T @ 
10.4 g/t Au.

Amex Exploration Inc. is a junior mining exploration company listed on the TSX 
Venture Exchange whose primary objective is to develop and bring into 
production viable gold and base metal deposits.

Jacques Marchand, P.Eng., who is a Qualified Persons as defined by Canadian NI 
43-101, has approved the technical information reported in this news release.

Forward-looking statements:

Except for statements of historical facts, all statements in this news release 
regarding, without limitation, new project acquisitions, future plans and 
objectives are forward-looking statements which involve risks and 
uncertainties. There can be no assurance that such statements will prove to be 
accurate; Actual results and future events could differ materially from those 
anticipated in such statements.

- 30 -

CONTACT INFO:

Jacques Trottier, PhD
President and Chief Executive Officer
(514) 866-8209

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=540526630