Source	Marketwire
Date	08/27/2015
Time	04:35:05 AM

Company	 SAVARY GOLD CORP.
Title	Savary Gold Obtains More Encouraging Drill Results at the Karankasso JV 
Project, Burkina Faso





    CDNX Symbol: SCA











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Savary Gold Corp.

TSX VENTURE SYMBOL: SCA

August 27, 2015

Savary Gold Obtains More Encouraging Drill Results at the Karankasso JV 
Project, Burkina Faso

Savary Drills 2.55 g/t Gold Over 9 Metres True Width and Extends the Kien East 
Gold System for 1,200 Metres to the Northeast

Kien East Zone Mineralization Open at Depth and Along Strike, Preliminary 
Metallurgical Work is Positive

TORONTO, ONTARIO--(Marketwired - Aug. 27, 2015) - Savary Gold Corp. (TSX 
VENTURE:SCA) ("Savary" or the "Company") is pleased to announce the results of 
a Q2, 2015 drill program at its Kien East Zone. The recent holes returned an 
intercept of 2.55 g/t gold over 18 metres (9 metres true width), which 
surpassed the previous best in the zone which had returned 2.00 g/t gold over 
21 metres (Savary Gold news release of April 30, 2013). The Kien East Zone is 
the northern-most area of gold mineralization defined along an approximately 45 
kilometre long corridor of gold enrichment (Savary news release of December 15, 
2014).

During the 2015 spring drill program Savary completed 30 reverse circulation 
holes totalling 4,101 metres over the Kien East Zone at its Karankasso Joint 
Venture Project in Burkina Faso, owned 65% by Savary and 35% by Sarama 
Resources Ltd. ("Sarama"). This release presents the results of all of the 
holes drilled in 2015. Highlight 2015 drill intercepts for the Kien East Zone 
are presented below:

/T/

--  2.84 g/t gold over 8 metres in hole 15-02

--  2.55 g/t gold over 18 metres in hole 15-03

--  0.70 g/t gold over 21 metres in hole 15-04

--  1.84 g/t gold over 8 metres in hole 15-63

--  1.52 g/t gold over 9 metres in hole 15-63

--  1.58 g/t gold over 6 metres in hole 15-64

--  1.49 g/t gold over 12 metres in hole 15-65

--  0.95 g/t gold over 13 metres in hole 15-67


/T/

Don Dudek, Savary's President and CEO commented: "Savary's 2015 drill program 
was successful in extending the gold mineralized zones both along strike and to 
depth, documenting the presence of a large, robust alteration system associated 
with the gold mineralization and radically changing the orientation of most of 
the mineralized zones. The discovery of shallow-dipping stacked lenses improves 
the open pit potential of the zones and the locally higher grades provide 
exploration encouragement."

The Karankasso Property (the "Property") is located approximately 300 
kilometres southwest of Ouagadougou, Burkina Faso's capital city, and 60 
kilometres east of Bobo Dioulasso, the second largest city in Burkina Faso. The 
Property can be accessed by a paved highway with both rail and grid power 
coming within approximately 65 kilometres of the Property.

During the period from April 21, 2015 to June 30, 2015, Savary and Sarama 
completed approximately 14,515 metres of drilling in 115 reverse circulation 
holes on the Property.

The Kien East Zone lies near the northern part of the Property and straddles 
the highway that has a direct link to Bobo Dioulasso. Drilling has returned 
higher grade intercepts of 8.90 g/t gold over 3.9 metres to wider sections of 
mineralization grading up to 2.55 g/t gold over 18 metres. Drill holes at Kien 
East have intersected at least fourteen, modelled, northerly- to 
northeast-trending, steeply- to shallow-dipping, stacked lenses of gold 
mineralization along an open ended 3.2 kilometre strike length (see Figure 1). 
Prior to this program the gold system had been traced for 2,000 metres along 
strike. It is anticipated that steeply-dipping gold zones can be extended 
further northeast along strike and down-dip and that the shallow-dipping gold 
zones can be extended to the south and down-dip. Gold-bearing mineralization is 
widespread, focussed at unit contacts, hosted by multiple rock types and 
associated with sericite-, quartz-, pyrite- and locally fuchsite-alteration.

The steeply dipping mineralization is associated with a northeast-trending, 
andesitic volcanics to dioritic intrusions that are sheared and altered. Up to 
four, near vertical dipping lenses have been defined with one of the lenses 
demonstrating reasonably good continuity along strike. Gold values are 
generally modest in grade ranging from 0.6 to 1.4 g/t gold in the assay 
composites.

The shallow-east-dipping mineralization (zones KA1, KA-KG - see table at end) 
is related to shears hosted predominantly by a feldspar porphyritic diorite 
intrusion. The 15 to 30 degree east-dipping zones lie in a 600 metre by 300 
metre area (Kien Flats area in Figure 1) where the mineralized structures 
rotate from predominantly northerly- trending to northeast trending. This zone 
of nine, modelled stacked lenses is open to the south, down dip to the east and 
to a lesser extent, to the north. As interpreted, most intercepts are close to 
true thickness with the exception of the hole 15-03 intercept of 2.55 g/t gold 
over 18 metres which is interpreted to have a true thickness of approximately 
nine metres. Overall, the weighted average grade of the flat-lying zones ranges 
from 1.3 to 1.5 g/t gold with true widths ranging from less than a metre to 
approximately 19 metres.

Future work will focus on tracing the mineralized zones to the northeast along 
the trend of the geophysical anomaly and extending the shallow-dipping 
mineralization down dip, down plunge and to the south.

To view "Figure 1: Kien East Zone - Surface Plan and Assay Summary",  please 
visit the following link: http://media3.marketwire.com/docs/1022685figure1.jpg

A summary of all assay composites, using a cut-off of 0.5 g/t gold, from all of 
the 2015 holes, is presented in Table 1.

Timed, bottle roll metallurgical tests were completed for four, 
gold-mineralized, fresh rock samples from the Kien East Zone in 2014. This work 
indicated an average gold recovery, for the four samples, of 95.4% (see Savary 
news release of August 21, 2014).

Results for drilling on the other targets that were drilled during this program 
will be presented over the next month.

QA/QC Comments

Savary's procedures for handling reverse circulation drill chips comprise 
initial riffle splitting of the rock chips from one metre drill length samples 
into approximately 2.5 kilogram samples, as well as description and logging 
into a database. A duplicate 2.5 kilogram sample, prepared at the same time as 
the assay sample, is kept as a reference for each sample. Assay standards, 
sample duplicates and assay blanks were inserted sequentially every 14 samples 
resulting in an assay standard inserted every 42 samples. This sampling 
procedure was periodically reviewed by Savary's President and CEO, and the 
Company QP, Don Dudek, P. Geo. All assay samples were collected at site by SGS 
Laboratory staff from Ouagadougou, Burkina Faso. Sample preparation and fire 
assays were performed by SGS Laboratories based in Ouagadougou. Each sample was 
dried, crushed to 85% passing 2mm and then split to 1.5 kg by riffle splitter. 
The 1.5 kg, 2 mm split was pulverized to 95% passing 106mm. Fifty grams of the 
pulverized material was analysed for gold via fire assay with an atomic 
absorption spectroscopy (AAS) finish. SGS Burkina Faso SA operates according to 
ISO 17025 standards and institutes a full Quality Assurance/Quality Control 
(QA/QC) program consisting of insertion of blanks, standard reference material, 
repeats and reject splits which in total account for up to 25% of all 
determinations conducted.

About Savary Gold

Savary Gold, a Canadian exploration company, along with partner, Sarama 
Resources Limited, are focused on exploring the 750 km2 Karankasso Property in 
Burkina Faso. The Properties is in the Birimian age Hounde Greenstone Belt, 
which hosts Semafo's Mana mine and additional gold deposits that are presently 
subject to extensive exploration efforts (including Endeavour Mining's Hounde 
Project, Roxgold's Yaramoko Project and Sarama's/Acacia's South Hounde JV 
Project, which is adjacent to the Karankasso JV property). For additional 
information please visit our website at www.savarygold.com.

Qualified Person

Don Dudek, P.Geo., President and CEO of the Company and a qualified person 
under National Instrument 43-101, has reviewed and approved the scientific and 
technical information in this press release.

SAVARY GOLD CORP.

On behalf of the Board,

Don Dudek, President & Chief Executive Officer

Cautionary Notes

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These statements 
include statements regarding the details of the drill program, the company's 
exploration plans, the focus on existing drill targets, potential extensions to 
the gold zones and new targets. These statements are based on current 
expectations and assumptions that are subject to risks and uncertainties. 
Actual results could differ materially because of factors discussed in the 
management discussion and analysis section of our interim and most recent 
annual financial statements or other reports and filings with the TSX Venture 
Exchange and applicable Canadian securities regulations. We do not assume any 
obligation to update any forward-looking statements, except as required by 
applicable laws.

This news release does not constitute an offer to sell or a solicitation of an 
offer to buy any of the securities in the United States. The securities have 
not been and will not be registered under the United States Securities Act of 
1933, as amended (the "1933 Act"), or any state securities laws and may not be 
offered or sold within the United States or to, or for the account or benefit 
of U.S. persons (as defined in Regulation S under the 1933 Act) absent such 
registration or an applicable exemption from such registration requirements.

/T/


----------------------------------------------------------------------------
Table 1 - 2015 Results Summary - Kien East Zone

----------------------------------------------------------------------------
Hole                            From        To     Width    Au g/t   Lens(1)
----------------------------------------------------------------------------
HS-RC-15-01                        4         6         2      1.65
----------------------------------------------------------------------------
HS-RC-15-02                       26        32         6      1.50        KA
----------------------------------------------------------------------------
HS-RC-15-02                       60        64         4      1.77        KB
----------------------------------------------------------------------------
HS-RC-15-02                      154       162         8      2.84        KS
----------------------------------------------------------------------------
HS-RC-15-02                      174       175         1      0.74
----------------------------------------------------------------------------
HS-RC-15-03                       15        19         4      1.38       KA1
----------------------------------------------------------------------------
HS-RC-15-03                       33        34         1      0.70
----------------------------------------------------------------------------
HS-RC-15-03                       67        72         5      1.58        KA
----------------------------------------------------------------------------
HS-RC-15-03                       85       103        18      2.55        KB
----------------------------------------------------------------------------
HS-RC-15-03                      107       109         2      0.53
----------------------------------------------------------------------------
HS-RC-15-03                      112       115         3      2.72
----------------------------------------------------------------------------
HS-RC-15-03                      129       130         1      0.73
----------------------------------------------------------------------------
HS-RC-15-04                       20        22         2      2.30        KA
----------------------------------------------------------------------------
HS-RC-15-04                       31        34         3      0.89        KB
----------------------------------------------------------------------------
HS-RC-15-04                       44        65        21      0.70        KW
----------------------------------------------------------------------------
HS-RC-15-04                       74        75         1      0.67
----------------------------------------------------------------------------
HS-RC-15-04                       84        85         1      1.08
----------------------------------------------------------------------------
HS-RC-15-04                      105       106         1      0.87        KS
----------------------------------------------------------------------------
HS-RC-15-05                                               NSV
----------------------------------------------------------------------------
HS-RC-15-06                       54        55         1      0.74       KA1
----------------------------------------------------------------------------
HS-RC-15-06                       69        71         2      1.17        KA
----------------------------------------------------------------------------
HS-RC-15-06                       97        98         1      1.18        KB
----------------------------------------------------------------------------
HS-RC-15-07                                               NSV
----------------------------------------------------------------------------
HS-RC-15-08                       20        21         1      0.54
----------------------------------------------------------------------------
HS-RC-15-08                       94        95         1      0.51
----------------------------------------------------------------------------
HS-RC-15-08                       98       100         2      0.74
----------------------------------------------------------------------------
HS-RC-15-08                      109       110         1      1.75
----------------------------------------------------------------------------
HS-RC-15-08                      120       124         4      1.27        KW
----------------------------------------------------------------------------
HS-RC-15-09                        1        18         7      0.35        KW
----------------------------------------------------------------------------
incl.                   6         7         1      0.50
----------------------------------------------------------------------------
incl.                   8         9         1      0.49          
----------------------------------------------------------------------------
incl.                  11        12         1      0.67
----------------------------------------------------------------------------
HS-RC-15-09                       95       104         9      0.30        KS
----------------------------------------------------------------------------
incl.                  95        96         1      0.78        KW
----------------------------------------------------------------------------
HS-RC-15-10                      109       124        15      0.57
----------------------------------------------------------------------------
HS-RC-15-11                       62        63         1      1.46
----------------------------------------------------------------------------
HS-RC-15-11                       87        88         1      0.80
----------------------------------------------------------------------------
HS-RC-15-11                      159       161         1      1.22
----------------------------------------------------------------------------
HS-RC-15-11                      173       201        28      0.38
----------------------------------------------------------------------------
incl                  180       190        10      0.62
----------------------------------------------------------------------------
incl                  180       183         3      0.99
----------------------------------------------------------------------------
HS-RC-15-12                                               NSR
----------------------------------------------------------------------------
HS-RC-15-13                                               NSR
----------------------------------------------------------------------------
HS-RC-15-14                      111       113         2      1.04
----------------------------------------------------------------------------
HS-RC-15-15                       96        97         1      0.69       KW4
----------------------------------------------------------------------------
HS-RC-15-16                       98       107         9      0.77        KW
----------------------------------------------------------------------------
HS-RC-15-17                       14        30        16      0.61
----------------------------------------------------------------------------
HS-RC-15-17                       38        41         3      1.06       KW3
----------------------------------------------------------------------------
HS-RC-15-17                      121       122         1      1.73
----------------------------------------------------------------------------
HS-RC-15-18                       54        55         1      0.61
----------------------------------------------------------------------------
HS-RC-15-19                        4         5         1      0.52
----------------------------------------------------------------------------
HS-RC-15-19                       19        21         1      1.57
----------------------------------------------------------------------------
HS-RC-15-19                       46        54         8      0.89       KW4
----------------------------------------------------------------------------
HS-RC-15-20                       98        99         1      1.12
----------------------------------------------------------------------------
HS-RC-15-20                      115       123         8      1.32        KW
----------------------------------------------------------------------------
HS-RC-15-21                       12        13         1      0.58
----------------------------------------------------------------------------
HS-RC-15-21                       15        16         1      0.50
----------------------------------------------------------------------------
HS-RC-15-21                       20        35        15      1.29        KW
----------------------------------------------------------------------------
HS-RC-15-21                       41        48         7      0.65       KW2
----------------------------------------------------------------------------
HS-RC-15-21                       66        70         4      0.69       KW3
----------------------------------------------------------------------------
HS-RC-15-21                       77        79         2      0.57
----------------------------------------------------------------------------
HS-RC-15-21                      104       105         1      0.58
----------------------------------------------------------------------------
HS-RC-15-22                       40        41         1      2.08
----------------------------------------------------------------------------
HS-RC-15-22                       78        80         2      0.64        KA
----------------------------------------------------------------------------
HS-RC-15-22                       85        86         1      0.50        KC
----------------------------------------------------------------------------
HS-RC-15-22                       90        91         1      1.50
----------------------------------------------------------------------------
HS-RC-15-22                      103       103         1      1.05        KD
----------------------------------------------------------------------------
HS-RC-15-22                      116       117         1      0.76        KE
----------------------------------------------------------------------------
HS-RC-15-22                      142       143         1      1.60
----------------------------------------------------------------------------
HS-RC-15-23                       59        61         2      0.60        KA
----------------------------------------------------------------------------
HS-RC-15-23                       90        91         1      0.74
----------------------------------------------------------------------------
HS-RC-15-23                       98       112        14      1.34        KC
----------------------------------------------------------------------------
HS-RC-15-23                      115       117         2      1.07
----------------------------------------------------------------------------
HS-RC-15-23                      122       123         1      0.56
----------------------------------------------------------------------------
HS-RC-15-23                      126       129         3      0.77
----------------------------------------------------------------------------
HS-RC-15-23                      135       140         5      2.03        KE
----------------------------------------------------------------------------
HS-RC-15-62                       34        38         4      1.55        KA
----------------------------------------------------------------------------
HS-RC-15-62                       57        63         5      0.67        KB
----------------------------------------------------------------------------
HS-RC-15-62                      189       195         6      1.19        KS
----------------------------------------------------------------------------
HS-RC-15-62                      229       230         1      2.27
----------------------------------------------------------------------------
HS-RC-15-63                       89        97         8      1.84        KA
----------------------------------------------------------------------------
HS-RC-15-63                      118       127         9      1.52        KB
----------------------------------------------------------------------------
HS-RC-15-64                        2         7         5      0.86        KA
----------------------------------------------------------------------------
HS-RC-15-64                       20        22         2      0.84
----------------------------------------------------------------------------
HS-RC-15-64                       29        35         6      1.58        KB
----------------------------------------------------------------------------
HS-RC-15-64                       42        43         1      1.55
----------------------------------------------------------------------------
HS-RC-15-64                      132       133         1      3.94
----------------------------------------------------------------------------
HS-RC-15-64                      152       153         1      5.87        KF
----------------------------------------------------------------------------
HS-RC-15-64                      158       159         1      0.62
----------------------------------------------------------------------------
HS-RC-15-64                      162       163         1      0.60
----------------------------------------------------------------------------
HS-RC-15-64                      177       186         8      0.96        KG
----------------------------------------------------------------------------
HS-RC-15-65                       63        65         2      0.71       KA1
----------------------------------------------------------------------------
HS-RC-15-65                       91        92         1      0.68
----------------------------------------------------------------------------
HS-RC-15-65                       96        97         1      1.59        KA
----------------------------------------------------------------------------
HS-RC-15-65                      104       116        12      1.49        KB
----------------------------------------------------------------------------
incl                  107       116         9      1.78
----------------------------------------------------------------------------
HS-RC-15-65                      120       124         4      1.08
----------------------------------------------------------------------------
HS-RC-15-65                      130       131         1      0.94
----------------------------------------------------------------------------
HS-RC-15-66                                     NSV
----------------------------------------------------------------------------
HS-RC-15-67                       74        76         2      0.58
----------------------------------------------------------------------------
HS-RC-15-67                       82        95        13      0.95        KW
----------------------------------------------------------------------------
(i) No Significant Values.
(ii) True widths are estimated at 50% to 100% of drilled length at the Kien
East Zone. This Table presents all composite assay values returning greater
than 0.5 g/t gold over 1 metre and those holes where no assays greater than
0.5 g/t gold over 1 metre were received.
( 1)KS is equivalent to Shear Zone on figure 1

/T/

- 30 -

CONTACT INFO:

Savary Gold Corp.
Don Dudek
647-259-2097
info@savarygold.com
www.savarygold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=540281801


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Savary Gold Corp.

TSX VENTURE SYMBOL: SCA

August 27, 2015

Savary Gold Obtains More Encouraging Drill Results at the Karankasso JV 
Project, Burkina Faso

Savary Drills 2.55 g/t Gold Over 9 Metres True Width and Extends the Kien East 
Gold System for 1,200 Metres to the Northeast

Kien East Zone Mineralization Open at Depth and Along Strike, Preliminary 
Metallurgical Work is Positive

TORONTO, ONTARIO--(Marketwired - Aug. 27, 2015) - Savary Gold Corp. (TSX 
VENTURE:SCA) ("Savary" or the "Company") is pleased to announce the results of 
a Q2, 2015 drill program at its Kien East Zone. The recent holes returned an 
intercept of 2.55 g/t gold over 18 metres (9 metres true width), which 
surpassed the previous best in the zone which had returned 2.00 g/t gold over 
21 metres (Savary Gold news release of April 30, 2013). The Kien East Zone is 
the northern-most area of gold mineralization defined along an approximately 45 
kilometre long corridor of gold enrichment (Savary news release of December 15, 
2014).

During the 2015 spring drill program Savary completed 30 reverse circulation 
holes totalling 4,101 metres over the Kien East Zone at its Karankasso Joint 
Venture Project in Burkina Faso, owned 65% by Savary and 35% by Sarama 
Resources Ltd. ("Sarama"). This release presents the results of all of the 
holes drilled in 2015. Highlight 2015 drill intercepts for the Kien East Zone 
are presented below:

/T/

--  2.84 g/t gold over 8 metres in hole 15-02

--  2.55 g/t gold over 18 metres in hole 15-03

--  0.70 g/t gold over 21 metres in hole 15-04

--  1.84 g/t gold over 8 metres in hole 15-63

--  1.52 g/t gold over 9 metres in hole 15-63

--  1.58 g/t gold over 6 metres in hole 15-64

--  1.49 g/t gold over 12 metres in hole 15-65

--  0.95 g/t gold over 13 metres in hole 15-67


/T/

Don Dudek, Savary's President and CEO commented: "Savary's 2015 drill program 
was successful in extending the gold mineralized zones both along strike and to 
depth, documenting the presence of a large, robust alteration system associated 
with the gold mineralization and radically changing the orientation of most of 
the mineralized zones. The discovery of shallow-dipping stacked lenses improves 
the open pit potential of the zones and the locally higher grades provide 
exploration encouragement."

The Karankasso Property (the "Property") is located approximately 300 
kilometres southwest of Ouagadougou, Burkina Faso's capital city, and 60 
kilometres east of Bobo Dioulasso, the second largest city in Burkina Faso. The 
Property can be accessed by a paved highway with both rail and grid power 
coming within approximately 65 kilometres of the Property.

During the period from April 21, 2015 to June 30, 2015, Savary and Sarama 
completed approximately 14,515 metres of drilling in 115 reverse circulation 
holes on the Property.

The Kien East Zone lies near the northern part of the Property and straddles 
the highway that has a direct link to Bobo Dioulasso. Drilling has returned 
higher grade intercepts of 8.90 g/t gold over 3.9 metres to wider sections of 
mineralization grading up to 2.55 g/t gold over 18 metres. Drill holes at Kien 
East have intersected at least fourteen, modelled, northerly- to 
northeast-trending, steeply- to shallow-dipping, stacked lenses of gold 
mineralization along an open ended 3.2 kilometre strike length (see Figure 1). 
Prior to this program the gold system had been traced for 2,000 metres along 
strike. It is anticipated that steeply-dipping gold zones can be extended 
further northeast along strike and down-dip and that the shallow-dipping gold 
zones can be extended to the south and down-dip. Gold-bearing mineralization is 
widespread, focussed at unit contacts, hosted by multiple rock types and 
associated with sericite-, quartz-, pyrite- and locally fuchsite-alteration.

The steeply dipping mineralization is associated with a northeast-trending, 
andesitic volcanics to dioritic intrusions that are sheared and altered. Up to 
four, near vertical dipping lenses have been defined with one of the lenses 
demonstrating reasonably good continuity along strike. Gold values are 
generally modest in grade ranging from 0.6 to 1.4 g/t gold in the assay 
composites.

The shallow-east-dipping mineralization (zones KA1, KA-KG - see table at end) 
is related to shears hosted predominantly by a feldspar porphyritic diorite 
intrusion. The 15 to 30 degree east-dipping zones lie in a 600 metre by 300 
metre area (Kien Flats area in Figure 1) where the mineralized structures 
rotate from predominantly northerly- trending to northeast trending. This zone 
of nine, modelled stacked lenses is open to the south, down dip to the east and 
to a lesser extent, to the north. As interpreted, most intercepts are close to 
true thickness with the exception of the hole 15-03 intercept of 2.55 g/t gold 
over 18 metres which is interpreted to have a true thickness of approximately 
nine metres. Overall, the weighted average grade of the flat-lying zones ranges 
from 1.3 to 1.5 g/t gold with true widths ranging from less than a metre to 
approximately 19 metres.

Future work will focus on tracing the mineralized zones to the northeast along 
the trend of the geophysical anomaly and extending the shallow-dipping 
mineralization down dip, down plunge and to the south.

To view "Figure 1: Kien East Zone - Surface Plan and Assay Summary",  please 
visit the following link: http://media3.marketwire.com/docs/1022685figure1.jpg

A summary of all assay composites, using a cut-off of 0.5 g/t gold, from all of 
the 2015 holes, is presented in Table 1.

Timed, bottle roll metallurgical tests were completed for four, 
gold-mineralized, fresh rock samples from the Kien East Zone in 2014. This work 
indicated an average gold recovery, for the four samples, of 95.4% (see Savary 
news release of August 21, 2014).

Results for drilling on the other targets that were drilled during this program 
will be presented over the next month.

QA/QC Comments

Savary's procedures for handling reverse circulation drill chips comprise 
initial riffle splitting of the rock chips from one metre drill length samples 
into approximately 2.5 kilogram samples, as well as description and logging 
into a database. A duplicate 2.5 kilogram sample, prepared at the same time as 
the assay sample, is kept as a reference for each sample. Assay standards, 
sample duplicates and assay blanks were inserted sequentially every 14 samples 
resulting in an assay standard inserted every 42 samples. This sampling 
procedure was periodically reviewed by Savary's President and CEO, and the 
Company QP, Don Dudek, P. Geo. All assay samples were collected at site by SGS 
Laboratory staff from Ouagadougou, Burkina Faso. Sample preparation and fire 
assays were performed by SGS Laboratories based in Ouagadougou. Each sample was 
dried, crushed to 85% passing 2mm and then split to 1.5 kg by riffle splitter. 
The 1.5 kg, 2 mm split was pulverized to 95% passing 106mm. Fifty grams of the 
pulverized material was analysed for gold via fire assay with an atomic 
absorption spectroscopy (AAS) finish. SGS Burkina Faso SA operates according to 
ISO 17025 standards and institutes a full Quality Assurance/Quality Control 
(QA/QC) program consisting of insertion of blanks, standard reference material, 
repeats and reject splits which in total account for up to 25% of all 
determinations conducted.

About Savary Gold

Savary Gold, a Canadian exploration company, along with partner, Sarama 
Resources Limited, are focused on exploring the 750 km2 Karankasso Property in 
Burkina Faso. The Properties is in the Birimian age Hounde Greenstone Belt, 
which hosts Semafo's Mana mine and additional gold deposits that are presently 
subject to extensive exploration efforts (including Endeavour Mining's Hounde 
Project, Roxgold's Yaramoko Project and Sarama's/Acacia's South Hounde JV 
Project, which is adjacent to the Karankasso JV property). For additional 
information please visit our website at www.savarygold.com.

Qualified Person

Don Dudek, P.Geo., President and CEO of the Company and a qualified person 
under National Instrument 43-101, has reviewed and approved the scientific and 
technical information in this press release.

SAVARY GOLD CORP.

On behalf of the Board,

Don Dudek, President & Chief Executive Officer

Cautionary Notes

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These statements 
include statements regarding the details of the drill program, the company's 
exploration plans, the focus on existing drill targets, potential extensions to 
the gold zones and new targets. These statements are based on current 
expectations and assumptions that are subject to risks and uncertainties. 
Actual results could differ materially because of factors discussed in the 
management discussion and analysis section of our interim and most recent 
annual financial statements or other reports and filings with the TSX Venture 
Exchange and applicable Canadian securities regulations. We do not assume any 
obligation to update any forward-looking statements, except as required by 
applicable laws.

This news release does not constitute an offer to sell or a solicitation of an 
offer to buy any of the securities in the United States. The securities have 
not been and will not be registered under the United States Securities Act of 
1933, as amended (the "1933 Act"), or any state securities laws and may not be 
offered or sold within the United States or to, or for the account or benefit 
of U.S. persons (as defined in Regulation S under the 1933 Act) absent such 
registration or an applicable exemption from such registration requirements.

/T/


----------------------------------------------------------------------------
Table 1 - 2015 Results Summary - Kien East Zone

----------------------------------------------------------------------------
Hole                            From        To     Width    Au g/t   Lens(1)
----------------------------------------------------------------------------
HS-RC-15-01                        4         6         2      1.65
----------------------------------------------------------------------------
HS-RC-15-02                       26        32         6      1.50        KA
----------------------------------------------------------------------------
HS-RC-15-02                       60        64         4      1.77        KB
----------------------------------------------------------------------------
HS-RC-15-02                      154       162         8      2.84        KS
----------------------------------------------------------------------------
HS-RC-15-02                      174       175         1      0.74
----------------------------------------------------------------------------
HS-RC-15-03                       15        19         4      1.38       KA1
----------------------------------------------------------------------------
HS-RC-15-03                       33        34         1      0.70
----------------------------------------------------------------------------
HS-RC-15-03                       67        72         5      1.58        KA
----------------------------------------------------------------------------
HS-RC-15-03                       85       103        18      2.55        KB
----------------------------------------------------------------------------
HS-RC-15-03                      107       109         2      0.53
----------------------------------------------------------------------------
HS-RC-15-03                      112       115         3      2.72
----------------------------------------------------------------------------
HS-RC-15-03                      129       130         1      0.73
----------------------------------------------------------------------------
HS-RC-15-04                       20        22         2      2.30        KA
----------------------------------------------------------------------------
HS-RC-15-04                       31        34         3      0.89        KB
----------------------------------------------------------------------------
HS-RC-15-04                       44        65        21      0.70        KW
----------------------------------------------------------------------------
HS-RC-15-04                       74        75         1      0.67
----------------------------------------------------------------------------
HS-RC-15-04                       84        85         1      1.08
----------------------------------------------------------------------------
HS-RC-15-04                      105       106         1      0.87        KS
----------------------------------------------------------------------------
HS-RC-15-05                                               NSV
----------------------------------------------------------------------------
HS-RC-15-06                       54        55         1      0.74       KA1
----------------------------------------------------------------------------
HS-RC-15-06                       69        71         2      1.17        KA
----------------------------------------------------------------------------
HS-RC-15-06                       97        98         1      1.18        KB
----------------------------------------------------------------------------
HS-RC-15-07                                               NSV
----------------------------------------------------------------------------
HS-RC-15-08                       20        21         1      0.54
----------------------------------------------------------------------------
HS-RC-15-08                       94        95         1      0.51
----------------------------------------------------------------------------
HS-RC-15-08                       98       100         2      0.74
----------------------------------------------------------------------------
HS-RC-15-08                      109       110         1      1.75
----------------------------------------------------------------------------
HS-RC-15-08                      120       124         4      1.27        KW
----------------------------------------------------------------------------
HS-RC-15-09                        1        18         7      0.35        KW
----------------------------------------------------------------------------
incl.                   6         7         1      0.50
----------------------------------------------------------------------------
incl.                   8         9         1      0.49          
----------------------------------------------------------------------------
incl.                  11        12         1      0.67
----------------------------------------------------------------------------
HS-RC-15-09                       95       104         9      0.30        KS
----------------------------------------------------------------------------
incl.                  95        96         1      0.78        KW
----------------------------------------------------------------------------
HS-RC-15-10                      109       124        15      0.57
----------------------------------------------------------------------------
HS-RC-15-11                       62        63         1      1.46
----------------------------------------------------------------------------
HS-RC-15-11                       87        88         1      0.80
----------------------------------------------------------------------------
HS-RC-15-11                      159       161         1      1.22
----------------------------------------------------------------------------
HS-RC-15-11                      173       201        28      0.38
----------------------------------------------------------------------------
incl                  180       190        10      0.62
----------------------------------------------------------------------------
incl                  180       183         3      0.99
----------------------------------------------------------------------------
HS-RC-15-12                                               NSR
----------------------------------------------------------------------------
HS-RC-15-13                                               NSR
----------------------------------------------------------------------------
HS-RC-15-14                      111       113         2      1.04
----------------------------------------------------------------------------
HS-RC-15-15                       96        97         1      0.69       KW4
----------------------------------------------------------------------------
HS-RC-15-16                       98       107         9      0.77        KW
----------------------------------------------------------------------------
HS-RC-15-17                       14        30        16      0.61
----------------------------------------------------------------------------
HS-RC-15-17                       38        41         3      1.06       KW3
----------------------------------------------------------------------------
HS-RC-15-17                      121       122         1      1.73
----------------------------------------------------------------------------
HS-RC-15-18                       54        55         1      0.61
----------------------------------------------------------------------------
HS-RC-15-19                        4         5         1      0.52
----------------------------------------------------------------------------
HS-RC-15-19                       19        21         1      1.57
----------------------------------------------------------------------------
HS-RC-15-19                       46        54         8      0.89       KW4
----------------------------------------------------------------------------
HS-RC-15-20                       98        99         1      1.12
----------------------------------------------------------------------------
HS-RC-15-20                      115       123         8      1.32        KW
----------------------------------------------------------------------------
HS-RC-15-21                       12        13         1      0.58
----------------------------------------------------------------------------
HS-RC-15-21                       15        16         1      0.50
----------------------------------------------------------------------------
HS-RC-15-21                       20        35        15      1.29        KW
----------------------------------------------------------------------------
HS-RC-15-21                       41        48         7      0.65       KW2
----------------------------------------------------------------------------
HS-RC-15-21                       66        70         4      0.69       KW3
----------------------------------------------------------------------------
HS-RC-15-21                       77        79         2      0.57
----------------------------------------------------------------------------
HS-RC-15-21                      104       105         1      0.58
----------------------------------------------------------------------------
HS-RC-15-22                       40        41         1      2.08
----------------------------------------------------------------------------
HS-RC-15-22                       78        80         2      0.64        KA
----------------------------------------------------------------------------
HS-RC-15-22                       85        86         1      0.50        KC
----------------------------------------------------------------------------
HS-RC-15-22                       90        91         1      1.50
----------------------------------------------------------------------------
HS-RC-15-22                      103       103         1      1.05        KD
----------------------------------------------------------------------------
HS-RC-15-22                      116       117         1      0.76        KE
----------------------------------------------------------------------------
HS-RC-15-22                      142       143         1      1.60
----------------------------------------------------------------------------
HS-RC-15-23                       59        61         2      0.60        KA
----------------------------------------------------------------------------
HS-RC-15-23                       90        91         1      0.74
----------------------------------------------------------------------------
HS-RC-15-23                       98       112        14      1.34        KC
----------------------------------------------------------------------------
HS-RC-15-23                      115       117         2      1.07
----------------------------------------------------------------------------
HS-RC-15-23                      122       123         1      0.56
----------------------------------------------------------------------------
HS-RC-15-23                      126       129         3      0.77
----------------------------------------------------------------------------
HS-RC-15-23                      135       140         5      2.03        KE
----------------------------------------------------------------------------
HS-RC-15-62                       34        38         4      1.55        KA
----------------------------------------------------------------------------
HS-RC-15-62                       57        63         5      0.67        KB
----------------------------------------------------------------------------
HS-RC-15-62                      189       195         6      1.19        KS
----------------------------------------------------------------------------
HS-RC-15-62                      229       230         1      2.27
----------------------------------------------------------------------------
HS-RC-15-63                       89        97         8      1.84        KA
----------------------------------------------------------------------------
HS-RC-15-63                      118       127         9      1.52        KB
----------------------------------------------------------------------------
HS-RC-15-64                        2         7         5      0.86        KA
----------------------------------------------------------------------------
HS-RC-15-64                       20        22         2      0.84
----------------------------------------------------------------------------
HS-RC-15-64                       29        35         6      1.58        KB
----------------------------------------------------------------------------
HS-RC-15-64                       42        43         1      1.55
----------------------------------------------------------------------------
HS-RC-15-64                      132       133         1      3.94
----------------------------------------------------------------------------
HS-RC-15-64                      152       153         1      5.87        KF
----------------------------------------------------------------------------
HS-RC-15-64                      158       159         1      0.62
----------------------------------------------------------------------------
HS-RC-15-64                      162       163         1      0.60
----------------------------------------------------------------------------
HS-RC-15-64                      177       186         8      0.96        KG
----------------------------------------------------------------------------
HS-RC-15-65                       63        65         2      0.71       KA1
----------------------------------------------------------------------------
HS-RC-15-65                       91        92         1      0.68
----------------------------------------------------------------------------
HS-RC-15-65                       96        97         1      1.59        KA
----------------------------------------------------------------------------
HS-RC-15-65                      104       116        12      1.49        KB
----------------------------------------------------------------------------
incl                  107       116         9      1.78
----------------------------------------------------------------------------
HS-RC-15-65                      120       124         4      1.08
----------------------------------------------------------------------------
HS-RC-15-65                      130       131         1      0.94
----------------------------------------------------------------------------
HS-RC-15-66                                     NSV
----------------------------------------------------------------------------
HS-RC-15-67                       74        76         2      0.58
----------------------------------------------------------------------------
HS-RC-15-67                       82        95        13      0.95        KW
----------------------------------------------------------------------------
(i) No Significant Values.
(ii) True widths are estimated at 50% to 100% of drilled length at the Kien
East Zone. This Table presents all composite assay values returning greater
than 0.5 g/t gold over 1 metre and those holes where no assays greater than
0.5 g/t gold over 1 metre were received.
( 1)KS is equivalent to Shear Zone on figure 1

/T/

- 30 -

CONTACT INFO:

Savary Gold Corp.
Don Dudek
647-259-2097
info@savarygold.com
www.savarygold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=540281801