Source	MARKET NEWS
Date	08/16/2016
Time	09:49:12 AM

Company	 Taranis Resources Inc.
Title	Discovers 
Multiple New Zones at Thor Assaying up





    CDNX Symbol: TRO











Press Release





TARANIS RESOURCES INC ("TRO-V;TNREF-0")
- Discovers Multiple New Zones at Thor Assaying up to 1,858 g/t
- Silver 100 m Southwest of the Existing Ag-Au-Pb-Zn-Cu Deposit

Taranis Resources Inc. (the "Company") is pleased to announce
that the results of five NQ drill holes drilled on its Thor Project
located west of the existing Ag-Au-Pb-Zn-Cu deposit.

All of the holes were drilled in the footwall of the existing
Resource, outside of the known NI 43-101 Resource and have conclusively
shown that the sulfide lodes at Thor are folded into multiple parallel
zones along the axis of the Thor Anticline that plunges shallowly to
the northwest.

The high-grade zones are tightly folded into a corridor at least
one km long that is 100 m wide at surface, and dips moderately to the
northeast along the east side of Great Northern and Broadview
Mountains. All of the intercepts reported occur from surface to a
maximum depth of 70 m below surface, but remain open at depth.

2016 Drilling Update

The following table shows the results of the first five drill
holes (Thor-155 was drilled at the onset of the program and was drilled
down-dip, and was devoid of mineralization). The core was re-examined
after the initial assays were received, and the core has undergone
additional sampling which is expected to widen some of the intercepts.



http://www.thenewswire.ca/archives?tnwcatalyst2=release_id%3D19801




Exploration is being focused on the central part of the Thor
Anticline, where a number of recent high-grade gold discoveries have
been made. These include the Gold Pit also located in the footwall of
the deposit in an outcrop (52.4 g/tonne Au and 1,542 g/t Ag/2.04 m) and
the SIF Zone (30.59 g/tonne Au/17.55 m). At Thor, gold appears to be
preferentially concentrated along the top of parasitic drag folds and
anticline axes.

John Gardiner, CEO of Taranis Resources Inc. comments "The
discovery of multiple, parallel high-grade zones in the initial five
holes at Thor has major implications for expansion at Thor. The
presence of multiple, stacked zones of high-grade mineralization makes
the project ideal for large-scale, low-cost open pit mining. Most of
the deposit is already exposed at surface along the east side of Great
Northern Mountain.

Recognition of the tight folding of the sulphide zones also gives
us a firm grasp of the structure of the deposit, and it now appears
that there could be multiple layers. Roscoe Postle Associates completed
an in-house Whittle open pit model of the Thor deposit, and found that
approximately 80% of the deposit was open pittable, but we expect that
this to dramatically increase with the discovery of these types of
en-echelon zones at Thor".

Qualified Person(s)

John Gardiner (P.Geol.) and Jim Helgeson (P.Geo.) are the
Qualified Persons on the Project.

Samples are taken under the direction of qualified geologists.
Core is sawed on-site and one half is retained for reference and
further analytical work including specific gravity determinations.
Samples of the other half are delivered by the Company via courier to
MS Analytical Labs in Langley, British Columbia. MS Analytical Labs is
an ISO-9001:2008 certified analytical laboratory. The Company inserts
standards every 10th sample for quality control in addition to the
stringent internal checks completed at MS Analytical. Samples are
dried, crushed, split and pulverized. Analysis for silver, copper, lead
and zinc and related trace elements was done by modified aqua regia
digestion with ICP finish, and gold by 30 gram fire assay with ICP
finish.

About Taranis Resources Inc.

Taranis currently has 49,766,116 shares issued and outstanding
(56,066,116 shares on a fully-diluted basis).

TARANIS RESOURCES INC.

Per:    John J. Gardiner (P. Geol.),

President and CEO

For further information contact:

//st

---------------------------------------------
|John Gardiner                            | |
|14247 West Iliff AvenueLakewood, Colorado| |
|Phone: (303) 716-5922                    | |
|Cell: (720) 209-3049                     | |
|johnjgardiner@earthlink.net              | |
---------------------------------------------

//et

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
NEWS RELEASE.

This News Release may contain forward looking statements based on
assumptions and judgments of management regarding future events or
results that may prove to be inaccurate as a result of factors beyond
its control, and actual results may differ materially from expected
results.





__________________________________________________
_______________________________________________
TSX Venture closing price for TRO-V
Date: 2016/08/12
Closing Price: 0.09
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1622800032TS11622801449-09460920160816