Source	MARKET NEWS
Date	08/01/2017
Time	07:51:41 AM

Company	 Panoro Minerals Ltd.
Title	Intersects 
195.2 m of Copper Mineralization at M





    CDNX Symbol: PML











Press Release





PANORO MINERALS LTD ("PML-V;POROF-0")
- Intersects 195.2 m of Copper Mineralization at Maria Jose Target
- At Cotabambas Project, Peru

Panoro Minerals Ltd. ("Panoro", the "Company") is pleased to
provide an update of its exploration drill program at its 100% owned
Cotabambas Cu/Au/Ag Project in Peru. Highlights are as follows:
Drillhole CB-157, the first hole completed at the Maria Jose zone,
intersected 195.2 m of primary copper mineralization grading 0.34 % Cu,
0.06 g/t Au and 1.6 g/t Ag.
Drillhole CB-158 at the Breccia zone, intersected 4.3 m of iron
oxides grading 0.9 g/t Au, 1.1 g/t Ag and 0.01 % Cu.
The drill program commenced with the mobilization of the first
drill rig at the end of May 2017 at the Breccia zone and a second rig
to Maria Jose zone. The drill core was logged and sampled on site and
samples were prepared and analyzed at ALS Chemex Laboratories in Lima.
Maria Jose Zone
The Maria Jose target is located between 1.0 and 2.5 km to the
north of the proposed North Pit as defined by the September 22, 2015
Preliminary Economic Assessment.  Hole CB-157 tested the MJ-2 target,
one of two prospects associated with a strong chargeability anomaly
within the Maria Jose zone and was completed to a total depth of 502.5
m.  The following table details the more significant intersections. A
location plan can be found at the companys website, www.panoro.com.
//st

Drillhole  From (m) To (m) Metres  Cu (%)  Au g/t     Ag g/t     Mo% Zone
CB-157     18.8     128.5  109.7     0.15    0.02     0.8     0.0023 Mixed
" "       200.9     272.8   71.9     0.17    0.01     1.0     0.0032 Primary
" "       272.8     467.9  195.2     0.34    0.06     1.6     0.0014 Primary
Including 336.0     356.0   20.0     0.51    0.07     2.4     0.0021 Primary
Including 423.3     444.4   21.2     0.42    0.07     1.8     0.0018 Primary
//et

The hole commenced within an andesite volcanic package from
surface to 200.0 m with supergene, propilitic alteration and variable
primary copper mineralization, including 109.7 m of mix mineralization
with grades of 0.15% Cu, 0.02 g/t Au and 0.8 g/t Ag.

From 200.9 m to 272.8 m the hole intersected potassically altered
quartz monzonite with primary chalcopyrite mineralization grading 0.17
% Cu, 0.01 g/t Au and 1.0 g/t Ag, before re-entering the andesitic
volcanics. A more strongly mineralized, silicified and potassically
altered interval with disseminations and veinlets of chalcopyrite which
straddles this contact graded 0.34 % Cu, 0.06 g/t Au and 1.6 g/t Ag
over 195.2 metres from 272.0 m to 467.9 m.

Drilling has shown that the extensive chargeability anomaly
associated with the Maria Jose zone is associated with varying levels
of disseminated pyrite and significant levels of chalcopyrite.
Additional drilling continues to test this anomaly.

Breccia Zone
The Breccia Target is located adjacent to the north side of the
proposed North Pit and is defined by a number of rock samples with
anomalous levels of gold distributed over an area of 1.0 km x 1.4 km
along with argillic alteration. Approximately 2,000 m of exploration
drilling is planned for the zone, of which four shallow drill holes
have been completed to date for a total of 558.1 m. The following table
details the more significant intersections.
//st
Drillhole  From(m) To(m)    Metres  Au g/t   Ag g/t  Cu (%)   Zone
CB-154     2.1     4.5      2.4     0.26     2.6     0.04     Iron Oxides
" "        6.1     8.1      2.0     0.75     3.4     0.02     Iron Oxides
" "       24.1     33.8     9.7     0.12     0.7     0.01     Iron Oxides
" "       39.0     44.6     5.6     0.15     2.0     0.02     Iron Oxides
" "       60.0     64.0     4.0     0.13     1.1     0.01     Iron Oxides
" "       70.3     82.4     12.2     0.18     2.0     0.02    Iron Oxides
Including 78.6     82.4     3.8     0.34     5.1     0.05     " "
CB-155    77.6     83.0     5.5     0.18     0.6     0.01     Iron Oxides
Including 81.6     83.0     1.5     0.27     1.0     0.00     " "
" "     102.1     104.2     2.2     0.41     18.4     0.02    Iron Oxides
Including 103.3   104.2     0.9     0.85     39.6     0.03    " "
CB-156    25.0     28.3     3.3     0.14     0.9     0.03     Iron Oxides
" "       77.3     81.8     4.5     0.11     1.4     0.01     " "
CB-158    18.7     23.0     4.3     0.90     1.1     0.01     Iron Oxides
Including 19.7     22.1     2.4     1.52     0.8     0.01     " "
//et

All four holes intersected shallow intervals of supergene iron
oxide mineralization and silica veinlets within the dacitic porphyry
intruding the dioritic host rocks, below which no primary copper
mineralization was found. Each contained a number of narrow
gold-mineralized intervals with low to moderate grades, demonstrating
the extension of oxide gold mineralization north from the known zone at
the north margin of the Ccalla zone.  Additional drilling will continue
to test the Breccia zone.

Exploration Program
A second drillhole, CB-161, has been completed in the Maria Jose
zone. It is collared approximately 140 m to the southwest of CB-157 and
has intersected primary and secondary mineralization beginning from
shallow depths.  Assay results are pending and will be announced when
batches are received and summarized.  Currently, two drill rigs are
operating at the MJ-2 target and will step out toward the MJ1 target.

Luquman Shaheen, President & CEO, of Panoro Minerals states, We
are pleased with the first results from the stepout and exploration
drill program.  The intersection of significant intervals of
mineralization at the Maria Jose zone is great news and an important
milestone for the Cotabambas Project.  This discovery validates our
exploration thesis of the potential for a cluster of porphyry deposits
around the current Ccalla and Azulccaca deposits.  Also, the
intersection of relatively shallow mineralization containing high
grades of gold and silver at the Breccia target looks promising.  We
look forward to advancing the ongoing exploration and step out drill
program with further definition of the targeted growth areas.

About Panoro
Panoro Minerals is a uniquely positioned Peru focused copper
exploration and development company. The company is advancing its
flagship project, Cotabambas Copper-Gold-Silver Project and its Antilla
Copper-Molybdenum Projects located in the strategically important area
of southern Peru. The company is well financed to expand, enhance and
advance its projects in the region where infrastructure such as
railway, roads, ports, water supply, power generation and transmission
are readily available and expanding quickly.  The region boasts the
recent investment of over $US 15 billion into the construction or
expansion of four large open pit copper mines.

Since 2007, the Company has completed over 70,000 m of exploration
drilling at these two key projects leading to substantial increases in
the mineral resource base for each, as summarized in the table below.

Summary of Cotabambas and Antilla Project Resources
//st
Project     Resource       Million
Classification Tonnes     Cu (%) Au (g/t) Ag (g/t)   Mo (%)
Cotabambas
Cu/Au/Ag   Indicated       117.1      0.42     0.23     2.74     0.001
Inferred        605.3      0.31     0.17     2.33     0.002
@ 0.20% CuEq
cutoff,
effective
October 2013,
Tetratech
Antilla
Cu/Mo      Indicated       291.8      0.34     -        -       0.01
Inferred         90.5      0.26     -        -       0.007
@ 0.175% CuEq
cutoff,
effective
May 2016,
Tetratech
//et

Preliminary Economic Assessments (PEA) have been completed for
both the Cotabambas and Antilla Projects, the key results are
summarized below.

Summary of Cotabambas and Antilla Project PEA Results
//st
Key Project Parameters                   Cotabambas  Antilla Cu/Mo
Cu/Au/Ag    Project
Project

Mill Feed, life of mine   million tonnes   483.1     350.4
Mill Feed, daily          tonnes           80,000    40,000
Strip Ratio, life of mine                  1.25 : 1  0.85 : 1

Before
Tax1             NPV7.5%  million USD      1,053     491
IRR      %                20.4      22.2
Payback  years            3.2       3.3

After
Tax1             NPV7.5%  million USD      684       225
IRR      %                16.7      15.1
Payback  years            3.6       4.1
Annual Average
Payable
Metals            Cu      thousand tonnes  70.5      36.8
Au      thousand ounces  95.1      -
Ag      thousand ounces  1,018.4   -
Mo      thousand tonnes  -         0.9

Initial Capital
Cost                      million USD      1,530     603

Project economics estimated at commodity prices of; Cu = US$3.00/lb, Au =
US$1,250/oz, Ag = US$18.50/oz, Mo = US$12/lb
//et

The PEAs are considered preliminary in nature and include Inferred
Mineral Resources that are considered too speculative to have the
economic considerations applied that would enable classification as
Mineral Reserves. There is no certainty that the conclusions within the
updated PEA will be realized. Mineral Resources are not Mineral
Reserves and do not have demonstrated economic viability.

Luis Vela, a Qualified Person under National Instrument 43-101,
has reviewed and approved the scientific and technical information in
this press release.

On behalf of the Board of Panoro Minerals Ltd.

Luquman Shaheen. PEng, PE, MBA
President & CEO

CAUTION REGARDING FORWARD LOOKING STATEMENTS:   Information and statements
contained in this news release that are not historical facts are
"forward-looking information" within the meaning of applicable Canadian
securities legislation and involve risks and uncertainties.

Forward-looking statements are subject to a variety of known and unknown
risks, uncertainties and other factors which could cause actual events or
results to differ materially from those expressed or implied by the
forward-looking statements, including, without limitation:

risks relating to metal price fluctuations;
risks relating to estimates of mineral resources, production, capital and
operating costs, decommissioning or reclamation expenses, proving to be
inaccurate;
the inherent operational risks associated with mining and mineral
exploration, development, mine construction and operating activities, many
of which are beyond Panoros control;
risks relating to Panoros ability to enforce Panoros legal rights under
permits or licenses or risk that Panoros will become subject to litigation
or arbitration that has an adverse outcome;
risks relating to Panoros projects being in Peru, including political,
economic and regulatory instability;
risks relating to the uncertainty of applications to obtain, extend or
renew licenses and permits;
risks relating to potential challenges to Panoros right to explore and/or
develop its projects;
risks relating to mineral resource estimates being based on interpretations
and assumptions which may result in less mineral production under actual
circumstances;
risks relating to Panoros operations being subject to environmental and
remediation requirements, which may increase the cost of doing business and
restrict Panoros operations;
risks relating to being adversely affected by environmental, safety and
regulatory risks, including increased regulatory burdens or delays and
changes of law;
risks relating to inadequate insurance or inability to obtain insurance;
risks relating to the fact that Panoros properties are not yet in
commercial production;
risks relating to fluctuations in foreign currency exchange rates, interest
rates and tax rates; and
risks relating to Panoros ability to raise funding to continue its
exploration, development and mining activities.
This list is not exhaustive of the factors that may affect the
forward-looking information and statements contained in this news release.
Should one or more of these risks and uncertainties materialize, or should
underlying assumptions prove incorrect, actual results may vary materially
from those described in the forward-looking information.  The
forward-looking information contained in this news release is based on
beliefs, expectations and opinions as of the date of this news release.
For the reasons set forth above, readers are cautioned not to place undue
reliance on forward-looking information.  Panoro does not undertake to
update any forward-looking information and statements included herein,
except in accordance with applicable securities laws.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.



Panoro Minerals Ltd.
Luquman Shaheen, President & CEO
TEL: 604.684.4246
FAX: 604.684.4200
Email: info@panoro.com
Web: www.panoro.com

Renmark Financial Communications Inc.












TSX Venture closing price for PML-V
Date: 2017/07/31
Closing Price: 0.16

TEL: (416) 644-2020 or (416) 939-3989
E-mail: blwelsh@renmarkfinancial.com
Internet: www.renmarkfinancial.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1721200023TS11721201533-07495620170801