Source	Marketwire
Date	08/09/2017
Time	04:01:21 AM

Company	 STRIKEPOINT GOLD INC.
Title	StrikePoint Gold Inc. Announces Encouraging Initial Results From Yukon 
Exploration





    CDNX Symbol: SKP











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: StrikePoint Gold Inc.

TSX VENTURE SYMBOL: SKP
OTCQB SYMBOL: STKXF

August 9, 2017

StrikePoint Gold Inc. Announces Encouraging Initial Results From Yukon 
Exploration


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Aug. 9, 2017) - StrikePoint Gold 
Inc. (TSX VENTURE:SKP)(OTCQB:STKXF) is pleased to report the encouraging 
results from surface sampling undertaken in June 2017 at its wholly owned 
Mahtin gold property. Rock chip samples from skarn material over an area 
extending for 900 m returned grades up to 9.20 g/t Au. Additional samples from 
an area previously thought to be unmineralized graded up to 2.20 g/t Au. A RAB 
drill program of six holes totaling 630m has been completed in this area. 
Results are pending.

Samples grading up to 293 g/t silver were also returned from an area 1km to the 
east of the drilled area suggesting mineralization extends into the adjacent 
valley. The results received to date suggest an area of interest extending over 
a 2km strike length. Additional step out sample results are pending. The 
majority of sulphides observed and encouraging gold and silver grades are from 
limestone skarns around the periphery of the Sprague Creek Stock. Additionally, 
arsenopyrite bearing quartz veins were sampled from within the granodiorite 
stock itself for which results are also pending.

The May-Qu target, 17 kilometers to the southeast of Mahtin North target has 
also been mapped and sampled. Initial results from grab sampling have returned 
assays including 2.22 g/t Au, 2.12g/t Au and 1.74 g/t Au. A RAB drill program 
of three holes totaling 300m has also been completed here.

Further assays are pending from the laboratory for both surface sampling and 
the initial drilling. Results will be released when these are finalized.

QA/QC

The Company maintains a rigorous QA/QC program with respect to the preparation, 
shipping, analysis and checking of all samples and data from the properties. 
Quality control for field sampling and drill samples at the Company's projects 
covers the complete chain of custody of samples, including sample handling 
procedures and analytical-related work, plus the insertion of standard and 
blank materials. The QA/QC program also includes data verification procedures. 
ALS Laboratories in Vancouver, Canada (ISO 17025:2005 accreditation) assayed 
all samples from the current field program using fire assay and ICP Mass 
Spectroscopy methods.

The technical information contained in this news release has been approved by 
Andy Randell, P. Geo., Vice President, Exploration of StrikePoint Gold. Mr. 
Randell is a qualified person as defined in NI 43-101.

For further information, please review the Corporate Presentation on the 
StrikePoint Gold Inc. website for a more detailed, comprehensive review of the 
2017 exploration program: 
http://www.strikepointgold.com/images/Yukon-Properties-Presentation.pdf

ON BEHALF OF THE BOARD of STRIKEPOINT GOLD INC.

Shawn Khunkhun, CEO and Director

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

StrikePoint Gold Inc.
Shawn Khunkhun
604-602-1440
sk@strikepointgold.com
www.strikepointgold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=597287880