Source	MARKET NEWS
Date	08/17/2017
Time	06:47:10 AM

Company	 Brixton Metals Corporation
Title	Samples 16% 
Cobalt And 182,065 G/t Silver At Lan





    CDNX Symbol: BBB











Press Release





BRIXTON METALS CORP ("BBB-V;BXTMF-0")
- Samples 16% Cobalt And 182,065 G/t Silver At Langis
- And Provides An Update On Its Projects

Brixton Metals Corporation (the "Company" or "Brixton") is pleased
to announce project updates for its projects located in both Ontario
and British Columbia, Canada.

2017 Thorn Gold-Silver Project, British Columbia

Brixton completed ten NQ-sized core drill holes for a total of
2,455 metres at the Chivas Zone. Drilling at the Chivas Zone was
designed to test the gold-in-soil anomaly identified in 2016. The
gold-in-soil anomaly at the Chivas Zone covers a 7 square kilometre
area and has corresponding chargeability anomalies from the 2016
Titan-24 DC/IP survey. In 2017 Brixton collected 517 soil and 56 rock
samples throughout the property and completed two weeks of 1:2500 and
1:5000 scale geological and alteration mapping at the Chivas Zone.
Aerial Lidar was conducted over a 210 square kilometre area. Brixton
expanded its claim group from 996 square kilometres to 1,114 square
kilometres.

Thorn Project 2017 drill results are pending at this time.

Thorn Project Soil Results

Using a 100 ppb cut off for the soil results, 69 samples are
greater than 100 ppb Au, 44 samples are greater than 200 ppb, 28
samples are greater than 400 ppb, 12 are greater than 800 ppb with the
two highest samples being 4,900 and 6,920 ppb Au.

Geological Mapping at the Chivas Zone Identifies a New Copper Trend
at Thorn

Mapping was successful in identifying a 115m by 1200m open-ended
corridor of copper mineralization with up to 1.14% Cu and 2.15 g/t Au
from surface rock sampling. The best values from rock grab samples were
4.49 g/t Au, 4.38% Cu and 443 g/t Ag. Please see map at the link:
http://brixtonmetals.com/wp/wp-content/uploads/2016/12/Chivas-Geology-NR-A2
017.jpg

Mineralization is dominantly hosted by
quartz-carbonate-py+/-galena-sphalerite-sulphosalt veins and polyphase
breccias cutting Stuhini Group volcanic rocks and is interpreted as
being related to an epithermal system transitional to a Cu-Au-Mo
porphyry system.

Geology was mapped by Marcus van Wermeskerken, B.Sc., he stated
"there is a fairly well developed zoning in both alteration and
mineralization, centered on the main porphyry intrusion. Starting at
the centre, there is a distinct trend along which a porphyry type
mineralization exists as disseminated chalcopyrite, malachite, quartz
stockwork zones with sericite. Outwards from this core, there is a zone
of scattered polymetallic veins and fault breccias, hematite, chlorite,
epidote and patchy potassic alteration. This alteration-mineralization
was measured on one side of the cuprous corridor for 600 metres. This
suggests there was a significant heat pump at the time of
mineralization. This is only at the very apex of what could potentially
be a much larger intrusion below. A significant amount of epithermal
type mineralization (polymetallic veins, chalcedony veins-breccia and
argillic alteration zones) was noted, which is typical in the periphery
of porphyry systems, suggesting potential for a mineralized system
below."

A reconnaissance soil line in a new area 2.7 kilometres south from
the southern end of the Chivas Zone returned an anomalous
copper-in-soils area with a single rock sample returning 4.38% Cu and
0.8 g/t Au (see link to map above).

About the Chivas Gold Zone (Thorn Project)

The Chivas Gold Zone was first identified in 2014 when the Company
collected 16 soil samples along a break in slope where 12 of the 16
samples where anomalous (above 30 ppb Au) in gold with a high of 11,000
ppb Au was found. There was no previous work reported from this area of
the property and this zone represents an important new mineralized
target. The Chivas Zone is located about 3 kilometres southwest from
the western edge of the sediment hosted Outlaw Gold Zone where hole 128
intersected 59.65m of 1.15 g/t Au, 5.64 g/t Ag, and about 4 kilometres
south from the silver rich Oban Diatreme Zone where hole 60 intersected
95m of 628 g/t Ag and 1.71 g/t Au. Host lithology to mineralization at
the Chivas Zone is Triassic Stuhini group mafic volcanics. The 7 square
kilometre gold-in-soil anomaly and the IP chargeability anomaly clearly
define an open-ended northwest trend. The red-line boundary
(Triassic-Jurassic unconformity) was mapped about 800 metres west of
the Chivas anomaly. According to Kyba and Nelson of the BCGS, most
major deposits in northwestern BC, including KSM, Brucejack and Eskay
Creek, occur within 2 km of this regional red-line marker, which
implies major regional-scale faults as metal-rich fluid pathways.
Please see link to the Chivas Zone:
http://brixtonmetals.com/properties/thorn-project/chivas-zone/

2017 Atlin Gold Project, British Columbia

Results from 26 rock samples returned a high of 24 g/t Au. Twelve
of the 26 samples were greater that 0.1 g/t Au. The samples were
collected in the vicinity of historic trenches on the LD claims;
however, at the time of sampling the trenches were reclaimed and filled
in. Brixton conducted an airborne magnetic survey of eight flight lines
covering a total of 4,571 line kilometres of high resolution magnetic
data. The traverse lines were flown East-West at a spacing of 200
metres with control lines flown North-South at a separation of 2000
metres. Nominal terrain clearance was specified at 100 metres above
ground. Compilation of historic data and interpretation of the airborne
magnetic survey is ongoing. Please see link to the Map showing the LD
claims:



http://brixtonmetals.com/wp/wp-content/uploads/2017/06/Atlin-Mineralization
-Map-NR-A2017.jpg

http://brixtonmetals.com/wp/wp-content/uploads/2017/06/Atlin-Geochem-NR-A20
17.jpg

Historical work on the LD claims includes 330 g/t Au (mini-bulk
sample), 1,615 g/t Au (rock grab sample) and 3m of 9.39 g/t Au (drill
core). Brixton's land package in the Atlin gold camp offers large
target areas for exploration in search of Barkerville style or
California style mother-lode gold deposits that may exist in
prospective host rocks that are masked by overburden. Please see link
to Atlin Gold Project page:
http://brixtonmetals.com/atlin-gold-project/

2017 Langis-Hudson Bay Ag-Co Project, Ontario

Historical data compilation continues for the Langis area.
Following the acquisition of the Penna lands from Agnico at the Langis
site, four rock grab samples from the Penna #7 shaft dump area were
submitted for analysis. The table below provides details which returned
up to 18% silver and 16% Cobalt. Samples contained abundant native
silver.

//st

Langis Penna Shaft #7 Dump Rock Samples

Sample                                    Cobalt   Silver    Silver

%        g/t       %

1                                         12.80    182,065   18.2

2                                         16.00    29,515    2.9

3                                         10.70    28,673    2.8

4                                         15.25    21,672    2.1
//et

The actual location or source of the sampled material is unknown;
however, it was likely sourced from underground workings between the #7
and #6 shaft. The qualified person has not done sufficient work to
verify the sample locations. The grab samples by nature are selective
samples and do not represent grades throughout the property. Cobalt was
analyzed using four acid digestion and the silver was analyzed by Fire
Assay Fusion and Gravimetric Finish and since the samples exceeded the
upper limit of 10,000 ppm the samples were treated as concentrate by
ALS Minerals.

Brixton added 178 hectares of mineral title lands to its Langis
Project. The one hundred percent interest was acquired from Mid-North
Engineering Services Ltd for consideration of 150,000 common shares of
Brixton and $5,000. The title is subject to a 1% NSR in favour of the
vendor where Brixton holds the right to purchase 0.5% NSR for $250,000.


The Langis Project is drill ready with both brownfield and
greenfield high-grade Ag-Co targets. Subject to available funding the
Company plans to conduct additional drilling at its Langis and Hudson
Bay Projects this fall and winter season. Please see link to the Langis
Project:
http://brixtonmetals.com/properties/langis-silver-cobalt-project/

Mr. Gary R. Thompson, P.Geo., is a Qualified Person as defined
under National Instrument 43-101 standards and has reviewed and
approved this news release.

About Brixton Metals Corporation

Brixton is a Canadian exploration and development company focused
on the advancement of its gold and silver projects toward feasibility.
The Company is actively seeking JV partners to advance one or more of
it projects.

Brixton Metals Corporation shares trade on the TSX-V under the
ticker symbol BBB. For more information about Brixton please visit our
website at www.brixtonmetals.com.

On Behalf of the Board of Directors

Mr. Gary R. Thompson, Chairman and CEO

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

Information set forth in this news release may involve
forward-looking statements under applicable securities laws.
Forward-looking statements are statements that relate to future, not
past, events. In this context, forward-looking statements often address
expected future business and financial performance, and often contain
words such as "anticipate", "believe", "plan", "estimate", "expect",
and "intend", statements that an action or event "may", "might",
"could", "should", or "will" be taken or occur, including statements
that address potential quantity and/or grade of minerals, potential
size and expansion of a mineralized zone, proposed timing of
exploration and development plans, or other similar expressions. All
statements, other than statements of historical fact included herein
including, without limitation, statements regarding the completion of
the acquisition, the anticipated closing of the acquisition, TSXV
approval, and the exploration potential of the property based on
resources estimates and forward looking statements. By their nature,
forward-looking statements involve known and unknown risks,
uncertainties and other factors which may cause our actual results,
performance or achievements, or other future events, to be materially
different from any future results, performance or achievements
expressed or implied by such forward-looking statements. Such factors
include, among others, the following risks: the need for additional
financing; operational risks associated with mineral exploration;
fluctuations in commodity prices; title matters; and the additional
risks identified in the annual information form of the Company or other
reports and filings with the TSXV and applicable Canadian securities
regulators. Forward-looking statements are made based on management's
beliefs, estimates and opinions on the date that statements are made
and the Company undertakes no obligation to update forward-looking
statements if these beliefs, estimates and opinions or other
circumstances should change, except as required by applicable
securities laws. Investors are cautioned against attributing undue
certainty to forward-looking statements.




























TSX Venture closing price for BBB-V
Date: 2017/08/16
Closing Price: 0.36

TEL:  604-630-9707   Mr. Gary R. Thompson, Chairman and CEO
Email: info@brixtonmetals.com
____________________________________________________________
(c)2017 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1722800023TS11722801040-06450820170817