Source	Marketwire
Date	12/07/2012
Time	02:03:58 PM

Company	 ZENA MINING CORP.
Title	Zena Mining Corp.: 2012 Exploration Program Completed at Lapin Barite 
Property





    CDNX Symbol: ZCC











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRE


FOR: Zena Mining Corp.

TSX VENTURE SYMBOL: ZCC

December 7, 2012

Zena Mining Corp.: 2012 Exploration Program Completed at Lapin Barite Property


VANCOUVER, BRITISH COLUMBIA--(Marketwire - Dec. 7, 2012) - Zena Mining Corp. 
(TSX VENTURE:ZCC) ("Zena" or the "Company") is pleased to announce that it has 
completed its 2012 exploration program on its Lapin Barite property situated 
near Rock Creek, B.C. The Company owns 100% of the rights to the Industrial 
Minerals subject to a 10% net profits interest and royalty and other payments 
based on production to the original underlying vendors.

Barite (Barium sulphate - BaSO4) the primary industrial mineral on this 
property, is a major component and the weighting agent used in drilling mud for 
the oil and gas industry's exploration and developmental drilling programs. In 
2004, Zena obtained a permit for exploration and test mining a small bulk 
sample.

In 2010, Zena explored the "B" zone deposit by excavator stripping, mapping, 
and diamond sawing representative samples. Stripping exposed an area roughly 40 
by 20 meters which contains at least five zones of Barite, of which the most 
important is the Main zone, exposed over a strike length of 20 meters and up to 
10 meters wide.

In September 2011, additional areas in the "B" zone were stripped, and argillic 
sediments were removed from the east wall of the Main zone. An excavator with a 
rock-breaker was used to expose the barite along its length, and about 200 
tonnes of barite was set aside from which 20 tonnes was mined and trucked to a 
storage site in Rock Creek B.C. From the "B" zone, 26 barite samples each from 
1-5 kg in size (averaging 3 kg) were collected from four separate areas and 
shipped to ALS Minerals Laboratory (ISO 17025 accredited) in North Vancouver, 
where Specific Gravity measurements were completed. The twenty-six samples from 
the Main Zone had specific gravity ranging from 3.63 to 4.41, with a weighted 
average of 4.12.

A minimum specific gravity of 4.10 is required for Barite used as a weighting 
medium for drilling mud.

In July 2012, a small work program was completed on the "B" zone, stripping an 
additional area approximately 20 meters northward from the 2011 work. 
Additional barite was broken out using an excavator and set aside for sampling 
and testing. Approximately 500 tonnes of barite is now piled at the side of the 
stripped area and is available for testing.

In October 2012, the barite was randomly sampled along the length of the mined 
material with 3 samples totalling approximately 25 kg. The weighted average 
specific gravity measured by ALS Canada Ltd. Laboratory was 3.83. Individual 
samples tested ranged from specific gravity of 2.67 to 4.09.

The property has at present three known zones with Barite mineralization, known 
as "A", "B" and "C" zones.

The Company's 2013 planned exploration program, subject to renewal of the 
exploration and test mining permit from the Mines Inspection Branch, is 
recommended to be approximately the same as the 2012 program, with a cost 
budget to be approximately the same as the 2012 program. The 2013 program will 
include additional stripping of the northern limits of the Barite lenses in the 
"B" zone, with the goal of producing a larger test sample. The Company may also 
include in the exploration program further review of the "A" zone.

This press release has been reviewed by Barry J. Price, M.Sc., P.Geo., an 
independent consultant based in Vancouver BC. Mr. Price reviewed the 2012 
stripping and sampled the test-mined material.

ON BEHALF OF THE BOARD

Kevin Hanson, Director

- 30 -

CONTACT INFO:

Zena Mining Corp.
Kevin Hanson
Director
604-681-2868

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

MWDisclaimer
If you no longer want to receive announcements from us, please do 
not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=396923562