Source	Marketwire
Date	12/16/2014
Time	05:00:18 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold's Intersects 7.79 g/t Gold Over 9.14 Meters at the Mary LC 
Deposit, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

December 16, 2014

Scorpio Gold's Intersects 7.79 g/t Gold Over 9.14 Meters at the Mary LC 
Deposit, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Dec. 16, 2014) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports further 
assay results from its 2014 drill program on the Mary LC deposit at the 70% 
owned Mineral Ridge project, located in Nevada.

On July 21, 2014, the Company reported an updated Life of Mine Plan ("LOM 
Plan") for the Mineral Ridge Operation, which includes the currently producing 
Drinkwater and Mary LC deposits and five adjacent satellite deposits. As of 
March 31, 2014, Probable Mineral Reserves for the Mary LC deposit totalled 
1,502,560 tons grading 0.061 ounces per ton (oz/ton) for 91,510 contained 
ounces gold. Probable Mineral Reserves are included within an Indicated Mineral 
Resource of 1,534,500 tons grading 0.063 oz/ton gold. Inferred Mineral 
Resources for the Mary LC deposit totalled 50,900 tons grading 0.061 oz/ton.

Pre-stripping of the Mary LC pit commenced in the first quarter of 2014 and 
extraction of development ore was realized in the second quarter of 2014. 
Continued infill and step-out drilling on the Mary LC deposit since the March 
31, 2014 cut-off date of the LOM Plan is designed to potentially upgrade and 
increase the reported mineral reserve and resource estimate and potentially 
extend life of mine.

Highlights of the most recent assay results received for 15 holes drilled on 
the Mary LC, include:

/T/

--  MR141183: 7.79 grams per tonne ("g/t") gold over 9.14 meters
--  MR141188: 7.02 g/t gold over 4.57 meters
--  MR141204: 5.16 g/t gold over 7.62 meters

/T/

Scorpio Gold's management considers these latest results from expansion 
drilling program on the Mary LC deposit to be positive, and anticipates that 
once the expansion drilling program is complete, the drill results will allow 
for a revised reserve and resource estimate on the Mary LC deposit.

A drill hole location map is available at: DH Plan

Table 1. Mary LC Deposit - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole       Azm   Dip   From     To  Width   From     To  Width   Gold   Gold
No.      (deg) (deg)   (ft)   (ft)   (ft)    (m)    (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR141179   225   -60     30     35      5   9.14  10.67   1.52  0.016   0.55
----------------------------------------------------------------------------
MR141180   225   -70    115    135     20  35.05  41.15   6.10  0.015   0.51
----------------------------------------------------------------------------
185    190      5  56.39  57.91   1.52  0.011   0.38
----------------------------------------------------------------------------
220    230     10  67.06  70.10   3.05  0.012   0.41
----------------------------------------------------------------------------
MR141181     0   -90    230    240     10  70.10  73.15   3.05  0.016   0.55
----------------------------------------------------------------------------
315    320      5  96.01  97.54   1.52  0.173   5.93
----------------------------------------------------------------------------
345    350      5 105.16 106.68   1.52  0.060   2.06
----------------------------------------------------------------------------
MR141182     0   -90     30     35      5   9.14  10.67   1.52  0.019   0.65
----------------------------------------------------------------------------
350    360     10 106.68 109.73   3.05  0.031   1.05
----------------------------------------------------------------------------
MR141183     0   -90     30     60     30   9.14  18.29   9.14  0.227   7.79
----------------------------------------------------------------------------
incl.                    30     45     15   9.14  13.72   4.57  0.424  14.53
----------------------------------------------------------------------------
210    215      5  64.01  65.53   1.52  0.013   0.45
----------------------------------------------------------------------------
MR141184     0   -90     40     45      5  12.19  13.72   1.52  0.024   0.82
----------------------------------------------------------------------------
120    130     10  36.58  39.62   3.05  0.106   3.63
----------------------------------------------------------------------------
MR141185   225   -70     30     35      5   9.14  10.67   1.52  0.056   1.92
----------------------------------------------------------------------------
95    105     10  28.96  32.00   3.05  0.047   1.59
----------------------------------------------------------------------------
190    195      5  57.91  59.44   1.52  0.014   0.48
----------------------------------------------------------------------------
MR141186     0   -90    215    220      5  65.53  67.06   1.52  0.016   0.56
----------------------------------------------------------------------------
255    265     10  77.72  80.77   3.05  0.019   0.67
----------------------------------------------------------------------------
MR141187   225   -70     90     95      5  27.43  28.96   1.52  0.020   0.69
----------------------------------------------------------------------------
185    200     15  56.39  60.96   4.57  0.018   0.61
----------------------------------------------------------------------------
MR141188     0   -90      0     15     15   0.00   4.57   4.57  0.053   1.82
----------------------------------------------------------------------------
80     95     15  24.38  28.96   4.57  0.205   7.02
----------------------------------------------------------------------------
incl.                    85     90      5  25.91  27.43   1.52  0.517  17.73
----------------------------------------------------------------------------
150    155      5  45.72  47.24   1.52  0.010   0.35
----------------------------------------------------------------------------
MR141189   225   -65      0      5      5   0.00   1.52   1.52  0.064   2.18
----------------------------------------------------------------------------
135    140      5  41.15  42.67   1.52  0.012   0.43
----------------------------------------------------------------------------
MR141190   225   -65    100    120     20  30.48  36.58   6.10  0.015   0.52
----------------------------------------------------------------------------
MR141202   225   -65    315    325     10  96.01  99.06   3.05  0.014   0.48
----------------------------------------------------------------------------
MR141203   225   -65     45     55     10  13.72  16.76   3.05  0.077   2.64
----------------------------------------------------------------------------
65     70      5  19.81  21.34   1.52  0.026   0.89
----------------------------------------------------------------------------
95    115     20  28.96  35.05   6.10  0.017   0.59
----------------------------------------------------------------------------
MR141204   225   -65    125    150     25   38.1  45.72   7.62  0.150   5.16
----------------------------------------------------------------------------
incl.                   130    135      5  39.62  41.15   1.52  0.472  16.18
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation ("RC") 
drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Waterton Global Value L.P. (30%), and Scorpio Gold is currently entitled to 
receive 80% of cash flow generated. Mineral Ridge is a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property and processing facility in Manhattan, 
Nevada. The Company is assessing its exploration plans for the Goldwedge 
property as well as the potential for toll milling at the Goldwedge plant, 
which is currently permitted for 400 tons per day.

Scorpio Gold's President, Steve Roebuck, PGeo, is a Qualified Person as defined 
by National Instrument 43-101 and has reviewed and approved the content of this 
release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Steve Roebuck, President

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including pit expansion on the Mary LC deposit. Such 
forward-looking statements involve known and unknown risks, uncertainties and 
other factors that could cause actual events or results to differ materially 
from estimated or anticipated events or results implied or expressed in such 
forward-looking statements, including risks involved in exploration programs 
and those risk factors outlined in the Company's Management Discussion and 
Analysis as filed on SEDAR. Any forward-looking statement speaks only as of the 
date on which it is made and, except as may be required by applicable 
securities laws, the Company disclaims any intent or obligation to update any 
forward-looking statement, whether as a result of new information, future 
events or results or otherwise. Forward-looking statements are not guarantees 
of future performance and accordingly undue reliance should not be put on such 
statements due to the inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Steve Roebuck
President
(819) 825-7618
sroebuck@scorpiogold.com
www.scorpiogold.com

or

Investor Relations:
Torrey Hills Capital
Jim Macdonald
(858) 456-7300
jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=511195838