Source	CANADA NEWSWIRE
Date	12/17/2014
Time	06:24:34 AM

Company	 Tasman Metals Ltd.
Title	Tasman expands critical metal portfolio with acquisition of two chromite
projects in Finland





    CDNX Symbol: TSM











Press Release	




" BC-Tasman-New-Projects   12-17 3011
News release via Canada NewsWire, Toronto 416-863-9350

Attention Business Editors:
^Tasman expands critical metal portfolio with acquisition of two chromite
projects in Finland@

VANCOUVER, Dec. 17, 2014 /CNW/ - Tasman Metals Ltd. ("Tasman" or the
"Company") (TSXV:TSM) (Frankfurt:T61) NYSE-MKT: TAS). The Company is pleased
to announce it has entered into a letter of agreement dated December 15, 2014,
(the "Letter Agreement") with Kipu Metals Corp. (the "Vendor") under which the
Company will acquire (the "Acquisition") a 100% interest in a portfolio of
stratiform chromite projects in north-eastern Finland totaling 11,400 ha in
size (the "Chromite Portfolio") in exchange for the refund of costs incurred
to date of C$45,529 by the Vendor. There is no additional consideration for
the Acquisition. Closing of the Acquisition is subject to TSX Venture Exchange
approval.
Mr. Michael Hudson, a director of the Company, and Mr. Mark Saxon, the
Company's President, CEO and a director, are also directors and shareholders
of the Vendor. As a result, the Acquisition is a related party transaction as
such term is defined under Multilateral Instrument 61-101 Protection of
Minority Security Holders in Special Transactions ("MI 61-101"). The
Acquisition is exempt from the valuation and minority shareholder approval
requirements pursuant to exemptions available to the Company under MI 61-101
as the total consideration being received by Mr. Hudson and Mr. Saxon does not
exceed 25% of Tasman's market capitalization.
Under the Acquisition, Tasman has acquired 2 chromite projects (Akanvaara
and Koitelainen) that lie approximately 75 km apart in north-eastern Finland
(Figure 1). The projects are secured by 120 exploration claims and claim
applications totaling 11,400 hectares in size. North-eastern Finland has been
a very active exploration district, following the discovery of the large
Sakati Cu-Ni deposit by Anglo American, as announced in November 2011.
Highlights
<<

--  The Chromite Portfolio includes two projects with very extensive
previous drilling, metallurgical testing and historical resources. Both
are easily accessible by road;
--  Projects lie along the geological trend of the producing Kemi chromite
mine;
--  In addition to stratiform chromite, the projects have demonstrated
potential for both platinum group elements (PGE's) and vanadium (V);
--  Chromite and PGE's are both defined as critical raw materials by the
European Commission due to the highly concentrated current supply.
Europe is a major consumer of chromite for stainless steel;
>>
"Acquisition of this advanced chromite portfolio provides Tasman with the
opportunity to broaden our reach in the critical metals arena within Europe"
said Mark Saxon, Tasman's President and CEO. "While we maintain our focus on
the exciting developments underway at our Norra Karr heavy REE project in
Sweden, we remain active in the pursuit of undervalued assets that suit our
current portfolio and strategy."
Based on its economic importance to European industry and a high risk of
supply disruption, both chromium and PGE's are defined as "critical" raw
materials within recent European Commission (EC) publications (see:
http://ec.europa.eu/enterprise/policies/raw-materials/critical/index_en.htm),
in line with the balance of Tasman's existing project portfolio.
Chromium (Cr) is an essential industrial element due in particular to its
strengthening effect on steel alloys and its resistance to corrosion. Most
(>90%) of the current global chromite production is destined for use in the
metallurgical industry, in particular for stainless steel which requires a
minimum of 10.5% Cr by mass to impart favorable strength and anti-corrosion
properties. The remaining chromite is used in the aeronautics (for the
protection of aluminium aircraft bodies), foundry, chemical and refractory
sectors. Overall, demand growth for stainless steel and therefore chromium is
forecast in the range 4-5% per year to 2020.
European stainless steel production is highly significant, second only to
China in scale and accounting for some 20% of global output. Europe's share of
world chromium metal demand is equally significant, estimated by the European
Commission at 1.8 million tonnes (approximately 18.5% of global consumption).
At present, 80% of this demand is supplied from South Africa, whilst together
Kazakhstan and South Africa hold greater than 85% of the currently known
global resources (USGS).
The Kemi mine of Outokumpu in northern Finland is the EU's only chromium
supplier.
Project Descriptions
The Akanvaara and Koitelainen chromite projects are of a stratiform
intrusion-hosted style that together with similar deposits on the Kola
Peninsula of Russia constitute one of the largest known undeveloped resources
of chromite in the world. The Akanvaara and Koitelainen intrusions are part of
a group of Archean/early Proterozoic mafic layered intrusions within the
Fennoscandian Shield, which show cumulate igneous layering similar to other
large layered intrusions (Fiskenaesset, Burakovka, Bushveld), and host
deposits of chromite, vanadium, titanium, PGE's and gold.
Akanvaara
The Akanvaara layered intrusion is located 140 km northeast of the town
of Rovaniemi, with simple vehicle access through a network of gravel logging
and drill roads. The closest rail access lies some 40km to the south, and a
commercial airport in Kemijärvi being 62 km to the northeast. The Akanvaara
project consists of 53 granted claims for 4750 hectares.
The Akanvaara mafic intrusion has a known surface area of about 50 km2,
with a strike length along magmatic layering of 10 km and a total
stratigraphic thickness of approximately 3.1 km. The intrusion is
characterised by a persistently layered sequence of mafic and ultramafic
gabbro, pyroxenite, anorthosite and chromitite (chromium enriched) above a
lower chilled margin.
The Geological Survey of Finland (GTK) discovered and explored the
Akanvaara intrusion from 1990 to 1999, at which point the project was offered
for tender. Work completed by GTK included ground geophysical surveys
(magnetic, electromagnetic, gravity); diamond drilling of 118 holes for a
total of 18,136 m; and laboratory scale beneficiation testing on a number of
mineralization styles. Twenty three (23) chromitite layers were discovered
within the Akanvaara intrusion, each with different thickness, strike extent
and potential, across a total stratigraphic thickness of 1,100 m. Mineralized
lenses vary from centimetre to tens of metres in thickness.
Following drilling, GTK completed an historic resource calculation on the
3 most persistent chromitite lenses and a vanadium enriched gabbro. Cumulate
layers are noted to be very strike extensive with predictable grade and
thickness. Historical resource estimates are provided in Table 1 and are based
upon a report entitled "Akanvaaran intrusion kromi-, kromivanadiini,
vanadiini- ja platinametalli- kultaesiintynay" by Mutatanen, T. 1998 on behalf
of the Geological Survey of Finland.
Table 1: Historical Resource Estimate for the Akanvaara Chromite Project,
Finland

Name             Historical         Cr %  PGE ppm        V %              
Comments

Resources

(Million Tonnes)
---           ---------------

Akanvaara LC(x)                  27.0  15.7           0.60    0.00
------------                   ----  ----           ----    ----

Akanvaara UC(x)                  18.1  22.8           0.91    0.40     Reef 
thickness is 1 m, extent
7.9 km along strike, tonnage is
estimated down to 300 m
vertical depth where the
occurrence is open along dip.
-------------                  ---- ----          ----   ----   
--------------------------------

Akanvaara
ULC(x)                          10.0  15.3           0.00    0.00
---------                      ----  ----           ----    ----

Base of                        20.0   0.0           0.00    0.34     The 6 - 13 
metres thick basal
Magnetic                                                        part of the 
magnetite gabbro
unit, with V-rich magnetite.
20 million metric tons down to
100 metres (vertical) depth,
with 0.34 % V, 0.10 % Cu, and
2.5 g/t Ag.

Gabbro(x)

(x)The data from these projects is historical in nature and was compiled
prior to the implementation of NI 43-101 reporting standards. Tasman has not
completed sufficient exploration to verify the estimates and we are not
treating them as NI 43-101 defined resources or reserves verified by a
qualified person; the historical estimate should not be relied upon.
GTK commissioned the Technical Research Centre of Finland (VTT) for
preliminary mineral processing testing. Samples from the UC horizon were used
for flotation tests, which yielded a chromite concentrate with 33.8% Cr2O3
(chromium oxide) and 0.55% V with recovery of 92% and 88% respectively. The
chromite concentrate was shown to be relatively rich in iron, low in alumina
and practically devoid of magnesium. This suggests Akanvaara chromite-vanadium
concentrate may have potential as a metallurgical and chemical grade raw
material for production of ferrochrome, chrome-vanadium alloys and chrome
chemicals.
Flotation tests completed on the ULC material gave a higher-grade
concentrate of 38.3% Cr203, with the promising recovery of 86%.
A series of magnetic concentrates (approximately 10 - 12 weight % of the
feed) were produced from the Magnetic Gabbro Unit which contained 1.55 - 1.59
weight % V with up to 60% recovery of vanadium. A number of copper
(Cu)-sulphide concentrates were also produced by flotation of this Magnetic
Gabbro sample with a grade of 8 - 14% Cu, 1.4 g/t Au, 53 - 57 g/t Ag, 0.073
g/t Rh and 0.068 g/t Pt.
Subsequent to GTK's tender, the property was held by Finnish company
Outokumpu, who evaluated Akanvaara for PGE's and recognised that
magnetite-bearing gabbros in the uppermost section of the intrusion where
little GTK drilling was complete were highly anomalous in PGE's (to 1.26 g/t).
Outokumpu completed 5 drill holes and undertook extensive surface sampling.
Koitelainen
The Koitelainen layered intrusion is located 75 km northwest of
Akanvaara. The nearest railroad is found in Salla, 100 km to the south, and
the area is accessible by car through a network of gravel logging and drill
roads. The Koitelainen project consists of 67 claim applications for 6650
hectares and is totally contained within a Natura 2000 area.
The Koitelainen intrusion is a flat, oval-shaped anticline, 26 km x 29 km
in size with an estimated maximum thickness of around 3.2 km. The interior of
the anticline is made up of Archean footwall rocks to the intrusion through
which the intrusion was emplaced. The intrusion is divided into an ultramafic
Lower Zone (LZ), a gabbroic Main Zone (MZ) and a gabbroic Upper Zone (UZ).
Chromite mineralization at Koitelainen was first discovered in 1977, and
two principal levels of chromite mineralization are now known. The Lower
Chromitite (LC) layers are found within a pyroxene cumulate, and are
continuous in drilling over a distance of about 20 km. Four to six layers each
over 0.3 m thick, with Cr2O3 from 10.6 to 32.2% have been discovered, the
thickest drill intersection being 2.9 metres. The basal contacts are generally
sharp; the hanging wall contact is gradational from massive chromitite to
chromite-disseminated pyroxenite. The Upper Chromitite (UC) layer is a
distinct interval up to 2.2 metres thick containing 21% Cr2O3, 0.4% V and 1.1
ppm PGE. The UC is strike continuous, and compositionally and mineralogically
homogeneous.
From 1973 to 1999, 131 holes for a total of 16,440 m were drilled at a
range of chromite, PGE and vanadium targets at Koitelainen. All drilling was
completed on behalf of GTK, and the core remains in storage in Finland.
Using 42 drill holes, GTK undertook a resource estimate for a vanadium
enriched ilmenomagnetite unit, discovered within the upper parts of the
Koitelainen layered intrusion. Using 17 drill holes and 4 drill holes, GTK
completed historic resource calculations on the Upper and Lower Chromitite
horizons respectively. The Upper Chromitite layer is 1.3 m thick, and is noted
to be very strike extensive with predictable grade and thickness. Historical
resource estimates are provided in Table 2 and are based upon a report
entitled "Koitelaisen malmitutkimukset vuosina 1979-1989" by Mutatanen, T.
1989 on behalf of the Geological Survey of Finland.
Table 2: Historical Resource Estimate for the Koitelainen Chromite
Project, Finland

Name                 Historical         Cr %  PGE ppm        V %              
Comments

Resources

(Million tonnes)
---                ---------------

Magnetite Gabbro(x)                  10.8   0.0            0.0     0.2     42 
drill holes used in resource
calculation.  4 strike
extensive mineralized units, up
to 40m thick.
-----------------                  ----  ---           ---    ---   
--------------------------------

Koitelainen UC(x)                    70.0  15.7           1.10     0.0     The 
distinct UC layer averages
1.3 m thick.  Resource to 500m
vertical depth. 17 drill holes
used in resource calculation.
---------------                    ---- ----          ----    ---   
-------------------------------

Koitelainen LC(x)                     2.0  14.4           1.38     0.4     The 
three to six LC layers
extends for at least 20 km
along strike.---------------                     --- ----          ----    
---   
---------------------------
(x)The data from these projects is historical in nature and was compiled
prior to the implementation of NI 43-101 reporting standards. Tasman has not
completed sufficient exploration to verify the estimates and we are not
treating them as NI 43-101 defined resources or reserves verified by a
qualified person; the historical estimate should not be relied upon.
Metallurgical testwork from Koitelainen has been poorly recorded and
appears limited to the Magnetite Gabbro. In 1976, it is reported that drill
core was used as feed materials for weak magnetic separation testwork.
Recovery of the magnetic material was approximately 90%, with a concentrate
grade of 50-50% Fe and 0.8-1.2% V.
Tasman's Qualified Person, Mr. Mark Saxon, President and Chief Executive
Officer of Tasman and a Fellow of the Australasian Institute of Mining and
Metallurgy and Member of the Australian Institute of Geoscientists, has
reviewed and verified the contents of this news release.
About Tasman Metals Ltd.
Tasman Metals Ltd is a Canadian mineral exploration and development
company focused on critical metals including Rare Earth Elements (REE's) and
tungsten (W) in Scandinavia. Tasman is listed on the TSX Venture Exchange
under the symbol "TSM" and the NYSE-MKT under the symbol "TAS". REE and
tungsten demand is increasing, due to the metals' unique properties that make
them essential for high technology and industry. Since over 95% of REE and 80%
of tungsten supply is sourced from China, the European Commission promotes
policy to develop domestic supply of critical metals to ensure the security of
industry. Tasman receives research funding from the European Commission.
Tasman's exploration portfolio is uniquely placed, with the capacity to
deliver strategic metals from politically stable, mining friendly
jurisdictions with developed infrastructure and skills. The Company's Norra
Karr and Olserum projects in Sweden are two of the most significant heavy REE
resources in the world, enriched in dysprosium, yttrium, terbium and
neodymium. The Company is now focused on the safe, sustainable and responsible
development of its Scandinavian mineral portfolio.
On behalf of the Board,
"Mark Saxon" Mark Sa

" BC-Tasman-New-Projects   12-17 3011
News release via Canada NewsWire, Toronto 416-863-9350

Attention Business Editors:
^Tasman expands critical metal portfolio with acquisition of two chromite
projects in Finland@

VANCOUVER, Dec. 17, 2014 /CNW/ - Tasman Metals Ltd. ("Tasman" or the
"Company") (TSXV:TSM) (Frankfurt:T61) NYSE-MKT: TAS). The Company is pleased
to announce it has entered into a letter of agreement dated December 15, 2014,
(the "Letter Agreement") with Kipu Metals Corp. (the "Vendor") under which the
Company will acquire (the "Acquisition") a 100% interest in a portfolio of
stratiform chromite projects in north-eastern Finland totaling 11,400 ha in
size (the "Chromite Portfolio") in exchange for the refund of costs incurred
to date of C$45,529 by the Vendor. There is no additional consideration for
the Acquisition. Closing of the Acquisition is subject to TSX Venture Exchange
approval.
Mr. Michael Hudson, a director of the Company, and Mr. Mark Saxon, the
Company's President, CEO and a director, are also directors and shareholders
of the Vendor. As a result, the Acquisition is a related party transaction as
such term is defined under Multilateral Instrument 61-101 Protection of
Minority Security Holders in Special Transactions ("MI 61-101"). The
Acquisition is exempt from the valuation and minority shareholder approval
requirements pursuant to exemptions available to the Company under MI 61-101
as the total consideration being received by Mr. Hudson and Mr. Saxon does not
exceed 25% of Tasman's market capitalization.
Under the Acquisition, Tasman has acquired 2 chromite projects (Akanvaara
and Koitelainen) that lie approximately 75 km apart in north-eastern Finland
(Figure 1). The projects are secured by 120 exploration claims and claim
applications totaling 11,400 hectares in size. North-eastern Finland has been
a very active exploration district, following the discovery of the large
Sakati Cu-Ni deposit by Anglo American, as announced in November 2011.
Highlights
<<

--  The Chromite Portfolio includes two projects with very extensive
previous drilling, metallurgical testing and historical resources. Both
are easily accessible by road;
--  Projects lie along the geological trend of the producing Kemi chromite
mine;
--  In addition to stratiform chromite, the projects have demonstrated
potential for both platinum group elements (PGE's) and vanadium (V);
--  Chromite and PGE's are both defined as critical raw materials by the
European Commission due to the highly concentrated current supply.
Europe is a major consumer of chromite for stainless steel;
>>
"Acquisition of this advanced chromite portfolio provides Tasman with the
opportunity to broaden our reach in the critical metals arena within Europe"
said Mark Saxon, Tasman's President and CEO. "While we maintain our focus on
the exciting developments underway at our Norra Karr heavy REE project in
Sweden, we remain active in the pursuit of undervalued assets that suit our
current portfolio and strategy."
Based on its economic importance to European industry and a high risk of
supply disruption, both chromium and PGE's are defined as "critical" raw
materials within recent European Commission (EC) publications (see:
http://ec.europa.eu/enterprise/policies/raw-materials/critical/index_en.htm),
in line with the balance of Tasman's existing project portfolio.
Chromium (Cr) is an essential industrial element due in particular to its
strengthening effect on steel alloys and its resistance to corrosion. Most
(>90%) of the current global chromite production is destined for use in the
metallurgical industry, in particular for stainless steel which requires a
minimum of 10.5% Cr by mass to impart favorable strength and anti-corrosion
properties. The remaining chromite is used in the aeronautics (for the
protection of aluminium aircraft bodies), foundry, chemical and refractory
sectors. Overall, demand growth for stainless steel and therefore chromium is
forecast in the range 4-5% per year to 2020.
European stainless steel production is highly significant, second only to
China in scale and accounting for some 20% of global output. Europe's share of
world chromium metal demand is equally significant, estimated by the European
Commission at 1.8 million tonnes (approximately 18.5% of global consumption).
At present, 80% of this demand is supplied from South Africa, whilst together
Kazakhstan and South Africa hold greater than 85% of the currently known
global resources (USGS).
The Kemi mine of Outokumpu in northern Finland is the EU's only chromium
supplier.
Project Descriptions
The Akanvaara and Koitelainen chromite projects are of a stratiform
intrusion-hosted style that together with similar deposits on the Kola
Peninsula of Russia constitute one of the largest known undeveloped resources
of chromite in the world. The Akanvaara and Koitelainen intrusions are part of
a group of Archean/early Proterozoic mafic layered intrusions within the
Fennoscandian Shield, which show cumulate igneous layering similar to other
large layered intrusions (Fiskenaesset, Burakovka, Bushveld), and host
deposits of chromite, vanadium, titanium, PGE's and gold.
Akanvaara
The Akanvaara layered intrusion is located 140 km northeast of the town
of Rovaniemi, with simple vehicle access through a network of gravel logging
and drill roads. The closest rail access lies some 40km to the south, and a
commercial airport in Kemijärvi being 62 km to the northeast. The Akanvaara
project consists of 53 granted claims for 4750 hectares.
The Akanvaara mafic intrusion has a known surface area of about 50 km2,
with a strike length along magmatic layering of 10 km and a total
stratigraphic thickness of approximately 3.1 km. The intrusion is
characterised by a persistently layered sequence of mafic and ultramafic
gabbro, pyroxenite, anorthosite and chromitite (chromium enriched) above a
lower chilled margin.
The Geological Survey of Finland (GTK) discovered and explored the
Akanvaara intrusion from 1990 to 1999, at which point the project was offered
for tender. Work completed by GTK included ground geophysical surveys
(magnetic, electromagnetic, gravity); diamond drilling of 118 holes for a
total of 18,136 m; and laboratory scale beneficiation testing on a number of
mineralization styles. Twenty three (23) chromitite layers were discovered
within the Akanvaara intrusion, each with different thickness, strike extent
and potential, across a total stratigraphic thickness of 1,100 m. Mineralized
lenses vary from centimetre to tens of metres in thickness.
Following drilling, GTK completed an historic resource calculation on the
3 most persistent chromitite lenses and a vanadium enriched gabbro. Cumulate
layers are noted to be very strike extensive with predictable grade and
thickness. Historical resource estimates are provided in Table 1 and are based
upon a report entitled "Akanvaaran intrusion kromi-, kromivanadiini,
vanadiini- ja platinametalli- kultaesiintynay" by Mutatanen, T. 1998 on behalf
of the Geological Survey of Finland.
Table 1: Historical Resource Estimate for the Akanvaara Chromite Project,
Finland

Name             Historical         Cr %  PGE ppm        V %              
Comments

Resources

(Million Tonnes)
---           ---------------

Akanvaara LC(x)                  27.0  15.7           0.60    0.00
------------                   ----  ----           ----    ----

Akanvaara UC(x)                  18.1  22.8           0.91    0.40     Reef 
thickness is 1 m, extent
7.9 km along strike, tonnage is
estimated down to 300 m
vertical depth where the
occurrence is open along dip.
-------------                  ---- ----          ----   ----   
--------------------------------

Akanvaara
ULC(x)                          10.0  15.3           0.00    0.00
---------                      ----  ----           ----    ----

Base of                        20.0   0.0           0.00    0.34     The 6 - 13 
metres thick basal
Magnetic                                                        part of the 
magnetite gabbro
unit, with V-rich magnetite.
20 million metric tons down to
100 metres (vertical) depth,
with 0.34 % V, 0.10 % Cu, and
2.5 g/t Ag.

Gabbro(x)

(x)The data from these projects is historical in nature and was compiled
prior to the implementation of NI 43-101 reporting standards. Tasman has not
completed sufficient exploration to verify the estimates and we are not
treating them as NI 43-101 defined resources or reserves verified by a
qualified person; the historical estimate should not be relied upon.
GTK commissioned the Technical Research Centre of Finland (VTT) for
preliminary mineral processing testing. Samples from the UC horizon were used
for flotation tests, which yielded a chromite concentrate with 33.8% Cr2O3
(chromium oxide) and 0.55% V with recovery of 92% and 88% respectively. The
chromite concentrate was shown to be relatively rich in iron, low in alumina
and practically devoid of magnesium. This suggests Akanvaara chromite-vanadium
concentrate may have potential as a metallurgical and chemical grade raw
material for production of ferrochrome, chrome-vanadium alloys and chrome
chemicals.
Flotation tests completed on the ULC material gave a higher-grade
concentrate of 38.3% Cr203, with the promising recovery of 86%.
A series of magnetic concentrates (approximately 10 - 12 weight % of the
feed) were produced from the Magnetic Gabbro Unit which contained 1.55 - 1.59
weight % V with up to 60% recovery of vanadium. A number of copper
(Cu)-sulphide concentrates were also produced by flotation of this Magnetic
Gabbro sample with a grade of 8 - 14% Cu, 1.4 g/t Au, 53 - 57 g/t Ag, 0.073
g/t Rh and 0.068 g/t Pt.
Subsequent to GTK's tender, the property was held by Finnish company
Outokumpu, who evaluated Akanvaara for PGE's and recognised that
magnetite-bearing gabbros in the uppermost section of the intrusion where
little GTK drilling was complete were highly anomalous in PGE's (to 1.26 g/t).
Outokumpu completed 5 drill holes and undertook extensive surface sampling.
Koitelainen
The Koitelainen layered intrusion is located 75 km northwest of
Akanvaara. The nearest railroad is found in Salla, 100 km to the south, and
the area is accessible by car through a network of gravel logging and drill
roads. The Koitelainen project consists of 67 claim applications for 6650
hectares and is totally contained within a Natura 2000 area.
The Koitelainen intrusion is a flat, oval-shaped anticline, 26 km x 29 km
in size with an estimated maximum thickness of around 3.2 km. The interior of
the anticline is made up of Archean footwall rocks to the intrusion through
which the intrusion was emplaced. The intrusion is divided into an ultramafic
Lower Zone (LZ), a gabbroic Main Zone (MZ) and a gabbroic Upper Zone (UZ).
Chromite mineralization at Koitelainen was first discovered in 1977, and
two principal levels of chromite mineralization are now known. The Lower
Chromitite (LC) layers are found within a pyroxene cumulate, and are
continuous in drilling over a distance of about 20 km. Four to six layers each
over 0.3 m thick, with Cr2O3 from 10.6 to 32.2% have been discovered, the
thickest drill intersection being 2.9 metres. The basal contacts are generally
sharp; the hanging wall contact is gradational from massive chromitite to
chromite-disseminated pyroxenite. The Upper Chromitite (UC) layer is a
distinct interval up to 2.2 metres thick containing 21% Cr2O3, 0.4% V and 1.1
ppm PGE. The UC is strike continuous, and compositionally and mineralogically
homogeneous.
From 1973 to 1999, 131 holes for a total of 16,440 m were drilled at a
range of chromite, PGE and vanadium targets at Koitelainen. All drilling was
completed on behalf of GTK, and the core remains in storage in Finland.
Using 42 drill holes, GTK undertook a resource estimate for a vanadium
enriched ilmenomagnetite unit, discovered within the upper parts of the
Koitelainen layered intrusion. Using 17 drill holes and 4 drill holes, GTK
completed historic resource calculations on the Upper and Lower Chromitite
horizons respectively. The Upper Chromitite layer is 1.3 m thick, and is noted
to be very strike extensive with predictable grade and thickness. Historical
resource estimates are provided in Table 2 and are based upon a report
entitled "Koitelaisen malmitutkimukset vuosina 1979-1989" by Mutatanen, T.
1989 on behalf of the Geological Survey of Finland.
Table 2: Historical Resource Estimate for the Koitelainen Chromite
Project, Finland

Name                 Historical         Cr %  PGE ppm        V %              
Comments

Resources

(Million tonnes)
---                ---------------

Magnetite Gabbro(x)                  10.8   0.0            0.0     0.2     42 
drill holes used in resource
calculation.  4 strike
extensive mineralized units, up
to 40m thick.
-----------------                  ----  ---           ---    ---   
--------------------------------

Koitelainen UC(x)                    70.0  15.7           1.10     0.0     The 
distinct UC layer averages
1.3 m thick.  Resource to 500m
vertical depth. 17 drill holes
used in resource calculation.
---------------                    ---- ----          ----    ---   
-------------------------------

Koitelainen LC(x)                     2.0  14.4           1.38     0.4     The 
three to six LC layers
extends for at least 20 km
along strike.---------------                     --- ----          ----    
---   
---------------------------
(x)The data from these projects is historical in nature and was compiled
prior to the implementation of NI 43-101 reporting standards. Tasman has not
completed sufficient exploration to verify the estimates and we are not
treating them as NI 43-101 defined resources or reserves verified by a
qualified person; the historical estimate should not be relied upon.
Metallurgical testwork from Koitelainen has been poorly recorded and
appears limited to the Magnetite Gabbro. In 1976, it is reported that drill
core was used as feed materials for weak magnetic separation testwork.
Recovery of the magnetic material was approximately 90%, with a concentrate
grade of 50-50% Fe and 0.8-1.2% V.
Tasman's Qualified Person, Mr. Mark Saxon, President and Chief Executive
Officer of Tasman and a Fellow of the Australasian Institute of Mining and
Metallurgy and Member of the Australian Institute of Geoscientists, has
reviewed and verified the contents of this news release.
About Tasman Metals Ltd.
Tasman Metals Ltd is a Canadian mineral exploration and development
company focused on critical metals including Rare Earth Elements (REE's) and
tungsten (W) in Scandinavia. Tasman is listed on the TSX Venture Exchange
under the symbol "TSM" and the NYSE-MKT under the symbol "TAS". REE and
tungsten demand is increasing, due to the metals' unique properties that make
them essential for high technology and industry. Since over 95% of REE and 80%
of tungsten supply is sourced from China, the European Commission promotes
policy to develop domestic supply of critical metals to ensure the security of
industry. Tasman receives research funding from the European Commission.
Tasman's exploration portfolio is uniquely placed, with the capacity to
deliver strategic metals from politically stable, mining friendly
jurisdictions with developed infrastructure and skills. The Company's Norra
Karr and Olserum projects in Sweden are two of the most significant heavy REE
resources in the world, enriched in dysprosium, yttrium, terbium and
neodymium. The Company is now focused on the safe, sustainable and responsible
development of its Scandinavian mineral portfolio.
On behalf of the Board,
"Mark Saxon" Mark Saxon, President & CEO
The TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the policies of the TSX Venture Exchange), the NYSE - MKT
nor the Frankfurt Stock Exchange accepts responsibility for the adequacy or
accuracy of this news release.
Cautionary Note to U.S. Investors Concerning Mineral Resources and
Reserves. In this news release, the definition of "mineral resources" is that
used by the Canadian securities administrators and conforms to the definition
utilized by CIM in the "CIM Standards on Mineral Resources and Reserves -
Definitions and Guidelines" adopted on August 20, 2000 and amended December
11, 2005.
The standards employed in estimating the mineral resources referenced in
this news release differ significantly from the requirements of the United
States Securities and Exchange Commission (the "SEC") and the resource
information reported may not be comparable to similar information reported by
United States companies. The term "resources" does not equate to "reserves"
and normally may not be included in documents filed with the SEC. "Resources"
are sometimes referred to as "mineralization" or "mineral deposits." While the
terms "mineral resource", "measured mineral resource", "indicated mineral
resource" and "inferred mineral resource" are recognized and required by
Canadian regulations, they are not defined terms under standards in the United
States and normally are not permitted to be used in reports and registration
statements filed with the SEC. The terms "mineral reserve," "proven mineral
reserve" and "probable mineral reserve" are Canadian mining terms as defined
in accordance with National Instrument 43-101 - Standards of Disclosure for
Mineral Projects ("NI 43-101") and the CIM - CIM Definition Standards on
Mineral Resources and Mineral Reserves, adopted by the CIM Council, as may be
amended from time to time by the CIM. These definitions differ from the
definitions in the United States Securities and Exchange Commission Industry
Guide 7 ("SEC Industry Guide 7") under the Securities Act of 1933. Under
Canadian rules, estimates of inferred mineral resources may not form the basis
of feasibility or prefeasibility studies, except in rare cases. Disclosure of
"contained ounces" in a resource is permitted disclosure under Canadian
regulations; however, the SEC normally only permits issuers to report
mineralization that does not constitute "reserves" by SEC standards as in
place tonnage and grade without reference to unit measures.
The estimation of measured, indicated and inferred mineral resources
involves greater uncertainty as to their existence and economic feasibility
than the estimation of proven and probable reserves. U.S. investors are
cautioned (i) not to assume that measured or indicated resources will be
converted into reserves and (ii) not to assume that estimates of inferred
mineral resources exist, are economically or legally minable, or will be
upgraded into measured or indicated mineral resources. It cannot be assumed
that the Company will identify any viable mineral resources on its properties
or that any mineral reserves, if any, can be recovered profitably, if at all.
As such, information contained in this news release and the documents
incorporated by reference herein concerning descriptions of mineralization and
resources under Canadian standards may not be comparable to similar
information made public by United States companies in SEC filings.
Cautionary Statements. Certain statements found in this release may
constitute forward-looking statements as defined in the U.S. Private
Securities Litigation Reform Act of 1995. Forward-looking statements reflect
the speaker's current views with respect to future events and financial
performance and include any statement that does not directly relate to a
current or historical fact. Such statements reflect the current risks,
uncertainties and assumptions related to certain factors including, without
limitations, competitive factors, general economic conditions, customer
relations, uncertainties related to the availability and costs of financing,
the interpretation and actual results of the Norra Karr preliminary
feasibility study, unexpected geological conditions, success of future
development initiatives, imprecision in resource estimates, ability to obtain
necessary permits and approvals, relationships with vendors and strategic
partners, the interest rate environment, governmental regulation and
supervision, seasonality, technological change, changes in industry practices,
changes in world metal markets, changes in equity markets, environmental and
safety risks, and one-time events. Should any one or more of these risks or
uncertainties materialize, or should any underlying assumptions prove
incorrect, actual results may vary materially from those described herein.
Forward-looking statements cannot be guaranteed and actual results may vary
materially due to the uncertainties and risks, known and unknown, associated
with such statements. Shareholders and other readers should not place undue
reliance on "forward-looking statements," as such statements speak only as of
the date of this release.
SOURCE Tasman Metals Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/December2014/17/c7871.html

-0-                           12/17/2014
/For further information: Investor Information: www.tasmanmetals.com,
1305 - 1090 West Georgia St., Vancouver, BC, V6E 3V7, Company Contact: Jim
Powell, V.P. - Corporate Development, + 1 (647) 478 8952, Email:
jpowell(at)tasmanmetals.com; or Mariana Bermudez, +1 (604) 685 9316, Email:
info(at)tasmanmetals.com/
/Web Site: www.tasmanmetals.com /
(TAS TSM.)

CO:  Tasman Metals Ltd.
ST:  British Columbia
IN:  MNG
SU:  TNM

-30-