Source	MARKET NEWS
Date	12/17/2014
Time	08:45:55 AM

Company	 Fjordland Exploration Inc.
Title	Fjordland and Commander Amend Agreement on South





    CDNX Symbol: FEX











Press Release	





Fjordland and Commander Amend Agreement on South Voisey's Bay NickelProject 
--->@NEWS RELEASE
FJORDLAND EXPLORATION INC. ("FEX-V")
COMMANDER RESOURCES LTD. ("CMD-V")
- Fjordland and Commander Amend Agreement on South Voisey's Bay
- Nickel Project

Fjordland Exploration Inc. and Commander Resources Ltd. have
amended the terms of a Memorandum of Understanding reported in a news
release on October 2, 2014 to enable Fjordland to earn up to a 75%
interest in the South Voisey's Bay ('sVB") nickel-copper-cobalt project
(originally a 70% interest) by increasing the Initial Work Commitment
by Fjordland from $250,000 to $350,000 and increasing the Initial
Option interest from 10% to 15%.  The funds provided by Fjordland are
being used for the implementation and interpretation of a geophysical
survey on Commander's SVB property in central Labrador to define and
delineate specific drill targets in an area of known conductors.

Work commenced on a 22.25 line-kilometre UTEM survey on November
10, 2014 and has now been completed.  The work program successfully
identified and delineated two strong conductors on the property. Field
work consisted of line-cutting, ground magnetic surveying and the EM
survey.  The survey was undertaken during winter weather conditions
including low cloud, and high winds, which necessitated grounding
aircraft for 6 days.

Based on preliminary field results, the two strong geophysical
conductors (Sandy and Zang), partially indicated by previous surveys in
the area, are now fully delineated. The strongest portion of the Sandy
conductor appears as an elongate ovoid approximately 400 metres by 500
metres in diameter. The eastern portion of the Sandy conductor extends
to within 100 metres of the Worm Gabbro dyke which is known to host
nickel sulphides.

Detailed surveying of the linear Zang conductor indicates that it
is approximately 200 to 300 metres long and comprised of two
sub-parallel conductive zones, located more than 100 metres apart.
Plotting of these sub-conductors indicates that one is situated along
the basal contact of the 500 metre thick, 10 kilometre long Worm
Gabbro. The second Zang sub-conductor is situated closer to the middle
of the Worm Gabbro and also extends parallel to the base. Nickel
deposits are often situated at, or near, the basal contact of such
gabbro bodies.

Final interpretation and modelling of sources for these EM
conductors will be done after complete processing of field results by
the survey contractor.

Bernard H. Kahlert P.Eng., a Director of Commander, is a Qualified
Person as defined by National Instrument 43-101 and has reviewed and
approved the technical disclosure of this news release.

On behalf of the Board of Directors of  On behalf of the Board of
Directors of
FJORDLAND EXPLORATION INC.    COMMANDER RESOURCES LTD.
"Richard C. Atkinson"         "Eric W. Norton"
Richard C. Atkinson           Eric W. Norton
President & CEO               President & CEO
Website: www.fjordlandex.com  Website: www.commanderresources.com
Email: info@fjordlandex.com   Email: info@commanderresources.com

Neither the TSX Venture Exchange nor its Regulation Services (as
that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

______________________________________
_______________________________________________
TSX Venture closing price for FEX-V
Date: 2014/12/11
Closing Price: 0.02
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1435000024TS11435001488-08434820141217