Source	Marketwire
Date	12/01/2014
Time	05:00:15 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Results from 2014 Expansion Drilling at the Bluelite 
Satellite Deposit, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

December 1, 2014

Scorpio Gold Reports Results from 2014 Expansion Drilling at the Bluelite 
Satellite Deposit, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Dec. 1, 2014) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports 
additional results from the 2014 expansion drilling program on the Bluelite 
deposit at its70% owned Mineral Ridge project, located in Nevada.

As reported in the Company's July 21, 2014 news release, an updated Life of 
Mine Plan ("LOM") for the Mineral Ridge Operation encompasses the currently 
producing Drinkwater and Mary LC pits and five adjacent satellite deposits, 
including the Bluelite deposit. The cut-off date for the LOM was March 31, 
2014. Continued drilling since the March 31, 2014 cut-off date is designed to 
potentially upgrade and increase the reported mineral reserve and resource 
estimate and potentially extend life of mine.

Drilling on the Bluelite deposit continues to meet with success, returning 
significant intercepts both within and extending outside of the pit shell 
outline modelled in the updated LOM. Management fully expects these results 
will lead to an upgrade and expansion of the mineral resources currently 
defined for the Bluelite deposit.

Highlights from this latest phase of drilling on the Bluelite deposit include:

/T/

--  MR141036: 1.47 grams per tonne ("g/t") gold over 10.67 meters
--  MR141037: 0.93 g/t gold over 16.76 meters
--  MR141040: 1.93 g/t gold over 7.62 meters
--  MR141067: 0.99 g/t gold over 13.72 meters
--  MR141117: 1.87 g/t gold over 9.14 meters
--  MR141120: 6.37 g/t gold over 9.14 meters

/T/

A drill hole location map is available at: DH Plan

Table 1. Bluelite Deposit - Significant Drill Results

/T/

----------------------------------------------------------------------------
Hole       Azm   Dip  From    To  Width    From      To  Width   Gold   Gold
No.      (deg) (deg)  (ft)  (ft)   (ft)     (m)     (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR14831    225   -75    50    60     10   15.24   18.29   3.05  0.017   0.57
----------------------------------------------------------------------------
360   370     10  109.73  112.78   3.05  0.019   0.64
----------------------------------------------------------------------------
440   480     40  134.11  146.30  12.19  0.018   0.61
----------------------------------------------------------------------------
MR14832    225   -55   180   185      5   54.86   56.39   1.52  0.011   0.38
----------------------------------------------------------------------------
340   345      5  103.63  105.16   1.52  0.015   0.51
----------------------------------------------------------------------------
370   375      5  112.78  114.30   1.52  0.015   0.51
----------------------------------------------------------------------------
520   535     15  158.50  163.07   4.57  0.014   0.48
----------------------------------------------------------------------------
570   580     10  173.74  176.78   3.05  0.020   0.67
----------------------------------------------------------------------------
655   665     10  199.64  202.69   3.05  0.023   0.77
----------------------------------------------------------------------------
685   715     30  208.79  217.93   9.14  0.040   1.38
----------------------------------------------------------------------------
MR14845      0   -90   265   295     30   80.77   89.92   9.14  0.023   0.80
----------------------------------------------------------------------------
315   325     10   96.01   99.06   3.05  0.030   1.01
----------------------------------------------------------------------------
340   350     10  103.63  106.68   3.05  0.025   0.86
----------------------------------------------------------------------------
385   390      5  117.35  118.87   1.52  0.065   2.23
----------------------------------------------------------------------------
425   435     10  129.54  132.59   3.05  0.023   0.79
----------------------------------------------------------------------------
MR14971      0   -90                 No Significant Results
----------------------------------------------------------------------------
MR141036   225   -75   200   235     35   60.96   71.63  10.67  0.043   1.47
----------------------------------------------------------------------------
285   290      5   86.87   88.39   1.52  0.010   0.34
----------------------------------------------------------------------------
295   300      5   89.92   91.44   1.52  0.010   0.34
----------------------------------------------------------------------------
305   310      5   92.96   94.49   1.52  0.010   0.34
----------------------------------------------------------------------------
385   400     15  117.35  121.92   4.57  0.039   1.34
----------------------------------------------------------------------------
450   485     35  137.16  147.83  10.67  0.017   0.60
----------------------------------------------------------------------------
MR141037   225   -55   210   230     20   64.01   70.10   6.10  0.017   0.58
----------------------------------------------------------------------------
285   290      5   86.87   88.39   1.52  0.011   0.36
----------------------------------------------------------------------------
390   395      5  118.87  120.40   1.52  0.019   0.65
----------------------------------------------------------------------------
210   230     20   64.01   70.10   6.10  0.017   0.58
----------------------------------------------------------------------------
425   480     55  129.54  146.30  16.76  0.027   0.93
----------------------------------------------------------------------------
MR141040     0   -90    30    35      5    9.14   10.67   1.52  0.015   0.51
----------------------------------------------------------------------------
160   165      5   48.77   50.29   1.52  0.013   0.45
----------------------------------------------------------------------------
290   295      5   88.39   89.92   1.52  0.018   0.62
----------------------------------------------------------------------------
320   330     10   97.54  100.58   3.05  0.055   1.87
----------------------------------------------------------------------------
345   360     15  105.16  109.73   4.57  0.022   0.75
----------------------------------------------------------------------------
380   405     25  115.82  123.44   7.62  0.056   1.93
----------------------------------------------------------------------------
MR141067     0   -90   120   125      5   36.58   38.10   1.52  0.057   1.94
----------------------------------------------------------------------------
215   220      5   65.53   67.06   1.52  0.010   0.34
----------------------------------------------------------------------------
240   245      5   73.15   74.68   1.52  0.013   0.45
----------------------------------------------------------------------------
275   285     10   83.82   86.87   3.05  0.027   0.91
----------------------------------------------------------------------------
300   345     45   91.44  105.16  13.72  0.029   0.99
----------------------------------------------------------------------------
400   405      5  121.92  123.44   1.52  0.024   0.82
----------------------------------------------------------------------------
445   450      5  135.64  137.16   1.52  0.024   0.83
----------------------------------------------------------------------------
500   505      5  152.40  153.92   1.52  0.019   0.63
----------------------------------------------------------------------------
525   530      5  160.02  161.54   1.52  0.085   2.91
----------------------------------------------------------------------------
635   640      5  193.55  195.07   1.52  0.019   0.64
----------------------------------------------------------------------------
MR141111     0   -90    55    60      5   16.76   18.29   1.52  0.042   1.44
----------------------------------------------------------------------------
325   330      5   99.06  100.58   1.52  0.015   0.51
----------------------------------------------------------------------------
MR141113     0   -90    50    60     10   15.24   18.29   3.05  0.033   1.12
----------------------------------------------------------------------------
80    85      5   24.38   25.91   1.52  0.020   0.67
----------------------------------------------------------------------------
200   205      5   60.96   62.48   1.52  0.010   0.35
----------------------------------------------------------------------------
MR141114     0   -90    50    60     10   15.24   18.29   3.05  0.087   2.98
----------------------------------------------------------------------------
MR141115     0   -90   430   445     15  131.06  135.64   4.57  0.025   0.86
----------------------------------------------------------------------------
MR141116     0   -90   205   230     25   62.48   70.10   7.62  0.036   1.25
----------------------------------------------------------------------------
245   260     15   74.68   79.25   4.57  0.018   0.63
----------------------------------------------------------------------------
290   295      5   88.39   89.92   1.52  0.051   1.75
----------------------------------------------------------------------------
440   450     10  134.11  137.16   3.05  0.066   2.26
----------------------------------------------------------------------------
470   475      5  143.26  144.78   1.52  0.084   2.86
----------------------------------------------------------------------------
MR141117     0   -90    10    15      5    3.05    4.57   1.52  0.026   0.89
----------------------------------------------------------------------------
240   270     30   73.15   82.30   9.14  0.055   1.87
----------------------------------------------------------------------------
incl.                  240   245      5   73.15   74.68   1.52  0.246   8.43
----------------------------------------------------------------------------
405   410      5  123.44  124.97   1.52  0.042   1.44
----------------------------------------------------------------------------
MR141118     0   -90    50    55      5   15.24   16.76   1.52  0.030   1.03
----------------------------------------------------------------------------
105   110      5   32.00   33.53   1.52  0.063   2.16
----------------------------------------------------------------------------
165   170      5   50.29   51.82   1.52  0.011   0.38
----------------------------------------------------------------------------
MR141120     0   -90   120   150     30   36.58   45.72   9.14  0.186   6.37
----------------------------------------------------------------------------
165   170      5   50.29   51.82   1.52  0.030   1.03
----------------------------------------------------------------------------
185   190      5   56.39   57.91   1.52  0.014   0.48
----------------------------------------------------------------------------

/T/

All holes presented in Table 1 were completed by reverse circulation (RC) 
drilling. True width is estimated at 90-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at: MR QAQC.

Upcoming Conference:

Scorpio Gold's President, Steve Roebuck, will be attending the Mines and Money 
London 2014 Conference held at the Business Design Centre, London, UK, on 
December 2-4, 2014. Mr. Roebuck looks forward to meeting shareholders and 
interested parties at booth F12. Further information is available at: Mines and 
Money London 2014.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Waterton Global Value L.P. (30%), and Scorpio Gold is currently entitled to 
receive 80% of cash flow generated. Mineral Ridge is a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property and processing facility in Manhattan, 
Nevada. The Company is assessing its exploration plans for the Goldwedge 
property as well as the potential for toll milling at the Goldwedge plant, 
which is currently permitted for 400 tons per day.

Scorpio Gold's President, Steve Roebuck, PGeo, is a Qualified Person as defined 
by National Instrument 43-101 and has reviewed and approved the content of this 
release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.
The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including potential further exploration or development 
of the Bluelite deposit, any potential expansion of the current pit shell 
outline thereof, and any potential increase in the mineral reserve and resource 
estimate in respect thereof. Such forward-looking statements involve known and 
unknown risks, uncertainties and other factors that could cause actual events 
or results to differ materially from estimated or anticipated events or results 
implied or expressed in such forward-looking statements, including risks 
involved in mineral exploration and development programs and those risk factors 
outlined in the Company's Management Discussion and Analysis as filed on SEDAR. 
Any forward-looking statement speaks only as of the date on which it is made 
and, except as may be required by applicable securities laws, the Company 
disclaims any intent or obligation to update any forward-looking statement, 
whether as a result of new information, future events or results or otherwise. 
Forward-looking statements are not guarantees of future performance and 
accordingly undue reliance should not be put on such statements due to the 
inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Steve Roebuck
President
(819) 825-7618
sroebuck@scorpiogold.com
www.scorpiogold.com

or

Investor Relations:
Jim Macdonald, Torrey Hills Capital
(858) 456-7300
jm@sdthc.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=509289134