Source	CANADA NEWSWIRE
Date	12/01/2014
Time	07:38:11 AM

Company	 Visible Gold Mines Inc.
Title	Visible Gold Mines 4,000 kilometers airborne survey 100% completed on
its new project in the James Bay region, Québec





    CDNX Symbol: VGD











Press Release	




" BC-VGMinesAirborneSurvey   12-01 0685
News release via CNW Telbec, Montreal 514-878-2520 -ME-

Attention Business Editors:
^Visible Gold Mines 4,000 kilometers airborne survey 100% completed on
its new project in the James Bay region, Québec@

ROUYN-NORANDA, QC, Dec. 1, 2014 /CNW Telbec/ - Visible Gold Mines Inc.
(TSXV: VGD) (Frankfurt: 3V4) is pleased to announce the completion of its
previously-announced of detailed helicopter-borne magnetic (MAG) and
time-domain electromagnetic (TDEM) Survey on its 167 EXTENSION project in the
Plan Nord region in the province of Québec. The survey began on November 13th
and was completed recently.
The MAG-TDEM geophysical survey consisted of a data acquisition program
for a total of 3,955 linear kilometres on two different survey block at 100
metre line spacing, see map at
http://visiblegoldmines.com/images/Ext167geophysics.jpg. Joël Dubé, Eng.,
consultant specialized in geophysics, will generate anomaly picking and
interpretation maps. Those products will be key in providing prospective
guidance on potential diamond drilling targets.
Most of the high grade boulders we have found are highly magnetics and
conductives. With the preliminary data we have received to date, we are able
to define in many areas the correlation between conductivity, high magnetism,
and high grade boulders' location. We are very anxious to bring the drilrig on
site. "We believe this is a very promising project" stated Martin Dallaire,
President and Chief Executive Officer of Visible Gold Mines.
Qualified Persons
Mr. Martin Dallaire, P.Eng., President and Chief Executive Officer of
Visible Gold Mines, is the qualified person on the 167 EXTENSION exploration
project information presented in this press release under National Instrument
43-101 Standards of Disclosure for Mineral Projects, is responsible for the
technical contents of this press release and has approved the disclosure of
the technical information contained herein. The data verification was
conducted by Jeannot Theberge, P.Geo. under the supervision of Martin
Dallaire, P.Eng.
Quality Control
Visible Gold Mines has implemented and adheres to a strict Quality
Assurance/Quality Control for the current exploration program. It includes one
mineralized gold standard, one duplicate and one blank for each batch of
samples. Analyses are performed by ALS Chemex, Val-d'Or, Québec, or
Techni-Lab, Ste-Germaine-Boulé, Québec, both accredited laboratories.
About Plan Nord 167 EXTENSION project
In 2011, when the Québec Government launched its ambitious Plan Nord
project to develop Québec's north, including the construction of a 243
kilometre-long all-season road that links Stornoway's Renard Diamond project
to the provincial highway network, Visible Gold Mines' management decided to
acquire the available mining rights along each side of the new road in order
to have access to new outcrops and strippings generated by the road
construction. Visible Gold Mines acquired claims by acquisition and staking
and so the 167 EXTENSION project was born. Out of the 140 kilometres of new
road available for mining exploration (the first 102 kilometres are a planned
provincial park), Visible Gold Mines owns mining claims on more than 110
kilometres of that new road. The road has been completed since October 1st,
2014 at a construction cost of approximately $350 million dollars. The 167
EXTENSION project is 100% owned by Visible Gold Mines and represents with
recent acquisitions approximately 54,734 hectares or 547 square kilometres.
About Visible Gold Mines
Visible Gold Mines Inc. is a dynamic corporation aggressively searching
for the next important gold deposit in the province of Québec, an area
consistently ranked as one of the world's best jurisdictions for mining and
exploration.
About Prospectair Geosurveys Inc.
Prospectair is a company specialized in airborne geophysical surveys
since 2002. It is owned and operated by Alain Tremblay, an experienced pilot,
technician and operator specialized in data acquisition. Prospectair uses the
latest high quality Heliborne TDEM technology, with a total weight of only 175
kg to make it easier to closely follow the topography. Since 2002 Prospectair
has completed thousands of kilometers of magnetic, radiometric and TDEM
airborne surveys internationally using its proprietary fleet of R44 Ravens II
and EC120B helicopters.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of the release.

SOURCE Visible Gold Mines Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/December2014/01/c2168.html

-0-                           12/01/2014
/For further information: Martin Dallaire, President and Chief Executive
Officer, Telephone: 819-762-0609, Fax: 819-762-0097, E-mail:
mdallaire(at)visiblegoldmines.com, Website: www.visiblegoldmines.com/
/Web Site: www.visiblegoldmines.com /
(VGD. 3V4)

CO:  Visible Gold Mines Inc.
ST:  Quebec
IN:  MNG MIN
SU:  ECO

-30-