Source	Filing Services Canada
Date	12/02/2014
Time	05:30:10 AM

Company	 GOLDEN PREDATOR MINING CORP.
Title	Metallurgical Tests Indicate 93.5% to 98.3% Overall Gold Recovery at 
Golden Predators 3 Aces Project, Yukon





    CDNX Symbol: GPY











Press Release	




SOURCE: Filing Services Canada
Date: 12/02/2014
Time: 08:30:00

Company: GOLDEN PREDATOR MINING CORP
Title:Metallurgical Tests Indicate 93.5% to 98.3% Overall Gold Recovery at 
Golden Predators 3 Aces Project, Yukon (GPY - TSXV) 
TSXV SYMBOL: GPY


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Golden Predator Mining Corp
TSXV SYMBOL: GPY
Tuesday, December 02, 2014 - 8:30 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/metallurgical-tests-indicate-935-983-overall-
gold-recovery-golden-predators-3-aces

Metallurgical Tests Indicate 93.5% to 98.3% Overall Gold Recovery at Golden 
Predators 3 Aces Project, Yukon


Hayden, Idaho (FSCwire) - Golden Predator Mining Corp. (TSX.V: GPY) (the 
Company) announces metallurgical testing has been completed on 3 large volume 
samples collected from the Sleeping Giant zone on the 3 Aces property in the 
Yukon Territory. Overall gold recoveries for the three samples were reported at 
98.3%, 97.9% and 93.5%. The three samples were processed in their entirety in 
bulk fashion by gravity and gravity tail leaching. The final results of the 
metallurgical testing on the three samples showed that very high overall gold 
recoveries can be achieved by simple initial gravity methods followed by final 
CN leaching of the tails.



Metallurgical Testing 

The final bulk processing of the three large samples was conducted by grinding 
the entire sample in batches of 10 kg to a target grind size of 80% passing 200 
microns. After grinding, the whole sample was fed through a Knelson 
concentrator for gold recovery. The results show the gravity gold recoveries at 
this grind size ranged from 74.6% to 88.5%. A split of the gravity tails from 
each sample was then ground to 80% passing 75 microns and subjected to cyanide 
leaching. The results showed the leach kinetics are very fast within the first 
24 hours and gold extraction from the tails ranged from 74.3% to 90.2% for the 
samples. Table 1 shows the gravity, CN leach and overall total gold recoveries 
for the samples.



Table 1: Gravity & CN Leach Total Gold Recoveries

To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/metallurgical-tests-indicate-935-983-overall-
gold-recovery-golden-predators-3-aces








The final test results also provided evidence that the use of a screen metallic 
assay method with an approximate 2,000 gram pulp (80% passing 150 mesh) is an 
appropriate method to obtain reliable gold grades from exploration and 
development samples. Table 2 shows the assay head grade versus the sample sizes 
and methods.



Table 2: Gold Grade by Test Method

To view this table, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/metallurgical-tests-indicate-935-983-overall-
gold-recovery-golden-predators-3-aces










3 Aces Project, Yukon 

The 3 Aces property consists of 1,108 contiguous quartz claims (23,000 
hectares) located in southeast Yukon. The property is located along the Nahanni 
Range Road which accesses the operational Cantung Mine located 40 kilometres to 
the north. 



The 3 Aces property contains a number of quartz veins and vein zones that cut 
Cambrian aged limestone, shale, quartz grits and pebble chert conglomerates of 
the Hyland Group. Previous sampling and exploration by Golden Predator 
(formerly Northern Tiger) has outlined extensive gold-in-soil anomalies over 
nine square kilometres, including numerous high grade gold showings. (see 
property map below).



The 3 Aces property is located in the traditional territory of the Kaska 
Nation. In January 2013, Golden Predator signed an Exploration Agreement with 
the Kaska Nation, as represented by the Ross River Dena Council and the Liard 
First Nation, with respect to activities within their traditional territories.



The technical content of this news release has been reviewed and approved by 
Michael Maslowski BSc, CPG, a consultant to the company and a Qualified Person 
as defined by National Instrument 43[[18]]101.





To view this image, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/metallurgical-tests-indicate-935-983-overall-
gold-recovery-golden-predators-3-aces









To view this image, please either click on the link below, or copy and paste 
the link into your browser:
http://www.fscwire.com/newsrelease/metallurgical-tests-indicate-935-983-overall-
gold-recovery-golden-predators-3-aces







Golden Predator Mining Corp.

Golden Predators corporate mandate is to advance the Brewery Creek project 
towards production through a joint venture arrangement. The Brewery Creek mine 
operated from 1996 to 2002, before closing due to low gold prices. Mining 
licenses and permits are in place for continued exploration along with a Socio 
Economic Accord with the Tr'ondek Hwech'in. The Company holds additional 
projects with current resources and/or new discovery potential, including the 
high-grade 3 Aces and Grew Creek gold projects and the Marg and Clear Lake 
polymetallic massive sulfide deposits.



For additional information:

Janet Lee-Sheriff, Chief Executive Officer

(208) 635-5415

info@goldenpredator.com (mailto:info@goldenpredator.com)

www.goldenpredator.com (http://www.goldenpredator.com)



1)NI 43-101 Technical Report on Resources, Brewery Creek Project, Yukon 
Territory, Canada by Donald Hulse, P.E., SME-RM, M. Claiborne Newton, III, 
Ph.D., SME-RM et al. Dated January 2014 filed on SEDAR.



Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in policies of the TSX Venture Exchange) accepts responsibility for 
the adequacy or accuracy of this release. 



No stock exchange, securities commission or other regulatory authority has 
approved or disapproved the information contained herein. This press release 
contains projections and forward-looking information that involve various risks 
and uncertainties regarding future events. Such forward-looking information can 
include without limitation statements based on current expectations involving a 
number of risks and uncertainties and are not guarantees of future performance. 
There are numerous risks and uncertainties that could cause actual results and 
the Companys plans and objectives to differ materially from those expressed in 
the forward-looking information. Actual results and future events could differ 
materially from those anticipated in such information. These and all subsequent 
written and oral forward-looking information are based on estimates and 
opinions of management on the dates they are made and are expressly qualified 
in their entirety by this notice. Except as required by law, the Company 
assumes no obligation to update forward-looking information should 
circumstances or management's estimates or opinions change.


To view this press release as a PDF file, click onto the following link:
http://www.fscwire.com/sites/default/files/news_release_pdf/goldenpred12022014.p
df
Source: Golden Predator Mining Corp (TSX Venture:GPY) 
http://www.goldenpredator.com



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2014 Filing Services Canada Inc.