Source	MARKET NEWS
Date	12/02/2014
Time	05:59:30 AM

Company	 Golden Predator Mining Corp.
Title	Metallurgical Tests Indicate 93.5% to 98.3% Over





    CDNX Symbol: GPY











Press Release	





Metallurgical Tests Indicate 93.5% to 98.3% Overall Gold Recovery atGolden 
Predator's 3 Aces Project, Yukon --->@NEWS RELEASE
GOLDEN PREDATOR MINING CORP ("GPY-V")
- Metallurgical Tests Indicate 93.5% to 98.3% Overall Gold
- Recovery at Golden Predator's 3 Aces Project, Yukon

Golden Predator Mining Corp. (the "Company") announces
metallurgical testing has been completed on 3 large volume samples
collected from the Sleeping Giant zone on the 3 Aces property in the
Yukon Territory. Overall gold recoveries for the three samples were
reported at 98.3%, 97.9% and 93.5%.  The three samples were processed
in their entirety in bulk fashion by gravity and gravity tail leaching.
The final results of the metallurgical testing on the three samples
showed that very high overall gold recoveries can be achieved by simple
initial gravity methods followed by final CN leaching of the tails.

Metallurgical Testing

The final bulk processing of the three large samples was conducted
by grinding the entire sample in batches of 10 kg to a target grind
size of 80% passing 200 microns.  After grinding, the whole sample was
fed through a Knelson concentrator for gold recovery.  The results show
the gravity gold recoveries at this grind size ranged from 74.6% to
88.5%.  A split of the gravity tails from each sample was then ground
to 80% passing 75 microns and subjected to cyanide leaching.  The
results showed the leach kinetics are very fast within the first 24
hours and gold extraction from the tails ranged from 74.3% to 90.2% for
the samples. Table 1 shows the gravity, CN leach and overall total gold
recoveries for the samples.

//st
Table 1: Gravity & CN Leach Total Gold Recoveries

Sample     Au Rec., %  Gravity  Gr-tail CN  Combined Gr &
GR-1        CN-1     Gr-tail CN
BS-3A13-03       Conc.    78.9        90.2           97.9
Tail     21.1        9.80            2.1
GR-2        CN-2
BS-3A13-02       Conc.    88.5        85.4           98.3
Tail     11.5        14.6            1.7
GR-3        GR-3
BS-3A13-01       Conc.    74.6        74.3           93.5
Tail     25.4        25.7            6.5
//et

The final test results also provided evidence that the use of a
screen metallic assay method with an approximate 2,000 gram pulp (80%
passing 150 mesh) is an appropriate method to obtain reliable gold
grades from exploration and development samples.  Table 2 shows the
assay head grade versus the sample sizes and methods.

//st
Table 2: Gold Grade by Test Method

Test Method   Gold Head Grade grams per tonne
BS-3A13-01   BS-3A13-02   BS-3A13-03
Screen Metallic
(2,000 gram
sub-sample)         1.6         10.5        215.5

GRG Testing
(20kg sub-sample)   1.79         10.5        212.5

Bulk Gravity
Processing         1.85         13.2        260.4

Sample weight
for bulk process  800kg        730kg        530kg
//et

3 Aces Project, Yukon

The 3 Aces property consists of 1,108 contiguous quartz claims
(23,000 hectares) located in southeast Yukon. The property is located
along the Nahanni Range Road which accesses the operational Cantung
Mine located 40 kilometres to the north.

The 3 Aces property contains a number of quartz veins and vein
zones that cut Cambrian aged limestone, shale, quartz grits and pebble
chert conglomerates of the Hyland Group.  Previous sampling and
exploration by Golden Predator (formerly Northern Tiger) has outlined
extensive gold-in-soil anomalies over nine square kilometres, including
numerous high grade gold showings.  (see property map  below).

The 3 Aces property is located in the traditional territory of the
Kaska Nation.  In January 2013, Golden Predator signed an Exploration
Agreement with the Kaska Nation, as represented by the Ross River Dena
Council and the Liard First Nation, with respect to activities within
their traditional territories.

The technical content of this news release has been reviewed and
approved by Michael Maslowski BSc, CPG, a consultant to the company and
a Qualified Person as defined by National Instrument 43-101.

Golden Predator Mining Corp.

Golden Predator's corporate mandate is to advance the Brewery
Creek project towards production through a joint venture arrangement.
The Brewery Creek mine operated from 1996 to 2002, before closing due
to low gold prices. Mining licenses and permits are in place for
continued exploration along with a Socio Economic Accord with the
Tr'ondek Hwech'in. The Company holds additional projects with current
resources and/or new discovery potential, including the high-grade 3
Aces and Grew Creek gold projects and the Marg and Clear Lake
polymetallic massive sulfide deposits.

For additional information:

Janet Lee-Sheriff, Chief Executive Officer

(208) 635-5415

info@goldenpredator.com

www.goldenpredator.com

1)NI 43-101 Technical Report on Resources, Brewery Creek Project,
Yukon Territory, Canada by Donald Hulse, P.E., SME-RM, M. Claiborne
Newton, III, Ph.D., SME-RM et al. Dated January 2014 filed on SEDAR.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

No stock exchange, securities commission or other regulatory
authority has approved or disapproved the information contained herein.
This press release contains projections and forward-looking information
that involve various risks and uncertainties regarding future events.
Such forward-looking information can include without limitation
statements based on current expectations involving a number of risks
and uncertainties and are not guarantees of future performance. There
are numerous risks and uncertainties that could cause actual results
and the Company's plans and objectives to differ materially from those
expressed in the forward-looking information. Actual results and future
events could differ materially from those anticipated in such
information. These and all subsequent written and oral forward-looking
information are based on estimates and opinions of management on the
dates they are made and are expressly qualified in their entirety by
this notice. Except as required by law, the Company assumes no
obligation to update forward-looking information should circumstances
or management's estimates or opinions change.

Source: Golden Predator Mining Corp























TSX Venture closing price for GPY-V
Date: 2014/11/28
Closing Price: 0.08

TEL: (208) 635-5415       Janet Lee-Sheriff,
info@goldenpredator.com   Chief Executive Officer
www.goldenpredator.com    Golden Predator Mining Corp
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1433500009TS11433500907-05575820141202