Source	MARKET NEWS
Date	12/03/2014
Time	10:48:07 AM

Company	 Westhaven Ventures Inc.
Title	Drills 
153.7 Metres of 0.18% Nickel and 0.010% C





    CDNX Symbol: WHN











Press Release	





WESTHAVEN VENTURES INC. ("WHN-V")
- Drills 153.7 Metres of 0.18% Nickel and 0.010% Cobalt at Ben

Westhaven Ventures Inc. is pleased to provide assay results from a
recently completed drill program at its 15,322 hectare BEN property,
located approximately 50 km north of Williams Lake, B.C. The drill
program consisted of 9 holes, totaling 930 metres of diamond drilling,
as a follow-up to previous drilling reported in the news release dated
October 7, 2014.
Highlights from the program include:
Hole BN14-16 intersected 19.7 metres of 0.28% Nickel (Ni) and
0.012% Cobalt (Co) starting
from bedrock surface
Hole BN14-19 intersected 153.7 metres of 0.18% Ni and 0.010% Co
starting from bedrock
surface
Hole BN14-22 intersected 57.7 metres of 0.21% Ni and 0.011% Co
Hole BN14-23 intersected 106.6 metres of 0.18% Ni and 0.010% Co
This most recent phase of widely spaced drilling, in several
separate areas, strengthens management's belief that large scale
tonnage potential exists on this easily accessible and well situated
property. A drill location map can be found on Westhaven's website at
http://westhavenventures.com/_resources/maps/airborne_magnetics.png

All drill holes targeted strong magnetic anomalies delineated by a
recently completed 122 line kilometre ground magnetic survey. Drill
holes BN14-15 and BN14-16 were designed to test the near surface
projection of the Skelton zone along strike from hole BN13-03 that
intersected 70.6 metres containing 0.31% nickel and 0.012% cobalt.
Holes BN14-17 and BN14-18 tested the eastern extension of the magnetic
anomaly 300 metres to the east.
BN14-19, located approximately 6 kilometres to the south of the
Skelton zone, tested the Southern lobe, a magnetic target 800 x 850
metres in area. Drilling intersected highly serpentinized ultramafic
rocks from bedrock surface to 186 metres depth containing 153 metres
grading 0.18% Ni and 0.010% Co that remains open in all directions.
BN14-20 and BN14-21 tested the Ring zone, a large 1,500 metre diameter
serpentine ring dyke located 2.2 kilometres northeast from BN14-19.
BN14-22 and BN14-23 tested the Northern lobe, a 4 kilometre long
northwest trending magnetic anomaly located 700 metres north of
BN14-21.
Every drill hole intersected shallow dipping bodies of
magnetite-rich serpentinized ultramafics containing nickel-sulphide
mineralization. A summary of notable intersections follows:
//st
From                          Ni %     Ni %
Hole               To (m)   Interval              (In       Co %    Ni S %
(m)                        (Total)  Sulphide)
BN14-15       9.0     23.4       14.4      0.27     0.23     0.012      85%
BN14-16       10.0    29.7       19.7      0.28     0.21     0.012      74%
BN14-17       45.0    54.5        9.5      0.19     0.12     0.010      65%
BN14-18       41.1    69.9       28.8      0.20     0.14     0.010      70%
BN14-19       33.0   186.7      153.7      0.18     0.09     0.010      52%
Incl       33.0   106.0       73.0      0.19     0.15     0.011      79%
BN14-20        9.6    60.2       50.6      0.18     0.15     0.010      82%
BN14-21       16.2    44.5       28.3      0.18     0.15     0.010      82%
and        72.2    99.7       27.5      0.17     0.13     0.011      76%
BN14-22       32.6    47.9       15.3      0.20     0.16     0.010      79%
and        63.1   120.8       57.7      0.21     0.17     0.011      80%
BN14-23       41.8   148.4      106.6      0.18     0.13     0.010      77%
//et
Note: Ni % (Total) denotes analyses derived from multi-element
Aqua Regia ICP-MS analyses. Ni %( In Sulphide) denotes analyses based
on the selective decomposition of nickel sulphide derived from ammonium
citrate and hydrogen peroxide leach analyses. Ni S % denotes percentage
of nickel present in sulphides.
Ben Property Overview
Since October 2013, 23 drill holes have been completed in 3
campaigns totaling 2,610 metres. Drilling has indicated that there are
large areas throughout the property that are underlain by nickeliferous
serpentine with high nickel sulphide content and large thicknesses.
Prior to this work there were no known nickel occurrences in this area
and as such this is a completely new discovery in an area of very
limited rock exposure and good proximity to infrastructure. Westhaven
has started preliminary level metallurgy testing to help determine the
mineralogical, comminution and metallurgical properties of the various
mineralized zones. The Company's focus is to continue exploring the
nickel-cobalt mineralization and determine the size potential of the
numerous mineralized areas.
On behalf of the Board of Directors
WESTHAVEN VENTURES INC.
"Gareth Thomas"
Gareth Thomas, Director
About Westhaven Ventures Inc.
Westhaven Ventures Inc. is a Canadian based exploration company
focused on the acquisition and exploration of prospective resource
properties. Westhaven is focused on advancing its Shovelnose gold and
BEN projects in British Columbia. Westhaven trades on the TSX Venture
Exchange under the ticker symbol WHN. For further information, please
call 604-681-5558 or visit Westhaven's website at
www.westhavenventures.com
Qualified Person Statement
L. John Peters, P.Geo., who is a Qualified Person within the
context of National Instrument 43-101 has read and takes responsibility
for this release.
Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

TSX Venture closing price for WHN-V
Date: 2014/12/02
Closing Price: 0.09

TEL:  604-681-5558      Westhaven Ventures Inc.
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1433600026TS11433601811-10452720141203