Source	CANADA NEWSWIRE
Date	12/03/2014
Time	11:21:17 AM

Company	 Westhaven Ventures Inc.
Title	Westhaven drills 153.7 metres of 0.18% nickel and 0.010% cobalt at BEN





    CDNX Symbol: WHN











Press Release	




" BC-Westhaven-drilling   12-03 0761
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Westhaven drills 153.7 metres of 0.18% nickel and 0.010% cobalt at BEN@

VANCOUVER, Dec. 3, 2014 /CNW/ - Westhaven Ventures Inc. (TSX-V:WHN) is
pleased to provide assay results from a recently completed drill program at
its 15,322 hectare BEN property, located approximately 50 km north of Williams
Lake, B.C. The drill program consisted of 9 holes, totaling 930 metres of
diamond drilling, as a follow-up to previous drilling reported in the news
release dated October 7, 2014.
Highlights from the program include:
<<

--  Hole BN14-16 intersected 19.7 metres of 0.28% Nickel (Ni) and 0.012%
Cobalt (Co) starting from bedrock surface
--  Hole BN14-19 intersected 153.7 metres of 0.18% Ni and 0.010% Co starting
from bedrock surface
--  Hole BN14-22 intersected 57.7 metres of 0.21% Ni and 0.011% Co
--  Hole BN14-23 intersected 106.6 metres of 0.18% Ni and 0.010% Co
>>
This most recent phase of widely spaced drilling, in several separate
areas, strengthens management's belief that large scale tonnage potential
exists on this easily accessible and well situated property. A drill location
map can be found on Westhaven's website at
http://westhavenventures.com/_resources/maps/airborne_magnetics.png
All drill holes targeted strong magnetic anomalies delineated by a
recently completed 122 line kilometre ground magnetic survey. Drill holes
BN14-15 and BN14-16 were designed to test the near surface projection of the
Skelton zone along strike from hole BN13-03 that intersected 70.6 metres
containing 0.31% nickel and 0.012% cobalt. Holes BN14-17 and BN14-18 tested
the eastern extension of the magnetic anomaly 300 metres to the east.
BN14-19, located approximately 6 kilometres to the south of the Skelton
zone, tested the Southern lobe, a magnetic target 800 x 850 metres in area.
Drilling intersected highly serpentinized ultramafic rocks from bedrock
surface to 186 metres depth containing 153 metres grading 0.18% Ni and 0.010%
Co that remains open in all directions. BN14-20 and BN14-21 tested the Ring
zone, a large 1,500 metre diameter serpentine ring dyke located 2.2 kilometres
northeast from BN14-19. BN14-22 and BN14-23 tested the Northern lobe, a 4
kilometre long northwest trending magnetic anomaly located 700 metres north of
BN14-21.
Every drill hole intersected shallow dipping bodies of magnetite-rich
serpentinized ultramafics containing nickel-sulphide mineralization. A summary
of notable intersections follows:
Hole   From       To       Interval               Ni %                  Ni 
%      Co %       Ni S %
(m)       (m)
(Total)         (In Sulphide)
---                                             ------          ------------

BN14-15       9.0      23.4           14.4            0.27                    
0.23      0.012        85%
-------       ---      ----           ----            ----                    
----      -----        ---

BN14-16      10.0      29.7           19.7            0.28                    
0.21      0.012        74%
-------      ----      ----           ----            ----                    
----      -----        ---

BN14-17      45.0      54.5            9.5            0.19                    
0.12      0.010        65%
-------      ----      ----            ---            ----                    
----      -----        ---

BN14-18      41.1      69.9           28.8            0.20                    
0.14      0.010        70%
-------      ----      ----           ----            ----                    
----      -----        ---

BN14-19      33.0     186.7          153.7            0.18                    
0.09      0.010        52%
-------      ----     -----          -----            ----                    
----      -----        ---

Incl        33.0     106.0           73.0            0.19                    
0.15      0.011        79%
----        ----     -----           ----            ----                    
----      -----        ---

BN14-20       9.6      60.2           50.6            0.18                    
0.15      0.010        82%
-------       ---      ----           ----            ----                    
----      -----        ---

BN14-21      16.2      44.5           28.3            0.18                    
0.15      0.010        82%
-------      ----      ----           ----            ----                    
----      -----        ---

and        72.2      99.7           27.5            0.17                    
0.13      0.011        76%
---        ----      ----           ----            ----                    
----      -----        ---

BN14-22      32.6      47.9           15.3            0.20                    
0.16      0.010        79%
-------      ----      ----           ----            ----                    
----      -----        ---

and        63.1     120.8           57.7            0.21                    
0.17      0.011        80%
---        ----     -----           ----            ----                    
----      -----        ---

BN14-23      41.8     148.4          106.6            0.18                    
0.13      0.010        77%
-------      ----     -----          -----            ----                    
----      -----        ---

Note: Ni % (Total) denotes analyses derived from multi-element Aqua Regia
ICP-MS analyses. Ni %( In Sulphide) denotes analyses based on the selective
decomposition of nickel sulphide derived from ammonium citrate and hydrogen
peroxide leach analyses. Ni S % denotes percentage of nickel present in
sulphides.
Ben Property Overview
Since October 2013, 23 drill holes have been completed in 3 campaigns
totaling 2,610 metres. Drilling has indicated that there are large areas
throughout the property that are underlain by nickeliferous serpentine with
high nickel sulphide content and large thicknesses. Prior to this work there
were no known nickel occurrences in this area and as such this is a completely
new discovery in an area of very limited rock exposure and good proximity to
infrastructure.
Westhaven has started preliminary level metallurgy testing to help
determine the mineralogical, comminution and metallurgical properties of the
various mineralized zones. The Company's focus is to continue exploring the
nickel-cobalt mineralization and determine the size potential of the numerous
mineralized areas.
On behalf of the Board of DirectorsWESTHAVEN VENTURES INC."Gareth Thomas"
Gareth Thomas, Director
About Westhaven Ventures Inc.
Westhaven Ventures Inc. is a Canadian based exploration company focused
on the acquisition and exploration of prospective resource properties.
Westhaven is focused on advancing its Shovelnose gold and BEN projects in
British Columbia. Westhaven trades on the TSX Venture Exchange under the
ticker symbol WHN.
Qualified Person Statement
L. John Peters, P.Geo., who is a Qualified Person within the context of
National Instrument 43-101 has read and takes responsibility for this release.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
SOURCE Westhaven Ventures Inc.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/December2014/03/c6812.html

-0-                           12/03/2014
/For further information: please call 604-681-5558 or visit Westhaven's
website at www.westhavenventures.com/
/Web Site: www.westhavenventures.com /
(WHN.)

CO:  Westhaven Ventures Inc.
ST:  British Columbia
IN:  MNG
SU:

-30-