Source	Marketwire
Date	12/15/2014
Time	04:00:22 AM

Company	 SAVARY GOLD CORP.
Title	Savary Gold's and Sarama's Field Program Discovers 24 New Zones of Gold 
Mineralization and Identifies Two New Gold Trends on the Karankasso JV Project, 
Burkina Faso





    CDNX Symbol: SCA











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Savary Gold Corp.

TSX VENTURE SYMBOL: SCA

December 15, 2014

Savary Gold's and Sarama's Field Program Discovers 24 New Zones of Gold 
Mineralization and Identifies Two New Gold Trends on the Karankasso JV Project, 
Burkina Faso

Five to Eight Kilometres Wide by 45 Kilometres Long Prospective Corridor for 
Gold Mineralization

TORONTO, ONTARIO--(Marketwired - Dec. 15, 2014) - Savary Gold Corp. (TSX 
VENTURE:SCA) ("Savary") and Sarama Resources Ltd. (TSX VENTURE:SWA) ("Sarama") 
announce new grab sample assay results from a recently completed field program 
on the Karankasso JV Project in southwestern Burkina Faso (see figure below). 
The 750 square kilometre Karankasso property is a 65/35 joint venture with 
Savary as operator. A summary of significant results are as follows:

/T/

--  2.11 g/t gold - New zone, Karan Trend - Highway quartz porphyry zone,
not drilled
--  2.20 g/t gold - New zone, Kuere West zone - not drilled
--  5.50 g/t gold - Kien West zone southern extension, not drilled
--  3.29 g/t gold - Kien West zone southern extension, not drilled
--  50.75 g/t gold - New zone southwest of Kueredougou West, not drilled
--  3.74 g/t gold - New zone, Kueredougou West southern extension, not
drilled
--  1.63 g/t gold - New zone west of Kueredougou West, not drilled
--  2.86 g/t gold - New zone, Kuere West trend, not drilled
--  24.90 g/t gold - New zone, Koure Trend, new zone, not drilled
--  28.25 g/t gold - New zone, Koure Trend, new zone, not drilled
--  5.4 g/t gold - New zone, 400 m west of Koure trend, not drilled
--  4.54 g/t gold - New zone, 250 m west of Koure trend, not drilled
--  12.48 g/t gold - New zone, 450 m west of Koure trend, not drilled
--  23.4 g/t Au - Serakoro 1 West zone, drill follow-up required
--  11.55 g/t gold - New zone, Karan trend, not drilled
--  13.5 g/t gold - New zone, Sera W trend, not drilled

/T/

Highlights of this work include the following target areas:

/T/

--  Recognition of numerous, new gold occurrences over a wider than
previously realized area, ranging from five to eight kilometres wide,
and that likely extends for the length of the concession package, a
distance of approximately 45 km. In addition to the dominant trends of
gold mineralization, numerous gold-bearing sub-structures have been
indentified between the larger scale structures.
--  Discovery of several new zones of felsic intrusion hosted gold
mineralization along the Sera W and Karan mineralization trends proximal
to the western margin of the Hounde Belt.
--  one zone, that intersects the highway, returning grab samples of
quartz veined felsic intrusion that returned 2.11 and 1.92 g/t Au
from two historic mining areas 430 metres by up to 40 metres wide
and 470 metres by up to 50 metres wide, respectively.
--  Discovery of the Koure Trend mineralization - samples from different
mineralized artisanal mining zones along a 3.8 km strike returned values
of 24.8 g/t Au, 28.25 g/t Au and 1.25 g/t Au. This trend has never been
drill tested and contains the visually strongest gold-bearing
mineralization on the property.
--  Discovery of several untested artisanal mining zones, with widths
ranging up to 35 metres wide, located 900 metres south of the recently
reported Kueredougou West zone.
--  Identification of likely structural controls for gold mineralization in
the Serakoro 1 West zone where previous drilling returned 3.7 g/t Au
over 27.0 metres and high gold values in an altered felsic intrusion
returned up to 23.4 g/t Au from outside the drill tested area.
--  Discovery of a new zone of intensive artisanal mining in the northwest
corner of the Serakoro 1 property that returned an assay of 13.5 g/t Au.
--  Discovery of the untested, up to 35 metres wide, Kuere West trend that
can be traced for 8.2 kilometres via a series of artisanal mining areas.
Samples from this trend returned up to 2.86 g/t Au.

/T/

"Once again the Karankasso project results exceeded our expectations" stated 
Don Dudek, President and CEO of Savary "Recently completed field work has not 
only demonstrated additional mineralization along known gold mineralized 
trends, but has also resulted in the discovery of several new multi-kilometre 
long gold mineralization trends which host 24 new gold zones that have returned 
values of greater than 1.0 g/t gold as well as several large areas of gold 
mineralization, that individually display size, grade and alteration 
characteristics which could result in a material discovery."

From November 18th to 30th, Savary and Sarama completed a reconnaissance field 
program covering the 750 square kilometre Karankasso Project area. The goal of 
the field program was to improve the understanding of the controls on the 
existing zones, visit and evaluate newly discovered artisanal mining sites and 
follow-up on untested gold-in-soil anomalies. During this program 128 rock 
samples were collected and information for 396 data sites was recorded. This 
work resulted in the discovery of 24 new gold zones returning greater than 1.0 
g/t Au and three new gold-bearing trends, Koure, Keure West and Karan trends. 
Assay details and general site descriptions are presented at the end of the 
release. Note that most rock samples were collected from artisanal waste rock 
piles as, in most cases, sampling directly from outcrop was not possible.

To view the Figure associated with this release, please visit the following 
link: http://media3.marketwire.com/docs/SAVARY1.jpg.

QP comments

In addition to the mapping and prospecting program, a detailed (50 metre by 25 
metre sample points) soil sampling program was carried out over an 800 metre by 
800 metre portion of the Serakoro 1 West zone where previous drilling returned 
up to 3.72 g/t Au over 27.0 metres. The goal of the program is to better 
define, what is expected to be, a locally high grade, conjugate vein, gold 
zones hosted by a fractured felsic intrusion.

An additional observation, specifically regarding the Serakoro 1 concession, is 
that outside of the main Sera W and Keure Trends, there is abundant laterite 
cover which masks the bedrock and thus reduces Savary's ability to trace gold 
zones along strike. This could be a reason why there is less artisanal activity 
on the Serakoro 1 property as compared to the Mandiasso and Diosso concessions 
to the north. An augur sampling or rotary air blast (RAB) program is being 
considered to aid in tracing the gold zones south into the Serakoro 1 
concession.

Once the soil sample results have been received, all new and existing drill 
targets will be prioritized and a follow-up exploration drill program will be 
developed for presentation to Savary's Board of Directors and Sarama's 
management team for review and approval.

QA/QC

All samples were collected in plastic bags, which were stapled shut with a 
sample tag before inserted into a larger poly sample bag for shipment to SGS 
Laboratories in Ouagadougou. Sample blanks and assay standards were inserted 
every ten prospecting samples resulting in 11% of the assayed samples being 
reference/blank control samples. Upon reception of the assay results, the 
results for the reference and blank control samples were compared against 
expected results. All standards and blank control samples returned results 
within expected ranges. Don Dudek, P. Geo. has reviewed and supervised the 
QA/QC program.

About Savary Gold

Savary Gold is a Canadian exploration company, along with partner, Sarama 
Resources Limited, are focused on exploring the Hounde South and Serakoro 1 
Gold Properties in Burkina Faso. The properties are in the Birimian age Hounde 
Greenstone Belt, which hosts Semafo's Mana mine and additional gold deposits 
that are presently subject to extensive exploration efforts (including 
Endeavour Mining's Hounde Project, Roxgold Yaramoko Project and Sarama's South 
Hounde Project, which is adjacent to Savary Gold's property). For additional 
information please visit our website at www.savarygold.com and follow us on 
Facebook, Linked-In and Twitter: @SavaryGold.

Don Dudek, P.Geo., President and CEO of the Company and a qualified person 
under National Instrument 43-101, has reviewed and approved the scientific and 
technical information in this press release.

SAVARY GOLD CORP.

On behalf of the Board

Don Dudek, President & Chief Executive Officer

Cautionary Notes

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These statements 
include statements regarding the field program, the discovery of new gold 
minerlaization, the identification of new gold trends, historical drill 
intercepts and the results of historical data being indicative of the potential 
of the property. These statements are based on current expectations and 
assumptions that are subject to risks and uncertainties. Actual results could 
differ materially because of factors discussed in the management discussion and 
analysis section of our interim and most recent annual financial statements or 
other reports and filings with the TSX Venture Exchange and applicable Canadian 
securities regulations. We do not assume any obligation to update any 
forward-looking statements, except as required by applicable laws. Fall 2014 
Karankasso Prospecting Program Sampling results


/T/

----------------------------------------------------------------------------
Au g/t Au      Sample #        Easting       Northing                   Zone
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
less than                                               artisanal zone, not
0.01              9301         403588        1205328           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
1.92               9302         403592        1205345           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.04               9303         403609        1205389           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
less than                                               artisanal zone, not
0.01              9304         403590        1205375           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 470 m by up
to 50 m wide
artisanal zone, not
2.11               9305         403362        1205498           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.2                9306         403575        1205149           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.03               9307         403574        1205209           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.04               9308         409532        1206855           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.39               9309         409700        1206955           drill tested
----------------------------------------------------------------------------
0.03               9311         408699        1207015
----------------------------------------------------------------------------
Kien East northeast
extension, 1.2 km by
up to 35 m wide
artisanal mining
1.94               9312         408059        1205123     trend, not drilled
----------------------------------------------------------------------------
Kien East northeast
extension, not
0.89               9313         408059        1205123                drilled
----------------------------------------------------------------------------
Kien West, nearby
drill hole not
drilled far enoughto intersect 225 m
by 5-10 m wide
artisanal mining
4.25               9314         406194        1203708                   zone
----------------------------------------------------------------------------
Kien West, nearby
drill hole just
missed 150 m by up
to 30 m wide
artisanal mining
1.16               9315         406253        1203685                   zone
----------------------------------------------------------------------------
Kien West, 200 m by
1-3 m wide artisanal
mining zone, not
0.56               9316         405966        1202430                drilled
----------------------------------------------------------------------------
0.02               9317         406659        1202282
----------------------------------------------------------------------------
Kien West trend, 350
m by 1-3 m wide
series of artisanal
0.25               9318         405736        1201853      pits, not drilled
----------------------------------------------------------------------------
Kien West trend, 350
m by 1-3 m wide
series of artisanal
5.55               9319         405741        1201853      pits, not drilled
----------------------------------------------------------------------------
Kien West trend, 350
m by 1-3 m wide
series of artisanal
0.47               9321         405815        1201924      pits, not drilled
----------------------------------------------------------------------------
Kien West trend, 50
m by 3-5 m wide
artisanal zone, not
0.12               9322         405605        1201304                 tested
----------------------------------------------------------------------------
Kien West trend, 50
m by 3-5 m wide
artisanal zone, not
3.29               9323         405621        1201318                 tested
----------------------------------------------------------------------------
Kuere Trend, Diosso
South zone parallel
zone, 270 m by 1-3 m
pitting area, not
0.24               9324         401296        1189746                drilled
----------------------------------------------------------------------------
Kuere Trend, Diosso
South zone parallel
zone, 270 m by 1-3 m
pitting area, not
0.58               9325         401217        1189614                drilled
----------------------------------------------------------------------------
Kuere Trend, Diosso
South zone parallel
trend, 15 m by 1-3 m
wide pitting area,
nearby RC hole
returned 1.37 g/t Au
over 4.0 m and 1.2
0.77               9326         401087        1189411      g/t Au over 2.0 m
----------------------------------------------------------------------------
New, 150 m west of
Koure trend, small
isolated artisanal
0.14               9327         401333        1188750                    pit
----------------------------------------------------------------------------
New, Koure trend,
200 m by 2-5 m wide
zone of artisanal
0.03               9328         401423        1188788    mining, not drilled
----------------------------------------------------------------------------
New, Koure trend,
200 m by 2-5 m wide
zone of artisanal
0.03               9329         401447        1188877    mining, not drilled
----------------------------------------------------------------------------
New, Koure trend,
200 m by 2-5 m wide
zone of artisanal
0.91               9331         401487        1188963    mining, not drilled
----------------------------------------------------------------------------
New, isolated
artisanal site, 150
m long by up to 30 m
wide, sericite-
fuchite alteration,
400 m east of Diosso
South zone, RAB
hole, 60 m north
returned 2.08 g/t Au
0.41               9332         401286        1189236             over 2.0 m
----------------------------------------------------------------------------
New, isolated
artisanal site, 150
m long by up to 30 m
wide, sericite-
fuchite alteration,
400 m east of Diosso
South zone, RAB
hole, 60 m north
returned 2.08 g/t Au
0.43               9333         401277        1189213             over 2.0 m
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
1.12               9334         400304        1189422       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
1.6                9335         400309        1189511       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
2.205              9336         400403        1189670       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.06               9337         400485        1189858       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.64               9338         400250        1189285       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.47               9339         400154        1189084       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.28               9341         400142        1188901       zone, not tested
----------------------------------------------------------------------------
New, Isolated
artisanal site, 35 m
long by 1-3 m wide,
may be related to
0.06               9342         400112        1188691       Kuere West Trend
----------------------------------------------------------------------------
0.09               9343         399468        1187424
----------------------------------------------------------------------------
Kuere Cross, new
zone on northeast
trending cross-
0.73               9344         404970        1197808              structure
----------------------------------------------------------------------------
0.07               9345         404971        1197809
----------------------------------------------------------------------------
0.15               9346         404870        1197916
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
0.05               9347         402407        1193130             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
6.17               9348         402388        1193109             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone ofartisanal mining,
Southern extension,
1.2                9349         402406        1193199             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
0.9                9351         402432        1193277             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
0.12               9352         402501        1193531             not tested
----------------------------------------------------------------------------
0.09               9353         402589        1193392
----------------------------------------------------------------------------
0.03               9354         402637        1193407
----------------------------------------------------------------------------
New zone, 350 m East
of Kuere trend, 40 m
by 15 m wide
artisanal mining
50.75              9355         402811        1193154       zone, not tested
----------------------------------------------------------------------------
New, Kuere west
trend, 65 m by 1-3 m
artisanal mining
area, RAB hole 110 m
north interested
1.45 g/t Au ober 4.0
3.74               9356         402325        1193907                      m
----------------------------------------------------------------------------
New, Kuere West
trend, 100 m by 1-3
m wide artisanal
0.41               9357         402547        1194474                   zone
----------------------------------------------------------------------------
New zone west of
Kuere West trend,
150 mby 40 m wide
artisanal pitting
1.63               9358         401821        1194739      area, not drilled
----------------------------------------------------------------------------
0.05               9360         402566        1194862
----------------------------------------------------------------------------
0.21               9361         401415        1193866
----------------------------------------------------------------------------
Keure West trend,
170 m by 1-2 m wide


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Savary Gold Corp.

TSX VENTURE SYMBOL: SCA

December 15, 2014

Savary Gold's and Sarama's Field Program Discovers 24 New Zones of Gold 
Mineralization and Identifies Two New Gold Trends on the Karankasso JV Project, 
Burkina Faso

Five to Eight Kilometres Wide by 45 Kilometres Long Prospective Corridor for 
Gold Mineralization

TORONTO, ONTARIO--(Marketwired - Dec. 15, 2014) - Savary Gold Corp. (TSX 
VENTURE:SCA) ("Savary") and Sarama Resources Ltd. (TSX VENTURE:SWA) ("Sarama") 
announce new grab sample assay results from a recently completed field program 
on the Karankasso JV Project in southwestern Burkina Faso (see figure below). 
The 750 square kilometre Karankasso property is a 65/35 joint venture with 
Savary as operator. A summary of significant results are as follows:

/T/

--  2.11 g/t gold - New zone, Karan Trend - Highway quartz porphyry zone,
not drilled
--  2.20 g/t gold - New zone, Kuere West zone - not drilled
--  5.50 g/t gold - Kien West zone southern extension, not drilled
--  3.29 g/t gold - Kien West zone southern extension, not drilled
--  50.75 g/t gold - New zone southwest of Kueredougou West, not drilled
--  3.74 g/t gold - New zone, Kueredougou West southern extension, not
drilled
--  1.63 g/t gold - New zone west of Kueredougou West, not drilled
--  2.86 g/t gold - New zone, Kuere West trend, not drilled
--  24.90 g/t gold - New zone, Koure Trend, new zone, not drilled
--  28.25 g/t gold - New zone, Koure Trend, new zone, not drilled
--  5.4 g/t gold - New zone, 400 m west of Koure trend, not drilled
--  4.54 g/t gold - New zone, 250 m west of Koure trend, not drilled
--  12.48 g/t gold - New zone, 450 m west of Koure trend, not drilled
--  23.4 g/t Au - Serakoro 1 West zone, drill follow-up required
--  11.55 g/t gold - New zone, Karan trend, not drilled
--  13.5 g/t gold - New zone, Sera W trend, not drilled

/T/

Highlights of this work include the following target areas:

/T/

--  Recognition of numerous, new gold occurrences over a wider than
previously realized area, ranging from five to eight kilometres wide,
and that likely extends for the length of the concession package, a
distance of approximately 45 km. In addition to the dominant trends of
gold mineralization, numerous gold-bearing sub-structures have been
indentified between the larger scale structures.
--  Discovery of several new zones of felsic intrusion hosted gold
mineralization along the Sera W and Karan mineralization trends proximal
to the western margin of the Hounde Belt.
--  one zone, that intersects the highway, returning grab samples of
quartz veined felsic intrusion that returned 2.11 and 1.92 g/t Au
from two historic mining areas 430 metres by up to 40 metres wide
and 470 metres by up to 50 metres wide, respectively.
--  Discovery of the Koure Trend mineralization - samples from different
mineralized artisanal mining zones along a 3.8 km strike returned values
of 24.8 g/t Au, 28.25 g/t Au and 1.25 g/t Au. This trend has never been
drill tested and contains the visually strongest gold-bearing
mineralization on the property.
--  Discovery of several untested artisanal mining zones, with widths
ranging up to 35 metres wide, located 900 metres south of the recently
reported Kueredougou West zone.
--  Identification of likely structural controls for gold mineralization in
the Serakoro 1 West zone where previous drilling returned 3.7 g/t Au
over 27.0 metres and high gold values in an altered felsic intrusion
returned up to 23.4 g/t Au from outside the drill tested area.
--  Discovery of a new zone of intensive artisanal mining in the northwest
corner of the Serakoro 1 property that returned an assay of 13.5 g/t Au.
--  Discovery of the untested, up to 35 metres wide, Kuere West trend that
can be traced for 8.2 kilometres via a series of artisanal mining areas.
Samples from this trend returned up to 2.86 g/t Au.

/T/

"Once again the Karankasso project results exceeded our expectations" stated 
Don Dudek, President and CEO of Savary "Recently completed field work has not 
only demonstrated additional mineralization along known gold mineralized 
trends, but has also resulted in the discovery of several new multi-kilometre 
long gold mineralization trends which host 24 new gold zones that have returned 
values of greater than 1.0 g/t gold as well as several large areas of gold 
mineralization, that individually display size, grade and alteration 
characteristics which could result in a material discovery."

From November 18th to 30th, Savary and Sarama completed a reconnaissance field 
program covering the 750 square kilometre Karankasso Project area. The goal of 
the field program was to improve the understanding of the controls on the 
existing zones, visit and evaluate newly discovered artisanal mining sites and 
follow-up on untested gold-in-soil anomalies. During this program 128 rock 
samples were collected and information for 396 data sites was recorded. This 
work resulted in the discovery of 24 new gold zones returning greater than 1.0 
g/t Au and three new gold-bearing trends, Koure, Keure West and Karan trends. 
Assay details and general site descriptions are presented at the end of the 
release. Note that most rock samples were collected from artisanal waste rock 
piles as, in most cases, sampling directly from outcrop was not possible.

To view the Figure associated with this release, please visit the following 
link: http://media3.marketwire.com/docs/SAVARY1.jpg.

QP comments

In addition to the mapping and prospecting program, a detailed (50 metre by 25 
metre sample points) soil sampling program was carried out over an 800 metre by 
800 metre portion of the Serakoro 1 West zone where previous drilling returned 
up to 3.72 g/t Au over 27.0 metres. The goal of the program is to better 
define, what is expected to be, a locally high grade, conjugate vein, gold 
zones hosted by a fractured felsic intrusion.

An additional observation, specifically regarding the Serakoro 1 concession, is 
that outside of the main Sera W and Keure Trends, there is abundant laterite 
cover which masks the bedrock and thus reduces Savary's ability to trace gold 
zones along strike. This could be a reason why there is less artisanal activity 
on the Serakoro 1 property as compared to the Mandiasso and Diosso concessions 
to the north. An augur sampling or rotary air blast (RAB) program is being 
considered to aid in tracing the gold zones south into the Serakoro 1 
concession.

Once the soil sample results have been received, all new and existing drill 
targets will be prioritized and a follow-up exploration drill program will be 
developed for presentation to Savary's Board of Directors and Sarama's 
management team for review and approval.

QA/QC

All samples were collected in plastic bags, which were stapled shut with a 
sample tag before inserted into a larger poly sample bag for shipment to SGS 
Laboratories in Ouagadougou. Sample blanks and assay standards were inserted 
every ten prospecting samples resulting in 11% of the assayed samples being 
reference/blank control samples. Upon reception of the assay results, the 
results for the reference and blank control samples were compared against 
expected results. All standards and blank control samples returned results 
within expected ranges. Don Dudek, P. Geo. has reviewed and supervised the 
QA/QC program.

About Savary Gold

Savary Gold is a Canadian exploration company, along with partner, Sarama 
Resources Limited, are focused on exploring the Hounde South and Serakoro 1 
Gold Properties in Burkina Faso. The properties are in the Birimian age Hounde 
Greenstone Belt, which hosts Semafo's Mana mine and additional gold deposits 
that are presently subject to extensive exploration efforts (including 
Endeavour Mining's Hounde Project, Roxgold Yaramoko Project and Sarama's South 
Hounde Project, which is adjacent to Savary Gold's property). For additional 
information please visit our website at www.savarygold.com and follow us on 
Facebook, Linked-In and Twitter: @SavaryGold.

Don Dudek, P.Geo., President and CEO of the Company and a qualified person 
under National Instrument 43-101, has reviewed and approved the scientific and 
technical information in this press release.

SAVARY GOLD CORP.

On behalf of the Board

Don Dudek, President & Chief Executive Officer

Cautionary Notes

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

This news release may contain forward-looking statements. These statements 
include statements regarding the field program, the discovery of new gold 
minerlaization, the identification of new gold trends, historical drill 
intercepts and the results of historical data being indicative of the potential 
of the property. These statements are based on current expectations and 
assumptions that are subject to risks and uncertainties. Actual results could 
differ materially because of factors discussed in the management discussion and 
analysis section of our interim and most recent annual financial statements or 
other reports and filings with the TSX Venture Exchange and applicable Canadian 
securities regulations. We do not assume any obligation to update any 
forward-looking statements, except as required by applicable laws. Fall 2014 
Karankasso Prospecting Program Sampling results


/T/

----------------------------------------------------------------------------
Au g/t Au      Sample #        Easting       Northing                   Zone
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
less than                                               artisanal zone, not
0.01              9301         403588        1205328           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
1.92               9302         403592        1205345           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.04               9303         403609        1205389           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
less than                                               artisanal zone, not
0.01              9304         403590        1205375           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 470 m by up
to 50 m wide
artisanal zone, not
2.11               9305         403362        1205498           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.2                9306         403575        1205149           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.03               9307         403574        1205209           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.04               9308         409532        1206855           drill tested
----------------------------------------------------------------------------
New - Karan East
Highway, 430 m by up
to 40 m wide
artisanal zone, not
0.39               9309         409700        1206955           drill tested
----------------------------------------------------------------------------
0.03               9311         408699        1207015
----------------------------------------------------------------------------
Kien East northeast
extension, 1.2 km by
up to 35 m wide
artisanal mining
1.94               9312         408059        1205123     trend, not drilled
----------------------------------------------------------------------------
Kien East northeast
extension, not
0.89               9313         408059        1205123                drilled
----------------------------------------------------------------------------
Kien West, nearby
drill hole not
drilled far enoughto intersect 225 m
by 5-10 m wide
artisanal mining
4.25               9314         406194        1203708                   zone
----------------------------------------------------------------------------
Kien West, nearby
drill hole just
missed 150 m by up
to 30 m wide
artisanal mining
1.16               9315         406253        1203685                   zone
----------------------------------------------------------------------------
Kien West, 200 m by
1-3 m wide artisanal
mining zone, not
0.56               9316         405966        1202430                drilled
----------------------------------------------------------------------------
0.02               9317         406659        1202282
----------------------------------------------------------------------------
Kien West trend, 350
m by 1-3 m wide
series of artisanal
0.25               9318         405736        1201853      pits, not drilled
----------------------------------------------------------------------------
Kien West trend, 350
m by 1-3 m wide
series of artisanal
5.55               9319         405741        1201853      pits, not drilled
----------------------------------------------------------------------------
Kien West trend, 350
m by 1-3 m wide
series of artisanal
0.47               9321         405815        1201924      pits, not drilled
----------------------------------------------------------------------------
Kien West trend, 50
m by 3-5 m wide
artisanal zone, not
0.12               9322         405605        1201304                 tested
----------------------------------------------------------------------------
Kien West trend, 50
m by 3-5 m wide
artisanal zone, not
3.29               9323         405621        1201318                 tested
----------------------------------------------------------------------------
Kuere Trend, Diosso
South zone parallel
zone, 270 m by 1-3 m
pitting area, not
0.24               9324         401296        1189746                drilled
----------------------------------------------------------------------------
Kuere Trend, Diosso
South zone parallel
zone, 270 m by 1-3 m
pitting area, not
0.58               9325         401217        1189614                drilled
----------------------------------------------------------------------------
Kuere Trend, Diosso
South zone parallel
trend, 15 m by 1-3 m
wide pitting area,
nearby RC hole
returned 1.37 g/t Au
over 4.0 m and 1.2
0.77               9326         401087        1189411      g/t Au over 2.0 m
----------------------------------------------------------------------------
New, 150 m west of
Koure trend, small
isolated artisanal
0.14               9327         401333        1188750                    pit
----------------------------------------------------------------------------
New, Koure trend,
200 m by 2-5 m wide
zone of artisanal
0.03               9328         401423        1188788    mining, not drilled
----------------------------------------------------------------------------
New, Koure trend,
200 m by 2-5 m wide
zone of artisanal
0.03               9329         401447        1188877    mining, not drilled
----------------------------------------------------------------------------
New, Koure trend,
200 m by 2-5 m wide
zone of artisanal
0.91               9331         401487        1188963    mining, not drilled
----------------------------------------------------------------------------
New, isolated
artisanal site, 150
m long by up to 30 m
wide, sericite-
fuchite alteration,
400 m east of Diosso
South zone, RAB
hole, 60 m north
returned 2.08 g/t Au
0.41               9332         401286        1189236             over 2.0 m
----------------------------------------------------------------------------
New, isolated
artisanal site, 150
m long by up to 30 m
wide, sericite-
fuchite alteration,
400 m east of Diosso
South zone, RAB
hole, 60 m north
returned 2.08 g/t Au
0.43               9333         401277        1189213             over 2.0 m
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
1.12               9334         400304        1189422       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
1.6                9335         400309        1189511       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
2.205              9336         400403        1189670       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.06               9337         400485        1189858       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.64               9338         400250        1189285       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.47               9339         400154        1189084       zone, not tested
----------------------------------------------------------------------------
Kuere West trend,
500m east of Diosso
South zone, 870 m by
up to 35 m wide
artisanal mining
0.28               9341         400142        1188901       zone, not tested
----------------------------------------------------------------------------
New, Isolated
artisanal site, 35 m
long by 1-3 m wide,
may be related to
0.06               9342         400112        1188691       Kuere West Trend
----------------------------------------------------------------------------
0.09               9343         399468        1187424
----------------------------------------------------------------------------
Kuere Cross, new
zone on northeast
trending cross-
0.73               9344         404970        1197808              structure
----------------------------------------------------------------------------
0.07               9345         404971        1197809
----------------------------------------------------------------------------
0.15               9346         404870        1197916
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
0.05               9347         402407        1193130             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
6.17               9348         402388        1193109             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone ofartisanal mining,
Southern extension,
1.2                9349         402406        1193199             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
0.9                9351         402432        1193277             not tested
----------------------------------------------------------------------------
New, Kuere Trend,
950 m south of
Keuredougou West
zone, 750 m by up to
35 m wide zone of
artisanal mining,
Southern extension,
0.12               9352         402501        1193531             not tested
----------------------------------------------------------------------------
0.09               9353         402589        1193392
----------------------------------------------------------------------------
0.03               9354         402637        1193407
----------------------------------------------------------------------------
New zone, 350 m East
of Kuere trend, 40 m
by 15 m wide
artisanal mining
50.75              9355         402811        1193154       zone, not tested
----------------------------------------------------------------------------
New, Kuere west
trend, 65 m by 1-3 m
artisanal mining
area, RAB hole 110 m
north interested
1.45 g/t Au ober 4.0
3.74               9356         402325        1193907                      m
----------------------------------------------------------------------------
New, Kuere West
trend, 100 m by 1-3
m wide artisanal
0.41               9357         402547        1194474                   zone
----------------------------------------------------------------------------
New zone west of
Kuere West trend,
150 mby 40 m wide
artisanal pitting
1.63               9358         401821        1194739      area, not drilled
----------------------------------------------------------------------------
0.05               9360         402566        1194862
----------------------------------------------------------------------------
0.21               9361         401415        1193866
----------------------------------------------------------------------------
Keure West trend,
170 m by 1-2 m wide
area with artisanal
pitting lines, RAB
hole 150 m south
intersected 0.99 g/t
1.15               9362         402636        1194744          Au over 3.0 m
----------------------------------------------------------------------------
0.08               9363         403142        1194536
----------------------------------------------------------------------------
Kuere West trend, 78
m by 1-2 m wide zone
of artisanal shafts,
RAB hole 120 m south
interested 0.99 g/t
2.86               9364         402775        1195084          Au over 1.0 m
----------------------------------------------------------------------------
New zone west of
Kuere West trend,
145 m by 1-3 m wide
artisanal mining
0.54               9365         402445        1197044      area, not drilled
----------------------------------------------------------------------------
Kueredougou West
0.06               9366         402776        1194665                   zone
----------------------------------------------------------------------------
Kueredougou West
0.54               9367         402743        1194549                   zone
----------------------------------------------------------------------------
Kueredougou West
zone, sample from
pit 60 m south of
1.91               9368         402653        1194294              last hole
----------------------------------------------------------------------------
New zone, 270 m east
of Kueredougou West
zone, 400 by 1-2 m
wide trend of
2.85               9369         403123        1194557         artisanal pits
----------------------------------------------------------------------------
0.06               9370         403377        1194812
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
1.82               9372         404482        1194673    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
24.8               9373         404478        1194697    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
6.47               9374         404496        1194820    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
less than                                              1.04 km and up to 55
0.01              9375         404542        1195065    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
0.11               9376         404579        1195179    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
0.5                9377         404665        1195325    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
0.02               9378         404562        1195359    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
0.14               9379         404457        1195395    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend, traced for
1.04 km and up to 55
0.46               9381         404369        1194360    m wide, not drilled
----------------------------------------------------------------------------
New Zone - Koure
Trend,, 1.8 km north
of sample group
9372-9381, 150 m
long by 1-5 m wide
pitting trend,
sulphide rich waste
28.25              9382         405572        1196876     piles, not drilled
----------------------------------------------------------------------------
0.055              9383         405600        1196913
----------------------------------------------------------------------------
less than
0.01              9384         405626        1196799
----------------------------------------------------------------------------
0.03               9385         405645        1196818
----------------------------------------------------------------------------
0.23               9386         404385        1195710
----------------------------------------------------------------------------
New Zone - 400 m
west of Koure Trend,
140 m by 50 m zone
of pitting, hosted
by pillow basalt,
5.4                9387         404404        1195643            not drilled
----------------------------------------------------------------------------
New Zone - 400 m
west of Koure Trend,
140 m by 50 m zone
of pitting, hosted
less than                                                 by pillow basalt,
0.01              9388         404280        1195731            not drilled
----------------------------------------------------------------------------
New Zone - 400 m
west of Koure Trend,
140 m by 50 m zone
of pitting, hosted
by pillow basalt,
1.1                9390         404315        1195712            not drilled
----------------------------------------------------------------------------
New Zone - 400 m
west of Koure Trend,
140 m by 50 m zone
of pitting, hosted
by pillow basalt,
1.76               9391         404635        1195770            not drilled
----------------------------------------------------------------------------
New Zone - 250 m
east of Kuere Trend,
230 m by 3-7 m wide
pitting area, RC
hole 80 m south
intersected 0.88 g/t
Au over 1.0 m and
0.81 g/t Au over 1.02.15               9392         404462        
1198104         m, not drilled
----------------------------------------------------------------------------
New Zone - 250 m
east of Kuere Trend,
230 m by 3-7 m wide
pitting area, not
26.8               9393         404521        1198269                drilled
----------------------------------------------------------------------------
0.21               9394         404576        1198333
----------------------------------------------------------------------------
0.04               9395         406537        1202038
----------------------------------------------------------------------------
New Zone 500 m west
of interpreted Koure
Trend, 48 m by 100 m
artisanal diggin
1.74               9396         406313        1201407      zone, not drilled
----------------------------------------------------------------------------
New Zone 250 m west
of interpreted -
Koure Trend, 450 m
by up to 40 m wide
4.54               9397         406543        1201278        cluster of pits
----------------------------------------------------------------------------
less than
0.01              9398         406543        1201012
----------------------------------------------------------------------------
New Zone, 420 m west
of interpreted Koure
Trend, 3 narrow
pitting trends up to
65 m long and 1-2 m
12.45              9400         406300        1200394                   wide
----------------------------------------------------------------------------
New zone, Koure
trend, area of 10+
30-40 m deep shafts
along a 160 m
strike, sample of
periferal
mineralization to
1.25               9401         405997        1197746    planned mining area
----------------------------------------------------------------------------
New, Isolated area
of artisanal digging
0.34               9402         403361        1193034     134 m by 25 m wide
----------------------------------------------------------------------------
Kuere trend, 300 m
by 1-10 m wide zone
of pitting, active
mining, historic RC
returned 4.93 g/t
over 1.0 m and 5.92
0.26               9403         401263        1190252         g/t over 3.0 m
----------------------------------------------------------------------------
New zone - Karan
West trend, 425 m by
1-3 m wide zone of
artisanal shafts,
mix of sheared
intermediate
volcanics and felsic
0.62               9404         398298        1189995              intrusion
----------------------------------------------------------------------------
New zone, 75 m by 1-
10m wide artisanal
zone with 30 m
shaft, sheared and
quartz veined felsic
0.21               9405         398547        1190744             intrusion,
----------------------------------------------------------------------------
0.03               9406         398369        1190598
----------------------------------------------------------------------------
New Zone - Karan
West trend,
Sericitized, pyritic
and quartz veined
intermediate volc
11.55              9407         398706        1191498   and felsic intrusion
----------------------------------------------------------------------------
Serakoro 1 West,
weakly silicified
and sericitic felsic
23.4               9410         392230        1176012              intrusion
----------------------------------------------------------------------------
less than
0.01              9411         392530        1176196
----------------------------------------------------------------------------
Serakoro 1 West,
weakly silicified
and sericitic felsic
13.3               9412         392527        1176218              intrusion
----------------------------------------------------------------------------
Serakoro 1 West,
weakly silicified
and sericitic felsic
0.72               9413         392522        1176758              intrusion
----------------------------------------------------------------------------
New zone - Kuere
Trend, Serakoro 1
concession, outcrop
sample, nearest hole
0.68               9414         396341        1176846            600 m south
----------------------------------------------------------------------------
less than
0.01              9415         396042        1176794
----------------------------------------------------------------------------
less than
0.01              9416         398198        1179472
----------------------------------------------------------------------------
less than
0.01              9417         397961        1182262
----------------------------------------------------------------------------
less than
0.01              9418         395916        1176573
----------------------------------------------------------------------------
0.19               9419         395957        1176331
----------------------------------------------------------------------------
0.07               9421         395959        1176286
----------------------------------------------------------------------------
0.06               9422         395599        1171693
----------------------------------------------------------------------------
less than
0.01              9423         395563        1171702
----------------------------------------------------------------------------
less than
0.01              9424         395529        1171697
----------------------------------------------------------------------------
less than
0.01              9425         395439        1171654
----------------------------------------------------------------------------
less than
0.01              9426         395624        1171920
----------------------------------------------------------------------------
Kuere Trend -
Serakoro Main zone
trend, tested, RC
hole 60 m north
returned 2.67 g/t Au
1.415              9427         395765        1173199            over 10.0 m
----------------------------------------------------------------------------
New zone, Kuere
Trend - Serakoro
Main zone, 392 m by
up to 5 m wide zone
of artisanal
pitting, sheared
intermediate
volcanic, narrow,
4.35               9428         396073        1173215            not drilled
----------------------------------------------------------------------------
New zone, 15 m by
0.5 to 1.0 m wide
slot into QV zone to
5 m depth, not
0.5                9430         395970        1173343                drilled
----------------------------------------------------------------------------
0.02               9431         395749        1173322
----------------------------------------------------------------------------
0.02               9432         396695        1173718
----------------------------------------------------------------------------
0.02               9433         393577        1182794
----------------------------------------------------------------------------
New zone - Sera W
trend, Serakoro 1
concession,
artisanal pitting
zone 280 m by 5-10 m
wide, shafts to 10 m
0.49               9434         393540        1182134       deep, not tested
----------------------------------------------------------------------------
New zone - Sera W
trend, Serakoro 1
concession,
artisanal pitting
zone 280 m by 5-10 m
wide, shafts to 10 m
3.29               9435         393555        1181901       deep, not tested
----------------------------------------------------------------------------
less than
0.01              9436         393548        1181907
----------------------------------------------------------------------------
New zone - Sera W
trend, quartz veined
felsic intrusion,
open pit artisanal
mining zone 100 m by
70 m, nearby RAB
holes returned up to
1.93 g/t Au over 2.0
metres, RC drill
0.64               9437         392590        1180214     follow-up required
----------------------------------------------------------------------------
0.11               9438         392609        1180149     as per sample 9437
----------------------------------------------------------------------------
less than
0.01              9439         393621        1181135                       
----------------------------------------------------------------------------
New Zone, 1.2 km
east of Sera W
trend, 2, 1 mwide by
150 m series of
artisanal pits from
5.3                9441         394110        1181227         1 m to 8m deep
----------------------------------------------------------------------------
New zone - Sera W
trend, quartz veined
intermediate to
mafic volcanic, 10+,
30-40 m deep shafts
across a 5-15 m wide
zone for 130 m along
13.5               9442         393466        1183945                 strike
----------------------------------------------------------------------------
Cherty unit with
brown tourmaline
patches, active
artisanal mining
0.02               9443         393516        1183960     area 30 m by 2-4 m
----------------------------------------------------------------------------

/T/

- 30 -

CONTACT INFO:

Savary Gold Corp.
Michael McAllister
Manager, Investor Relations
416-309-2134
info@savarygold.com
www.savarygold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=511062224