Source	Marketwire
Date	12/18/2014
Time	09:19:07 AM

Company	 SAMCO GOLD LIMITED
Title	Samco Gold Provides Further Information on the Dino Property in Central 
Peru





    CDNX Symbol: SGA











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Samco Gold Limited

TSX VENTURE SYMBOL: SGA

December 18, 2014

Samco Gold Provides Further Information on the Dino Property in Central Peru


TORONTO, ONTARIO--(Marketwired - Dec. 18, 2014) - Samco Gold Limited (TSX 
VENTURE:SGA) ("Samco Gold" or the "Company") is pleased to provide additional 
information on the Dino Property in Central Peru further to its announcement on 
the proposed acquisition of SAMCO Minerals S.A. and Cia Dorita MA S.A.C. 
("SMCD").

OVERVIEW

Samco Minerals S.A and Cia Dorita MA S.A.C. ("SMCD") hold approximately 5,510 
hectares of mineral rights in the Mantaro District, located in the heart of the 
Polymetallic Belt of Central Peru (the "Dino Property"), hosting discordant 
vein (feeder) and stratabound manto zinc, lead and silver mineralisation 
described as carbonate replacement deposits (CRD). The Polymetallic Belt is a 
900 km long belt hosting numerous prolific mining operations, including 
Morococha, Cerro de Pasco, Antamina, San Gregorio, San Vicente and others. 
SMCD's mineral holdings display similar structural and geological settings and 
mineralogy to several of these operations, though SMCD does not consider the 
results of those operations as necessarily indicative of a similar scale of 
mineralisation on the Dino Property.

LOCATION, GEOGRAPHY AND ACCESS

The Dino Property is located in Central Peru, approximately 180 km 
east-northeast of the capital Lima within the Eastern Cordillera of the Central 
Peru Andes. The centre of the Dino Property lies approximately 18 km 
north-northwest of the provincial capital Jauja. Elevations range from about 
3,600 m to 4,200 m above mean sea level. The Dino Property comprises twelve 
concessions totalling some 5,510 hectares (55.1 km2). All concessions are 100% 
owned by SMCD. There are no seasonal limits on operations.

To view "Figure 1: Location Map", please visit the following link: 
http://media3.marketwire.com/docs/samco_gold_fig01_dec18.pdf

PREVIOUS EXPLORATION ACTIVITIES

Exploration activities carried out by SMCD to date include:

/T/

--  Interpretation of very high resolution satellite imagery interpretation
(WorldView 2) and ASTER.
--  Detailed geological surface mapping and "ground truthing" of satellite
interpretation maps.
--  Underground sampling and geological mapping of Dino Mine.
--  Mineral resource estimation for Dino Mine.
--  156 line kilometres of IP survey (pole-pole array).
--  Ground magnetic survey at 200m line spacing covering the entire Dino
Property and beyond.
--  Soil geochemical survey (greater than 6,500 MMI soil samples).
--  Surface trenching within the Dino-Astucia-Pacapaccha area.
--  Reconnaissance Zinc Zap survey.

/T/

DINO MINE

The vein system at the Dino Mine was historically mined on four levels that are 
separated by 50 metres vertically. The vein system has an exposed strike of 
over 350 meters and is open along strike and at depth, indicating significant 
upside potential for high-grade vein mineralisation at the Dino Mine. Apart 
from high-grade vein mineralisation, two stratabound (strike and dip parallel) 
replacement bodies termed mantos, have been identified within the Dino Mine. 
One of these has a width of about 2m and returned grades of 10.2% Zn, 10.8% Pb 
and 74 g/t Ag from face sampling, the second comprises a series of narrow 
replacement horizons within a 70cm wide limestone unit.

To view "Figure 2: Long section of Dino Mine - historic workings and 
underground sampling results", please visit the following link: 
http://media3.marketwire.com/docs/samco_gold_fig02_dec18.pdf

MINERAL RESOURCE ESTIMATE

In 2010, SMCD requested that ACA Howe conduct a block model mineral resource 
estimate on the Dino Mine, based on the most recent sampling and mapping 
results. This would assist in the planning of future drilling to raise the 
confidence level of the resources. This mineral resource estimate is considered 
current.

Raw data used in the resource estimation study consists of channel sampling 
undertaken by Anglorand Gold in 2007, and more limited sampling by SMCD in 
2010. The samples of the Dino vein system were collected every 5 m along Level 
#3, the stope connecting Level #3 with Level #2, the decline from Level #3 to 
the vertical shaft, and on the historic Level #4. The 5 m intervals were 
measured by tape from the mouth of the mine, and every 5 m the sample location 
was marked on the side wall with red paint that is still visible. Samples were 
collected as chip samples from a 20 to 40 cm wide channel, comprising footwall, 
vein and hanging wall (footwall and hanging wall only where available for 
sampling). Individual sample weight averaged between about 2 to 4 kg. Sampling, 
sample storage and sample dispatch to the laboratory was supervised by the 
project geologist at all times.

Samples taken during the surveys were assayed at the SGS-Lakefield laboratory 
in Lima, which is an independent ISO 9001:2000 certified facility. The samples 
were analysed for zinc, lead, silver, arsenic and antimony using multi-element 
ICP (Inductively Coupled Plasma) and MS (Mass Spectrometer) assaying 
techniques. Samples assaying in excess of 20% zinc or 20% lead were 
additionally assayed by volumetric assay method in order to ensure accurate 
assay values for high-grade samples. The wet and dry weight of each sample was 
recorded by the laboratory.

No check samples or standards were submitted to the assayer and reliance was 
placed on the internal QA/QC applied by SGS-Lakefield. While the assay results 
indicated that the internal QA/QC procedures were adequate, the lack of checks 
or standards limits the mineral resource estimate. The data indicated 
width-weighted average grades of 15.88% Zn, 8.03% Pb and 2 oz/t Ag over an 
average width of 116 cm for the material left behind by historic mining 
operations.

Prior to resource estimation, ACA Howe collected a limited series of chip 
channels from the Dino Mine at sites identifiable from previous sampling. 
Sampling sites observed by ACA Howe indicated that the samples had been 
collected in a representative manner, except in a few instances where karstic 
fissures were observed within the vein system that were essentially washed out 
by ground water. This could have removed high grade oxide material from the 
samples, resulting in a low grade bias in a small number of samples.

The ACA Howe samples were prepared and analysed using the same techniques as 
those used during the previous work. While the individual results could vary 
significantly, indicating the local variability of the mineralisation, the 
overall averages of the original and ACA Howe check samples are reasonably 
similar, confirming the presence of high grade sulphide and silver 
mineralisation within the Dino Mine. It was considered that the original sample 
data were suitable for the mineral resource estimation.

Geo-referenced mine plans obtained from SMCD and a number of sections were 
imported and geo-referenced for visualisation in 3D. Sectional compilations 
included geological interpretations of the geology surrounding the Dino Mine in 
cross and long section and a longitudinal sectional view of the Dino Mine 
workings. The block model cell size was developed by considering the geological 
model, possible high grade shoot dimensions and grade characteristics as well 
as potential mining methods. An up/down dip (Y axis) height of 20 m by an along 
strike (X axis) width of 5 m was chosen. The limited 5 m block width is equal 
to the sample spacing along strike and will prevent the dilution of blocks due 
to impact of low grade proximal samples along strike. The block height was 
selected to ensure shoot definition was maintained up and down dip.

Inferred mineral resources were estimated in the Dino Mine as shown in the 
table below:

/T/

----------------------------------------------------------------------------
Material Domain     Tonnes  Zn (%)  Pb (%) Ag (g/t)  Zn (t)  Pb (t) Ag (ozs)
----------------------------------------------------------------------------
NW Vein             54,000   12.30    7.39       48   7,000   4,000   84,000
----------------------------------------------------------------------------
Central Vein       103,000    5.80    4.92       26   6,000   5,000   86,000
----------------------------------------------------------------------------
SE1 Vein            55,000   22.49    5.68       48  12,000   3,000   85,000
----------------------------------------------------------------------------
SE2 Vein            20,000   30.80    6.79       88   6,000   1,000   56,000
----------------------------------------------------------------------------
Subtotal - Veins  232,000   13.42    5.84       42  31,000  13,000  311,000
----------------------------------------------------------------------------
Manto              91,000   10.20   10.80       74   9,000  10,000  217,000
----------------------------------------------------------------------------
Total             323,000   12.51    7.24       51  40,000  23,000  528,000
----------------------------------------------------------------------------
(i) See Note 1 below

/T/

The classification of interpolated blocks was undertaken by considering the 
following criteria:

/T/

--  Interpolation criteria based on sample density, search and interpolation
parameters.
--  Assessment of the reliability of geological, sample, survey and bulk
density data.
--  Robustness of the geological model.
--  Grade continuity confidence.

/T/

The following has been taken into account when classifying mineral resources at 
Dino:

/T/

--  No QA/QC data is available for either the 2007 Anglorand Gold or 2010
SAMCO exploration programmes. It is therefore not possible to determine
the precision or accuracy of the assayed sample grades used in mineral
resource estimation.
--  Sample numbers for each vein remain relatively low and no meaningful
statistical evaluation has been undertaken.
--  The current data spacing over the project is still not adequate to
define indicated or measured mineral resources, since grade continuity
in three dimensions at current data spacings cannot be demonstrated with
the required level of confidence.
--  It is possible that the galleries and declines were preferentially mined
out during the development of the underground workings. It appears that
the level #2 to level #3 decline is associated with a large stope. This
has the potential to skew underground samples towards lower grades in
remnant pillars.
--  The characteristics of shoots have not been defined down dip. Sampling
has been undertaken along linear transects with very limited overlap up
and down dip.
--  Insufficient survey work has been undertaken to accurately determine the
volume of material already extracted from the Dino vein system for the
estimation of indicated mineral resource volumes.

/T/

Geochemical surface sampling indicates that the vein system at the Dino Mine 
may host further mineralised veins within a greater than 150 metre wide zone, 
of which only about 15 metres (four veins) are exposed within the underground 
workings.

EXPLORATION POTENTIAL ELSEWHERE ON THE DINO PROPERTY

The exploration studies have resulted in the delineation of at least four 
targets for high-grade vein mineralisation ("feeders") similar to that at the 
Dino Mine and eight dolomitised manto units in the area between the Dino Mine 
and the Pacapaccha surface workings, located some 5km south of the Dino Mine. 
Despite intense surface leaching, some of these manto units display strong 
Zn-Pb-Ag mineralisation.

Manto mineralisation is indicated by coincident geophysical and soil 
geochemical MMI soil sampling anomalies, by surface showings over a strike 
length of about 8 kilometres that is corroborated by mineralised surface and 
underground manto exposures (Dino Mine, Astucia and Pacapaccha surface 
workings), as well as anomalous Zinc Zap reactions (staining method indicative 
for zinc mineralisation). Manto mineralisation is typically associated with 
individual dolomitic units distributed within a zone up to 500 metres wide in 
the Chambara Formation (Lower Pucara Group). Selected surface trench samples at 
Astucia and Pacapaccha returned assays of 6.33% Zn, 3.16% Pb and 16.22g/t Ag 
over 4.50 metres (Astucia) and 18.14% Zn, 0.18% Pb and 29.7g/t Ag over 2.80 
metres (Pacapaccha).

PLANNED EXPLORATION ACTIVITIES

The environmental permit for the Phase 1 surface drilling programme (DIA) has 
already been granted by the Peruvian Ministry of Energy & Mines. Land use 
agreements with the local communities allowing SMCD access for exploration 
programmes are in place. The surface rights at the Dino Mine have already been 
purchased (70 hectares). Technical studies for the environmental permit (EIAsd) 
required for underground development and underground drilling (over and above 
the already granted DIA) has already commenced.

An underground drill programme totalling up to 5,000 metres of diamond drilling 
has been planned with the aim of significantly extending the high-grade mineral 
resources at the Dino Mine. A surface diamond drilling programme totalling some 
5,000 metres has been designed to delineate extensions of the compliant 
high-grade mineral resources at the Dino Mine, as well as testing various 
targets delineated by geophysical, soil geochemical and geological surveys 
during the preceding exploration programme, particularly large volume mantos 
and high-grade vein targets.

/T/

Note 1:
Mineral resources which are not mineral reserves do not have demonstrated
economic viability. The estimate of mineral resources may be materially
affected by environmental, permitting, legal, title, taxation, socio-
political, marketing, or other relevant issues.
(1) The quantity and grade of reported Inferred resources in this estimation
are uncertain in nature and there has been insufficient exploration to
define these Inferred resources as an Indicated or Measured mineral resource
and it is uncertain if further exploration will result in upgrading them to
an Indicated or Measured mineral resource category.
(2) The Dino updated mineral resource estimate was prepared by Mr. Leon
McGarry, B.Sc., P.Geo., of ACA Howe International Limited and has an
effective date of November 20, 2010.
(3) The mineral resources in this press release were estimated using the
Canadian Institute of Mining, Metallurgy and Petroleum (CIM), CIM Standards
on Mineral Resources and Reserves, Definitions and Guidelines prepared by
the CIM Standing Committee on Reserve Definitions and adopted by CIM
Council.
(4) Tonnage figures have been rounded up or down to the nearest 1000t. Ag
ounces have been calculated using 31.1035g = 1oz; Pb and Zn tonnes have 
beencalculated using 2204.622 lbs = 1 tonne. Reported block model resources are
unconstrained by a cut off value.
(5) Bulk densities of 3.2 t/m3, were used for tonnage calculations at the
Dino Deposit.
(6) No minimum metal cut-off grade is applied for mineral resource
reporting.

/T/

About Samco Gold

Samco Gold's principal business has been the acquisition, exploration and 
development of precious metals resource properties in Argentina and the region. 
The Company's principal mineral property in Argentina is the El Dorado 
Monserrat ("EDM") epithermal gold project, located in the Deseado Massif region 
of Santa Cruz Province. With an experienced board and management team including 
a strong Argentinean complement, the Company's goal remains to become an 
Argentinean producer of gold and silver through the exploration and development 
of EDM. Samco Gold also owns a portfolio of other mineral exploration 
properties in the Deseado Massif, the most notable of which is the Corina 
property.

By virtue of this transaction, Samco Gold extends its principal business 
activities into Peru with the intention of becoming a Peruvian producer of 
zinc, lead and silver through the exploration and development of the Dino 
Property.

Additional details on the Company are available on SEDAR (www.sedar.com).

Dr. David Patrick, Managing Director of ACA Howe International Limited is a 
Qualified Person within the meaning of Canadian National Instrument 43-101 who 
prepared or supervised the preparation of the technical information that forms 
the basis for the disclosure on the Dino Property and has reviewed and approved 
the technical content of this release. An NI 43-101 report will be finalized 
and filed on SEDAR within 45 days of this release supporting the disclosure 
herein.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange), accepts 
responsibility for the adequacy or accuracy of this release.

FORWARD LOOKING STATEMENTS

This press release contains forward-looking statements which can be identified 
by the use of words "will", "expects", "believe", "potential", "near term", 
"targets", "anticipated", "goal", and phrases or statements that certain 
actions, events or results "may", "would", or "will" be taken, occur or be 
achieved.

Forward-looking statements involve known and unknown risks, assumptions, future 
events, conditions, uncertainties and other factors which may cause the actual 
results, performance or achievements to be materially different from any future 
results, prediction, projection, forecast, performance or achievements 
expressed or implied by the forward-looking statements. Such factors include, 
among others, completion of the SPA, the obtaining of the necessary financing 
and regulatory and shareholder approvals, as required, under the SPA, including 
any administrative or government approvals; changes in project parameters as 
plans continue to be refined; future prices of gold, zinc and other metals; 
future exploration results at the EDM, Corina and/or Dino properties; the 
reliability of historical information; possible variations in grade or recovery 
rates; failure of equipment or processes to operate as anticipated; labour 
disputes and other risks of the mining industry; delays in obtaining 
governmental approvals or financing or in the completion of exploration, as 
well as those factors disclosed in Samco Gold's disclosure documents publicly 
available under the Company's profile on the SEDAR website at www.sedar.com. 
Although Samco Gold has attempted to identify important factors that could 
cause actual actions, events or results to differ materially from those 
described in forward-looking statements, there may be other factors that cause 
actions, events or results not to be as anticipated, estimated or intended. 
There can be no assurance that forward-looking statements will prove to be 
accurate, as actual results and future events could differ materially from 
those anticipated in such statements. Accordingly, readers should not place 
undue reliance on forward-looking statements. The Company does not intend, and 
does not assume any obligations, to update forward-looking statements, whether 
as a result of new information, future events or otherwise, unless otherwise 
required by applicable securities laws.

- 30 -

CONTACT INFO:

Samco Gold Limited
Charles Koppel
Executive Chairman and Chief Executive Officer
+44 (0) 20 7647 2530
ck@samcogold.com
www.samcogold.com

or

Bell Pottinger
Daniel Thole / Marianna Bowes
Financial Communications
+44 (0) 20 3772 2500

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=511753796