Source	MARKET NEWS
Date	12/18/2014
Time	09:29:06 AM

Company	 Samco Gold Limited
Title	Provides Further 
Information On The Dino Propert





    CDNX Symbol: SGA











Press Release	




[200/News Release]SGAVSAMCO GOLD LTDDEC 18 2014  09:28 AMProvides Further 
Information On The Dino Property --->@NEWS RELEASE
SAMCO GOLD LTD ("SGA-V")
- Provides Further Information On The Dino Property
- In Central Peru

Samco Gold Limited ("Samco Gold" or the "Company") is pleased to
provide additional information on the Dino Property in Central Peru
further to its announcement on the proposed acquisition of SAMCO
Minerals S.A. and Cia Dorita MA S.A.C. ("SMCD").

OVERVIEW

Samco Minerals S.A and Cia Dorita MA S.A.C. ("SMCD") hold
approximately 5,510 hectares of mineral rights in the Mantaro District,
located in the heart of the Polymetallic Belt of Central Peru (the
"Dino Property"), hosting discordant vein (feeder) and stratabound
manto zinc, lead and silver mineralisation described as carbonate
replacement deposits (CRD). The Polymetallic Belt is a 900 km long belt
hosting numerous prolific mining operations, including Morococha, Cerro
de Pasco, Antamina, San Gregorio, San Vicente and others. SMCD's
mineral holdings display similar structural and geological settings and
mineralogy to several of these operations, though SMCD does not
consider the results of those operations as necessarily indicative of a
similar scale of mineralisation on the Dino Property.

LOCATION, GEOGRAPHY AND ACCESS

The Dino Property is located in Central Peru, approximately 180 km
east-northeast of the capital Lima within the Eastern Cordillera of the
Central Peru Andes. The centre of the Dino Property lies approximately
18 km north-northwest of the provincial capital Jauja. Elevations range
from about 3,600 m to 4,200 m above mean sea level. The Dino Property
comprises twelve concessions totalling some 5,510 hectares (55.1 km2).
All concessions are 100% owned by SMCD. There are no seasonal limits on
operations.

To view "Figure 1: Location Map", please visit the following link:
http://media3.marketwire.com/docs/samco_gold_fig01_dec18.pdf

PREVIOUS EXPLORATION ACTIVITIES

Exploration activities carried out by SMCD to date include:

--  Interpretation of very high resolution satellite imagery interpretation
(WorldView 2) and ASTER. --  Detailed geological surface mapping
and "ground truthing" of satellite
interpretation maps. --  Underground sampling and geological
mapping of Dino Mine. --  Mineral resource estimation for Dino Mine. --
156 line kilometres of IP survey (pole-pole array). --  Ground magnetic
survey at 200m line spacing covering the entire Dino
Property and beyond. --  Soil geochemical survey (greater than
6,500 MMI soil samples). --  Surface trenching within the
Dino-Astucia-Pacapaccha area. --  Reconnaissance Zinc Zap survey.

DINO MINE

The vein system at the Dino Mine was historically mined on four
levels that are separated by 50 metres vertically. The vein system has
an exposed strike of over 350 meters and is open along strike and at
depth, indicating significant upside potential for high-grade vein
mineralisation at the Dino Mine. Apart from high-grade vein
mineralisation, two stratabound (strike and dip parallel) replacement
bodies termed mantos, have been identified within the Dino Mine. One of
these has a width of about 2m and returned grades of 10.2% Zn, 10.8% Pb
and 74 g/t Ag from face sampling, the second comprises a series of
narrow replacement horizons within a 70cm wide limestone unit.

To view "Figure 2: Long section of Dino Mine - historic workings
and underground sampling results", please visit the following link:
http://media3.marketwire.com/docs/samco_gold_fig02_dec18.pdf

MINERAL RESOURCE ESTIMATE

In 2010, SMCD requested that ACA Howe conduct a block model
mineral resource estimate on the Dino Mine, based on the most recent
sampling and mapping results. This would assist in the planning of
future drilling to raise the confidence level of the resources. This
mineral resource estimate is considered current.

Raw data used in the resource estimation study consists of channel
sampling undertaken by Anglorand Gold in 2007, and more limited
sampling by SMCD in 2010. The samples of the Dino vein system were
collected every 5 m along Level #3, the stope connecting Level #3 with
Level #2, the decline from Level #3 to the vertical shaft, and on the
historic Level #4. The 5 m intervals were measured by tape from the
mouth of the mine, and every 5 m the sample location was marked on the
side wall with red paint that is still visible. Samples were collected
as chip samples from a 20 to 40 cm wide channel, comprising footwall,
vein and hanging wall (footwall and hanging wall only where available
for sampling). Individual sample weight averaged between about 2 to 4
kg. Sampling, sample storage and sample dispatch to the laboratory was
supervised by the project geologist at all times.

Samples taken during the surveys were assayed at the SGS-Lakefield
laboratory in Lima, which is an independent ISO 9001:2000 certified
facility. The samples were analysed for zinc, lead, silver, arsenic and
antimony using multi-element ICP (Inductively Coupled Plasma) and MS
(Mass Spectrometer) assaying techniques. Samples assaying in excess of
20% zinc or 20% lead were additionally assayed by volumetric assay
method in order to ensure accurate assay values for high-grade samples.
The wet and dry weight of each sample was recorded by the laboratory.

No check samples or standards were submitted to the assayer and
reliance was placed on the internal QA/QC applied by SGS-Lakefield.
While the assay results indicated that the internal QA/QC procedures
were adequate, the lack of checks or standards limits the mineral
resource estimate. The data indicated width-weighted average grades of
15.88% Zn, 8.03% Pb and 2 oz/t Ag over an average width of 116 cm for
the material left behind by historic mining operations.

Prior to resource estimation, ACA Howe collected a limited series
of chip channels from the Dino Mine at sites identifiable from previous
sampling. Sampling sites observed by ACA Howe indicated that the
samples had been collected in a representative manner, except in a few
instances where karstic fissures were observed within the vein system
that were essentially washed out by ground water. This could have
removed high grade oxide material from the samples, resulting in a low
grade bias in a small number of samples.

The ACA Howe samples were prepared and analysed using the same
techniques as those used during the previous work. While the individual
results could vary significantly, indicating the local variability of
the mineralisation, the overall averages of the original and ACA Howe
check samples are reasonably similar, confirming the presence of high
grade sulphide and silver mineralisation within the Dino Mine. It was
considered that the original sample data were suitable for the mineral
resource estimation.

Geo-referenced mine plans obtained from SMCD and a number of
sections were imported and geo-referenced for visualisation in 3D.
Sectional compilations included geological interpretations of the
geology surrounding the Dino Mine in cross and long section and a
longitudinal sectional view of the Dino Mine workings. The block model
cell size was developed by considering the geological model, possible
high grade shoot dimensions and grade characteristics as well as
potential mining methods. An up/down dip (Y axis) height of 20 m by an
along strike (X axis) width of 5 m was chosen. The limited 5 m block
width is equal to the sample spacing along strike and will prevent the
dilution of blocks due to impact of low grade proximal samples along
strike. The block height was selected to ensure shoot definition was
maintained up and down dip.

Inferred mineral resources were estimated in the Dino Mine as
shown in the table below:

//st

-----------------------------------------------------------------------
-----
Material Domain     Tonnes  Zn (%)  Pb (%) Ag (g/t)  Zn (t)  Pb (t) Ag (ozs)
---------------------------------------------------------------------------
-
NW Vein             54,000   12.30    7.39       48   7,000   4,000   84,000
---------------------------------------------------------------------------
-
Central Vein       103,000    5.80    4.92       26   6,000   5,000   86,000
---------------------------------------------------------------------------
-
SE1 Vein            55,000   22.49    5.68       48  12,000   3,000   85,000
---------------------------------------------------------------------------
-
SE2 Vein            20,000   30.80    6.79       88   6,000   1,000   56,000
---------------------------------------------------------------------------
-
Subtotal - Veins  232,000   13.42    5.84       42  31,000  13,000  311,000
---------------------------------------------------------------------------
-
Manto              91,000   10.20   10.80       74   9,000  10,000  217,000
---------------------------------------------------------------------------
-
Total             323,000   12.51    7.24       51  40,000  23,000  528,000
---------------------------------------------------------------------------
-
(i) See Note 1 below
The classification of interpolated blocks was undertaken by considering
the following criteria:
--  Interpolation criteria based on sample density, search and interpolation
parameters.
--  Assessment of the reliability of geological, sample, survey and bulk
density data.
--  Robustness of the geological model.
--  Grade continuity confidence.

The following has been taken into account when classifying mineral
resources at Dino:

--  No QA/QC data is available for either the 2007 Anglorand Gold or 2010
SAMCO exploration programmes. It is therefore not possible to determine
the precision or accuracy of the assayed sample grades used in mineral
resource estimation.
--  Sample numbers for each vein remain relatively low and no meaningful
statistical evaluation has been undertaken.
--  The current data spacing over the project is still not adequate to
define indicated or measured mineral resources, since grade continuity
in three dimensions at current data spacings cannot be demonstrated with
the required level of confidence.
--  It is possible that the galleries and declines were preferentially mined
out during the development of the underground workings. It appears that
the level #2 to level #3 decline is associated with a large stope. This
has the potential to skew underground samples towards lower grades in
remnant pillars.
--  The characteristics of shoots have not been defined down dip. Sampling
has been undertaken along linear transects with very limited overlap up
and down dip.
--  Insufficient survey work has been undertaken to accurately determine the
volume of material already extracted from the Dino vein system for the
estimation of indicated mineral resource volumes
//et

Geochemical surface sampling indicates that the vein system at the
Dino Mine may host further mineralised veins within a )150 metre wide
zone, of which only about 15 metres (four veins) are exposed within the
underground workings.

EXPLORATION POTENTIAL ELSEWHERE ON THE DINO PROPERTY

The exploration studies have resulted in the delineation of at
least four targets for high-grade vein mineralisation ("feeders")
similar to that at the Dino Mine and eight dolomitised manto units in
the area between the Dino Mine and the Pacapaccha surface workings,
located some 5km south of the Dino Mine. Despite intense surface
leaching, some of these manto units display strong Zn-Pb-Ag
mineralisation.

Manto mineralisation is indicated by coincident geophysical and
soil geochemical MMI soil sampling anomalies, by surface showings over
a strike length of about 8 kilometres that is corroborated by
mineralised surface and underground manto exposures (Dino Mine, Astucia
and Pacapaccha surface workings), as well as anomalous Zinc Zap
reactions (staining method indicative for zinc mineralisation). Manto
mineralisation is typically associated with individual dolomitic units
distributed within a zone up to 500 metres wide in the Chambara
Formation (Lower Pucara Group). Selected surface trench samples at
Astucia and Pacapaccha returned assays of 6.33% Zn, 3.16% Pb and
16.22g/t Ag over 4.50 metres (Astucia) and 18.14% Zn, 0.18% Pb and
29.7g/t Ag over 2.80 metres (Pacapaccha).

PLANNED EXPLORATION ACTIVITIES

The environmental permit for the Phase 1 surface drilling
programme (DIA) has already been granted by the Peruvian Ministry of
Energy & Mines. Land use agreements with the local communities allowing
SMCD access for exploration programmes are in place. The surface rights
at the Dino Mine have already been purchased (70 hectares). Technical
studies for the environmental permit (EIAsd) required for underground
development and underground drilling (over and above the already
granted DIA) has already commenced.

An underground drill programme totalling up to 5,000 metres of
diamond drilling has been planned with the aim of significantly
extending the high-grade mineral resources at the Dino Mine. A surface
diamond drilling programme totalling some 5,000 metres has been
designed to delineate extensions of the compliant high-grade mineral
resources at the Dino Mine, as well as testing various targets
delineated by geophysical, soil geochemical and geological surveys
during the preceding exploration programme, particularly large volume
mantos and high-grade vein targets.

//st

Note 1:
Mineral resources which are not mineral reserves do not have demonstrated
economic viability. The estimate of mineral resources may be materially
affected by environmental, permitting, legal, title, taxation,
socio-political, marketing, or other relevant issues.
(1) The quantity & grade of reported Inferred resources in this estimation
are uncertain in nature & there has been insufficient exploration to define
these Inferred resources as an Indicated or Measured mineral resource & it
is uncertain if further exploration will result in upgrading them to an
Indicated or Measured mineral resource category.
(2) The Dino updated mineral resource estimate was prepared by Mr. Leon
McGarry, B.Sc., P.Geo., of ACA Howe International Limited & has an
effective date of Nov 20, 2010.
(3) The mineral resources in this press release were estimated using the
Canadian Institute of Mining, Metallurgy & Petroleum (CIM), CIM Standards
on Mineral Resources & Reserves, Definitions & Guidelines prepared by the
CIM Standing Committee on Reserve Definitions & adopted by CIM Council.
(4) Tonnage figures have been rounded up or down to the nearest 1000t. Ag
ounces have been calculated using 31.1035g = 1oz; Pb & Zn tonnes have been
calculated using 2204.622 lbs = 1 tonne. Reported block model resources are
unconstrained by a cut off value.
(5) Bulk densities of 3.2 t/m3, were used for tonnage calculations at theDino 
Deposit.
(6) No minimum metal cut-off grade is applied for mineral resource
reporting.

//et

About Samco Gold

Samco Gold's principal business has been the acquisition,
exploration and development of precious metals resource properties in
Argentina and the region. The Company's principal mineral property in
Argentina is the El Dorado Monserrat ("EDM") epithermal gold project,
located in the Deseado Massif region of Santa Cruz Province. With an
experienced board and management team including a strong Argentinean
complement, the Company's goal remains to become an Argentinean
producer of gold and silver through the exploration and development of
EDM. Samco Gold also owns a portfolio of other mineral exploration
properties in the Deseado Massif, the most notable of which is the
Corina property.

By virtue of this transaction, Samco Gold extends its principal
business activities into Peru with the intention of becoming a Peruvian
producer of zinc, lead and silver through the exploration and
development of the Dino Property.

Additional details on the Company are available on SEDAR
(www.sedar.com).

Dr. David Patrick, Managing Director of ACA Howe International
Limited is a Qualified Person within the meaning of Canadian National
Instrument 43-101 who prepared or supervised the preparation of the
technical information that forms the basis for the disclosure on the
Dino Property and has reviewed and approved the technical content of
this release. An NI 43-101 report will be finalized and filed on SEDAR
within 45 days of this release supporting the disclosure herein.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange), accepts responsibility for the adequacy or accuracy of this
release.

FORWARD LOOKING STATEMENTS

This press release contains forward-looking statements which can
be identified by the use of words "will", "expects", "believe",
"potential", "near term", "targets", "anticipated", "goal", and phrases
or statements that certain actions, events or results "may", "would",
or "will" be taken, occur or be achieved.

Forward-looking statements involve known and unknown risks,
assumptions, future events, conditions, uncertainties and other factors
which may cause the actual results, performance or achievements to be
materially different from any future results, prediction, projection,
forecast, performance or achievements expressed or implied by the
forward-looking statements. Such factors include, among others,
completion of the SPA, the obtaining of the necessary financing and
regulatory and shareholder approvals, as required, under the SPA,
including any administrative or government approvals; changes in
project parameters as plans continue to be refined; future prices of
gold, zinc and other metals; future exploration results at the EDM,
Corina and/or Dino properties; the reliability of historical
information; possible variations in grade or recovery rates; failure of
equipment or processes to operate as anticipated; labour disputes and
other risks of the mining industry; delays in obtaining governmental
approvals or financing or in the completion of exploration, as well as
those factors disclosed in Samco Gold's disclosure documents publicly
available under the Company's profile on the SEDAR website at
www.sedar.com. Although Samco Gold has attempted to identify important
factors that could cause actual actions, events or results to differ
materially from those described in forward-looking statements, there
may be other factors that cause actions, events or results not to be as
anticipated, estimated or intended. There can be no assurance that
forward-looking statements will prove to be accurate, as actual results
and future events could differ materially from those anticipated in
such statements. Accordingly, readers should not place undue reliance
on forward-looking statements. The Company does not intend, and does
not assume any obligations, to update forward-looking statements,
whether as a result of new information, future events or otherwise,
unless otherwise required by applicable securities laws.

ENQUIRIES:
Samco Gold Limited
Charles Koppel
Executive Chairman and Chief Executive Officer
+44 (0) 20 7647 2530
ck@samcogold.com
www.samcogold.com

Bell Pottinger
Daniel Thole / Marianna Bowes
Financial Communications
+44 (0) 20 3772 2500
TSX Venture closing price for SGA-V
Date: 2014/12/16
Closing Price: 0.35

TEL:  +44 (0) 20 7647 2530      Samco Gold Limited
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1435100038TS11435101708-09283320141218