Source	Marketwire
Date	12/22/2014
Time	05:00:44 AM

Company	 SCORPIO GOLD CORPORATION
Title	Scorpio Gold Reports Final Results from 2014 Expansion Drilling at the 
Oromonte and Wedge Satellite Deposits, Mineral Ridge Project, Nevada





    CDNX Symbol: SGN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Scorpio Gold Corporation

TSX VENTURE SYMBOL: SGN

December 22, 2014

Scorpio Gold Reports Final Results from 2014 Expansion Drilling at the Oromonte 
and Wedge Satellite Deposits, Mineral Ridge Project, Nevada


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Dec. 22, 2014) - Scorpio Gold 
Corporation ("Scorpio Gold" or the "Company") (TSX VENTURE:SGN) reports final 
assay results from its 2014 expansion drilling program on the Oromonte and 
Wedge deposits at its 70% owned Mineral Ridge project, located in Nevada. Both 
deposits are located west of the Drinkwater pit and north of the leach pad.

Results presented in Tables 1 and 2 post-date the March 31, 2014 cut-off date 
for the LOM Plan that was reported in the Company's July 21, 2014 news release. 
The three holes drilled at Oromonte are 75-150 meter step-out holes to the 
southwest of the deposit in a previously untested area. Oromonte continues to 
be the least explored of the satellite deposits and further drilling is planned 
in 2015. The four holes drilled on the Wedge deposit lie outside of the 2014 
floated cone outline. In conjunction with drill results reported in the 
Company's July 8, 2014 news release, results from the 2014 expansion drilling 
program are expected to increase and upgrade the current resource estimate for 
the Wedge deposit.

Map links:

Oromonte Drill Plan

Wedge Drill Plan.

/T/

Table 1. Oromonte Deposit - Significant Drill Results

----------------------------------------------------------------------------
Hole      Azm    Dip   From     To  Width   From     To  Width   Gold   Gold
No.     (deg)  (deg)   (ft)   (ft)   (ft)    (m)    (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR14836     0    -90     95    100      5  28.96  30.48   1.52  0.010   0.34
----------------------------------------------------------------------------
525    535     10 160.02 163.07   3.05  0.015   0.50
----------------------------------------------------------------------------
MR14844     0    -90    475    480      5 144.78 146.30   1.52  0.015   0.51
----------------------------------------------------------------------------
MR14846     0    -90    235    240      5  71.63  73.15   1.52  0.019   0.65
----------------------------------------------------------------------------
340    345      5 103.63 105.16   1.52  0.020   0.68
----------------------------------------------------------------------------
500    505      5 152.40 153.92   1.52  0.025   0.84
----------------------------------------------------------------------------

Table 2. Wedge Deposit - Significant Drill Results

----------------------------------------------------------------------------
Hole       Azm   Dip   From     To  Width   From     To  Width   Gold   Gold
No.      (deg) (deg)   (ft)   (ft)   (ft)    (m)    (m)    (m)  (OPT)  (g/t)
----------------------------------------------------------------------------
MR141064     0   -90     90    105     15  27.43  32.00   4.57  0.009   0.31
----------------------------------------------------------------------------
MR141065     0   -90                 No Significant Results
----------------------------------------------------------------------------
MR141066     0   -90     30     35      5   9.14  10.67   1.52  0.044   1.51
----------------------------------------------------------------------------
55     60      5  16.76  18.29   1.52  0.016   0.55
----------------------------------------------------------------------------
MR141068     0   -90                 No Significant Results
----------------------------------------------------------------------------

/T/

All holes presented in the above tables were completed by reverse circulation 
(RC) drilling. True width is estimated at 80-100% of downhole width. Analytical 
results were performed by American Assay Laboratory Inc. in Sparks, Nevada, an 
ISO/IEC 17025:2005 accredited facility. External check assays to verify lab 
accuracy are routinely completed by ALS Chemex, an ISO 9001:2000 certified and 
ISO/IEC 17025:2005 accredited facility. Further details are presented in the 
Company's quality assurance and quality control program for the Mineral Ridge 
project at: MR QAQC.

About Scorpio Gold

Scorpio Gold holds a 70% interest in the producing Mineral Ridge gold mining 
operation located in Esmeralda County, Nevada with joint venture partner 
Waterton Global Value L.P. (30%), and Scorpio Gold is currently entitled to 
receive 80% of cash flow generated. Mineral Ridge is a conventional open pit 
mining and heap leach operation. The Mineral Ridge property is host to multiple 
gold-bearing structures, veins and lenses at exploration, development and 
production stages. Scorpio Gold also holds a 100% interest in the advanced 
exploration-stage Goldwedge property and processing facility in Manhattan, 
Nevada. The Company is assessing its exploration plans for the Goldwedge 
property as well as the potential for toll milling at the Goldwedge plant, 
which is currently permitted for 400 tons per day.

Scorpio Gold's President, Steve Roebuck, PGeo, is a Qualified Person as defined 
by National Instrument 43-101 and has reviewed and approved the content of this 
release.

ON BEHALF OF THE BOARD

SCORPIO GOLD CORPORATION

Peter J. Hawley, CEO

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

The Company relies on litigation protection for forward-looking statements. 
This news release contains forward-looking statements that are based on the 
Company's current expectations and estimates. Forward-looking statements are 
frequently characterized by words such as "plan", "expect", "project", 
"intend", "believe", "anticipate", "estimate", "suggest", "indicate" and other 
similar words or statements that certain events or conditions "may" or "will" 
occur, and include, without limitation, statements regarding the Company's 
plans with respect to the exploration, development and exploitation of its 
Mineral Ridge project, including potential further exploration or development 
of the Wedge and Oromonte deposits, any potential expansion of the current pit 
shell outline for the Wedge deposit, and any potential increase in the mineral 
reserve and resource estimate in respect thereof. Such forward-looking 
statements involve known and unknown risks, uncertainties and other factors 
that could cause actual events or results to differ materially from estimated 
or anticipated events or results implied or expressed in such forward-looking 
statements, including risks involved in mineral exploration and development 
programs and those risk factors outlined in the Company's Management Discussion 
and Analysis as filed on SEDAR. Any forward-looking statement speaks only as of 
the date on which it is made and, except as may be required by applicable 
securities laws, the Company disclaims any intent or obligation to update any 
forward-looking statement, whether as a result of new information, future 
events or results or otherwise. Forward-looking statements are not guarantees 
of future performance and accordingly undue reliance should not be put on such 
statements due to the inherent uncertainty thereof.

- 30 -

CONTACT INFO:

Scorpio Gold Corporation
Steve Roebuck
President
(819) 825-7618
sroebuck@scorpiogold.com

or

Investor Relations:
Jim Macdonald
Torrey Hills Capital
(858) 456-7300
jm@sdthc.com
www.scorpiogold.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=511842646