Source	CANADA NEWSWIRE
Date	12/23/2014
Time	05:34:24 AM

Company	 Asher Resources Corporation
Title	Asher Completes Phase II Drilling Program at King Mine and Further
Defines the Porphyry Copper-Gold System and Mesothermal Gold Zone





    CDNX Symbol: ACN











Press Release	




" BC-ACN-KingMinePhaseII   12-23 2033
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Asher Completes Phase II Drilling Program at King Mine and Further
Defines the Porphyry Copper-Gold System and Mesothermal Gold Zone@

Highlights:
Hole KM -13
<<

--  116 meters grading 0.075% copper
o Including 6.7 meters of 0.42% copper
--  49 meters grading 0.043% copper
>>
Hole KM-14
<<

--  15.2 meters grading 0.81 g/t gold
o Including 4.7 meters grading 2.00 g/t gold
>>
Hole KM-15
<<

--  9.1 meters grading 0.74 g/t gold
o Including 1.5 meters grading 3.36 g/t gold
--  2.2 meters grading 1.22 g/t gold
--  4.6 meters grading 1.20 g/t gold
--  27.5 meters grading 0.035% copper
o within 65.5 meters grading 0.053% zinc
>>
Hole KM-17
<<

--  9.1 meters grading 0.20g/t gold
o Including 3.1 meters grading 0.32 g/t gold
--  4.6 meters grading 0.71 g/t gold and
--  53.4 meters grading 0.078% copper
--  70.2 meters grading 0.033% zinc
>>
Hole KM-18
<<

--  47.5 meters grading 0.51 g/t gold
--  Including 12.2 meters grading 1.24 g/t gold
--  Including 1.5 meters grading 1.00 g.t gold
--  Including 1.5 meters grading 1.15 g/t gold within
--  47.5 meters grading 0.051% copper
--  4.5 meters grading 0.90 g/t gold within
--  27.4 meters grading 0.027% copper and
--  45.7 meters grading 0.031% zinc
>>
TORONTO, Dec. 23, 2014 /CNW/ - Asher Resources Corp. ACN - TSX.V (the
"Company") is pleased to announce assay results from the Company's recently
completed 1,376 meter reverse circulation rotary exploration drilling program
at its King Mine gold - copper project near the town of Gabbs, and 10 miles
west of the past producing Rawhide mine in north central Nevada.
Project activities, to date, including geological mapping, surface rock
sampling, induced polarization /magnetic surveys and an initial phase of
drilling have defined a copper- gold porphyry system with a potential high
grade gold zone on the margin. The Phase II drilling program was designed to
further define the porphyry system by targeting magnetic anomalies identified
through 3D image processing and to further delineate the northern end of the
800 meter long gold zone.
Hole KM-12Hole KM-12 with an azimuth of 270° and dip of -60° and depth of
277 meters was collared 224 meters due east of previous drill hole KM-5. It
was targeting increased anomalous copper and molybdenum values encountered
deep in drill hole KM-5 which was terminated in a fault zone prior to reaching
its target depth. Drill hole KM-12 intersected strongly silicified andesitic
rocks with up to 10% pyrite and several narrow zones (1.5 to 3 meter length)
of anomalous gold values in the 0.1 to 0.2 g/t range. Zones of anomalous
copper (+0.01%) were intersected between 157 meters and 195 meters (38 meters)
grading 0.02% and 207 meters to 267 meters (59 meters) grading 0.02%. Zinc
values which are common in the system were all less than the anomalous
threshold of 0.02%.
Hole KM-13Hole KM-13, with an azimuth of 191° and dip of -60° to a final
depth of 305 meters, was drilled from the prior KM-6 pad site to test a weak
magnetic feature on the southeast side of the main magnetic low which defines
to the overall porphyry system. The drill hole intersected propylitically
altered andesite with 3% to 6% sulphide minerals. The drill hole returned
multiple zones of highly anomalous copper with intersections grading 0.075%
copper over 116 meters, including 0.42% copper over 6.7 meters, 49 meters
grading 0.043% copper and 41 meters grading 0.024% copper. Anomalous zinc was
encountered over lengths of 36.6 meters grading 0.031% zinc and 27.4 meters
grading 0.024% zinc. Erratic gold values in the 0.1 to 0.2 g/t range were
present. A single gold assay grading 0.74 g/t over 1.5 meters was intersected
in the drill hole.
Hole KM-14, East Gold ZoneHole KM-14 with an azimuth of 225° and dip of
-70° to a final depth of 122 meters was collared 65 meters northeast and 20
meters topographically above the previous KM-3 / KM-4 drill pad where
intersections of 3.72 g/t gold over 7.62 meters and 3.26 g/t gold over 9.15
meters were encountered. The drill hole was designed to further test the area
of old, shallow, historic workings, surface gold values and the KM-3 and KM-4
intercepts. The drill hole intersected variably silicified and altered
andesite with 1% to 8% fine disseminated sulphide minerals. Anomalous god was
intersected over 15.2 meters assaying 0.82 g/t gold, including 4.7 meters
assaying 2.00 g/t gold. Narrow zones, 6.1 meters to 15.2 meters, of 100 to 250
ppm copper. The drill hole also carried anomalous zinc over 44.2 meters
grading 0.026% zinc.
Hole KM-15, East Gold Zone
Hole KM-15 with an azimuth of 225° and dip of -45° to a final depth of
107 meters was collared at the same pad site as KM-14, 65 meters northeast and
20 meters topographically above the previous KM-3 / KM-4 drill pad where
intersections of 3.72 g/t gold over 7.62 meters and 3.26 g/t gold over 9.15
meters were encountered. The drill hole was designed to further test the area
of old, shallow, historic workings, surface gold values and the KM-3 and KM-4
intercepts. The drill hole intersected variably silicified and altered
andesite with 1% to 8% fine disseminated sulphide minerals. The drill hole
intersected seveal gold zones, 9.1 meters grading 0.74 g/t gold, including
1.52 meters grading 3.36 g/t gold, 2.2 meters grading 1.22 g/t gold, and 4.6
meters grading 1.20 g/t gold. Anomalous copper was intersected over 27.5
meters grading 0.031% Copper. Anomalous zinc was intersected over a 65.5 meter
length grading 0.053% zinc.
Hole KM-16Hole KM-16 with an azimuth of 015° and dip of -60° and drilled
to a depth of 244 meters and located on the southwestern edge of the circular
magnetic footprint of the porphyry system. The hole was targeted on an
irregular shaped magnetic low based on the 3D interpretive magnetic model and
deemed to be magnetite destructive alteration associated with the porphyry
mineralizing event. It intersected variably silicified and hornfelsed (inner
propylitic alteration) andesite throughout with 1% to 10% fine disseminated
pyrite. No significant mineralization was encountered. Best gold assays
returned 6.1 meters grading 0.151 g/t gold and a single assay of 1.52 meters
grading 0.116 g/t gold. Copper values were weakly anomalous with a section of
86.9 meters grading 0.012% copper. Zinc values were all below anomalous
thresholds of 0.02%.
Hole KM-17, East Gold ZoneHole KM-17 with an azimuth of 180° and dip of
-70° was drilled to a depth of 122 meters from the KM-14/KM-15 pad site. It
intersected variably silicified and altered andesite as in KM-14/KM-15 with
Two gold zones were encountered. An intersection of 9.1 meters grading 0.20
g/t gold, including 3.1 meters grading 0.32 g/t gold, and a second
intersection of 4.6 meters grading 0.71g/t gold. Anomalous copper was
intersected over a 53.4 meter length averaging 0.048% copper. Anomalous zinc
was intersected over a 45.7 meter length averaging 0.033% zinc.
Hole KM-18, East Gold Zone
Hole KM-18 with an azimuth of 180° and dip of -45° was drilled to a depth
of 106.7 meters from the KM-14/KM-15 pad site. It intersected variably
silicified and altered andesite as in KM-14/KM-15 with 1% to 4% finely
disseminated sulphide minerals. Drilling intersected an upper zone of
mineralization with 47.3 meters grading 0.51 g/t gold, including 12.2 meters
grading 1.24 g/t gold, 1.52 meters grading 1.00 g/t gold and 1.52 meters
grading 1.15 g/t gold. A deeper gold zone was intersected over 4.5 meters
grading 0.90 g/t gold. Zones of anomalous copper were encountered over 47.3
meters grading 0.051% copper and 27.4 meters grading 0.027% copper. Zones of
anomalous zinc were encountered over 47.3 meters grading 0.078% zinc and 45.7
meters grading 0.031% zinc.
Hole KM-19, East Gold ZoneHole KM-19 with an azimuth of 045° and dip of
-45° was drilled to a depth of 91.5 meters. The drill hole was collared on the
KM-3 / KM-4 pad site and intersected moderately chlorititic and sericitic
andesite with 2% to 6% sulphide minerals below 48.8 meters. A mineralized zone
over 9.2 meters graded 0.134 g/t gold, 0.045% copper, 0.023% lead and 0.034%
zinc, including 3.1 meters grading 0.26 g/t gold at the very end of the drill
hole. Anomalous zinc averaging 0.031% was present from the collar to the
bottom of the hole a length of 91.5 meters.
All intersections are down hole lengths only. At this time, true widths
cannot be determined from available information.
These and other intersections are presented in the following table.
ASSAY HIGHLIGHTS TABLE

2014 King Mine Phase II Drilling Highlights


Hole
No.                      Target                      From                 
To                Interval      Gold       Copper        
Zinc                    Comment
(m)                 (m)                              g/t           %           %
---                                                   ---                 
---                              ---          ---         ---


KM-12                     Porphyry                         234.7                
236.3                 1.52      0.424         0.018        0.012    0.2 g/t 
cut-off

157                  195                   38                    0.02          
---  100 ppm cut-off

207                  267                   59                    0.02          
---  100 ppm cut-off

KM-13                     Porphyry                          
44.2                 53.4                 9.15      0.139         0.064         
0.02   0.1 g/t cut-off

102.1                108.2                  6.1      0.302         
0.083         0.02   0.2 g/t cut-off

144.8                152.8                  7.6      0.165         
0.108          ---

213.4                214.9                 1.52      0.743         
0.037          ---

38                  154                  116                   0.075

Including       80.8                 87.5                  
6.7                    0.42

189                  238                   49                   0.043

250                  291                   41                    0.24

9.1                 45.7                 36.6                                
0.31   200 ppm cut-off

211.9                239.3                 27.4                               
0.024   200 ppm cut-off

KM-14                     E. Gold Zone                      
59.5                   61                 1.52       1.45         
0.048          ---

68.6                 83.8                 15.2       0.81         
0.037          ---

Including       68.6                 73.1                  4.6       
2.00         0.103        0.027

KM-15                     E. Gold Zone                       
4.6                 13.7                  9.1       0.74         0.024          
---

Including       12.2                 13.7                 1.52       
3.36         0.034        0.022

57.9                 60.1                  2.2       1.22         0.075        
0.110

94.5                 99.0                  4.6       1.20         0.061         
0.03

45.7                 73.2                 27.5                   
0.031               copper zone

41.2                106.7                 65.5                   
0.053               zinc zone

KM-16                     Porphyry                          
41.2                 47.3                  6.1      0.152         
0.014          ---

copper and zinc below anomalous threshold

KM-17                     E. Gold Zone                      
18.3                 27.4                  9.1       0.71         0.051        
0.021   0.1 g/t cut-off

57.9                 62.5                  4.6       1.00         0.056        
0.029   0.2 g/t cut-off

13.7                 67.1                 53.4                   
0.048               copper zone

51.8                  122                 70.2                               
0.033   zinc zone

KM-18                     E. Gold Zone                      
12.2                 59.5                 47.3       0.51         0.051        
0.078   0.1 g/t cut-off

Including       12.2                 24.4                 12.2       
1.24         0.069        0.021

Including       35.1                 36.6                 1.52       
1.00         0.079        0.028

Including       56.4                 57.9                 1.52       
1.15         0.029        0.047

73.2                 77.7                  4.5       0.90         0.039        
0.039

12.2                 59.5                 47.3                   0.051        
0.078   Cu-Zn zone

65.5                   93                 27.4                   
0.027               copper zone

61                106.7                 45.7                               
0.031   zinc zone
KM-19                     E. Gold Zone                      
33.5                   35                 1.52      0.386         
0.023          ---

82.3                 91.5                  9.2      0.134         0.045        
0.034   0.1 g/t cut-off

Including       88.4                 91.5                  3.1      
0.261         0.064        0.023   0.2 g/t cut-off end of hole

Sample analyses were carried out by ALS Minerals with sample preparation
in Reno and analytical procedures in North Vancouver. ALS Mineral is an ISO
9001:2008 accredited laboratory applying the highest standards of QC and QA
procedures. Project samples were analyzed for 35 elements with aqua regia
digestion and ICP-AES technique. Gold was analyzed as a 30 gram aliquat by
fire assay and finished by atomic absorption determination. Duplicate samples
of King project drill cuttings were submitted in the field at 30.5 meter
intervals as a check on ALS sample preparation and analytical procedures. At
the laboratory, ALS introduces sample blanks, standards and duplicates as
internal checks on the integrity of all sample preparation and analytical
procedures. These results are reported to the client as a "QC certificate of
analysis".
The technical information herein was reviewed and approved by Paul R.
Mattinen, CPG-AIPG Asher's qualified person on its King Mine project based on
NI 43-101 and NI 43-101F1 regulations.
We seek Safe Harbor.
About Asher Resources:
Asher Resources Corporation is a gold exploration company headquartered
in Toronto, Ontario, with a regional office in Reno, Nevada. Asher's mission
is to discover high quality North American precious metal resources with its
current focus in southern British Columbia and the Nevada great basin.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release does not constitute an offer to sell or a solicitation
of an offer to sell any securities in the United States. The securities have
not been and will not be registered under the United States Securities Act of
1933, as amended (the "U.S. Securities Act") or any state securities laws and
may not be offered or sold within the United States or to U.S. Persons unless
registered under the U.S. Securities Act and applicable state securities laws
or an exemption from such registration is available.
SOURCE Asher Resources Corporation



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/December2014/23/c6818.html

-0-                           12/23/2014
/For further information: Richard Buzbuzian at: Telephone: (416)
361-6167, Email: rbuzbuzian(at)asher-resourc

" BC-ACN-KingMinePhaseII   12-23 2033
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Asher Completes Phase II Drilling Program at King Mine and Further
Defines the Porphyry Copper-Gold System and Mesothermal Gold Zone@

Highlights:
Hole KM -13
<<

--  116 meters grading 0.075% copper
o Including 6.7 meters of 0.42% copper
--  49 meters grading 0.043% copper
>>
Hole KM-14
<<

--  15.2 meters grading 0.81 g/t gold
o Including 4.7 meters grading 2.00 g/t gold
>>
Hole KM-15
<<

--  9.1 meters grading 0.74 g/t gold
o Including 1.5 meters grading 3.36 g/t gold
--  2.2 meters grading 1.22 g/t gold
--  4.6 meters grading 1.20 g/t gold
--  27.5 meters grading 0.035% copper
o within 65.5 meters grading 0.053% zinc
>>
Hole KM-17
<<

--  9.1 meters grading 0.20g/t gold
o Including 3.1 meters grading 0.32 g/t gold
--  4.6 meters grading 0.71 g/t gold and
--  53.4 meters grading 0.078% copper
--  70.2 meters grading 0.033% zinc
>>
Hole KM-18
<<

--  47.5 meters grading 0.51 g/t gold
--  Including 12.2 meters grading 1.24 g/t gold
--  Including 1.5 meters grading 1.00 g.t gold
--  Including 1.5 meters grading 1.15 g/t gold within
--  47.5 meters grading 0.051% copper
--  4.5 meters grading 0.90 g/t gold within
--  27.4 meters grading 0.027% copper and
--  45.7 meters grading 0.031% zinc
>>
TORONTO, Dec. 23, 2014 /CNW/ - Asher Resources Corp. ACN - TSX.V (the
"Company") is pleased to announce assay results from the Company's recently
completed 1,376 meter reverse circulation rotary exploration drilling program
at its King Mine gold - copper project near the town of Gabbs, and 10 miles
west of the past producing Rawhide mine in north central Nevada.
Project activities, to date, including geological mapping, surface rock
sampling, induced polarization /magnetic surveys and an initial phase of
drilling have defined a copper- gold porphyry system with a potential high
grade gold zone on the margin. The Phase II drilling program was designed to
further define the porphyry system by targeting magnetic anomalies identified
through 3D image processing and to further delineate the northern end of the
800 meter long gold zone.
Hole KM-12Hole KM-12 with an azimuth of 270° and dip of -60° and depth of
277 meters was collared 224 meters due east of previous drill hole KM-5. It
was targeting increased anomalous copper and molybdenum values encountered
deep in drill hole KM-5 which was terminated in a fault zone prior to reaching
its target depth. Drill hole KM-12 intersected strongly silicified andesitic
rocks with up to 10% pyrite and several narrow zones (1.5 to 3 meter length)
of anomalous gold values in the 0.1 to 0.2 g/t range. Zones of anomalous
copper (+0.01%) were intersected between 157 meters and 195 meters (38 meters)
grading 0.02% and 207 meters to 267 meters (59 meters) grading 0.02%. Zinc
values which are common in the system were all less than the anomalous
threshold of 0.02%.
Hole KM-13Hole KM-13, with an azimuth of 191° and dip of -60° to a final
depth of 305 meters, was drilled from the prior KM-6 pad site to test a weak
magnetic feature on the southeast side of the main magnetic low which defines
to the overall porphyry system. The drill hole intersected propylitically
altered andesite with 3% to 6% sulphide minerals. The drill hole returned
multiple zones of highly anomalous copper with intersections grading 0.075%
copper over 116 meters, including 0.42% copper over 6.7 meters, 49 meters
grading 0.043% copper and 41 meters grading 0.024% copper. Anomalous zinc was
encountered over lengths of 36.6 meters grading 0.031% zinc and 27.4 meters
grading 0.024% zinc. Erratic gold values in the 0.1 to 0.2 g/t range were
present. A single gold assay grading 0.74 g/t over 1.5 meters was intersected
in the drill hole.
Hole KM-14, East Gold ZoneHole KM-14 with an azimuth of 225° and dip of
-70° to a final depth of 122 meters was collared 65 meters northeast and 20
meters topographically above the previous KM-3 / KM-4 drill pad where
intersections of 3.72 g/t gold over 7.62 meters and 3.26 g/t gold over 9.15
meters were encountered. The drill hole was designed to further test the area
of old, shallow, historic workings, surface gold values and the KM-3 and KM-4
intercepts. The drill hole intersected variably silicified and altered
andesite with 1% to 8% fine disseminated sulphide minerals. Anomalous god was
intersected over 15.2 meters assaying 0.82 g/t gold, including 4.7 meters
assaying 2.00 g/t gold. Narrow zones, 6.1 meters to 15.2 meters, of 100 to 250
ppm copper. The drill hole also carried anomalous zinc over 44.2 meters
grading 0.026% zinc.
Hole KM-15, East Gold Zone
Hole KM-15 with an azimuth of 225° and dip of -45° to a final depth of
107 meters was collared at the same pad site as KM-14, 65 meters northeast and
20 meters topographically above the previous KM-3 / KM-4 drill pad where
intersections of 3.72 g/t gold over 7.62 meters and 3.26 g/t gold over 9.15
meters were encountered. The drill hole was designed to further test the area
of old, shallow, historic workings, surface gold values and the KM-3 and KM-4
intercepts. The drill hole intersected variably silicified and altered
andesite with 1% to 8% fine disseminated sulphide minerals. The drill hole
intersected seveal gold zones, 9.1 meters grading 0.74 g/t gold, including
1.52 meters grading 3.36 g/t gold, 2.2 meters grading 1.22 g/t gold, and 4.6
meters grading 1.20 g/t gold. Anomalous copper was intersected over 27.5
meters grading 0.031% Copper. Anomalous zinc was intersected over a 65.5 meter
length grading 0.053% zinc.
Hole KM-16Hole KM-16 with an azimuth of 015° and dip of -60° and drilled
to a depth of 244 meters and located on the southwestern edge of the circular
magnetic footprint of the porphyry system. The hole was targeted on an
irregular shaped magnetic low based on the 3D interpretive magnetic model and
deemed to be magnetite destructive alteration associated with the porphyry
mineralizing event. It intersected variably silicified and hornfelsed (inner
propylitic alteration) andesite throughout with 1% to 10% fine disseminated
pyrite. No significant mineralization was encountered. Best gold assays
returned 6.1 meters grading 0.151 g/t gold and a single assay of 1.52 meters
grading 0.116 g/t gold. Copper values were weakly anomalous with a section of
86.9 meters grading 0.012% copper. Zinc values were all below anomalous
thresholds of 0.02%.
Hole KM-17, East Gold ZoneHole KM-17 with an azimuth of 180° and dip of
-70° was drilled to a depth of 122 meters from the KM-14/KM-15 pad site. It
intersected variably silicified and altered andesite as in KM-14/KM-15 with
Two gold zones were encountered. An intersection of 9.1 meters grading 0.20
g/t gold, including 3.1 meters grading 0.32 g/t gold, and a second
intersection of 4.6 meters grading 0.71g/t gold. Anomalous copper was
intersected over a 53.4 meter length averaging 0.048% copper. Anomalous zinc
was intersected over a 45.7 meter length averaging 0.033% zinc.
Hole KM-18, East Gold Zone
Hole KM-18 with an azimuth of 180° and dip of -45° was drilled to a depth
of 106.7 meters from the KM-14/KM-15 pad site. It intersected variably
silicified and altered andesite as in KM-14/KM-15 with 1% to 4% finely
disseminated sulphide minerals. Drilling intersected an upper zone of
mineralization with 47.3 meters grading 0.51 g/t gold, including 12.2 meters
grading 1.24 g/t gold, 1.52 meters grading 1.00 g/t gold and 1.52 meters
grading 1.15 g/t gold. A deeper gold zone was intersected over 4.5 meters
grading 0.90 g/t gold. Zones of anomalous copper were encountered over 47.3
meters grading 0.051% copper and 27.4 meters grading 0.027% copper. Zones of
anomalous zinc were encountered over 47.3 meters grading 0.078% zinc and 45.7
meters grading 0.031% zinc.
Hole KM-19, East Gold ZoneHole KM-19 with an azimuth of 045° and dip of
-45° was drilled to a depth of 91.5 meters. The drill hole was collared on the
KM-3 / KM-4 pad site and intersected moderately chlorititic and sericitic
andesite with 2% to 6% sulphide minerals below 48.8 meters. A mineralized zone
over 9.2 meters graded 0.134 g/t gold, 0.045% copper, 0.023% lead and 0.034%
zinc, including 3.1 meters grading 0.26 g/t gold at the very end of the drill
hole. Anomalous zinc averaging 0.031% was present from the collar to the
bottom of the hole a length of 91.5 meters.
All intersections are down hole lengths only. At this time, true widths
cannot be determined from available information.
These and other intersections are presented in the following table.
ASSAY HIGHLIGHTS TABLE

2014 King Mine Phase II Drilling Highlights


Hole
No.                      Target                      From                 
To                Interval      Gold       Copper        
Zinc                    Comment
(m)                 (m)                              g/t           %           %
---                                                   ---                 
---                              ---          ---         ---


KM-12                     Porphyry                         234.7                
236.3                 1.52      0.424         0.018        0.012    0.2 g/t 
cut-off

157                  195                   38                    0.02          
---  100 ppm cut-off

207                  267                   59                    0.02          
---  100 ppm cut-off

KM-13                     Porphyry                          
44.2                 53.4                 9.15      0.139         0.064         
0.02   0.1 g/t cut-off

102.1                108.2                  6.1      0.302         
0.083         0.02   0.2 g/t cut-off

144.8                152.8                  7.6      0.165         
0.108          ---

213.4                214.9                 1.52      0.743         
0.037          ---

38                  154                  116                   0.075

Including       80.8                 87.5                  
6.7                    0.42

189                  238                   49                   0.043

250                  291                   41                    0.24

9.1                 45.7                 36.6                                
0.31   200 ppm cut-off

211.9                239.3                 27.4                               
0.024   200 ppm cut-off

KM-14                     E. Gold Zone                      
59.5                   61                 1.52       1.45         
0.048          ---

68.6                 83.8                 15.2       0.81         
0.037          ---

Including       68.6                 73.1                  4.6       
2.00         0.103        0.027

KM-15                     E. Gold Zone                       
4.6                 13.7                  9.1       0.74         0.024          
---

Including       12.2                 13.7                 1.52       
3.36         0.034        0.022

57.9                 60.1                  2.2       1.22         0.075        
0.110

94.5                 99.0                  4.6       1.20         0.061         
0.03

45.7                 73.2                 27.5                   
0.031               copper zone

41.2                106.7                 65.5                   
0.053               zinc zone

KM-16                     Porphyry                          
41.2                 47.3                  6.1      0.152         
0.014          ---

copper and zinc below anomalous threshold

KM-17                     E. Gold Zone                      
18.3                 27.4                  9.1       0.71         0.051        
0.021   0.1 g/t cut-off

57.9                 62.5                  4.6       1.00         0.056        
0.029   0.2 g/t cut-off

13.7                 67.1                 53.4                   
0.048               copper zone

51.8                  122                 70.2                               
0.033   zinc zone

KM-18                     E. Gold Zone                      
12.2                 59.5                 47.3       0.51         0.051        
0.078   0.1 g/t cut-off

Including       12.2                 24.4                 12.2       
1.24         0.069        0.021

Including       35.1                 36.6                 1.52       
1.00         0.079        0.028

Including       56.4                 57.9                 1.52       
1.15         0.029        0.047

73.2                 77.7                  4.5       0.90         0.039        
0.039

12.2                 59.5                 47.3                   0.051        
0.078   Cu-Zn zone

65.5                   93                 27.4                   
0.027               copper zone

61                106.7                 45.7                               
0.031   zinc zone
KM-19                     E. Gold Zone                      
33.5                   35                 1.52      0.386         
0.023          ---

82.3                 91.5                  9.2      0.134         0.045        
0.034   0.1 g/t cut-off

Including       88.4                 91.5                  3.1      
0.261         0.064        0.023   0.2 g/t cut-off end of hole

Sample analyses were carried out by ALS Minerals with sample preparation
in Reno and analytical procedures in North Vancouver. ALS Mineral is an ISO
9001:2008 accredited laboratory applying the highest standards of QC and QA
procedures. Project samples were analyzed for 35 elements with aqua regia
digestion and ICP-AES technique. Gold was analyzed as a 30 gram aliquat by
fire assay and finished by atomic absorption determination. Duplicate samples
of King project drill cuttings were submitted in the field at 30.5 meter
intervals as a check on ALS sample preparation and analytical procedures. At
the laboratory, ALS introduces sample blanks, standards and duplicates as
internal checks on the integrity of all sample preparation and analytical
procedures. These results are reported to the client as a "QC certificate of
analysis".
The technical information herein was reviewed and approved by Paul R.
Mattinen, CPG-AIPG Asher's qualified person on its King Mine project based on
NI 43-101 and NI 43-101F1 regulations.
We seek Safe Harbor.
About Asher Resources:
Asher Resources Corporation is a gold exploration company headquartered
in Toronto, Ontario, with a regional office in Reno, Nevada. Asher's mission
is to discover high quality North American precious metal resources with its
current focus in southern British Columbia and the Nevada great basin.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This news release does not constitute an offer to sell or a solicitation
of an offer to sell any securities in the United States. The securities have
not been and will not be registered under the United States Securities Act of
1933, as amended (the "U.S. Securities Act") or any state securities laws and
may not be offered or sold within the United States or to U.S. Persons unless
registered under the U.S. Securities Act and applicable state securities laws
or an exemption from such registration is available.
SOURCE Asher Resources Corporation



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/December2014/23/c6818.html

-0-                           12/23/2014
/For further information: Richard Buzbuzian at: Telephone: (416)
361-6167, Email: rbuzbuzian(at)asher-resources.com/
/Web Site: www.asher-resources.com /
(ACN.)

CO:  Asher Resources Corporation
ST:  Ontario
IN:  MNG
SU:

-30-