Source	MARKET NEWS
Date	12/23/2014
Time	05:51:42 AM

Company	 Asher Resources Corporation
Title	Completes 
Phase II Drilling Program at King Mine





    CDNX Symbol: ACN











Press Release	





ASHER RESOURCES CORP ("ACN-V")
- Completes Phase II Drilling Program at King Mine and Further
- Defines the Porphyry Copper-Gold System and Mesothermal Gold
- Zone

Asher Resources Corp. (the "Company") is pleased to announce assay
results from the Company's recently completed 1,376 meter reverse
circulation rotary exploration drilling program at its King Mine gold -
copper project near the town of Gabbs, and 10 miles west of the past
producing Rawhide mine in north central Nevada.

Project activities, to date, including geological mapping, surface
rock sampling, induced polarization /magnetic surveys and an initial
phase of drilling have defined a copper- gold porphyry system with a
potential high grade gold zone on the margin.  The Phase II drilling
program was designed to further define the porphyry system by targeting
magnetic anomalies identified through 3D image processing and to
further delineate the northern end of the 800 meter long gold zone.

Hole KM-12
Hole KM-12 with an azimuth of 270 and dip of -60 and depth of 277
meters was collared 224 meters due east of previous drill hole KM-5.
It was targeting increased anomalous copper and molybdenum values
encountered deep in drill hole KM-5 which was terminated in a fault
zone prior to reaching its target depth.  Drill hole KM-12 intersected
strongly silicified andesitic rocks with up to 10% pyrite and several
narrow zones (1.5 to 3 meter length) of anomalous gold values in the
0.1 to 0.2 g/t range.  Zones of anomalous copper (+0.01%) were
intersected between 157 meters and 195 meters (38 meters) grading 0.02%
and 207 meters to 267 meters (59 meters) grading 0.02%.  Zinc values
which are common in the system were all less than the anomalous
threshold of 0.02%.

Hole KM-13
Hole KM-13, with an azimuth of 191 and dip of -60 to a final depth
of 305 meters, was drilled from the prior KM-6 pad site to test a weak
magnetic feature on the southeast side of the main magnetic low which
defines to the overall porphyry system.  The drill hole intersected
propylitically altered andesite with 3% to 6% sulphide minerals.  The
drill hole returned multiple zones of highly anomalous copper with
intersections grading 0.075% copper over 116 meters, including 0.42%
copper over 6.7 meters, 49 meters grading 0.043% copper and 41 meters
grading 0.024% copper. Anomalous zinc was encountered over lengths of
36.6 meters grading 0.031% zinc and 27.4 meters grading 0.024% zinc.
Erratic gold values in the 0.1 to 0.2 g/t range were present.  A single
gold assay grading 0.74 g/t over 1.5 meters was intersected in the
drill hole.

Hole KM-14,  East Gold Zone
Hole KM-14 with an azimuth of 225 and dip of -70 to a final depth
of 122 meters was collared 65 meters northeast and 20 meters
topographically above the previous KM-3 / KM-4 drill pad where
intersections of 3.72 g/t gold over 7.62 meters and 3.26 g/t gold over
9.15 meters  were encountered. The drill hole was designed to further
test the area of old, shallow, historic workings, surface gold values
and the KM-3 and KM-4 intercepts. The drill hole intersected variably
silicified and altered andesite with 1% to 8% fine disseminated
sulphide minerals.  Anomalous god was intersected over 15.2 meters
assaying 0.82 g/t gold, including 4.7 meters assaying 2.00 g/t gold.
Narrow zones, 6.1 meters to 15.2 meters, of 100 to 250 ppm copper.  The
drill hole also carried anomalous zinc over 44.2 meters grading 0.026%
zinc.

Hole KM-15,  East Gold Zone

Hole KM-15 with an azimuth of 225 and dip of -45 to a final depth
of 107 meters was collared at the same pad site as KM-14, 65 meters
northeast and 20 meters topographically above the previous KM-3 / KM-4
drill pad where intersections of 3.72 g/t gold over 7.62 meters and
3.26 g/t gold over 9.15 meters  were encountered.  The drill hole was
designed to further test the area of old, shallow, historic workings,
surface gold values and the KM-3 and KM-4 intercepts.  The drill hole
intersected variably silicified and altered andesite with 1% to 8% fine
disseminated sulphide minerals.  The drill hole intersected seveal gold
zones, 9.1 meters grading 0.74 g/t gold, including 1.52 meters grading
3.36 g/t gold, 2.2 meters grading 1.22 g/t gold, and 4.6 meters grading
1.20 g/t gold.  Anomalous copper was intersected over 27.5 meters
grading 0.031% Copper.  Anomalous zinc was intersected over a 65.5
meter length grading 0.053% zinc.

Hole KM-16
Hole KM-16 with an azimuth of 015 and dip of -60 and drilled to a
depth of 244 meters and located on the southwestern edge of the
circular magnetic footprint of the porphyry system.  The hole was
targeted on an irregular shaped magnetic low based on the 3D
interpretive magnetic model and deemed to be magnetite destructive
alteration associated with the porphyry mineralizing event.  It
intersected variably silicified and hornfelsed (inner propylitic
alteration) andesite throughout with 1% to 10% fine disseminated
pyrite.  No significant mineralization was encountered. Best gold
assays returned 6.1 meters grading 0.151 g/t gold and a single assay of
1.52 meters grading 0.116 g/t gold.  Copper values were weakly
anomalous with a section of 86.9 meters grading 0.012% copper. Zinc
values were all below anomalous thresholds of 0.02%.

Hole KM-17,  East Gold Zone
Hole KM-17 with an azimuth of 180 and dip of -70 was drilled to a
depth of 122 meters from the KM-14/KM-15 pad site.  It intersected
variably silicified and altered andesite as in KM-14/KM-15 with   Two
gold zones were encountered.  An intersection of 9.1 meters grading
0.20 g/t gold, including 3.1 meters grading 0.32 g/t gold, and a second
intersection of 4.6 meters grading 0.71g/t gold.  Anomalous copper was
intersected over a 53.4 meter length averaging 0.048% copper.
Anomalous zinc was intersected over a 45.7 meter length averaging
0.033% zinc.

Hole KM-18,  East Gold Zone

Hole KM-18 with an azimuth of 180 and dip of -45 was drilled to a
depth of 106.7 meters from the KM-14/KM-15 pad site.  It intersected
variably silicified and altered andesite as in KM-14/KM-15 with 1% to
4% finely disseminated sulphide minerals.  Drilling intersected an
upper zone of mineralization with 47.3 meters grading 0.51 g/t gold,
including 12.2 meters grading 1.24 g/t gold, 1.52 meters grading 1.00
g/t gold and 1.52 meters grading 1.15 g/t gold.  A deeper gold zone was
intersected over 4.5 meters grading 0.90 g/t gold.  Zones of anomalous
copper were encountered over 47.3 meters grading 0.051% copper and 27.4
meters grading 0.027% copper.  Zones of anomalous zinc were encountered
over 47.3 meters grading 0.078% zinc and 45.7 meters grading 0.031%
zinc.

Hole KM-19,  East Gold Zone
Hole KM-19 with an azimuth of 045 and dip of -45 was drilled to a
depth of 91.5 meters.  The drill hole was collared on the KM-3 / KM-4
pad site and intersected moderately chlorititic and sericitic andesite
with 2% to 6% sulphide minerals below 48.8 meters.  A mineralized zone
over 9.2 meters graded 0.134 g/t gold, 0.045% copper, 0.023% lead and
0.034% zinc, including 3.1 meters grading 0.26 g/t gold at the very end
of the drill hole.  Anomalous zinc averaging 0.031% was present from
the collar to the bottom of the hole a length of 91.5 meters.

All intersections are down hole lengths only.  At this time, true
widths cannot be determined from available information.

These and other intersections are presented in the following
table.

ASSAY HIGHLIGHTS TABLE

//st
*********   TABLE AVAILABLE AT:   ********
http://www.asher-resources.com/s/NewsReleases.asp?ReportID=688823&_Type=New
s-Releases&_Title=Asher-Completes-Phase-II-Drilling-Program-at-King-Mine-an
d-Further-Defines-...
//et

Sample analyses were carried out by ALS Minerals with sample
preparation in Reno and analytical procedures in North Vancouver.  ALS
Mineral is an ISO 9001:2008 accredited laboratory applying the highest
standards of QC and QA procedures.  Project samples were analyzed for
35 elements with aqua regia digestion and ICP-AES technique.  Gold was
analyzed as a 30 gram aliquat by fire assay and finished by atomic
absorption determination. Duplicate samples of King project drill
cuttings were submitted in the field at 30.5 meter intervals as a check
on ALS sample preparation and analytical procedures.  At the
laboratory, ALS introduces sample blanks, standards and duplicates as
internal checks on the integrity of all sample preparation and
analytical procedures.  These results are reported to the client as a
"QC certificate of analysis".

The technical information herein was reviewed and approved by Paul
R. Mattinen, CPG-AIPG Asher's qualified person on its King Mine project
based on NI 43-101 and NI 43-101F1 regulations.

We seek Safe Harbor.

About Asher Resources:

Asher Resources Corporation is a gold exploration company
headquartered in Toronto, Ontario, with a regional office in Reno,
Nevada. Asher's mission is to discover high quality North American
precious metal resources with its current focus in southern British
Columbia and the Nevada great basin.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

This news release does not constitute an offer to sell or a
solicitation of an offer to sell any securities in the United States.
The securities have not been and will not be registered under the
United States Securities Act of 1933, as amended (the "U.S. Securities
Act") or any state securities laws and may not be offered or sold
within the United States or to U.S. Persons unless registered under the
U.S. Securities Act and applicable state securities laws or an
exemption from such registration is available.

TSX Venture closing price for ACN-V
Date: 2014/12/19
Closing Price: 0.04

TEL:  (416) 361-6167 Richard Buzbuzian
EMAIL:  rbuzbuzian@asher-resources.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1435600008TS11435600528-05501820141223