Source	MARKET NEWS
Date	12/15/2015
Time	03:39:24 PM

Company	 Falco Resources Ltd.
Title	Reports 
Positive Flotation & Leaching Results At





    CDNX Symbol: FPC











Press Release





FALCO RESOURCES LTD ("FPC-V")
- Reports Positive Flotation & Leaching Results At Horne 5
- Deposit

Falco Resources ("Falco") is pleased to announce the results of
preliminary metallurgical testwork performed on drill cores originating
from two mineralized zones of the Horne 5 deposit, located in
Rouyn-Noranda, Quebec. Comminution, open-circuit sequential flotation
and leaching tests were performed to assess potential metal recoveries
and base metal concentrate grades.A The flowsheet tested produced
copper and zinc flotation concentrates with saleable concentrate
grades. Precious metals were recovered to these base metal concentrates
and from flotation of a pyrite concentrate and its subsequent leaching.


"These initial positive metallurgical results are key to
demonstrate the strength of the Horne 5 deposit.A We are very
encouraged by the initial results, overall these results indicate that
the Horne 5 deposit is amenable to flotation and leaching resulting in
strong recoveries for all four metals," commented Luc Lessard,
President & CEO.

METALLURGICAL TESTWORK OBJECTIVES

The metallurgical testwork program conducted at SGS Lakefield,
under the supervision of James MacDonald and coordinated by BBA, was
designed to characterize gold deportment, mineral association, gold
liberation, comminution parameters, flotation recovery of base and
associated precious metals and precious metal cyanidation recovery.

HEAD ASSAY AND MINERALOGY

Metallurgical testing was performed on two composites (M1/2 and
M3) with average head grades of 0.32% and 0.19% Cu, respectively (see
Table 1).A The two samples were chosen from two zones of the deposit.A
Sample M1/2 is high copper-low zinc material, while M3 is low
copper-high zinc.A Testing at these two opposite ranges of grade was
meant to provide an indication of the influence of head grade on base
metal recovery.

Table 1: Sample Composite Head Assays

//st
Sample         Cu (%)     Zn (%)     Au (g/t)     Ag (g/t)     S (%)
M1/2             0.32       0.06         0.96          3.4        16
M3               0.19       1.23         4.49           46        30
//et

The mineralogical study indicated that gold is hosted in several
minerals, including calaverite, petzite, sylvanite, electrum and
kustelite.A The overall average gold mineral grain size is 3mm. Gold
association with pyrite is high, ranging from 73% to 99.5%. Copper and
zinc are present as chalcopyrite and sphalerite, respectively.

GRINDABILITY

Consideration was given to the mineralization and lithological
characteristics of the drill cores when proceeding with the comminution
sample selection. Three samples were chosen to represent the ore body's
variability range. Samples representing 100% massive sulphide (M.S),
100% rhyolitic tuff (Rh_tuff) and 100% rhyolite, breccias and rhyolitic
tuff (Rh/Br) were selected from the available material for SAG mill
comminution (SMC) (Axb), Bond rod mill (RWi) and Bond ball mill (BWi)
work indexA determinations.A The results show a good correlation with
the material's specific gravity (S.G.). The material hardness was
lowest for the massive sulphide sample as demonstrated in Table 2 and
Figures 1 to 3.

Table 2: Comminution Testwork Results

//st
Sample                 S.G.       Axb      RWi (kWh/t)      BWi (kWh/t)
100% M.S.               4.6      61.0             10.7              7.5
100% Rh/Br              3.2      34.3             18.2             16.1
100% Rh_tuff            2.9      24.5             23.0             21.5
//et

FLOTATION RECOVERY

Sample M1/2 was tested for copper and pyrite flotation only as it
did not contain any zinc. Selective flotation of copper, zinc and
pyrite was conducted for sample M3 to maximize payable metal recovery.
Both samples were subjected to a conventional rougher and two stage
cleaner flowsheet and testwork was completed in open circuit as opposed
to locked-cycle mode.

Flotation at a finer grind size, 65 mm vs 85 mm, had a positive
effect on copper recovery in sample M3 due to improved liberation of
chalcopyrite.

Copper recovery was lower for the low-grading copper sample M3,
compared to that of sample M1/2, as illustrated in Figure 4. The mass
pull in the 2nd cleaner concentrate ranged from 0.44% for M3 to 1.46%
for M1/2.

Gold recovery to the 2nd Cu cleaner concentrate varied with 57.3%
for M3 and 27.3% for M1/2. Additional recovery is anticipated under
locked-cycle conditions with a recycling of the intermediate tailings
streams.

New tests conditions with sample M3 (M3* in Figure 4) showed
improved copper recovery in the rougher stage. Consequently, higher
cleaner stage copper recovery is anticipated.

Zinc flotation was performed for sample M3 only. The concentrate
characteristics for rougher, 1st cleaner and 2nd cleaner stages are
shown in Figure 5. The mass pull to the 2nd cleaner concentrate is
1.7%. Only 1.4% of the gold is recovered in this final concentrate,
which is positive since it would normally not be payable under typical
smelting terms.

For the same M1/2 and M3 tests for which the Cu and Zn flotation
results are reported above, the indicated gold recoveries to the pyrite
flotation concentrates were 84.8% and 92.9% respectively.A It should be
noted that these recoveries are based solely on the gold values sent to
pyrite flotation and do not consider the intermediate tailings streams
of final concentrates within the Cu and Zn cleaning circuits.

CYANIDE LEACHING RECOVERY

Prior to cyanide leaching, the pyrite concentrate was reground to
10 Am.A Following a 12 hour preconditioning, leaching was carried out
at 35% solids for 72 hours with the cyanide controlled at a
concentration of 1.5 g/L in solution.A The addition of lead nitrate
improved both leaching kinetics and gold recovery.A Gold recovery from
leaching of the pyrite concentrate ranged from 81.3% to 88.7% for M1/2
and 81.9% to 84.8% for M3. Silver recovery was 90.1% for M1/2 and 84.9%
for M3.

Two leaching tests were performed on a M1/2 pyrite flotation
tailing sample to characterize flotation gold losses as either
refractory (not recoverable by cyanide leaching) or non-refractory
(recoverable by cyanide leaching).A Leaching was done at 35% solids and
with a cyanide concentration of 1 g/L maintained in solution.A Gold
recoveries of 75.3% and 74.7% were achieved after 48 hours.

FURTHER WORK TO BE CONDUCTED

Perform additional open-circuit flotation tests on composites from
different zones to improve the representativity of the ore tested
throughout the deposit.

Further copper cleaner circuit testwork to improve concentrate
grade and maximize copper recovery for low copper head grade samples.

Perform an economic tradeoff to evaluate the impact of concentrate
grade/recovery on downstream precious metal recovery.

Perform locked-cycle flotation testwork on composites representing
the expected Yr 1-3 mine life ore grade and life of mine head grade.

Further leaching testwork to optimize gold leaching kinetics of
the pyrite concentrate.

Qualified Person

The scientific and technical information regarding the
metallurgical test work results for the Horne 5 results set out in this
news release was conducted by SGS Lakefield under the supervision of
Mr. James MacDonald, Senior Project Manager/Metallurgist.

The scientific and technical information regarding the
metallurgical test work results for the Horne 5 results set out in this
news release has been reviewed and approved by Mr. Pierre Lacombe of
BBA Inc. Mr. Lacombe is a P.Eng. with the Ordre ingenieurs du Quebec,
and is a "qualified person" as defined by NI 43-101.

The scientific and technical information set out in this news
release has been approved by Christian Laroche, Director - Processing
of Osisko Mining Group. Mr.A Laroche is a P.Eng. with the Ordre
ingenieurs du Quebec, and is a "qualified person" as defined by NI
43-101.

About Falco

Falco Resources Ltd. is one of the largest mineral claim holders
in the Province of Quebec, with extensive land holdings in the Abitibi
Greenstone Belt. Falco owns 74,000 hectares of land in the
Rouyn-Noranda mining camp, which represents 70% of the entire camp and
includes 13 former gold and base metal mine sites. Falco's principal
property is the Horne Mine, which was operated by Noranda from 1927 to
1976 and produced 11.6 million ounces of gold and 2.5 billion pounds of
copper. A maiden 43-101 mineral resource estimate for the HorneA 5
deposit delineated an initial inferred resource of 2.8A Moz AuEq at
3.41 g/t AuEq (25.3 million tonnes grading 2.64 g/t Au, 0.23% Cu and
0.7% Zn, for 2.2 Moz Au -- see March 4, 2014 press release for
details).

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
press release.

Cautionary Note Regarding Forward-Looking Statements

This news release contains forward-looking statements and
forward-looking information (together, "forward-looking statements")
within the meaning of applicable securities laws and the United States
Private Securities Litigation Reform Act of 1995. All statements, other
than statements of historical facts, are forward-looking statements.
Generally, forward-looking statements can be identified by the use of
terminology such as "plans", "expects', "estimates", "intends",
"anticipates", "believes" or variations of such words, or statements
that certain actions, events or results "may", "could", "would",
"might", "will be taken", "occur" or "be achieved" and includes,
without limitation, realization of higher gold and copper recovery and
performance of described additional work. Forward-looking statements
involve risks, uncertainties and other factors that could cause actual
results, performance, prospects and opportunities to differ materially
from those expressed or implied by such forward-looking statements.
Factors that could cause actual results to differ materially from these
forward-looking statements include the reliability of the historical
data referenced in this press release and those risks set out in
Falco's public documents, including in each management discussion and
analysis, filed on SEDAR at www.sedar.com. Although Falco believes that
the assumptions and factors used in preparing the forward-looking
statements are reasonable, undue reliance should not be placed on these
statements, which only apply as of the date of this news release, and
no assurance can be given that such events will occur in the disclosed
times frames or at all. Except where required by applicable law, Falco
disclaims any intention or obligation to update or revise any
forward-looking statement, whether as a result of new information,
future events or otherwise.

Cautionary Note Concerning Mineral Resources

This press release uses the term "inferred" resources. We advise
investors that while this term is recognized and required by Canadian
regulations, the United States Securities and Exchange Commission does
not recognize it. "Inferred" resources have a great amount of
uncertainty as to their existence and as to their economic and legal
feasibility. It cannot be assumed that all or any part of an inferred
resource will ever be upgraded to a higher category. Under Canadian
rules, estimates of inferred mineral resources may not form the basis
of feasibility or other economic studies. United States investors are
cautioned not to assume that all or any part of measured or indicated
mineral resources will ever be converted into mineral reserves. United
States investors are also cautioned not to assume that all or any part
of an inferred mineral resource exists, or is economically or legally
mineable.

TSX Venture closing price for FPC-V
Date: 2015/12/14
Closing Price: 0.25

TEL:  514.905.3162  Vincent Metcalfe, Chief Financial Officer
EMAIL:  info@falcores.com
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1534800065TS11534802543-15381420151215