Source	Marketwire
Date	12/09/2015
Time	05:05:02 AM

Company	 ROCKHAVEN RESOURCES LTD.
Title	Rockhaven Announces Expanded Inferred Mineral Resource Estimate of 
1,358,000 oz Gold and 26,962,000 oz Silver at Klaza Property, Yukon





    CDNX Symbol: RK











Press Release




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Rockhaven Resources Ltd.

TSX VENTURE SYMBOL: RK

December 9, 2015

Rockhaven Announces Expanded Inferred Mineral Resource Estimate of 1,358,000 oz 
Gold and 26,962,000 oz Silver at Klaza Property, Yukon


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Dec. 9, 2015) - Rockhaven Resources 
Ltd. (TSX VENTURE:RK) ("Rockhaven") is pleased to announce an updated Mineral 
Resource estimate for its 100%-owned and road-accessible Klaza property, 
located in the Dawson Range Gold Belt of southern Yukon. The updated Mineral 
Resource estimate incorporates results from drilling in 2015 at the Klaza and 
BRX zones, including the newly modelled Eastern BRX Zone and a number of 
subsidiary veins associated with the main structures.

The updated Mineral Resource was prepared by AMC Mining Consultants (Canada) 
Ltd. This new estimate comprises a total Inferred Mineral Resource of 9,421,000 
tonnes grading 4.48 g/t gold, 89.02 g/t silver, 0.75% lead and 0.95% zinc, and 
contains 1,358,000 oz gold, 26,962,000 oz silver, 155,417,000 lbs lead and 
197,891,000 lbs zinc. The Mineral Resource has a gold equivalent metal content 
of 1,793,000 oz at a gold equivalent grade of 5.92 g/t. Results of this Mineral 
Resource estimate are summarized below.

/T/

Table 1: Klaza Property - Total Inferred Mineral Resource Estimate Summary,
December 9, 2015(1,5)
----------------------------------------------------------------------------
Grade
----------------------------------------------------------
Tonnes                                                  Au
(kt)    Au (g/t)  Ag (g/t)    Pb (%)     Zn (%) EQ(4)(g/t)
----------------------------------------------------------------------------
Pit-              2,366
Constrained(2,3)             5.12     94.51      0.93       1.18       6.71
----------------------------------------------------------------------------
Underground(3)    7,054       4.27     87.18      0.69       0.88       5.65
----------------------------------------------------------------------------
Total             9,421       4.48     89.02      0.75       0.95       5.92
----------------------------------------------------------------------------

----------------------------------------------------------------------------
Contained Metal
----------------------------------------------------------
Tonnes                                                  Au
(kt)    Au (koz)  Ag (koz)  Pb (klb)   Zn (klb) EQ(4)(koz)
----------------------------------------------------------------------------
Pit-              2,366
Constrained(2,3)              389     7,190    48,258     61,475        510
----------------------------------------------------------------------------
Underground(3)    7,054        969    19,772   107,159    136,416      1,282
----------------------------------------------------------------------------
Total             9,421      1,358    26,962   155,417    197,891      1,793
----------------------------------------------------------------------------
(1)  CIM definition standards were used for the Mineral Resource.
The Qualified Person is Adrienne Ross, P. Geo. of AMC Mining
Consultants (Canada) Ltd.
Using drilling results to September 30, 2015.
(2)  Near surface mineral resources are constrained by an optimized pit
shell at a gold price of US$1300 oz.
(3)  Cut-off grades applied to the pit-constrained and underground resources
are 1.3 g/t Au EQ and 2.75 g/t Au EQ respectively.
(4)  Gold equivalent values were calculated using the following formula: Au
EQ=Au+Ag/85+Pb/3.74+Zn/5.04 and assuming: US$1300 oz Au, US$20 oz Ag,
US$0.90 lb Pb and US$0.90 lb Zn with recoveries for each metal of Au:
96%, Ag: 91%, Pb: 85% and Zn: 85%.
(5)  Numbers may not add due to rounding. Mineral resources that are not
mineral reserves do not have demonstrated economic viability. All metal
prices are quoted in US$at an exchange rate of $0.80 US to $1.00
Canadian.

/T/

"The updated Mineral Resource clearly demonstrates the potential of the road 
accessible Klaza deposit" stated Matt Turner, President and CEO of Rockhaven. 
"Deposit-wide metallurgical testing shows silver, lead and zinc are important 
co-products that could enhance the economics of the deposit. There is a high 
probability for further expansion because the mineralized zones included in the 
Mineral Resource are open for extension along strike and to depth and there are 
other parallel zones on the property that have not yet been systematically 
evaluated. We look forward to future exploration at Klaza with the focus of 
continuing to add more ounces of high-grade mineralization at a very low 
discovery cost per ounce."

Compared to the Mineral Resource announced in January 2015, this represents an 
increase of 503,000 oz gold, using a 1.5 g/t gold-only cut-off applied to both 
the pit-constrained and underground components in order to directly compare at 
the same cut-off value. The following table summarizes the tonnage and gold 
ounce differences between the January and December, 2015 Mineral Resource 
estimates.

/T/

Table 2: Difference between January 2015 and December 2015 Inferred Gold
Mineral Resources(i)
----------------------------------------------------------------------------
Contained Increase in
Metal ounces (koz
Tonnes (Kt)    Au (g/t)    (koz Au)         Au)  % Increase
----------------------------------------------------------------------------
January 2015           7,040        4.19         948         503          53
----------------------------------------------------
December 2015         10,899        4.14       1,451
----------------------------------------------------------------------------
(i)Details pertaining to the January 2015 Mineral Resource can be found in
the Klaza Property Amended Technical Report dated June 19, 2015 which can be
viewed at http://www.sedar.com/ under the Rockhaven profile or on
Rockhaven's website.

/T/

The main reasons for the differences between the current estimate and the 
previous estimate are additional drilling information, modelling of subsidiary 
structures in the Central Klaza area, and inclusion of the Eastern BRX zone 
into the Mineral Resource area. The Mineral Resource has also been 
pit-constrained with different cut-off grades for the near surface and 
underground mineralization.

Resource Methodology

The Mineral Resource model was re-interpreted following the successful 2015 
drill program. Geological wire-frames representing high-grade veins were 
modeled in GEMS using available drill data. The model was constructed based 
upon structural controls, lithological boundaries and mineralogical domains.

A total of 71 domains were built in order to define the high-grade 
mineralization and different structural trends within each zone. Samples were 
capped for all variables within each domain where required. Block grades were 
estimated by Ordinary Kriging of composites within each domain. Densities of 
individual blocks were calculated using a regression formula based on density 
measurements taken and iron, lead, zinc and copper grades.

Tables showing the Mineral Resource at varying cut-off grades can be found 
attached. Additional tables summarizing the results of the Mineral Resource 
estimation for each zone can be found on Rockhaven's website at 
www.rockhavenresources.com.

Metallurgy

This Mineral Resource estimate has been prepared using updated metallurgical 
projections shown below, which reflect ongoing improvements from testing at 
Blue Coast Research Ltd., and especially recent successes in enhancing the 
quality of the lead and zinc concentrates.

/T/

Table 3: Klaza Property - Metallurgical Projections
----------------------------------------------------------------------------
Grade (%)                            Recovery (%)
------------------------------------------------------------
Lead      Zinc      Gold    Silver      Lead      Zinc
----------------------------------------------------------------------------
Dore                     -         -        87        11         -         -
----------------------------------------------------------------------------
Lead concentrate        60         3         4        53        85         -
----------------------------------------------------------------------------
Zinc concentrate         2        48         5        27         -        85
----------------------------------------------------------------------------
Total to payable
product               n/a       n/a        96        91        85        85
----------------------------------------------------------------------------

/T/

The process flowsheet comprises conventional sequential flotation of lead, zinc 
and an arsenopyrite-enriched concentrate followed by pressure oxidation and 
leaching of the arsenopyrite concentrate, together with a leach of residual 
precious metals from the flotation tails. Precious metals are also leached from 
the lead concentrate to reduce gold grade sent to the smelter and increase 
recovery to dore. Final products from this process are precious-metal rich lead 
and zinc concentrates and gold as dore.

These projections are based on testwork comprising the Western Klaza, Western 
BRX, Central Klaza and Central BRX zones, and do not include the Eastern BRX. 
Ongoing metallurgical testwork is expected to demonstrate how the treatment 
process can be optimized to benefit from the inclusion of Eastern BRX material.

Qualified Persons

The Mineral Resource estimate was completed by AMC Mining Consultants (Canada) 
Ltd. Adrienne Ross, Ph.D., P.Geo., Principal Geologist with AMC is the 
Qualified Person for the purpose of National Instrument 43-101 for all 
technical information pertaining to the current Mineral Resource.

Results for the metallurgical test program were provided and approved by Chris 
Martin, C.Eng., of Blue Coast Metallurgy Ltd. and Qualified Person for the 
purpose of National Instrument 43-101.

All other technical information in this news release has been approved by 
Matthew R. Dumala, P.Eng., a geological engineer with Archer, Cathro & 
Associates (1981) Limited and Qualified Person for the purpose of National 
Instrument 43-101.

The Qualified Persons under the terms of National Instrument 43-101 have 
reviewed the technical content of this press release for the Klaza property and 
have approved its dissemination.

Further details supporting the geological model, estimation procedure and 
metallurgical testwork will be available in a National Instrument 43-101 report 
authored by Adrienne Ross, Ph.D., P.Geo., of AMC Mining Consultants (Canada) 
Ltd., Chris J. Martin, C.Eng., of Blue Coast Metallurgy Ltd. and Matthew R. 
Dumala, P.Eng., of Archer, Cathro & Associates (1981) Limited. The report will 
be posted under the Rockhaven profile at www.sedar.com within 45 days from the 
date of this news release.

About Rockhaven

Rockhaven Resources Ltd. is a tightly-held company focused on growth through 
the advancement of its Klaza project. For additional information concerning 
Rockhaven Resources Ltd. or its various exploration projects please visit 
Rockhaven's website at www.rockhavenresources.com.

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

/T/

Table 4: Klaza Property - Total Inferred Pit-Constrained Mineral Resource at
Varying Cut-Off Grades(1,2,4)
----------------------------------------------------------------------------
COG       Tonnes          Au          Ag          Pb          Zn     AuEQ(3)
(AuEQ)    (kt)         (g/t)       (g/t)         (%)         (%)       (g/t)
----------------------------------------------------------------------------
0.5       2,427         5.01       92.40        0.90        1.16        6.57
----------------------------------------------------------------------------
1.0       2,413         5.03       92.89        0.91        1.16        6.60
----------------------------------------------------------------------------
1.3       2,366         5.12       94.51        0.93        1.18        6.71
----------------------------------------------------------------------------
1.5       2,329         5.18       95.78        0.94        1.19        6.79
----------------------------------------------------------------------------
2.0       2,250         5.32       98.22        0.96        1.22        6.97
----------------------------------------------------------------------------
2.5       2,125         5.53      102.12        0.99        1.27        7.25
----------------------------------------------------------------------------
2.75      2,071         5.62      103.72        1.01        1.29        7.37
----------------------------------------------------------------------------
3.0       2,023         5.70      105.42        1.03        1.31        7.48
----------------------------------------------------------------------------
3.5       1,904         5.90      109.77        1.07        1.34        7.74
----------------------------------------------------------------------------
4.0       1,729         6.20      116.16        1.13        1.39        8.14
----------------------------------------------------------------------------
5.0       1,414         6.83      128.08        1.24        1.47        8.96
----------------------------------------------------------------------------




----------------------------------------------------------------------------
COG       Tonnes          Au          Ag          Pb          Zn     
AuEQ(3)(AuEQ)    (kt)         (koz)       (koz)       (klb)       (klb)       
(koz)
----------------------------------------------------------------------------
0.5       2,427          391       7,211      48,399      61,878         513
----------------------------------------------------------------------------
1.0       2,413          391       7,207      48,374      61,806         512
----------------------------------------------------------------------------
1.3       2,366          389       7,190      48,258      61,475         510
----------------------------------------------------------------------------
1.5       2,329          388       7,172      48,110      61,227         509
----------------------------------------------------------------------------
2.0       2,250          385       7,106      47,600      60,520         504
----------------------------------------------------------------------------
2.5       2,125          378       6,977      46,608      59,491         495
----------------------------------------------------------------------------
2.75      2,071          374       6,906      46,133      58,935         491
----------------------------------------------------------------------------
3.0       2,023          371       6,855      45,748      58,347         486
----------------------------------------------------------------------------
3.5       1,904          361       6,719      44,787      56,383         474
----------------------------------------------------------------------------
4.0       1,729          344       6,457      43,142      52,826         453
----------------------------------------------------------------------------
5.0       1,414          310       5,823      38,742      45,712         407
----------------------------------------------------------------------------



Table 5: Klaza Property - Total Inferred Underground Mineral Resource at
Varying Cut-Off Grades(1,4)
----------------------------------------------------------------------------
COG       Tonnes          Au          Ag          Pb          Zn     AuEQ(3)
(AuEQ)    (kt)         (g/t)       (g/t)         (%)         (%)       (g/t)
----------------------------------------------------------------------------
1.0       10,354        3.40       69.66        0.55        0.73        4.51
----------------------------------------------------------------------------
1.5       10,036        3.48       71.22        0.57        0.75        4.62
----------------------------------------------------------------------------
2.0       9,030         3.72       75.92        0.60        0.79        4.93
----------------------------------------------------------------------------
2.5       7,612         4.10       83.66        0.66        0.85        5.43
----------------------------------------------------------------------------
2.75      7,054         4.27       87.18        0.69        0.88        5.65
----------------------------------------------------------------------------
3.0       6,470         4.46       91.25        0.72        0.91        5.91
----------------------------------------------------------------------------
3.5       5,396         4.86       99.70        0.78        0.96        6.44
----------------------------------------------------------------------------
4.0       4,489         5.25      109.59        0.86        1.04        6.98
----------------------------------------------------------------------------
5.0       3,297         5.93      125.50        0.98        1.14        7.90
----------------------------------------------------------------------------
6.0       2,214         6.81      145.07        1.13        1.25        9.07
----------------------------------------------------------------------------
7.0       1,503         7.75      163.48        1.32        1.40       10.30
----------------------------------------------------------------------------

----------------------------------------------------------------------------
COG       Tonnes          Au          Ag          Pb          Zn     AuEQ(3)
(AuEQ)    (kt)         (koz)       (koz)       (klb)       (klb)       (koz)
----------------------------------------------------------------------------
1.0       10,354       1,132      23,191     126,518     167,211       1,503
----------------------------------------------------------------------------
1.5       10,036       1,122      22,981     125,240     165,363       1,489
----------------------------------------------------------------------------
2.0       9,030        1,080      22,041     119,835     157,228       1,431
----------------------------------------------------------------------------
2.5       7,612        1,004      20,476     111,544     143,428       1,330
----------------------------------------------------------------------------
2.75      7,054          969      19,772     107,159     136,416       1,282
----------------------------------------------------------------------------
3.0       6,470          928      18,982     102,383     129,119       1,228
----------------------------------------------------------------------------
3.5       5,396          844      17,296      92,381     114,652       1,117
----------------------------------------------------------------------------
4.0       4,489          758      15,817      85,073     103,390       1,007
----------------------------------------------------------------------------
5.0       3,297          629      13,301      71,504      82,622         837
----------------------------------------------------------------------------
6.0       2,214          485      10,328      55,401      61,007         646
----------------------------------------------------------------------------
7.0       1,503          375       7,901      43,589      46,317         498
----------------------------------------------------------------------------
(1)  CIM definition standards were used for the Mineral Resource.
The Qualified Person is Adrienne Ross, P. Geo. of AMC Mining
Consultants (Canada) Ltd.
Using drilling results to September 30, 2015.
(2)  Near surface mineral resources are constrained by an optimized pit
shell at a gold price of US$1300 oz.
(3)  Gold equivalent values were calculated using the following formula:
AuEQ=Au+Ag/85+Pb/3.74+Zn/5.04 and assuming: US$1300 oz Au, US$20 oz Ag,
US$0.90 lb Pb and US$0.90 lb Zn with recoveries for each metal of Au:
96%, Ag: 91%, Pb: 85% and Zn: 85%.
(4)  Numbers may not add due to rounding. Mineral resources that are not
mineral reserves do not have demonstrated economic viability. metal
prices are quoted in US$at an exchange rate of $0.80 US to $1.00
Canadian.

/T/

- 30 -

CONTACT INFO:

Matthew Turner
President, CEO and Director
Rockhaven Resources Ltd.
T:604-687-2522
mturner@rockhavenresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=551762743