Source	CANADA NEWSWIRE
Date	12/03/2015
Time	05:03:11 AM

Company	 Rathdowney Resources Ltd.
Title	Rathdowney Drilling Highlights Excellent Resource Potential, Builds on
Positive Results from Project Olza Preliminary Economic Assessment





    CDNX Symbol: RTH











Press Release




" BC-Rathdowney-Olza-updte   12-03 2007
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Rathdowney Drilling Highlights Excellent Resource Potential, Builds on
Positive Results from Project Olza Preliminary Economic Assessment@

VANCOUVER, Dec. 3, 2015 /CNW/ - Rathdowney Resources Ltd. ("Rathdowney"
or the "Company") (TSXV: RTH) announces additional positive results from
drilling, supporting mine planning programs at its flagship Olza
Zinc-Lead-Silver Project in southwest Poland.
Proven zinc-lead district with excellent resource potential
Project Olza is located in the Upper Silesian mining district, a region
of world-class Mississippi Valley type ("MVT") deposits as recognized by the
USGS1, and which includes long-life mines such as Pomorzany and Olkusz.
Significant zinc-lead deposits in the area of Project Olza were identified,
historically, through 180,000 m of drilling conducted in the 1950s to 1980s by
the Polish State Survey. Rathdowney's drilling program in 2011-2013 began to
test these extensive deposits, and to December 2014 had outlined 24.4 million
tonnes of inferred mineral resources grading 7.02% Zn+Pb (at a 2% Zn cut-off)2
with excellent additional resource potential. Information in the table below
provides a comparison with other Upper Silesian deposits and well-known MVT
districts.
District    Mine      Status        Production +R/R Grade
--------    ----      ------        --------------- -----

Upper
Silesian,
Poland     Pomorzany Producing     93.8 Mt(3)      4.08% Zn, 1.26% Pb
----------  --------- ---------     ---------       ------------------

Upper
Silesian,
Poland     Olkusz    Past Producer 19.5 Mt(3)      3.83% Zn, 2.08% Pb
----------  ------    ------------- ---------       ------------------

Pine Point,
Canada               Past producer 76.11 Mt4       6.51% Zn, 2.91% Pb
-----------           ------------- ---------       ------------------

Viburnum
Trend, USA           Producing     215.91 Mt4      0.93% Zn, 6.47% Pb
-----------           ---------     ----------      ------------------
Rathdowney's drilling in 2014-2015 has been focused in the vicinity of
Zone 5, one of several zones that comprise the current mineral resource.
Todays' results are from 15 new holes (OLZ-256 to OLZ-270), each of which was
drilled outside of the resource-area at Zone 5 as shown on the map at
http://www.rathdowneyresources.com/i/pdf/rdr/OLZA_MAP__NR_Dec_15.pdf . Eleven
of the 15 new holes include significant mineralization, detailed in the Table
of Assay Results attached to this release. Highlights include:
<<

--  7.0 m of 6.5% Zn+Pb and 30.6 g/t Ag, including 2.2 m of 17.4% Zn+Pb and
54.2 g/t Ag in hole OLZ-256
--  7.3 m of 6.4% Zn+Pb and 10.7 g/t Ag, including 4.9 m of 8.5% Zn+Pb and
14.7 g/t Ag and 2.7 m of 13.1% Zn+Pb and 25.2 g/t Ag in hole OLZ-261
>>
This is the third tranche of holes from the 2014-2015 program (also see
Rathdowney News Releases dated September 22, 2015 and June 23, 2015) which,
collectively, are demonstrating good continuity in the mineralization to the
northwest and northeast of Zone 5. The results clearly underline the potential
for expansion of Zone 5 and highlight the excellent prospects for further
resource increases across the Project Olza concessions with additional
drilling.
Key geotechnical data was also collected from each drill hole for
engineering studies to assess the suitability of the Zone 5 area for
development of site facilities. Concurrently, hydrogeological studies and
environmental data collection programs are being conducted over an extensive
area to fully assess and consider the existing conditions in the broader
region. In combination with the geotechnical data from drilling, these studies
will provide the details to support site specifications for mine development,
water management and other important planning activities to be used in project
permitting for a modern, long-life mine.
Prime location with existing low-cost infrastructure
In addition to its geological potential, Project Olza has a number of
advantages when compared to many other emerging Zn-Pb mine development
projects. Mining has taken place in the Upper Silesian district since the 12th
century, and as a result, there is extensive infrastructure, including power
and rail already in place as well as a skilled local workforce. Situated in
the heart of Europe, the existing rail infrastructure provides Project Olza
with direct, low-cost access to ports and smelters.
These advantages are reflected in the results from the Preliminary
Economic Assessment ("PEA") announced earlier this year. The Project Olza PEA
shows strong potential financial returns for a conventional 6,000 tonnes per
day bulk room and pillar mine with standard on-site processing yielding two
marketable low iron zinc and lead concentrates5. Project Olza would be a
low-cost producer of an average of 197 million pounds of zinc and 59 million
pounds of lead, annually, readily available to markets in Europe and
throughout the world.
President and CEO Robert Konski said:
"Our drilling continues to demonstrate the excellent resource potential
at Project Olza, building on the PEA and providing a strong foundation for
comprehensive mine planning studies. Project Olza's central location in a
stable region with a long mining history is a key advantage to our project,
further enhancing its technical merits. We look forward to continuing our work
with the communities and the government, and advancing toward a modern
long-life mining operation in Poland."
About Rathdowney and Project Olza
Rathdowney Resources Ltd. is focused on advancing Project Olza through
permitting and into production. Project Olza is located in the Upper Silesian
Mining District of southwestern Poland, a world-class region of Mississippi
Valley-type deposits with well-developed mining infrastructure. Easily
accessible by road, the Olza project site is a one-hour drive from Krakow, a
major city with full services, including an international airport. The
deposits at Olza are 25 km from the ZGH zinc smelter at Boleslaw. A railway
line runs through the Olza project-area, linking it to smelters throughout
Europe and to ports on the Baltic Sea.
Rathdowney is committed to responsible mineral exploration and
development with respectful, mutually beneficial discussions and opportunities
for local communities. Our Project Olza community specialists discuss our
programs with representatives of local communities and government during all
phases of work, and are currently in discussions with community members and
others regarding the results of the PEA and other programs.
Dr. Keith Roberts, PGeo, is the qualified person for the drilling program
at Project Olza and has reviewed the drilling information in this release.
Other technical information has been reviewed by David Copeland, PEng, a
qualified person who is also Chairman and a Director of Rathdowney.
On behalf of the Board of DirectorsRobert KonskiPresident & CEO
Notes:1 Sangster, D.F., USGS, 1990, Mississippi Valley-Type and Sedex
lead-zinc deposits: A comparative examination: Transactions of the Institution
of Mining and Metallurgy, sec. B, v. 99, p. B21-B42.2 Individual grades are
5.53% Zn and 1.49% Pb. For further information see Rathdowney's new release
dated February 2, 2015. Mineral resources that are not mineral reserves do not
have demonstrated economic viability.3 Production + remaining reserves at
2010; www.geoportal.pl 4 Leach, David L. et al, USGS, 2010, A Deposit Model
for Mississippi Valley Type Lead-Zinc Ores, Chapter A, Mineral Resource
Deposit Models; Production + remaining resources at 2005.5 For additional
details on the PEA, see Rathdowney's news releases dated April 20, 2015 and
May 14, 2015.
Notes 1, 3, and 4 are associated with deposits that are not on the Olza
property. They are mainly reported production and derived from government
sources. They are historical in nature (see dates stated) and the work
necessary to verify them has not been undertaken by a qualified person.
Table of Assay Results
Drill Hole                   From             To        Length       
Pb+Zn         Zn         Pb         Ag

Number                      (m)             (m)         (m)         (%)        
(%)        (%)      (g/t)
------                      ---            ---         ---          ---         
---         ---       -----

OLZ-256                                                104.20       
111.15          6.95         6.54        6.33        0.21    30.6
-------                                                ------       
------          ----         ----        ----        ----    ----

Incl                  107.05       109.28          2.23        17.39       
17.02        0.37    54.2
----                  ------       ------          ----        -----       
-----        ----    ----

OLZ-258                                             102.80       
105.80          3.00         3.77        1.33        2.44    11.0
-------                                             ------       
------          ----         ----        ----        ----    ----

Incl                  103.40       105.50          2.10         4.80        
1.47        3.33    13.3
----                  ------       ------          ----         ----        
----        ----    ----

OLZ-259                                              99.50       
100.50          1.00         3.34        3.29        0.05     6.8
-------                                              -----       
------          ----         ----        ----        ----     ---

OLZ-260                                             126.85       
136.40          9.55         0.86        0.45        0.41     3.1
-------                                             ------       
------          ----         ----        ----        ----     ---

Incl                  132.85       134.40          1.55         1.67        
1.06        0.61    10.2
----                  ------       ------          ----         ----        
----        ----    ----

OLZ-261                                             147.00       
154.26          7.26         6.41        6.01        0.40    10.7
-------                                             ------       
------          ----         ----        ----        ----    ----

Incl                  149.35       154.26          4.91         8.52        
8.00        0.52    14.7
----                  ------       ------          ----         ----        
----        ----    ----

And                   151.61       154.26          2.65        13.05       
13.04        0.01    25.2
---                   ------       ------          ----        -----       
-----        ----    ----

OLZ-262                                             154.00       
160.00          6.00         1.64        1.42        0.22     2.0
-------                                             ------       
------          ----         ----        ----        ----     ---

Incl                  155.60       157.40          1.80         2.90        
2.78        0.12     3.3
----                  ------       ------          ----         ----        
----        ----     ---

OLZ-265                                             119.90       
120.70          0.80         6.51        6.50        0.01    60.1
-------                                             ------       
------          ----         ----        ----        ----    ----

OLZ-266                                             158.00       
159.95          1.95         5.79        5.16        0.63    18.1
-------                                             ------       
------          ----         ----        ----        ----    ----

OLZ-267                                             147.00       
152.60          5.60         1.57        1.24        0.33     0.9
-------                                             ------       
------          ----         ----        ----        ----     ---

158.40       162.20          3.80         1.80        1.78        0.02     2.4
------       ------          ----         ----        ----        ----     ---

Incl                  161.00       162.20          1.20         3.23        
3.23       0.003     4.9
----                  ------       ------          ----         ----        
----       -----     ---

OLZ-268                                             158.60       
160.10          1.50         2.20        2.08        0.12     4.3
-------                                             ------       
------          ----         ----        ----        ----     ---

OLZ-270                                             157.00       
160.20          3.20         1.90        1.27        0.63     2.3
-------                                             ------       
------          ----         ----        ----        ----     ---

Incl                  158.80       159.25          0.45         8.32        
4.08        4.24    13.9
----                  ------       ------          ----         ----        
----        ----    ----

All diamond core holes were drilled vertically through the sub-horizontal 
mineralized horizons so

intersections represent approximate true widths. No significant results in 
holes 257, 263, 264

and 269. (x)Figures may not add due to rounding.
----------------------------------------------

Sample preparation for the current drilling
program is performed at the Bureau Veritas
(BV) laboratory in Krakow, Poland. Core
samples are weighed, dried and crushed to
>70% passing 10 mesh (2 mm), then 500 g sub-
samples are riffle split and pulverized to
>85% passing 200 mesh (75 µm).  Samples are
shipped by air freight to the Vancouver
laboratory of Bureau Veritas Commodities
Canada Ltd., an ISO 9001 accredited
laboratory, for analysis. All samples are
assayed for Pb, Zn, Ag and 38 additional
elements by 4 acid (HF-HNO3-HClO4, HCl)digestion of an 0.5 g sample with an ICP-
AES/ICP-MS (inductively coupled atomic
emission spectrometry/mass spectrometry)
finish (BV Code: MA270). Samples with Zn
values >40% or Pb values >10%, the upper
limits for the MA270 method, are re-
analyzed by BV method MA371; 4 acid
digestion of 0.1 g sample with ICP-AES
finish. As part of a comprehensive QAQC
program, one standard and one replicate are
inserted into the sample stream in each
group of 20 samples, as well as one or more
blanks in each analytical batch.
---------------------------------------------
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This release includes certain statements that may be deemed
"forward-looking statements". All statements in this release, other than
statements of historical facts, that address exploration drilling,
exploitation activities and events or developments that the Company expects,
are forward looking statements. Although the Company believes the expectations
expressed in such forward-looking statements are based on reasonable
assumptions, such statements are not guarantees of future performance and
actual results or developments may differ materially from those in the
forward-looking statements. Assumptions used by the Company to develop
forward-looking statements include the following: the Olza project will obtain
all required environmental and other permits and all land use and other
licenses, studies and development of the Olza project will continue to be
positive, and no geological or technical problems will occur. Factors that
could cause

" BC-Rathdowney-Olza-updte   12-03 2007
News release via Canada NewsWire, Toronto 416-863-9350 -ME-

Attention Business Editors:
^Rathdowney Drilling Highlights Excellent Resource Potential, Builds on
Positive Results from Project Olza Preliminary Economic Assessment@

VANCOUVER, Dec. 3, 2015 /CNW/ - Rathdowney Resources Ltd. ("Rathdowney"
or the "Company") (TSXV: RTH) announces additional positive results from
drilling, supporting mine planning programs at its flagship Olza
Zinc-Lead-Silver Project in southwest Poland.
Proven zinc-lead district with excellent resource potential
Project Olza is located in the Upper Silesian mining district, a region
of world-class Mississippi Valley type ("MVT") deposits as recognized by the
USGS1, and which includes long-life mines such as Pomorzany and Olkusz.
Significant zinc-lead deposits in the area of Project Olza were identified,
historically, through 180,000 m of drilling conducted in the 1950s to 1980s by
the Polish State Survey. Rathdowney's drilling program in 2011-2013 began to
test these extensive deposits, and to December 2014 had outlined 24.4 million
tonnes of inferred mineral resources grading 7.02% Zn+Pb (at a 2% Zn cut-off)2
with excellent additional resource potential. Information in the table below
provides a comparison with other Upper Silesian deposits and well-known MVT
districts.
District    Mine      Status        Production +R/R Grade
--------    ----      ------        --------------- -----

Upper
Silesian,
Poland     Pomorzany Producing     93.8 Mt(3)      4.08% Zn, 1.26% Pb
----------  --------- ---------     ---------       ------------------

Upper
Silesian,
Poland     Olkusz    Past Producer 19.5 Mt(3)      3.83% Zn, 2.08% Pb
----------  ------    ------------- ---------       ------------------

Pine Point,
Canada               Past producer 76.11 Mt4       6.51% Zn, 2.91% Pb
-----------           ------------- ---------       ------------------

Viburnum
Trend, USA           Producing     215.91 Mt4      0.93% Zn, 6.47% Pb
-----------           ---------     ----------      ------------------
Rathdowney's drilling in 2014-2015 has been focused in the vicinity of
Zone 5, one of several zones that comprise the current mineral resource.
Todays' results are from 15 new holes (OLZ-256 to OLZ-270), each of which was
drilled outside of the resource-area at Zone 5 as shown on the map at
http://www.rathdowneyresources.com/i/pdf/rdr/OLZA_MAP__NR_Dec_15.pdf . Eleven
of the 15 new holes include significant mineralization, detailed in the Table
of Assay Results attached to this release. Highlights include:
<<

--  7.0 m of 6.5% Zn+Pb and 30.6 g/t Ag, including 2.2 m of 17.4% Zn+Pb and
54.2 g/t Ag in hole OLZ-256
--  7.3 m of 6.4% Zn+Pb and 10.7 g/t Ag, including 4.9 m of 8.5% Zn+Pb and
14.7 g/t Ag and 2.7 m of 13.1% Zn+Pb and 25.2 g/t Ag in hole OLZ-261
>>
This is the third tranche of holes from the 2014-2015 program (also see
Rathdowney News Releases dated September 22, 2015 and June 23, 2015) which,
collectively, are demonstrating good continuity in the mineralization to the
northwest and northeast of Zone 5. The results clearly underline the potential
for expansion of Zone 5 and highlight the excellent prospects for further
resource increases across the Project Olza concessions with additional
drilling.
Key geotechnical data was also collected from each drill hole for
engineering studies to assess the suitability of the Zone 5 area for
development of site facilities. Concurrently, hydrogeological studies and
environmental data collection programs are being conducted over an extensive
area to fully assess and consider the existing conditions in the broader
region. In combination with the geotechnical data from drilling, these studies
will provide the details to support site specifications for mine development,
water management and other important planning activities to be used in project
permitting for a modern, long-life mine.
Prime location with existing low-cost infrastructure
In addition to its geological potential, Project Olza has a number of
advantages when compared to many other emerging Zn-Pb mine development
projects. Mining has taken place in the Upper Silesian district since the 12th
century, and as a result, there is extensive infrastructure, including power
and rail already in place as well as a skilled local workforce. Situated in
the heart of Europe, the existing rail infrastructure provides Project Olza
with direct, low-cost access to ports and smelters.
These advantages are reflected in the results from the Preliminary
Economic Assessment ("PEA") announced earlier this year. The Project Olza PEA
shows strong potential financial returns for a conventional 6,000 tonnes per
day bulk room and pillar mine with standard on-site processing yielding two
marketable low iron zinc and lead concentrates5. Project Olza would be a
low-cost producer of an average of 197 million pounds of zinc and 59 million
pounds of lead, annually, readily available to markets in Europe and
throughout the world.
President and CEO Robert Konski said:
"Our drilling continues to demonstrate the excellent resource potential
at Project Olza, building on the PEA and providing a strong foundation for
comprehensive mine planning studies. Project Olza's central location in a
stable region with a long mining history is a key advantage to our project,
further enhancing its technical merits. We look forward to continuing our work
with the communities and the government, and advancing toward a modern
long-life mining operation in Poland."
About Rathdowney and Project Olza
Rathdowney Resources Ltd. is focused on advancing Project Olza through
permitting and into production. Project Olza is located in the Upper Silesian
Mining District of southwestern Poland, a world-class region of Mississippi
Valley-type deposits with well-developed mining infrastructure. Easily
accessible by road, the Olza project site is a one-hour drive from Krakow, a
major city with full services, including an international airport. The
deposits at Olza are 25 km from the ZGH zinc smelter at Boleslaw. A railway
line runs through the Olza project-area, linking it to smelters throughout
Europe and to ports on the Baltic Sea.
Rathdowney is committed to responsible mineral exploration and
development with respectful, mutually beneficial discussions and opportunities
for local communities. Our Project Olza community specialists discuss our
programs with representatives of local communities and government during all
phases of work, and are currently in discussions with community members and
others regarding the results of the PEA and other programs.
Dr. Keith Roberts, PGeo, is the qualified person for the drilling program
at Project Olza and has reviewed the drilling information in this release.
Other technical information has been reviewed by David Copeland, PEng, a
qualified person who is also Chairman and a Director of Rathdowney.
On behalf of the Board of DirectorsRobert KonskiPresident & CEO
Notes:1 Sangster, D.F., USGS, 1990, Mississippi Valley-Type and Sedex
lead-zinc deposits: A comparative examination: Transactions of the Institution
of Mining and Metallurgy, sec. B, v. 99, p. B21-B42.2 Individual grades are
5.53% Zn and 1.49% Pb. For further information see Rathdowney's new release
dated February 2, 2015. Mineral resources that are not mineral reserves do not
have demonstrated economic viability.3 Production + remaining reserves at
2010; www.geoportal.pl 4 Leach, David L. et al, USGS, 2010, A Deposit Model
for Mississippi Valley Type Lead-Zinc Ores, Chapter A, Mineral Resource
Deposit Models; Production + remaining resources at 2005.5 For additional
details on the PEA, see Rathdowney's news releases dated April 20, 2015 and
May 14, 2015.
Notes 1, 3, and 4 are associated with deposits that are not on the Olza
property. They are mainly reported production and derived from government
sources. They are historical in nature (see dates stated) and the work
necessary to verify them has not been undertaken by a qualified person.
Table of Assay Results
Drill Hole                   From             To        Length       
Pb+Zn         Zn         Pb         Ag

Number                      (m)             (m)         (m)         (%)        
(%)        (%)      (g/t)
------                      ---            ---         ---          ---         
---         ---       -----

OLZ-256                                                104.20       
111.15          6.95         6.54        6.33        0.21    30.6
-------                                                ------       
------          ----         ----        ----        ----    ----

Incl                  107.05       109.28          2.23        17.39       
17.02        0.37    54.2
----                  ------       ------          ----        -----       
-----        ----    ----

OLZ-258                                             102.80       
105.80          3.00         3.77        1.33        2.44    11.0
-------                                             ------       
------          ----         ----        ----        ----    ----

Incl                  103.40       105.50          2.10         4.80        
1.47        3.33    13.3
----                  ------       ------          ----         ----        
----        ----    ----

OLZ-259                                              99.50       
100.50          1.00         3.34        3.29        0.05     6.8
-------                                              -----       
------          ----         ----        ----        ----     ---

OLZ-260                                             126.85       
136.40          9.55         0.86        0.45        0.41     3.1
-------                                             ------       
------          ----         ----        ----        ----     ---

Incl                  132.85       134.40          1.55         1.67        
1.06        0.61    10.2
----                  ------       ------          ----         ----        
----        ----    ----

OLZ-261                                             147.00       
154.26          7.26         6.41        6.01        0.40    10.7
-------                                             ------       
------          ----         ----        ----        ----    ----

Incl                  149.35       154.26          4.91         8.52        
8.00        0.52    14.7
----                  ------       ------          ----         ----        
----        ----    ----

And                   151.61       154.26          2.65        13.05       
13.04        0.01    25.2
---                   ------       ------          ----        -----       
-----        ----    ----

OLZ-262                                             154.00       
160.00          6.00         1.64        1.42        0.22     2.0
-------                                             ------       
------          ----         ----        ----        ----     ---

Incl                  155.60       157.40          1.80         2.90        
2.78        0.12     3.3
----                  ------       ------          ----         ----        
----        ----     ---

OLZ-265                                             119.90       
120.70          0.80         6.51        6.50        0.01    60.1
-------                                             ------       
------          ----         ----        ----        ----    ----

OLZ-266                                             158.00       
159.95          1.95         5.79        5.16        0.63    18.1
-------                                             ------       
------          ----         ----        ----        ----    ----

OLZ-267                                             147.00       
152.60          5.60         1.57        1.24        0.33     0.9
-------                                             ------       
------          ----         ----        ----        ----     ---

158.40       162.20          3.80         1.80        1.78        0.02     2.4
------       ------          ----         ----        ----        ----     ---

Incl                  161.00       162.20          1.20         3.23        
3.23       0.003     4.9
----                  ------       ------          ----         ----        
----       -----     ---

OLZ-268                                             158.60       
160.10          1.50         2.20        2.08        0.12     4.3
-------                                             ------       
------          ----         ----        ----        ----     ---

OLZ-270                                             157.00       
160.20          3.20         1.90        1.27        0.63     2.3
-------                                             ------       
------          ----         ----        ----        ----     ---

Incl                  158.80       159.25          0.45         8.32        
4.08        4.24    13.9
----                  ------       ------          ----         ----        
----        ----    ----

All diamond core holes were drilled vertically through the sub-horizontal 
mineralized horizons so

intersections represent approximate true widths. No significant results in 
holes 257, 263, 264

and 269. (x)Figures may not add due to rounding.
----------------------------------------------

Sample preparation for the current drilling
program is performed at the Bureau Veritas
(BV) laboratory in Krakow, Poland. Core
samples are weighed, dried and crushed to
>70% passing 10 mesh (2 mm), then 500 g sub-
samples are riffle split and pulverized to
>85% passing 200 mesh (75 µm).  Samples are
shipped by air freight to the Vancouver
laboratory of Bureau Veritas Commodities
Canada Ltd., an ISO 9001 accredited
laboratory, for analysis. All samples are
assayed for Pb, Zn, Ag and 38 additional
elements by 4 acid (HF-HNO3-HClO4, HCl)digestion of an 0.5 g sample with an ICP-
AES/ICP-MS (inductively coupled atomic
emission spectrometry/mass spectrometry)
finish (BV Code: MA270). Samples with Zn
values >40% or Pb values >10%, the upper
limits for the MA270 method, are re-
analyzed by BV method MA371; 4 acid
digestion of 0.1 g sample with ICP-AES
finish. As part of a comprehensive QAQC
program, one standard and one replicate are
inserted into the sample stream in each
group of 20 samples, as well as one or more
blanks in each analytical batch.
---------------------------------------------
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
This release includes certain statements that may be deemed
"forward-looking statements". All statements in this release, other than
statements of historical facts, that address exploration drilling,
exploitation activities and events or developments that the Company expects,
are forward looking statements. Although the Company believes the expectations
expressed in such forward-looking statements are based on reasonable
assumptions, such statements are not guarantees of future performance and
actual results or developments may differ materially from those in the
forward-looking statements. Assumptions used by the Company to develop
forward-looking statements include the following: the Olza project will obtain
all required environmental and other permits and all land use and other
licenses, studies and development of the Olza project will continue to be
positive, and no geological or technical problems will occur. Factors that
could cause actual results to differ materially from those in forward-looking
statements include market prices, exploitation and exploration successes,
continuity of mineralization, potential environmental issues and liabilities
associated with exploration, development and mining activities, uncertainties
related to the ability to obtain necessary permits, licenses and title and
delays due to third party opposition, changes in government policies regarding
mining and natural resource exploration and exploitation, continued
availability of capital and financing, and general economic, market or
business conditions. Investors are cautioned that any such statements are not
guarantees of future performance and actual results or developments may differ
materially from those projected in the forward-looking statements. For more
information on the Company, investors should review the Company's continuous
disclosure filings that are available at www.sedar.com.
Information Concerning Estimates of Inferred Resources
This news release uses the term "inferred mineral resources". Rathdowney
Resources Ltd. advises investors that although these terms are recognized and
required by Canadian regulations (under National Instrument 43-101 Standards
of Disclosure for Mineral Projects), the U.S. Securities and Exchange
Commission does not recognize them. Investors are cautioned not to assume that
any part or all of the mineral deposits in these categories will ever be
converted into reserves. In addition, "inferred resources" have a great amount
of uncertainty as to their existence, and economic and legal feasibility. It
cannot be assumed that all or any part of an Inferred Mineral Resource will
ever be upgraded to a higher category. Under Canadian rules, estimates of
Inferred Mineral Resources may not form the basis of feasibility or
pre-feasibility studies, or economic studies except for Preliminary Economic
Assessment as defined under 43-101. Investors are cautioned not to assume that
part or all of an inferred resource exists, or is economically or legally
mineable.
SOURCE Rathdowney Resources Ltd.



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/December2015/03/c8821.html

-0-                           12/03/2015
/For further information: For further details, visit the Company website
www.rathdowneyresources.com or contact Susie Bell, Investor Relations Tel
604-684-6365 or Toll free (NA): 1-800-667-2114/
/Web Site: www.rathdowneyresources.com /
(RTH.)

CO:  Rathdowney Resources Ltd.
ST:  British Columbia
IN:  MNG
SU:  ERP

-30-