Source	Marketwire
Date	12/07/2015
Time	12:59:10 PM

Company	 MUNDORO CAPITAL INC.
Title	Mundoro Announces Results From Drilling Program on Serbian Properties





    CDNX Symbol: MUN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Mundoro Capital Inc.

TSX VENTURE SYMBOL: MUN

December 7, 2015

Mundoro Announces Results From Drilling Program on Serbian Properties


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Dec. 7, 2015) - Mundoro Capital 
Inc. (TSX VENTURE:MUN) (www.mundoro.com) ("Mundoro" or the "Company") reports 
First Quantum Minerals has completed 5,369 meters of drilling on four of the 
Company's 100%-owned exploration licenses: Savinac, Sumrakovac, Bacevica and 
Osnic (the "Southern Timok Properties") which are located at the southern end 
of the Timok Magmatic Complex ("TMC") in northeastern Serbia (see Location Map 
of Drilling). Drilling commenced in July 2015 under the Option Agreement 
("Option Agreement") between Mundoro and FQM. FQM has completed more than the 
minimum 5,000 meters of drilling required by the October 30, 2015 deadline 
under the Option Agreement. FQM can provide written notice to Mundoro by 
December 15, 2015 should it wish to enter into a joint venture for the Southern 
Timok Properties.

Teo Dechev, CEO and President highlighted, "This drilling program, which was 
solely funded by FQM, aimed to test various mineralized systems over an area of 
over 400 sq.km. The drilling identified large areas of zoned hydrothermal 
alteration, intersected new mineralized zones and added valuable geological, 
structural and geochemical information. The drilling and geophysics work 
conducted by FQM has met all of Mundoro's property commitments on the Southern 
Timok Properties until 2016 and has demonstrated merit for further exploration 
work on these, and newly identified targets."

Summary of FQM Drill Holes

Both diamond core drilling (DD) and reverse circulation drilling (RC) methods 
were used in this program. RC drilling was used as the faster method, to sample 
the shallower targets while diamond core tails were used to extend holes in 
difficult ground conditions. A summary table of the holes drilled on each 
property is shown below:

/T/


----------------------------------------------------------------------------
Project                       TABLE A: FQM DRILLING SUMMARY
---------------------------------------------------------------
Total No.
No. of        RC        No.        DD      of DD     Total
RC holes       (m)   of holes       (m)      holes       (m)
----------------------------------------------------------------------------
Sumrakovac             6     609.0          6   1,897.4         12   2,506.4
----------------------------------------------------------------------------
Savinac                0         -          4    1606.8          4    1606.8
----------------------------------------------------------------------------
Bacevica               4     755.0          0         -          4     755.0
----------------------------------------------------------------------------
Osnic                  3     501.0          0         -          3     501.0
----------------------------------------------------------------------------
Total         13   1,865.0         10   3,504.2         23   5,369.2
----------------------------------------------------------------------------


---------------------------------------------------------------------------
TABLE B: FQM DRILL HOLE DESCRIPTION
---------------------------------------------------------------------------
Azimuth    Inclination          Depth
Project                Hole ID    ( degrees )    ( degrees )            (m)
---------------------------------------------------------------------------
Sumrakovac             STRC001            235            -75          161.0
---------------------------------------------------------------------------
Sumrakovac             STRC002            235            -75           59.0
---------------------------------------------------------------------------
Sumrakovac             STRC003             55            -65           83.0
---------------------------------------------------------------------------
Sumrakovac             STRC004             55            -75          110.0
---------------------------------------------------------------------------
Sumrakovac             STRC005             55            -75          113.0
---------------------------------------------------------------------------
Sumrakovac             STRD005             55            -75          288.9
---------------------------------------------------------------------------
Sumrakovac             STRC006            235            -75           83.0
---------------------------------------------------------------------------
Sumrakovac             STDD002             65            -65          389.7
---------------------------------------------------------------------------
Sumrakovac             STDD003            238            -65          312.0
---------------------------------------------------------------------------
Sumrakovac             STDD004             55            -65          384.0
---------------------------------------------------------------------------
Sumrakovac             STDD007             45            -70          401.8
---------------------------------------------------------------------------
Sumrakovac             STDD008             45            -70         121.00
---------------------------------------------------------------------------
Savinac                STDD001            270            -75          638.6
---------------------------------------------------------------------------
Savinac                STDD005            270            -75          290.9
---------------------------------------------------------------------------
Savinac                STDD006             70            -65          200.8
---------------------------------------------------------------------------
Savinac                STDD009             60            -75         476.50
---------------------------------------------------------------------------
Bacevica               STRC007             45            -75             62
---------------------------------------------------------------------------
Bacevica               STRC008             45            -75            251
---------------------------------------------------------------------------
Bacevica               STRC009             45            -75            191
---------------------------------------------------------------------------
Bacevica               STRC010             55            -60            251
---------------------------------------------------------------------------
Osnic                  STRC011            266            -75            179
---------------------------------------------------------------------------
Osnic                  STRC012            360            -90            161
---------------------------------------------------------------------------
Osnic                  STRC013            360            -90            161
---------------------------------------------------------------------------


/T/

The Sumrakovac license:

The aim of this first phase drilling was to test for near surface porphyry 
style mineralization associated with the outcropping Skorusa stockwork and 
K-silicate alteration. A total of twelve drill holes (2,506 m) were drilled on 
the Sumrakovac license to test three targets located within a 3 sq.km area of 
hydrothermally altered volcanics.

Skorusa Highlights

Current drilling supports that mineralization found in the outcropping Skorusa 
stockwork extends from intersections in both historical and current drill 
holes. The Company believes the combination of: (i) alteration assemblages 
(phyllic overprinting potassic), (ii) A-B type veining, hydrothermal magnetite 
veining, quartz-molybdenite veining, and (iii) stockwork and disseminated 
chalcopyrite mineralization intersected in STDD002 and STD007, is, indicative 
of proximity to several mineralized porphyry centers.

Drilling also supports the existence of a large porphyry related alteration 
system with at least two mineralized centers (Skorusa and Skorusa East). 
Potential for mineralization at depth remains untested. Alternating weak 
potassic alteration (found as halos around vein contacts) with propylitic 
alteration, suggests the periphery of a system. Based on this campaign, the 
Company believes that the Sumrakovac license has strong potential to host large 
porphyry systems.

Skorusa target

Drill holes STDD002, STDD003, STDD004, holes STRC001, STRC002, STRC003 drilled 
to test the Skorusa area by targeting the outcropping porphyry mineralization 
and the concomitant molybdenum anomaly SE of it.

/T/

--  STDD002 was collared 270m SW of the outcropping stockwork mineralization
intending to validate encouraging results from surface sampling and
historical drill hole as well as to verify the orientation of the
mineralized zone.
--  Several types of quartz sulphide veining including quartz sulphide
stockwork veins were observed. Veins containing chalcopyrite occur at a
consistent but low vein frequency. A zone of well-developed stockwork
veining occurs at, and below, the footwall contact between monzo-diorite
and andesite units, which returned a composite assay interval of 36m @
0.19% Cu and 0.21 g/t Au.
--  Drill results are consistent with outcropping stockwork veining (23m @
0.17% Cu; 0.72 g/t Au) and historical results. This drilling highlights
a 210m long mineralized section requiring follow-up drilling.
--  Holes STDD003, STDD004, STRC001, STRC002, and STRC003 were designed to
test the greater than 10 ppm Mo anomaly that extends over 1 km to the SE
from the outcropping stockwork in Skorusa Creek.
--  STDD004 includes several intervals of phyllic after potassic
assemblages. Although assays yielded only anomalous Cu-Mo, these initial
drill holes support the continuation of the Skorusa porphyry alteration
towards the south and the existence of extensive potassic alteration.

/T/

Skorusa North target

Two holes were drilled at the Skorusa North target, which is interpreted as the 
continuation of the Skorusa porphyry system to north.

/T/

--  STDD007 was collared 750m north-east of STDD002 in strong phillic
altered andesite volcanics and volcanoclastics down to 41.40m, followed
by an overprinted potassic-altered andesite containing pyrite-
chalcopyrite down to 123.5m, followed by weak potassic alteration
characterized by quartz-chalcopyrite veinlets with K-spar halo, biotite
and epidote overprinted by sericite-pyrite-chlorite (phyllic)
alteration. While visible chalcopyrite is present throughout as both
disseminations and veinlets, the tenor of Cu mineralization remains
anomalous at up to 0.1% Cu.
--  STDD008 (121m) was collared in quartz-sericite altered andesite down to
25.9m, followed by propylitic alteration with quartz-pyrite-magnetite
veinlets to 79m, followed by diorite to the end of hole. At several
intervals it intersected quartz-pyrite-Mo veinlets suggesting close
proximity to a mineralized source.

/T/

Skorusa East target

The Skorusa East target was tested by RC drill holes STRC004, STRC005 and 
STRC006 totaling 306m and one DD drill hole, STRD005, totaling 288.9m as 
diamond tail continuation of RC drill hole STRC005 from 113m.

/T/

--  All of these holes intersected hydrothermally altered andesite volcanics
interpreted to be part of larger footprints of a porphyry system. Trace
disseminated chalcopyrite and quartz-chalcopyrite-pyrite B-veins were
encountered throughout the STRD005 drillhole suggesting existence of a
different mineralized center to the east.


Table 1: Highlights of Drilling Results from Sumrakovac

--------------------------------------------------------------------------
Drill             From      To    Interval      Cu      Au    CuEq    AuEq
Hole ID            (m)     (m)         (m)     (%)   (g/t)     (%)   (g/t)
--------------------------------------------------------------------------
STDD002            289     325          36    0.19    0.21    0.35    0.46
--------------------------------------------------------------------------
Including          313     321           8    0.30    0.43    0.62    0.83
--------------------------------------------------------------------------
STRD005            259     261           2    0.11    0.11    0.26    0.19
--------------------------------------------------------------------------
STDD007            124     126           2    0.12    0.03    0.14    0.19
------------------------------------------------------------
152     154           2    0.11    0.03    0.13    0.18
------------------------------------------------------------
166     170           4    0.10    0.03    0.12    0.16
--------------------------------------------------------------------------

Gold Equivalent ("AuEq.") is calculated using the formula AuEq =
(g/t/Au)+((%Cu) x (22.0462) x ($/lbCu)) / ((1/31.1035) x ($/ozAu)). Copper
equivalent (CuEq%) is calculated using the formula CuEq = (%Cu) +
((g/t/AuEq) x (1/31.1035) x ($/ozAu)) / ((22.0462) x ($/lbCu)). Metal prices
used are: gold price of US$1100/oz, copper price of US$2.13/lb. All
thicknesses from intersections from drill holes are down-hole drilled
thicknesses or outcrop sample length thickness. True widths cannot be
determined from the information available.


/T/

The Savinac license:

Savinac North target was tested with three diamond drill holes totaling 1606.8m.

Savinac North target

Drilling at Savinac North confirmed large volumes of hydrothermally altered 
andesite volcanics ranging between argillic, phillic, and propylitic 
assemblages, and validates a zoned hydrothermal system with potential for 
discovery of epithermal and porphyry style mineralization.

/T/

--  Several anomalous Au-Ag and Cu-Au intervals intersected throughout the
entire length of drill hole STDD001 (see Table 2: Highlights of Drilling
Results from Savinac), as well as the historical results, clearly
suggest it is a mineralized system of high sulphidation affinity.  --  STDD001 
was collared in a Mo anomaly high coincident with a discrete
halo of proximal phyllic alteration. The hole intersected a thick
phyllic alteration zone in andesites and andesitic breccias. ASD results
demonstrate there is no advanced argillic alteration in the hole
validating the initial interpretation of a degraded lithocap.
--  The alteration in STDD001 grades from pervasive intense phyllic, to an
intermediate argillic assemblage cut by occasional D-like pyrite veins
with discrete bleached haloes. A faulted domain intersected between 160
and 200m includes chalcopyrite-bearing sulfide-rich veins that are
consistent with the deeper parts of many porphyry systems.
--  STDD005 and STDD006 intersected strongly argillic altered andesite and
tuff breccia at upper levels transitioning to propylitic alteration at
depth and containing consistent 2-3% amounts of pyrite throughout.
--  Further work is warranted to explore within the large footprint marked
by several lithocaps.

/T/

Markov Kamen North target

Markov Kamen was tested with one drill hole, STDD009 (476.5m), which was 
collared in strongly phyllic-argillic altered andesite volcanics.

/T/

--  This target was highlighted by strong molybdenum (+Au-Ag-As-Sb) soil
anomalism. Hydrothermal breccia with a sulphide matrix (pyrite + black
sulphides) and rounded silicified and/or phyllic-argillic altered clasts
is pervasive throughout the entire length of hole.
--  Late polymetallic quartz-galena-sphalerite veins were intersected at
91.2m and 132.3m. A zone of silicification, vuggy silica with massive to
semi-massive sulphides (mainly pyrite), and hydrothermal breccia layers
with a sulphide matrix extends from 208.10m to the EOH.
--  Visible copper mineralization was intersected as trace chalcopyrite from
441.5m to approx. 459.60m (18.1m). Due to technical problems the drill
hole terminated at 476.5m depth while still in sulphide bearing breccia.
--  Significant hydrothermal breccia, massive sulphides and vuggy silica
intersected in STDD009 confirms a high sulphidation style epithermal
system of intermediate level controlled by a NW structure dipping to the
SW. Current results (see Table 2: Highlights of Drilling Results from
Savinac) are encouraging and show anomalous grades and mineralized
intervals at depth.
--  One massive sulphide and vuggy silica interval returned 25m @ 0.54 g/t
Au including single 2m interval assaying up to 2 g/t Au and 0.45 % Cu.

/T/

Tilva Rosh target

Drilling in 2014 at the Tilva Rosh target (3.2km North of STDD009) intersected 
significant Au-Cu mineralization related to the same structural trend (see 
press release from 19 August, 2014). The NW structural trend is highlighted by: 
(i) soil anomalism, (ii) argillic to advanced argillic alteration and (iii) a 
magnetic low anomaly trending for 8.5 km.

/T/


Table 2: Highlights of Drilling Results from Savinac

----------------------------------------------------------------------------
Drill                                      Cu
Hole ID        From     To    Interval    (%)     Au      Ag    CuEq    AuEq
(m)    (m)         (m)         (g/t)   (g/t)     (%)   (g/t)
----------------------------------------------------------------------------
STDD001        60.3     66         5.7          0.14    0.68       -    0.15
----------------------------------------------------------------
86    100          14          0.26    4.20       -    0.33
----------------------------------------------------------------
98    100           2   0.21   0.29    9.68    0.55    0.73
----------------------------------------------------------------
176    178           2   0.22    0.5    7.12    0.69    0.91
----------------------------------------------------------------
214    216           2   0.25   0.18    2.22    0.42    0.55
----------------------------------------------------------------
580    582           2   0.23      -       -    0.23
----------------------------------------------------------------------------
STDD006          44     46           2          0.62    0.48            0.63
----------------------------------------------------------------------------
134    136           2           0.2     3.0            0.25
----------------------------------------------------------------------------
160    162           2           1.1     1.1            1.12
----------------------------------------------------------------------------
STDD009          90    104          14      -   0.36     2.5       -    0.40
----------------------------------------------------------------
128    136           8      -   0.13     9.4       -    0.29
----------------------------------------------------------------
188    192           4      -   0.21    12.2       -    0.41
----------------------------------------------------------------
274    276           2   0.29   0.15    1.58    0.43    0.57
----------------------------------------------------------------
320    345          25      -   0.54    3.65       -    0.60
----------------------------------------------------------------
Including   324.5    327         2.5   0.45   0.29   14.45    0.85    1.13
----------------------------------------------------------------
Including     333    341           8      -   1.04    3.78       -    1.10
----------------------------------------------------------------------------

Gold Equivalent ("AuEq.") is calculated using the formula AuEq =
(g/t/Au)+((%Cu) x (22.0462) x ($/lbCu)) / ((1/31.1035) x ($/ozAu)). Copper
equivalent (CuEq%) is calculated using the formula CuEq = (%Cu) +
((g/t/AuEq) x (1/31.1035) x ($/ozAu)) / ((22.0462) x ($/lbCu)). Metal prices
used are: gold price of US$1100/oz, copper price of US$2.13/lb. All
thicknesses from intersections from drill holes are down-hole drilled
thicknesses or outcrop sample length thickness. True widths cannot be
determined from the information available.


/T/

The Bacevica and Osnic licenses:

Four RC holes have been drilled at Bacevica totaling 755m and three in Osnic 
totaling 501m. Although no reportable assayed intervals were received the 
information collected will add to the overall interpretation of the South Timok 
Properties as well as to the ongoing exploration at both of these licenses.

Sampling, Analysis and Qualified Person

Drillhole orientations were surveyed at approximately 50 meters intervals. 
Drill core was collected from drill sites by the FQM geologists and processed 
and sampled at the Company's core shed according to industry best practice 
standard procedures. Samples were collected as 1/4 PQ or HQ core at two meters 
length intervals. Oriented core with high confidence was marked with solid red 
line and regular measurements collected.

RC drill samples were collected at 1.0m sample intervals. Approximately 30.0 kg 
of material (dust and rock chips) is collected in a cyclone from 1m interval. 
The sample is run through splitter where 1/8 (approx. 3.0-4.0kg) of material is 
collected as a representative of 1.0m sample interval which is sent to the lab. 
For logging and future additional analyses, rock chips from each meter are 
collected and stored in rock chip trays.

All samples are assayed using 30 gram fire assay with atomic absorption finish 
and ME-MS61 by ALS Romania. The entire sample was crushed to 2mm, then split 
off a 1 kg sample and pulverized the split to better than 85% passing 75 
microns. Quality Assurance and Quality Control procedures include the 
systematic insertion of standards and duplicates into the sample streams. 
Duplicate core samples are taken every 20 samples standards are inserted after 
every 33 samples and blanks after every 20th sample. All data collected from 
detailed logging and assay results from the laboratories are routinely verified 
and entered in an Access data base.

Technical information contained in this Press Release has been reviewed and 
approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by National 
Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian based public company which is focused on generating value 
for its shareholders through utilizing the collective expertise of our 
directors, management and technical team to invest in mineral projects that 
have the potential to generate future returns to shareholders.

Caution Concerning Forward-Looking Statements

Information included, attached to or incorporated by reference into this News 
Release may contain forward-looking statements. All statements, other than 
statements of historical fact, included or incorporated by reference in this 
News Release are forward-looking statements, including, without limitation, 
statements regarding FQM's option to notify Mundoro by December 15, 2015 of its 
wishes to enter into a joint venture on the Southern Timok Properties 
activities, events or developments that the Board and/or management expects or 
anticipates may occur in the future. These forward-looking statements can be 
identified by the use of forward-looking words such as "will", "expect", 
"intend", "plan", "estimate", "anticipate", "believe" or "continue" or similar 
words or the negative thereof. The material assumptions that were applied in 
making the forward looking statements in this News Release include expectations 
as to the Company's future strategy and business plan and execution of the 
Company's existing plans. There can be no assurance that the plans, intentions 
or expectations upon which these forward-looking statements are based will 
occur. We caution readers of this News Release not to place undue reliance on 
forward looking statements contained in this News Release, which are not a 
guarantee of performance and are subject to a number of uncertainties and other 
factors that could cause actual results to differ materially from those 
expressed or implied by such forward-looking statements. These factors include 
general economic and market conditions, changes in law, regulatory processes, 
the status of Mundoro's assets and financial condition, actions of competitors 
and the ability to implement business strategies and pursue business 
opportunities. The forward-looking statements contained in this News Release 
are expressly qualified in their entirety by this cautionary statement. The 
forward-looking statements included in this News Release are made as of the 
date of this News Release and the Board undertakes no obligation to publicly 
update such forward-looking statements to reflect new information, subsequent 
events or otherwise, except as required by law. Shareholders are cautioned that 
all forward-looking statements involve risks and uncertainties and for a more 
detailed discussion of such risks and other factors that could cause actual 
results to differ materially from those expressed or implied by such 
forward-looking statements, refer to the Company's filings with the Canadian 
securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Mundoro Capital Inc.
Teo Dechev
CEO
+1-604-669-8055x101

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=551568290


NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Mundoro Capital Inc.

TSX VENTURE SYMBOL: MUN

December 7, 2015

Mundoro Announces Results From Drilling Program on Serbian Properties


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Dec. 7, 2015) - Mundoro Capital 
Inc. (TSX VENTURE:MUN) (www.mundoro.com) ("Mundoro" or the "Company") reports 
First Quantum Minerals has completed 5,369 meters of drilling on four of the 
Company's 100%-owned exploration licenses: Savinac, Sumrakovac, Bacevica and 
Osnic (the "Southern Timok Properties") which are located at the southern end 
of the Timok Magmatic Complex ("TMC") in northeastern Serbia (see Location Map 
of Drilling). Drilling commenced in July 2015 under the Option Agreement 
("Option Agreement") between Mundoro and FQM. FQM has completed more than the 
minimum 5,000 meters of drilling required by the October 30, 2015 deadline 
under the Option Agreement. FQM can provide written notice to Mundoro by 
December 15, 2015 should it wish to enter into a joint venture for the Southern 
Timok Properties.

Teo Dechev, CEO and President highlighted, "This drilling program, which was 
solely funded by FQM, aimed to test various mineralized systems over an area of 
over 400 sq.km. The drilling identified large areas of zoned hydrothermal 
alteration, intersected new mineralized zones and added valuable geological, 
structural and geochemical information. The drilling and geophysics work 
conducted by FQM has met all of Mundoro's property commitments on the Southern 
Timok Properties until 2016 and has demonstrated merit for further exploration 
work on these, and newly identified targets."

Summary of FQM Drill Holes

Both diamond core drilling (DD) and reverse circulation drilling (RC) methods 
were used in this program. RC drilling was used as the faster method, to sample 
the shallower targets while diamond core tails were used to extend holes in 
difficult ground conditions. A summary table of the holes drilled on each 
property is shown below:

/T/


----------------------------------------------------------------------------
Project                       TABLE A: FQM DRILLING SUMMARY
---------------------------------------------------------------
Total No.
No. of        RC        No.        DD      of DD     Total
RC holes       (m)   of holes       (m)      holes       (m)
----------------------------------------------------------------------------
Sumrakovac             6     609.0          6   1,897.4         12   2,506.4
----------------------------------------------------------------------------
Savinac                0         -          4    1606.8          4    1606.8
----------------------------------------------------------------------------
Bacevica               4     755.0          0         -          4     755.0
----------------------------------------------------------------------------
Osnic                  3     501.0          0         -          3     501.0
----------------------------------------------------------------------------
Total         13   1,865.0         10   3,504.2         23   5,369.2
----------------------------------------------------------------------------


---------------------------------------------------------------------------
TABLE B: FQM DRILL HOLE DESCRIPTION
---------------------------------------------------------------------------
Azimuth    Inclination          Depth
Project                Hole ID    ( degrees )    ( degrees )            (m)
---------------------------------------------------------------------------
Sumrakovac             STRC001            235            -75          161.0
---------------------------------------------------------------------------
Sumrakovac             STRC002            235            -75           59.0
---------------------------------------------------------------------------
Sumrakovac             STRC003             55            -65           83.0
---------------------------------------------------------------------------
Sumrakovac             STRC004             55            -75          110.0
---------------------------------------------------------------------------
Sumrakovac             STRC005             55            -75          113.0
---------------------------------------------------------------------------
Sumrakovac             STRD005             55            -75          288.9
---------------------------------------------------------------------------
Sumrakovac             STRC006            235            -75           83.0
---------------------------------------------------------------------------
Sumrakovac             STDD002             65            -65          389.7
---------------------------------------------------------------------------
Sumrakovac             STDD003            238            -65          312.0
---------------------------------------------------------------------------
Sumrakovac             STDD004             55            -65          384.0
---------------------------------------------------------------------------
Sumrakovac             STDD007             45            -70          401.8
---------------------------------------------------------------------------
Sumrakovac             STDD008             45            -70         121.00
---------------------------------------------------------------------------
Savinac                STDD001            270            -75          638.6
---------------------------------------------------------------------------
Savinac                STDD005            270            -75          290.9
---------------------------------------------------------------------------
Savinac                STDD006             70            -65          200.8
---------------------------------------------------------------------------
Savinac                STDD009             60            -75         476.50
---------------------------------------------------------------------------
Bacevica               STRC007             45            -75             62
---------------------------------------------------------------------------
Bacevica               STRC008             45            -75            251
---------------------------------------------------------------------------
Bacevica               STRC009             45            -75            191
---------------------------------------------------------------------------
Bacevica               STRC010             55            -60            251
---------------------------------------------------------------------------
Osnic                  STRC011            266            -75            179
---------------------------------------------------------------------------
Osnic                  STRC012            360            -90            161
---------------------------------------------------------------------------
Osnic                  STRC013            360            -90            161
---------------------------------------------------------------------------


/T/

The Sumrakovac license:

The aim of this first phase drilling was to test for near surface porphyry 
style mineralization associated with the outcropping Skorusa stockwork and 
K-silicate alteration. A total of twelve drill holes (2,506 m) were drilled on 
the Sumrakovac license to test three targets located within a 3 sq.km area of 
hydrothermally altered volcanics.

Skorusa Highlights

Current drilling supports that mineralization found in the outcropping Skorusa 
stockwork extends from intersections in both historical and current drill 
holes. The Company believes the combination of: (i) alteration assemblages 
(phyllic overprinting potassic), (ii) A-B type veining, hydrothermal magnetite 
veining, quartz-molybdenite veining, and (iii) stockwork and disseminated 
chalcopyrite mineralization intersected in STDD002 and STD007, is, indicative 
of proximity to several mineralized porphyry centers.

Drilling also supports the existence of a large porphyry related alteration 
system with at least two mineralized centers (Skorusa and Skorusa East). 
Potential for mineralization at depth remains untested. Alternating weak 
potassic alteration (found as halos around vein contacts) with propylitic 
alteration, suggests the periphery of a system. Based on this campaign, the 
Company believes that the Sumrakovac license has strong potential to host large 
porphyry systems.

Skorusa target

Drill holes STDD002, STDD003, STDD004, holes STRC001, STRC002, STRC003 drilled 
to test the Skorusa area by targeting the outcropping porphyry mineralization 
and the concomitant molybdenum anomaly SE of it.

/T/

--  STDD002 was collared 270m SW of the outcropping stockwork mineralization
intending to validate encouraging results from surface sampling and
historical drill hole as well as to verify the orientation of the
mineralized zone.
--  Several types of quartz sulphide veining including quartz sulphide
stockwork veins were observed. Veins containing chalcopyrite occur at a
consistent but low vein frequency. A zone of well-developed stockwork
veining occurs at, and below, the footwall contact between monzo-diorite
and andesite units, which returned a composite assay interval of 36m @
0.19% Cu and 0.21 g/t Au.
--  Drill results are consistent with outcropping stockwork veining (23m @
0.17% Cu; 0.72 g/t Au) and historical results. This drilling highlights
a 210m long mineralized section requiring follow-up drilling.
--  Holes STDD003, STDD004, STRC001, STRC002, and STRC003 were designed to
test the greater than 10 ppm Mo anomaly that extends over 1 km to the SE
from the outcropping stockwork in Skorusa Creek.
--  STDD004 includes several intervals of phyllic after potassic
assemblages. Although assays yielded only anomalous Cu-Mo, these initial
drill holes support the continuation of the Skorusa porphyry alteration
towards the south and the existence of extensive potassic alteration.

/T/

Skorusa North target

Two holes were drilled at the Skorusa North target, which is interpreted as the 
continuation of the Skorusa porphyry system to north.

/T/

--  STDD007 was collared 750m north-east of STDD002 in strong phillic
altered andesite volcanics and volcanoclastics down to 41.40m, followed
by an overprinted potassic-altered andesite containing pyrite-
chalcopyrite down to 123.5m, followed by weak potassic alteration
characterized by quartz-chalcopyrite veinlets with K-spar halo, biotite
and epidote overprinted by sericite-pyrite-chlorite (phyllic)
alteration. While visible chalcopyrite is present throughout as both
disseminations and veinlets, the tenor of Cu mineralization remains
anomalous at up to 0.1% Cu.
--  STDD008 (121m) was collared in quartz-sericite altered andesite down to
25.9m, followed by propylitic alteration with quartz-pyrite-magnetite
veinlets to 79m, followed by diorite to the end of hole. At several
intervals it intersected quartz-pyrite-Mo veinlets suggesting close
proximity to a mineralized source.

/T/

Skorusa East target

The Skorusa East target was tested by RC drill holes STRC004, STRC005 and 
STRC006 totaling 306m and one DD drill hole, STRD005, totaling 288.9m as 
diamond tail continuation of RC drill hole STRC005 from 113m.

/T/

--  All of these holes intersected hydrothermally altered andesite volcanics
interpreted to be part of larger footprints of a porphyry system. Trace
disseminated chalcopyrite and quartz-chalcopyrite-pyrite B-veins were
encountered throughout the STRD005 drillhole suggesting existence of a
different mineralized center to the east.


Table 1: Highlights of Drilling Results from Sumrakovac

--------------------------------------------------------------------------
Drill             From      To    Interval      Cu      Au    CuEq    AuEq
Hole ID            (m)     (m)         (m)     (%)   (g/t)     (%)   (g/t)
--------------------------------------------------------------------------
STDD002            289     325          36    0.19    0.21    0.35    0.46
--------------------------------------------------------------------------
Including          313     321           8    0.30    0.43    0.62    0.83
--------------------------------------------------------------------------
STRD005            259     261           2    0.11    0.11    0.26    0.19
--------------------------------------------------------------------------
STDD007            124     126           2    0.12    0.03    0.14    0.19
------------------------------------------------------------
152     154           2    0.11    0.03    0.13    0.18
------------------------------------------------------------
166     170           4    0.10    0.03    0.12    0.16
--------------------------------------------------------------------------

Gold Equivalent ("AuEq.") is calculated using the formula AuEq =
(g/t/Au)+((%Cu) x (22.0462) x ($/lbCu)) / ((1/31.1035) x ($/ozAu)). Copper
equivalent (CuEq%) is calculated using the formula CuEq = (%Cu) +
((g/t/AuEq) x (1/31.1035) x ($/ozAu)) / ((22.0462) x ($/lbCu)). Metal prices
used are: gold price of US$1100/oz, copper price of US$2.13/lb. All
thicknesses from intersections from drill holes are down-hole drilled
thicknesses or outcrop sample length thickness. True widths cannot be
determined from the information available.


/T/

The Savinac license:

Savinac North target was tested with three diamond drill holes totaling 1606.8m.

Savinac North target

Drilling at Savinac North confirmed large volumes of hydrothermally altered 
andesite volcanics ranging between argillic, phillic, and propylitic 
assemblages, and validates a zoned hydrothermal system with potential for 
discovery of epithermal and porphyry style mineralization.

/T/

--  Several anomalous Au-Ag and Cu-Au intervals intersected throughout the
entire length of drill hole STDD001 (see Table 2: Highlights of Drilling
Results from Savinac), as well as the historical results, clearly
suggest it is a mineralized system of high sulphidation affinity.  --  STDD001 
was collared in a Mo anomaly high coincident with a discrete
halo of proximal phyllic alteration. The hole intersected a thick
phyllic alteration zone in andesites and andesitic breccias. ASD results
demonstrate there is no advanced argillic alteration in the hole
validating the initial interpretation of a degraded lithocap.
--  The alteration in STDD001 grades from pervasive intense phyllic, to an
intermediate argillic assemblage cut by occasional D-like pyrite veins
with discrete bleached haloes. A faulted domain intersected between 160
and 200m includes chalcopyrite-bearing sulfide-rich veins that are
consistent with the deeper parts of many porphyry systems.
--  STDD005 and STDD006 intersected strongly argillic altered andesite and
tuff breccia at upper levels transitioning to propylitic alteration at
depth and containing consistent 2-3% amounts of pyrite throughout.
--  Further work is warranted to explore within the large footprint marked
by several lithocaps.

/T/

Markov Kamen North target

Markov Kamen was tested with one drill hole, STDD009 (476.5m), which was 
collared in strongly phyllic-argillic altered andesite volcanics.

/T/

--  This target was highlighted by strong molybdenum (+Au-Ag-As-Sb) soil
anomalism. Hydrothermal breccia with a sulphide matrix (pyrite + black
sulphides) and rounded silicified and/or phyllic-argillic altered clasts
is pervasive throughout the entire length of hole.
--  Late polymetallic quartz-galena-sphalerite veins were intersected at
91.2m and 132.3m. A zone of silicification, vuggy silica with massive to
semi-massive sulphides (mainly pyrite), and hydrothermal breccia layers
with a sulphide matrix extends from 208.10m to the EOH.
--  Visible copper mineralization was intersected as trace chalcopyrite from
441.5m to approx. 459.60m (18.1m). Due to technical problems the drill
hole terminated at 476.5m depth while still in sulphide bearing breccia.
--  Significant hydrothermal breccia, massive sulphides and vuggy silica
intersected in STDD009 confirms a high sulphidation style epithermal
system of intermediate level controlled by a NW structure dipping to the
SW. Current results (see Table 2: Highlights of Drilling Results from
Savinac) are encouraging and show anomalous grades and mineralized
intervals at depth.
--  One massive sulphide and vuggy silica interval returned 25m @ 0.54 g/t
Au including single 2m interval assaying up to 2 g/t Au and 0.45 % Cu.

/T/

Tilva Rosh target

Drilling in 2014 at the Tilva Rosh target (3.2km North of STDD009) intersected 
significant Au-Cu mineralization related to the same structural trend (see 
press release from 19 August, 2014). The NW structural trend is highlighted by: 
(i) soil anomalism, (ii) argillic to advanced argillic alteration and (iii) a 
magnetic low anomaly trending for 8.5 km.

/T/


Table 2: Highlights of Drilling Results from Savinac

----------------------------------------------------------------------------
Drill                                      Cu
Hole ID        From     To    Interval    (%)     Au      Ag    CuEq    AuEq
(m)    (m)         (m)         (g/t)   (g/t)     (%)   (g/t)
----------------------------------------------------------------------------
STDD001        60.3     66         5.7          0.14    0.68       -    0.15
----------------------------------------------------------------
86    100          14          0.26    4.20       -    0.33
----------------------------------------------------------------
98    100           2   0.21   0.29    9.68    0.55    0.73
----------------------------------------------------------------
176    178           2   0.22    0.5    7.12    0.69    0.91
----------------------------------------------------------------
214    216           2   0.25   0.18    2.22    0.42    0.55
----------------------------------------------------------------
580    582           2   0.23      -       -    0.23
----------------------------------------------------------------------------
STDD006          44     46           2          0.62    0.48            0.63
----------------------------------------------------------------------------
134    136           2           0.2     3.0            0.25
----------------------------------------------------------------------------
160    162           2           1.1     1.1            1.12
----------------------------------------------------------------------------
STDD009          90    104          14      -   0.36     2.5       -    0.40
----------------------------------------------------------------
128    136           8      -   0.13     9.4       -    0.29
----------------------------------------------------------------
188    192           4      -   0.21    12.2       -    0.41
----------------------------------------------------------------
274    276           2   0.29   0.15    1.58    0.43    0.57
----------------------------------------------------------------
320    345          25      -   0.54    3.65       -    0.60
----------------------------------------------------------------
Including   324.5    327         2.5   0.45   0.29   14.45    0.85    1.13
----------------------------------------------------------------
Including     333    341           8      -   1.04    3.78       -    1.10
----------------------------------------------------------------------------

Gold Equivalent ("AuEq.") is calculated using the formula AuEq =
(g/t/Au)+((%Cu) x (22.0462) x ($/lbCu)) / ((1/31.1035) x ($/ozAu)). Copper
equivalent (CuEq%) is calculated using the formula CuEq = (%Cu) +
((g/t/AuEq) x (1/31.1035) x ($/ozAu)) / ((22.0462) x ($/lbCu)). Metal prices
used are: gold price of US$1100/oz, copper price of US$2.13/lb. All
thicknesses from intersections from drill holes are down-hole drilled
thicknesses or outcrop sample length thickness. True widths cannot be
determined from the information available.


/T/

The Bacevica and Osnic licenses:

Four RC holes have been drilled at Bacevica totaling 755m and three in Osnic 
totaling 501m. Although no reportable assayed intervals were received the 
information collected will add to the overall interpretation of the South Timok 
Properties as well as to the ongoing exploration at both of these licenses.

Sampling, Analysis and Qualified Person

Drillhole orientations were surveyed at approximately 50 meters intervals. 
Drill core was collected from drill sites by the FQM geologists and processed 
and sampled at the Company's core shed according to industry best practice 
standard procedures. Samples were collected as 1/4 PQ or HQ core at two meters 
length intervals. Oriented core with high confidence was marked with solid red 
line and regular measurements collected.

RC drill samples were collected at 1.0m sample intervals. Approximately 30.0 kg 
of material (dust and rock chips) is collected in a cyclone from 1m interval. 
The sample is run through splitter where 1/8 (approx. 3.0-4.0kg) of material is 
collected as a representative of 1.0m sample interval which is sent to the lab. 
For logging and future additional analyses, rock chips from each meter are 
collected and stored in rock chip trays.

All samples are assayed using 30 gram fire assay with atomic absorption finish 
and ME-MS61 by ALS Romania. The entire sample was crushed to 2mm, then split 
off a 1 kg sample and pulverized the split to better than 85% passing 75 
microns. Quality Assurance and Quality Control procedures include the 
systematic insertion of standards and duplicates into the sample streams. 
Duplicate core samples are taken every 20 samples standards are inserted after 
every 33 samples and blanks after every 20th sample. All data collected from 
detailed logging and assay results from the laboratories are routinely verified 
and entered in an Access data base.

Technical information contained in this Press Release has been reviewed and 
approved by Mr. G. Magaranov, P. Geo., Qualified Person as defined by National 
Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian based public company which is focused on generating value 
for its shareholders through utilizing the collective expertise of our 
directors, management and technical team to invest in mineral projects that 
have the potential to generate future returns to shareholders.

Caution Concerning Forward-Looking Statements

Information included, attached to or incorporated by reference into this News 
Release may contain forward-looking statements. All statements, other than 
statements of historical fact, included or incorporated by reference in this 
News Release are forward-looking statements, including, without limitation, 
statements regarding FQM's option to notify Mundoro by December 15, 2015 of its 
wishes to enter into a joint venture on the Southern Timok Properties 
activities, events or developments that the Board and/or management expects or 
anticipates may occur in the future. These forward-looking statements can be 
identified by the use of forward-looking words such as "will", "expect", 
"intend", "plan", "estimate", "anticipate", "believe" or "continue" or similar 
words or the negative thereof. The material assumptions that were applied in 
making the forward looking statements in this News Release include expectations 
as to the Company's future strategy and business plan and execution of the 
Company's existing plans. There can be no assurance that the plans, intentions 
or expectations upon which these forward-looking statements are based will 
occur. We caution readers of this News Release not to place undue reliance on 
forward looking statements contained in this News Release, which are not a 
guarantee of performance and are subject to a number of uncertainties and other 
factors that could cause actual results to differ materially from those 
expressed or implied by such forward-looking statements. These factors include 
general economic and market conditions, changes in law, regulatory processes, 
the status of Mundoro's assets and financial condition, actions of competitors 
and the ability to implement business strategies and pursue business 
opportunities. The forward-looking statements contained in this News Release 
are expressly qualified in their entirety by this cautionary statement. The 
forward-looking statements included in this News Release are made as of the 
date of this News Release and the Board undertakes no obligation to publicly 
update such forward-looking statements to reflect new information, subsequent 
events or otherwise, except as required by law. Shareholders are cautioned that 
all forward-looking statements involve risks and uncertainties and for a more 
detailed discussion of such risks and other factors that could cause actual 
results to differ materially from those expressed or implied by such 
forward-looking statements, refer to the Company's filings with the Canadian 
securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Mundoro Capital Inc.
Teo Dechev
CEO
+1-604-669-8055x101

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=551568290