Source	MARKET NEWS
Date	12/07/2015
Time	01:21:49 PM

Company	 Mundoro Capital Inc.
Title	Results 
From Drilling Program On Serbian Propert





    CDNX Symbol: MUN











Press Release	




[200/News Release]MUNVMUNDORO CAPITAL INCDEC 07 2015  13:20 PMResults 
From Drilling Program On Serbian Properties --->@NEWS RELEASE
MUNDORO CAPITAL INC ("MUN-V;MUNMF-0")
- Results From Drilling Program On Serbian Properties

Mundoro Capital Inc. (www.mundoro.com) ("Mundoro" or the "Company")
reports First Quantum Minerals has completed 5,369 meters of drilling
on four of the Company's 100%-owned exploration licenses: Savinac,
Sumrakovac, Bacevica and Osnic (the "Southern Timok Properties") which
are located at the southern end of the Timok Magmatic Complex ("TMC")
in northeastern Serbia (see Location Map of Drilling). Drilling
commenced in July 2015 under the Option Agreement ("Option Agreement")
between Mundoro and FQM. FQM has completed more than the minimum 5,000
meters of drilling required by the October 30, 2015 deadline under the
Option Agreement. FQM can provide written notice to Mundoro by December
15, 2015 should it wish to enter into a joint venture for the Southern
Timok Properties.

Teo Dechev, CEO and President highlighted, "This drilling program,
which was solely funded by FQM, aimed to test various mineralized
systems over an area of over 400 sq.km. The drilling identified large
areas of zoned hydrothermal alteration, intersected new mineralized
zones and added valuable geological, structural and geochemical
information. The drilling and geophysics work conducted by FQM has met
all of Mundoro's property commitments on the Southern Timok Properties
until 2016 and has demonstrated merit for further exploration work on
these, and newly identified targets."

Summary of FQM Drill Holes

Both diamond core drilling (DD) and reverse circulation drilling
(RC) methods were used in this program. RC drilling was used as the
faster method, to sample the shallower targets while diamond core tails
were used to extend holes in difficult ground conditions. A summary
table of the holes drilled on each property is shown below:

//st
---------------------------------------------------------------------------
-
Project                       TABLE A: FQM DRILLING SUMMARY

---------------------------------------------------------------
Total No.
No. of        RC        No.        DD      of DD
Total
RC holes       (m)   of holes       (m)      holes
(m)
---------------------------------------------------------------------------
-
Sumrakovac             6     609.0          6   1,897.4         12
2,506.4
---------------------------------------------------------------------------
-
Savinac                0         -          4    1606.8          4
1606.8
---------------------------------------------------------------------------
-
Bacevica               4     755.0          0         -          4
755.0
---------------------------------------------------------------------------
-
Osnic                  3     501.0          0         -          3
501.0
---------------------------------------------------------------------------
-
Total         13   1,865.0         10   3,504.2         23
5,369.2
---------------------------------------------------------------------------
-



---------------------------------------------------------------------------
TABLE B: FQM DRILL HOLE DESCRIPTION
---------------------------------------------------------------------------
Azimuth    Inclination          Depth
Project                Hole ID    ( degrees )    ( degrees )            (m)
---------------------------------------------------------------------------
Sumrakovac             STRC001            235            -75          161.0
---------------------------------------------------------------------------
Sumrakovac             STRC002            235            -75           59.0
---------------------------------------------------------------------------
Sumrakovac             STRC003             55            -65           83.0
---------------------------------------------------------------------------
Sumrakovac             STRC004             55            -75          110.0
---------------------------------------------------------------------------
Sumrakovac             STRC005             55            -75          113.0
---------------------------------------------------------------------------
Sumrakovac             STRD005             55            -75          288.9
---------------------------------------------------------------------------
Sumrakovac             STRC006            235            -75           83.0
---------------------------------------------------------------------------
Sumrakovac             STDD002             65            -65          389.7
---------------------------------------------------------------------------
Sumrakovac             STDD003            238            -65          312.0
---------------------------------------------------------------------------
Sumrakovac             STDD004             55            -65          384.0
---------------------------------------------------------------------------
Sumrakovac             STDD007             45            -70          401.8
---------------------------------------------------------------------------
Sumrakovac             STDD008             45            -70         121.00
---------------------------------------------------------------------------
Savinac                STDD001            270            -75          638.6
---------------------------------------------------------------------------
Savinac                STDD005            270            -75          290.9
---------------------------------------------------------------------------
Savinac                STDD006             70            -65          200.8
---------------------------------------------------------------------------
Savinac                STDD009             60            -75         476.50
---------------------------------------------------------------------------
Bacevica               STRC007             45            -75             62
---------------------------------------------------------------------------
Bacevica               STRC008             45            -75            251
---------------------------------------------------------------------------
Bacevica               STRC009             45            -75            191
---------------------------------------------------------------------------
Bacevica               STRC010             55            -60            251
---------------------------------------------------------------------------
Osnic                  STRC011            266            -75            179
---------------------------------------------------------------------------
Osnic                  STRC012            360            -90            161
---------------------------------------------------------------------------
Osnic                  STRC013            360            -90            161
---------------------------------------------------------------------------



The Sumrakovac license:
The aim of this first phase drilling was to test for near surface porphyry
style mineralization associated with the outcropping Skorusa stockwork and
K-silicate alteration. A total of twelve drill holes (2,506 m) were drilled
on the Sumrakovac license to test three targets located within a 3 sq.km
area of hydrothermally altered volcanics.
Skorusa Highlights
Current drilling supports that mineralization found in the outcropping
Skorusa stockwork extends from intersections in both historical and current
drill holes. The Company believes the combination of: (i) alteration
assemblages (phyllic overprinting potassic), (ii) A-B type veining,
hydrothermal magnetite veining, quartz-molybdenite veining, and (iii)
stockwork and disseminated chalcopyrite mineralization intersected in
STDD002 and STD007, is, indicative of proximity to several mineralized
porphyry centers.
Drilling also supports the existence of a large porphyry related alteration
system with at least two mineralized centers (Skorusa and Skorusa East).
Potential for mineralization at depth remains untested. Alternating weak
potassic alteration (found as halos around vein contacts) with propylitic
alteration, suggests the periphery of a system. Based on this campaign, the
Company believes that the Sumrakovac license has strong potential to host
large porphyry systems.
Skorusa target
Drill holes STDD002, STDD003, STDD004, holes STRC001, STRC002, STRC003
drilled to test the Skorusa area by targeting the outcropping porphyry
mineralization and the concomitant molybdenum anomaly SE of it.
--  STDD002 was collared 270m SW of the outcropping stockwork
mineralization
intending to validate encouraging results from surface sampling and
historical drill hole as well as to verify the orientation of the
mineralized zone.
--  Several types of quartz sulphide veining including quartz sulphide
stockwork veins were observed. Veins containing chalcopyrite occur at a
consistent but low vein frequency. A zone of well-developed stockwork
veining occurs at, and below, the footwall contact between
monzo-diorite
and andesite units, which returned a composite assay interval of 36m @
0.19% Cu and 0.21 g/t Au.
--  Drill results are consistent with outcropping stockwork veining (23m @
0.17% Cu; 0.72 g/t Au) and historical results. This drilling highlights
a 210m long mineralized section requiring follow-up drilling.
--  Holes STDD003, STDD004, STRC001, STRC002, and STRC003 were designed to
test the greater than 10 ppm Mo anomaly that extends over 1 km to the
SE
from the outcropping stockwork in Skorusa Creek.
--  STDD004 includes several intervals of phyllic after potassic
assemblages. Although assays yielded only anomalous Cu-Mo, these
initial
drill holes support the continuation of the Skorusa porphyry alteration
towards the south and the existence of extensive potassic alteration.

Skorusa North target
Two holes were drilled at the Skorusa North target, which is interpreted as
the continuation of the Skorusa porphyry system to north.
--  STDD007 was collared 750m north-east of STDD002 in strong phillic
altered andesite volcanics and volcanoclastics down to 41.40m, followed
by an overprinted potassic-altered andesite containing pyrite-
chalcopyrite down to 123.5m, followed by weak potassic alteration
characterized by quartz-chalcopyrite veinlets with K-spar halo, biotite
and epidote overprinted by sericite-pyrite-chlorite (phyllic)
alteration. While visible chalcopyrite is present throughout as both
disseminations and veinlets, the tenor of Cu mineralization remains
anomalous at up to 0.1% Cu.
--  STDD008 (121m) was collared in quartz-sericite altered andesite down to
25.9m, followed by propylitic alteration with quartz-pyrite-magnetite
veinlets to 79m, followed by diorite to the end of hole. At several
intervals it intersected quartz-pyrite-Mo veinlets suggesting close
proximity to a mineralized source.

Skorusa East target
The Skorusa East target was tested by RC drill holes STRC004, STRC005 and
STRC006 totaling 306m and one DD drill hole, STRD005, totaling 288.9m as
diamond tail continuation of RC drill hole STRC005 from 113m.
--  All of these holes intersected hydrothermally altered andesite
volcanics
interpreted to be part of larger footprints of a porphyry system. Trace
disseminated chalcopyrite and quartz-chalcopyrite-pyrite B-veins were
encountered throughout the STRD005 drillhole suggesting existence of a
different mineralized center to the east.

Table 1: Highlights of Drilling Results from Sumrakovac

--------------------------------------------------------------------------
Drill             From      To    Interval      Cu      Au    CuEq    AuEq
Hole ID            (m)     (m)         (m)     (%)   (g/t)     (%)   (g/t)
--------------------------------------------------------------------------
STDD002            289     325          36    0.19    0.21    0.35    0.46
--------------------------------------------------------------------------
Including          313     321           8    0.30    0.43    0.62    0.83
--------------------------------------------------------------------------
STRD005            259     261           2    0.11    0.11    0.26    0.19
--------------------------------------------------------------------------
STDD007            124     126           2    0.12    0.03    0.14    0.19
------------------------------------------------------------
152     154           2    0.11    0.03    0.13    0.18
------------------------------------------------------------
166     170           4    0.10    0.03    0.12    0.16
--------------------------------------------------------------------------
//et

//st
Gold Equivalent ("AuEq.") is calculated using the formula AuEq =
(g/t/Au)+[(%Cu) x (22.0462) x ($/lbCu)]  [(1/31.1035) x ($/ozAu)]. Copper
equivalent (CuEq%) is calculated using the formula CuEq = (%Cu) +
[(g/t/AuEq) x (1/31.1035) x ($/ozAu)]  [(22.0462) x ($/lbCu)]. Metal prices
used are: gold price of US$1100/oz, copper price of US$2.13/lb. All
thicknesses from intersections from drill holes are down-hole drilled
thicknesses or outcrop sample length thickness. True widths cannot be
determined from the information available.

//et

The Bacevica and Osnic licenses:

Four RC holes have been drilled at Bacevica totaling 755m and
three in Osnic totaling 501m. Although no reportable assayed intervals
were received the information collected will add to the overall
interpretation of the South Timok Properties as well as to the ongoing
exploration at both of these licenses.

Sampling, Analysis and Qualified Person

Drillhole orientations were surveyed at approximately 50 meters
intervals. Drill core was collected from drill sites by the FQM
geologists and processed and sampled at the Company's core shed
according to industry best practice standard procedures. Samples were
collected as 1/4 PQ or HQ core at two meters length intervals. Oriented
core with high confidence was marked with solid red line and regular
measurements collected.

RC drill samples were collected at 1.0m sample intervals.
Approximately 30.0 kg of material (dust and rock chips) is collected in
a cyclone from 1m interval. The sample is run through splitter where
1/8 (approx. 3.0-4.0kg) of material is collected as a representative of
1.0m sample interval which is sent to the lab. For logging and future
additional analyses, rock chips from each meter are collected and
stored in rock chip trays.

All samples are assayed using 30 gram fire assay with atomic
absorption finish and ME-MS61 by ALS Romania. The entire sample wascrushed to 
2mm, then split off a 1 kg sample and pulverized the split
to better than 85% passing 75 microns. Quality Assurance and Quality
Control procedures include the systematic insertion of standards and
duplicates into the sample streams. Duplicate core samples are taken
every 20 samples standards are inserted after every 33 samples and
blanks after every 20th sample. All data collected from detailed
logging and assay results from the laboratories are routinely verified
and entered in an Access data base.

Technical information contained in this Press Release has been
reviewed and approved by Mr. G. Magaranov, P. Geo., Qualified Person as
defined by National Instrument 43-101.

On behalf of the Company,

Teo Dechev, Chief Executive Officer, President and Director

About Mundoro Capital Inc.

Mundoro is a Canadian based public company which is focused on
generating value for its shareholders through utilizing the collective
expertise of our directors, management and technical team to invest in
mineral projects that have the potential to generate future returns to
shareholders.

Caution Concerning Forward-Looking Statements

Information included, attached to or incorporated by reference
into this News Release may contain forward-looking statements. All
statements, other than statements of historical fact, included or
incorporated by reference in this News Release are forward-looking
statements, including, without limitation, statements regarding FQM's
option to notify Mundoro by December 15, 2015 of its wishes to enter
into a joint venture on the Southern Timok Properties activities,
events or developments that the Board and/or management expects or
anticipates may occur in the future. These forward-looking statements
can be identified by the use of forward-looking words such as "will",
"expect", "intend", "plan", "estimate", "anticipate", "believe" or
"continue" or similar words or the negative thereof. The material
assumptions that were applied in making the forward looking statements
in this News Release include expectations as to the Company's future
strategy and business plan and execution of the Company's existing
plans. There can be no assurance that the plans, intentions or
expectations upon which these forward-looking statements are based will
occur. We caution readers of this News Release not to place undue
reliance on forward looking statements contained in this News Release,
which are not a guarantee of performance and are subject to a number of
uncertainties and other factors that could cause actual results to
differ materially from those expressed or implied by such
forward-looking statements. These factors include general economic and
market conditions, changes in law, regulatory processes, the status of
Mundoro's assets and financial condition, actions of competitors and
the ability to implement business strategies and pursue business
opportunities. The forward-looking statements contained in this News
Release are expressly qualified in their entirety by this cautionary
statement. The forward-looking statements included in this News Release
are made as of the date of this News Release and the Board undertakes
no obligation to publicly update such forward-looking statements to
reflect new information, subsequent events or otherwise, except as
required by law. Shareholders are cautioned that all forward-looking
statements involve risks and uncertainties and for a more detailed
discussion of such risks and other factors that could cause actual
results to differ materially from those expressed or implied by such
forward-looking statements, refer to the Company's filings with the
Canadian securities regulators available on www.sedar.com.

Neither TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

Mundoro Capital Inc.
Teo Dechev
CEO
+1-604-669-8055x101
______________________________________
_______________________________________________
TSX Venture closing price for MUN-V
Date: 2015/12/04
Closing Price: 0.08
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1534000038TS11534001779-13201320151207