Source	Business Wire
Date	12/09/2015
Time	01:30:08 PM

Company	 ATLANTA GOLD INC.
Title	Atlanta Gold Reports Assay Results of Surface Mineralized Material ...





    CDNX Symbol: ATG











Press Release




Dec. 9, 2015 21:30 UTC

Atlanta Gold Reports Assay Results of Surface Mineralized Material  Excavated 
from Neal Property 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Atlanta Gold Inc. 

TSX VENTURE SYMBOL: ATG 

TORONTO--(BUSINESS WIRE)-- Atlanta Gold Inc. (the "Company") (TSXV: ATG; OTC 
Pink: ATLDF) today  announced assay results from the bulk sampling of surface 
mineralized  material obtained from the Neal Property under a Notice of 
Motorized  Exploration (“NOME”). Neal Development, LP (the “Partnership”),  was 
created by the Company’s wholly-owned subsidiary, Atlanta Gold  Corporation 
(“AGC”), to explore and develop the Neal Property  (See the Company's news 
releases of April 7, 2015 and June 11, 2015).  Exploration commenced in 
mid-July and the NOME was submitted to the  Idaho Department of Lands on July 
22, 2015. 

The bulk sample excavation at the Neal Property continued into November,  
producing an estimated eight thousand (8,000) short tons of gold-bearing  
material. The bulk sample was excavated from exposed material within  three (3) 
contiguous acres. Five hundred and sixty-two (562) samples in  eight (8) 
batches, primarily from stockpiles, were tested and analyzed  by two (2) 
laboratories resulting in a weighted average gold grade of  0.1494 ounces per 
ton (“opt”) (5.12 grams per tonne (“gpt”)). 

The two laboratories are Inspectorate America (“Inspectorate”) in  Sparks, 
Nevada and Queenstake-Jerritt Canyon Mine Assay Laboratory (“Jerritt  Canyon”) 
42 miles north of Elko, Nevada. 

  	  	  	  	  	  	  	  	
  	  	  

Batch Number
		Lab Report Date 		
				Number of Samples 
						
						Average Gold Grade in opt 
								
								Average Gold 
Grade in gpt 
										
Lab Name
1 		August 4, 2015 		8 		
0.2328 		7.98 		Inspectorate 
2 		August 6, 2015 		4 		
0.0022 		0.08 		Inspectorate 
3 		August 24, 2015 		22 		
0.2029 		6.96 		Inspectorate 
4 		August 31, 2015 		14 		
0.0601 		2.06 		Inspectorate 
5 		September 30, 2015 		66 		
0.0172 		0.59 		Jerritt Canyon 
6 		October 6, 2015 		109 		
0.0708 		2.43 		Jerritt Canyon 
7 		October 30, 2015 		214 		
0.0804 		2.76 		Inspectorate 
8 		November 30, 2015 		125 		
0.4057 		13.91 		Inspectorate 

Three hundred and eighty-seven (387) samples in six (6) batches were  tested 
and analyzed by Inspectorate. Procedures included crush, split,  pulverize 250g 
to 200 mesh and fire assay 30g for gold with an AAS  finish. Blanks and 
standards were inserted among the samples for quality  control and quality 
assurance. Inspectorate is an ISO 9001 certified  laboratory and is independent 
from the Company. 

One hundred and seventy-five (175) samples in two (2) batches were sent  to 
Jerritt Canyon. Jerritt Canyon is a non-accredited laboratory and is  
independent from the Company. The Jerritt Canyon laboratory’s protocol  is to 
crush, split, pulverize 200g to 150 mesh and fire assay a 29g  sample for gold 
with a gravimetric finish. Standards were inserted for  quality control and 
quality assurance. 

Records of custody were recorded from sample sites to assay laboratories  for 
shipments to both laboratories. 

Wm. Ernest Simmons, President and CEO of the Company stated, “We are  excited 
about the results from this four-month bulk sampling and testing  program. 
After some initial grab sampling and drilling, the decision was  made to focus 
on target areas which were along recognizable surface  structures in two main 
areas referred to as “J” and “M”. This last batch  of one hundred and 
twenty-five (125) samples proved to be the most  interesting with a weighted 
average gold grade of 0.4057 opt (13.91 gpt)  including a high of 5.1500 opt 
(176.57 gpt) and a low of 0.0040 opt  (0.14 gpt).” 

The assays from area “J” averaged 0.4314 opt gold (14.79 gpt) and the  assays 
from area “M” averaged 0.4035 opt gold (13.83 gpt). The sample  areas referred 
to as “M” and “J” are 250 by 250 foot (76.2 by 76.2  meter) grid squares 
diagonal to each other and trending northeasterly.  These squares cover the 
main part of the recognizable shear zones and  include most of the surface 
exposures of the shear zones. Samples from  “M” and “J” are from excavations 
along the exposed structures. 

Of the one hundred and twenty-five (125) samples tested and analyzed by  
Inspectorate, ninety-seven (97) were over 0.1000 opt (3.43 gpt). All  sample 
results from areas “M” and “J” are listed below: 

Sample #	  	Au opt	  	Location	  	
Sample #	  	Au opt	  	Location	  	
Sample #	  	Au opt	  	Location
1420423 		5.1500 		M 		
1420472 		0.2830 		M 		
1420015 		0.1220 		M 
1420424 		5.0850 		M 		
1420442 		0.2750 		M 		
1420433 		0.1220 		M 
1420425 		4.2410 		M 		
1420478 		0.2590 		M 		
1420456 		0.1200 		M 
1420475 		1.9710 		M 		
1420041 		0.2470 		J 		
1420457 		0.1190 		M 
1420481 		1.6280 		M 		
1420490 		0.2470 		M 		
1420031 		0.1170 		M 
1420479 		1.5740 		M 		
1420499 		0.2450 		M 		
1420023 		0.1140 		M 
1420473 		1.3650 		M 		
1420429 		0.2360 		M 		
1420488 		0.1140 		M 
1420468 		1.3020 		M 		
1420040 		0.2330 		J 		
1420491 		0.1130 		M 
1420017 		0.9890 		M 		
1420445 		0.2310 		M 		
1420477 		0.1120 		M 
1420458 		0.8590 		M 		
1420454 		0.2270 		M 		
1420487 		0.1110 		M 
1420016 		0.8550 		M 		
1420430 		0.2230 		M 		
1420432 		0.1100 		M 
1420455 		0.7930 		M 		
1420460 		0.2070 		M 		
1420427 		0.1080 		M 
1420038 		0.7710 		J 		
1420463 		0.2030 		M 		
1420448 		0.1030 		M 
1420451 		0.7520 		M 		
1420483 		0.2000 		M 		
1420022 		0.0960 		M 
1420498 		0.7020 		M 		
1420465 		0.1940 		M 		
1420471 		0.0940 		M 
1420482 		0.6800 		M 		
1420037 		0.1930 		M 		
1420036 		0.0920 		M 
1420047 		0.6540 		J 		
1420467 		0.1900 		M 		
1420032 		0.0910 		M 
1420013 		0.6040 		M 		
1420452 		0.1880 		M 		
1420024 		0.0900 		M 
1420044 		0.5180 		J 		
1420021 		0.1870 		M 		
1420440 		0.0860 		M 
1420045 		0.5090 		J 		
1420008 		0.1850 		M 		
1420026 		0.0840 		M 
1420010 		0.4980 		M 		
1420039 		0.1830 		J 		
1420495 		0.0830 		M 
1420019 		0.4880 		M 		
1420014 		0.1820 		M 		
1420007 		0.0820 		M 
1420464 		0.4630 		M 		
1420450 		0.1810 		M 		
1420489 		0.0810 		M 
1420462 		0.4580 		M 		
1420459 		0.1800 		M 		
1420443 		0.0790 		M 
1420003 		0.4550 		M 		
1420461 		0.1790 		M 		
1420434 		0.0700 		M 
1420042 		0.4500 		J 		
1420033 		0.1690 		M 		
1420035 		0.0630 		M 
1420439 		0.4460 		M 		
1420485 		0.1690 		M 		
1420437 		0.0620 		M 
1420476 		0.4140 		M 		
1420426 		0.1600 		M 		
1420436 		0.0610 		M 
1420484 		0.4140 		M 		
1420444 		0.1590 		M 		
1420474 		0.0590 		M 
1420002 		0.4110 		M 		
1420494 		0.1590 		M 		
1420030 		0.0570 		M 
1420025 		0.4040 		M 		
1420027 		0.1530 		M 		
1420449 		0.0480 		M 
1420001 		0.3930 		M 		
1420453 		0.1520 		M 		
1420029 		0.0450 		M 
1420043 		0.3810 		J 		
1420497 		0.1520 		M 		
1420496 		0.0400 		M 
1420493 		0.3810 		M 		
1420028 		0.1510 		M 		
1420034 		0.0390 		M 
1420012 		0.3720 		M 		
1420441 		0.1510 		M 		
1420431 		0.0360 		M 
1420046 		0.3680 		J 		
1420500 		0.1500 		M 		
1420009 		0.0340 		M 
1420020 		0.3630 		M 		
1420469 		0.1450 		M 		
1420006 		0.0290 		M 
1420470 		0.3280 		M 		
1420011 		0.1430 		M 		
1420435 		0.0220 		M 
1420480 		0.3220 		M 		
1420492 		0.1420 		M 		
1420428 		0.0170 		M 
1420018 		0.2970 		M 		
1420486 		0.1310 		M 		
1420005 		0.0150 		M 
1420446 		0.2870 		M 		
1420447 		0.1260 		M 		
1420004 		0.0040 		M 
1420466 		0.2860 		M 		
1420438 		0.1230 		
M 						

This recent exploration sampling of the Neal Property has been  insufficient to 
define a mineral resource, and it is uncertain if  further similar exploration 
will result in there being a viable,  delineated mineral resource. 

Qualified PersonInformation of a technical nature in this  news release has 
been reviewed by William L. Josey, who is a designated  “Qualified Person” 
under NI 43-101 regulations. Mr. Josey is an  independent geologist, who is a 
Registered Member of the Society for  Mining, Metallurgy, and Exploration, Inc. 
(SME) and a Registered  Geologist in the State of Arizona. Mr. Josey was on 
site during one of  the early stages of sampling and offered suggestions on 
sampling.  Subsequent sampling was under the supervision of senior, 
experienced  Company personnel. 

About the CompanyAtlanta Gold Inc. holds through its  100% owned subsidiary, 
AGC, leases, options or ownership interests in  its Atlanta properties which 
comprise approximately 2,159 acres (8.74  square kilometres) located 90 air 
kilometres east of Boise, in Elmore  County, Idaho. A long history of mining 
makes Atlanta very suitable for  development of new mining projects. The 
Company is focused on advancing  its core asset, Atlanta, towards mine 
development and production. 

The Company is also focused on advancing its exploration and processing  
methods on the Neal Property, which is located approximately 15 miles  from 
Boise, Idaho and comprises approximately 192 acres (0.78 square  kilometres). 
The Neal Property’s geology is similar to that of the  Atlanta Project; in 
that, there are northeasterly-trending shear zones  in granodioritic host 
rocks. The Neal Property provides the Company with  all-season access to 
further refine the processing equipment and  procedures. AGC holds a five-year 
lease on the Neal Property and has  staked an additional seven contiguous 
claims on public land that was  open to mineral entry. 

To receive Company news via email, contact info@atgoldinc.com  and mention 
“Atlanta Gold News” in the subject line. 

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER  (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE)  ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE. 

[IMAGE]

View source version on businesswire.com: 
http://www.businesswire.com/news/home/20151209006495/en/

Contacts

Atlanta Gold Inc.Wm. Ernest Simmons, 208-424-3343President  and CEOFax: 
208-338-6513esimmons@atlantagold.comorPeili  Miao, 416-777-0013Chief Financial 
OfficerFax: 416-777-0014peilimiao@atgoldinc.com 

Source: Atlanta Gold Inc.


Dec. 9, 2015 21:30 UTC

Atlanta Gold Reports Assay Results of Surface Mineralized Material  Excavated 
from Neal Property 

NEWS RELEASE SUBMITTED BY BUSINESS WIRE 

FOR: Atlanta Gold Inc. 

TSX VENTURE SYMBOL: ATG 

TORONTO--(BUSINESS WIRE)-- Atlanta Gold Inc. (the "Company") (TSXV: ATG; OTC 
Pink: ATLDF) today  announced assay results from the bulk sampling of surface 
mineralized  material obtained from the Neal Property under a Notice of 
Motorized  Exploration (“NOME”). Neal Development, LP (the “Partnership”),  was 
created by the Company’s wholly-owned subsidiary, Atlanta Gold  Corporation 
(“AGC”), to explore and develop the Neal Property  (See the Company's news 
releases of April 7, 2015 and June 11, 2015).  Exploration commenced in 
mid-July and the NOME was submitted to the  Idaho Department of Lands on July 
22, 2015. 

The bulk sample excavation at the Neal Property continued into November,  
producing an estimated eight thousand (8,000) short tons of gold-bearing  
material. The bulk sample was excavated from exposed material within  three (3) 
contiguous acres. Five hundred and sixty-two (562) samples in  eight (8) 
batches, primarily from stockpiles, were tested and analyzed  by two (2) 
laboratories resulting in a weighted average gold grade of  0.1494 ounces per 
ton (“opt”) (5.12 grams per tonne (“gpt”)). 

The two laboratories are Inspectorate America (“Inspectorate”) in  Sparks, 
Nevada and Queenstake-Jerritt Canyon Mine Assay Laboratory (“Jerritt  Canyon”) 
42 miles north of Elko, Nevada. 

  	  	  	  	  	  	  	  	  	  	  

Batch Number
		Lab Report Date 	
				Number of Samples 
					
						Average Gold Grade in opt 
							
								Average Gold Grade in gpt 
										Lab Name
1 		August 4, 2015 		8 		0.2328 		7.98 		Inspectorate 
2 		August 6, 2015 		4 		0.0022 		0.08 		Inspectorate 
3 		August 24, 2015 		22 		0.2029 		6.96 		Inspectorate 
4 		August 31, 2015 		14 		0.0601 		2.06 		Inspectorate 
5 		September 30, 2015 		66 		0.0172 		0.59 		Jerritt Canyon 
6 		October 6, 2015 		109 		0.0708 		2.43 		Jerritt Canyon 
7 		October 30, 2015 		214 		0.0804 		2.76 		Inspectorate 
8 		November 30, 2015 		125 		0.4057 		13.91 		Inspectorate 

Three hundred and eighty-seven (387) samples in six (6) batches were  tested 
and analyzed by Inspectorate. Procedures included crush, split,  pulverize 250g 
to 200 mesh and fire assay 30g for gold with an AAS  finish. Blanks and 
standards were inserted among the samples for quality  control and quality 
assurance. Inspectorate is an ISO 9001 certified  laboratory and is independent 
from the Company. 

One hundred and seventy-five (175) samples in two (2) batches were sent  to 
Jerritt Canyon. Jerritt Canyon is a non-accredited laboratory and is  
independent from the Company. The Jerritt Canyon laboratory’s protocol  is to 
crush, split, pulverize 200g to 150 mesh and fire assay a 29g  sample for gold 
with a gravimetric finish. Standards were inserted for  quality control and 
quality assurance. 

Records of custody were recorded from sample sites to assay laboratories  for 
shipments to both laboratories. 

Wm. Ernest Simmons, President and CEO of the Company stated, “We are  excited 
about the results from this four-month bulk sampling and testing  program. 
After some initial grab sampling and drilling, the decision was  made to focus 
on target areas which were along recognizable surface  structures in two main 
areas referred to as “J” and “M”. This last batch  of one hundred and 
twenty-five (125) samples proved to be the most  interesting with a weighted 
average gold grade of 0.4057 opt (13.91 gpt)  including a high of 5.1500 opt 
(176.57 gpt) and a low of 0.0040 opt  (0.14 gpt).” 

The assays from area “J” averaged 0.4314 opt gold (14.79 gpt) and the  assays 
from area “M” averaged 0.4035 opt gold (13.83 gpt). The sample  areas referred 
to as “M” and “J” are 250 by 250 foot (76.2 by 76.2  meter) grid squares 
diagonal to each other and trending northeasterly.  These squares cover the 
main part of the recognizable shear zones and  include most of the surface 
exposures of the shear zones. Samples from  “M” and “J” are from excavations 
along the exposed structures. 

Of the one hundred and twenty-five (125) samples tested and analyzed by  
Inspectorate, ninety-seven (97) were over 0.1000 opt (3.43 gpt). All  sample 
results from areas “M” and “J” are listed below: 

Sample #	  	Au opt	  	Location	  	Sample #	  	Au opt	  	Location	  	Sample #	  	Au opt	  	Location
1420423 		5.1500 		M 		1420472 		0.2830 		M 		1420015 		0.1220 		M 
1420424 		5.0850 		M 		1420442 		0.2750 		M 		1420433 		0.1220 		M 
1420425 		4.2410 		M 		1420478 		0.2590 		M 		1420456 		0.1200 		M 
1420475 		1.9710 		M 		1420041 		0.2470 		J 		1420457 		0.1190 		M 
1420481 		1.6280 		M 		1420490 		0.2470 		M 		1420031 		0.1170 		M 
1420479 		1.5740 		M 		1420499 		0.2450 		M 		1420023 		0.1140 		M 
1420473 		1.3650 		M 		1420429 		0.2360 		M 		1420488 		0.1140 		M 
1420468 		1.3020 		M 		1420040 		0.2330 		J 		1420491 		0.1130 		M 
1420017 		0.9890 		M 		1420445 		0.2310 		M 		1420477 		0.1120 		M 
1420458 		0.8590 		M 		1420454 		0.2270 		M 		1420487 		0.1110 		M 
1420016 		0.8550 		M 		1420430 		0.2230 		M 		1420432 		0.1100 		M 
1420455 		0.7930 		M 		1420460 		0.2070 		M 		1420427 		0.1080 		M 
1420038 		0.7710 		J 		1420463 		0.2030 		M 		1420448 		0.1030 		M 
1420451 		0.7520 		M 		1420483 		0.2000 		M 		1420022 		0.0960 		M 
1420498 		0.7020 		M 		1420465 		0.1940 		M 		1420471 		0.0940 		M 
1420482 		0.6800 		M 		1420037 		0.1930 		M 		1420036 		0.0920 		M 
1420047 																																																																																																																																																																																																																																																												0.6540 		J 		1420467 		0.1900 		M 		1420032 		0.0910 		M 
1420013 		0.6040 		M 		1420452 		0.1880 		M 		1420024 		0.0900 		M 
1420044 		0.5180 		J 		1420021 		0.1870 		M 		1420440 		0.0860 		M 
1420045 		0.5090 		J 		1420008 		0.1850 		M 		1420026 		0.0840 		M 
1420010 		0.4980 		M 		1420039 		0.1830 		J 		1420495 		0.0830 		M 
1420019 		0.4880 		M 		1420014 		0.1820 		M 		1420007 		0.0820 		M 
1420464 		0.4630 		M 		1420450 		0.1810 		M 		1420489 		0.0810 		M 
1420462 		0.4580 		M 		1420459 		0.1800 		M 		1420443 		0.0790 		M 
1420003 		0.4550 		M 		1420461 		0.1790 		M 		1420434 		0.0700 		M 
1420042 		0.4500 		J 		1420033 		0.1690 		M 		1420035 		0.0630 		M 
1420439 		0.4460 		M 		1420485 		0.1690 		M 		1420437 		0.0620 		M 
1420476 		0.4140 		M 		1420426 		0.1600 		M 		1420436 		0.0610 		M 
1420484 		0.4140 		M 		1420444 		0.1590 		M 		1420474 		0.0590 		M 
1420002 		0.4110 		M 		1420494 		0.1590 		M 		1420030 		0.0570 		M 
1420025 		0.4040 		M 		1420027 		0.1530 		M 		1420449 		0.0480 		M 
1420001 		0.3930 		M 		1420453 		0.1520 		M 		1420029 		0.0450 		M 
1420043 		0.3810 		J 		1420497 		0.1520 		M 		1420496 		0.0400 		M 
1420493 		0.3810 		M 		1420028 		0.1510 		M 		1420034 		0.0390 		M 
1420012 		0.3720 		M 		1420441 		0.1510 		M 		1420431 		0.0360 		M 
1420046 		0.3680 		J 		1420500 		0.1500 		M 		1420009 		0.0340 		M 
1420020 		0.3630 		M 		1420469 		0.1450 		M 		1420006 		0.0290 		M 
1420470 		0.3280 		M 		1420011 		0.1430 		M 		1420435 		0.0220 		M 
1420480 		0.3220 		M 		1420492 		0.1420 		M 		1420428 		0.0170 		M 
1420018 		0.2970 		M 		1420486 		0.1310 		M 		1420005 		0.0150 		M 
1420446 		0.2870 		M 		1420447 		0.1260 		M 		1420004 		0.0040 		M 
1420466 		0.2860 		M 		1420438 		0.1230 		M 						

This recent exploration sampling of the Neal Property has been  insufficient to 
define a mineral resource, and it is uncertain if  further similar exploration 
will result in there being a viable,  delineated mineral resource. 

Qualified PersonInformation of a technical nature in this  news release has 
been reviewed by William L. Josey, who is a designated  “Qualified Person” 
under NI 43-101 regulations. Mr. Josey is an  independent geologist, who is a 
Registered Member of the Society for  Mining, Metallurgy, and Exploration, Inc. 
(SME) and a Registered  Geologist in the State of Arizona. Mr. Josey was on 
site during one of  the early stages of sampling and offered suggestions on 
sampling.  Subsequent sampling was under the supervision of senior, 
experienced  Company personnel. 

About the CompanyAtlanta Gold Inc. holds through its  100% owned subsidiary, 
AGC, leases, options or ownership interests in  its Atlanta properties which 
comprise approximately 2,159 acres (8.74  square kilometres) located 90 air 
kilometres east of Boise, in Elmore  County, Idaho. A long history of mining 
makes Atlanta very suitable for  development of new mining projects. The 
Company is focused on advancing  its core asset, Atlanta, towards mine 
development and production. 

The Company is also focused on advancing its exploration and processing  
methods on the Neal Property, which is located approximately 15 miles  from 
Boise, Idaho and comprises approximately 192 acres (0.78 square  kilometres). 
The Neal Property’s geology is similar to that of the  Atlanta Project; in 
that, there are northeasterly-trending shear zones  in granodioritic host 
rocks. The Neal Property provides the Company with  all-season access to 
further refine the processing equipment and  procedures. AGC holds a five-year 
lease on the Neal Property and has  staked an additional seven contiguous 
claims on public land that was  open to mineral entry. 

To receive Company news via email, contact info@atgoldinc.com  and mention 
“Atlanta Gold News” in the subject line. 

NEITHER THE TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER  (AS THAT 
TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE)  ACCEPTS 
RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE. 

[IMAGE]

View source version on businesswire.com: 
http://www.businesswire.com/news/home/20151209006495/en/

Contacts

Atlanta Gold Inc.Wm. Ernest Simmons, 208-424-3343President  and CEOFax: 
208-338-6513esimmons@atlantagold.comorPeili  Miao, 416-777-0013Chief Financial 
OfficerFax: 416-777-0014peilimiao@atgoldinc.com 

Source: Atlanta Gold Inc.
Powered by Business Wire