Source	Filing Services Canada
Date	12/08/2016
Time	05:25:12 AM

Company	 ENDURANCE GOLD CORPORATION
Title	Endurance Confirms Significant Gold Zone at Elephant Mountain, Alaska





    CDNX Symbol: EDG











Press Release




SOURCE: Filing Services Canada
Date: 12/08/2016
Time: 08:25:00

Company: ENDURANCE GOLD CORPORATION
Title:Endurance Confirms Significant Gold Zone at Elephant Mountain, Alaska 
(EDG - TSXV) 
TSXV SYMBOL: EDG


NEWS TRANSMITTED BY FILING SERVICES CANADA
FOR: Endurance Gold Corporation
TSXV SYMBOL: EDG
Thursday, December 08, 2016 - 8:25 AM

Original Source Location: 
http://www.fscwire.com/newsrelease/endurance-confirms-significant-gold-zone-elep
hant-mountain-alaska

Endurance Confirms Significant Gold Zone at Elephant Mountain, Alaska

North Zone drill hole returns 0.40 gpt gold over 147.1 metres, including 0.63 
gpt gold over 48.2 metres 


Vancouver, British Columbia (FSCwire) - Endurance Gold Corporation (EDG  TSX.V, 
Endurance) is pleased to announce further assay results from the 2016 drill 
program on its 100% optioned Elephant Mountain Gold Property in Alaska, located 
on roads about 76 miles (123 kilometres (km)) northwest of Fairbanks. As 
announced on September 27, 2016 three (3) diamond drill holes were completed on 
the South Zone and one diamond drill hole was completed on the North Zone for a 
total of 598 metres (m) drilled.



1.4 km north of the South Zone discovery (announced on October 31, 2016), 
drilling at the North Zone has successfully confirmed a wide intersection of 
0.40 grams per tonne gold (gpt Au) over 147.1 m including a 0.63 gpt Au over 
48.2 m confirming the existence of gold-rich alteration system associated with 
elevated arsenic. 



At this North Zone Target, intermittent exposures of outcrop define a one 
square km alteration zone on surface consisting of disseminated 
pyrite-arsenopyrite in pervasively silicified, sericite, and clay altered 
granodiorite associated with a gold-arsenic soil anomaly. This area was 
previously drill tested by Placer Dome Inc. and others (PDI) in which a drill 
section of six drill holes indicated a large volume of rock exceeding 550 m 
across and 100 m vertical depth that exceeded 100 parts per billion (ppb) gold, 
hosted in pervasively silicified, sericite, and clay altered granodiorite 
similar to alteration and mineralization observed on surface. The North Zone 
drill section with histogram gold results is attached to this press release or 
can be viewed at www.endurancegold.com (http://www.endurancegold.com).



Endurance completed one diamond drill hole EL 16-13 (Az 180 Dip-45) which 
tested the slightly higher grade core of the prior drill section within this 
broad low-grade zone. EL 16-13 was drilled to a total angled depth of 180.75 m 
and encountered silicified and phylllic (sericite) altered granodiorite 
throughout the entire core length. About 150 m of this length, starting at 
surface, encountered up to 1.5% pervasive disseminated pyrite and arsenopyrite 
with arsenopyrite and pyrite bearing quartz veinlets. The entire length of the 
drill hole is in-part oxidized with the oxidation related to fractures and 
oxidized quartz-sulphide veinlets. Assay results are 0.40 gpt Au over 147.1 m 
including a 0.63 gpt Au over 48.2 m. True width is currently unknown although 
correlation of the greater than 0.50 gpt gold mineralization for the North Zone 
drill section shows an apparent sub-horizontal orientation. A PDI drill hole 
located at approximately the same location as EL 16-13 returned an average 
grade of 0.514 gpt Au over an interval of 99.4 m.



"This 2016 North Zone drill hole located 1.4 km north of our earlier discovery 
hole with 4.09 gpt Au over 4.6 m indicates a large and complex gold 
mineralizing system that is largely untested with drilling" commented Robert 
Boyd, President and CEO of Endurance. "The extensive soil anomalies, a large 
untested IP chargeability anomaly between the South Zone and North Zone 
discoveries indicates that additional exploration is required to discover the 
postulated higher grade feeder structures at the North Zone and to fully 
explain the average grade and width of the South Zone discovery. We look 
forward to planning for a 2017 exploration program at Elephant that will expand 
on these discoveries.



South Zone - The South Zone drill hole EL 16-15 (Az 055 Dip-45) which underlies 
the western portion of the South Zone soil anomaly, intersected a wide oxidized 
and disrupted zone which includes multiple areas of faulting, brecciation and 
clay gouge. Only about 68% of the core was recovered for the entire 114 m 
length of the drill hole EL 16-15. The best assay results from this drilling 
include an intersection of 0.52 gpt Au over 3.04 m which includes 1.13 gpt Au 
over 1.06 m. This intersection is associated with one of the zones of clay 
gouge breccia and fault rubble and 24% of the core was not recovered through 
this interval suggesting possible loss of oxidized mineralization.



The South Zone drill hole EL 16-16 (Az 235 Dip-45) is located on the east side 
of the South Zone soil anomaly 249 m north west of EL 16-14 and intersected 
primarily syenomonzonite, minor diorite, with veinlet zones throughout its 
entire length with some inliers of altered sediments. The best assay results 
from this drilling include intersection of 0.59 gpt Au over 2.44 m and 0.48 gpt 
Au over 2.44 m. These intersections are associated with minor pyrite and 
arsenopyrite associated with a quartz veinlet zone in syenomonzonite and a clay 
gouge zone in silicified and carbonate altered diorite and sediments. It is now 
interpreted that this hole was collared too far to the west to intersect the 
interpreted northwestern strike extension of the EL 16-14 South Zone discovery.



Expansion of Property - The Elephant Mountain Property was expanded through the 
staking of three additional Alaska state mineral claims in September 2016.



Future Plans  A program of geophysics, soil geochemistry and diamond drilling 
will commence the planning stages over year end. Drill holes EL 16-14A/B and EL 
16-16 have only been selectively sampled based on visual arsenopyrite and/or 
stibnite mineralization. As part of the winter phase of the program, further 
splitting and sampling of these drill holes may be undertaken to evaluate 
unsampled zones of vein stock work and low-suphide silicification.



ENDURANCE GOLD CORPORATION



Robert T. Boyd



FOR FURTHER INFORMATION, PLEASE CONTACT

Endurance Gold Corporation

(604) 682-2707, info@endurancegold.com (mailto:info@endurancegold.com)

www.endurancegold.com (http://www.endurancegold.com/)



Robert T. Boyd, P.Geo. is a qualified person as defined in National Instrument 
43-101 and supervised the compilation of the information forming the basis for 
this release. The drill intersections in this release may not represent the 
true width of the intersection. The split drill core samples from this program 
were analyzed at ALS Minerals using Au-AA23, Au-GRA21 (>10 g/t), and ME-MS61L. 
No assays for antimony or arsenic were completed on samples with values 
exceeding 10,000 ppm. Confirmation standards were inserted within sample 
shipments by Endurance as well as ALS Minerals inserted standards with each 
shipment analyzed. 



Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this news release. This news 
release may contain forward looking statements based on assumptions and 
judgments of management regarding future events or results that may prove to be 
inaccurate as a result of factors beyond its control, and actual results may 
differ materially from the expected results


To view this press release as a PDF file, click onto the following link:
http://www.fscwire.com/sites/default/files/news_release_pdf/EnduranceDec82016.pd
f
Source: Endurance Gold Corporation (TSX Venture:EDG, OTC Bulletin Board:ENDGF) 
http://www.endurancegold.com



Maximum News Dissemination by FSCwire. http://www.fscwire.com



Copyright(C)2016 Filing Services Canada Inc.