Source	MARKET NEWS
Date	12/08/2016
Time	05:41:50 AM

Company	 Endurance Gold Corporation
Title	Confirms 
Significant GoldZone at Elephant Mounta





    CDNX Symbol: EDG











Press Release





ENDURANCE GOLD CORP ("EDG-V")
- Confirms Significant GoldZone at Elephant Mountain, Alaska

North Zone drill hole returns 0.40 gpt gold over 147.1 metres,
including 0.63 gpt gold over 48.2 metres

Endurance Gold Corporation ("Endurance") is pleased to announce
further assay results from the 2016 drill program on its 100% optioned
Elephant Mountain Gold Property in Alaska, located on roads about 76
miles (123 kilometres ("km")) northwest of Fairbanks. As announced on
September 27, 2016 three (3) diamond drill holes were completed on the
South Zone and one diamond drill hole was completed on the North Zone
for a total of 598 metres ("m") drilled.

1.4 km north of the South Zone discovery (announced on October 31,
2016), drilling at the North Zone has successfully confirmed a wide
intersection of 0.40 grams per tonne gold ("gpt Au") over 147.1 m
including a 0.63 gpt Au over 48.2 m confirming the existence of
gold-rich alteration system associated with elevated arsenic.

At this North Zone Target, intermittent exposures of outcrop
define a one square km alteration zone on surface consisting of
disseminated pyrite-arsenopyrite in pervasively silicified, sericite,
and clay altered granodiorite associated with a gold-arsenic soil
anomaly. This area was previously drill tested by Placer Dome Inc. and
others ("PDI") in which a drill section of six drill holes indicated a
large volume of rock exceeding 550 m across and 100 m vertical depth
that exceeded 100 parts per billion ("ppb") gold, hosted in pervasively
silicified, sericite, and clay altered granodiorite similar to
alteration and mineralization observed on surface. The North Zone drill
section with histogram gold results is attached to this press release
or can be viewed at www.endurancegold.com.

Endurance completed one diamond drill hole EL 16-13 (Az 180
Dip-45) which tested the slightly higher grade core of the prior drill
section within this broad low-grade zone. EL 16-13 was drilled to a
total angled depth of 180.75 m and encountered silicified and phylllic
(sericite) altered granodiorite throughout the entire core length.
About 150 m of this length, starting at surface, encountered up to 1.5%
pervasive disseminated pyrite and arsenopyrite with arsenopyrite and
pyrite bearing quartz veinlets. The entire length of the drill hole is
in-part oxidized with the oxidation related to fractures and oxidized
quartz-sulphide veinlets. Assay results are 0.40 gpt Au over 147.1 m
including a 0.63 gpt Au over 48.2 m. True width is currently unknown
although correlation of the greater than 0.50 gpt gold mineralization
for the North Zone drill section shows an apparent sub-horizontal
orientation. A PDI drill hole located at approximately the same
location as EL 16-13 returned an average grade of 0.514 gpt Au over an
interval of 99.4 m.

"This 2016 North Zone drill hole located 1.4 km north of our
earlier discovery hole with 4.09 gpt Au over 4.6 m indicates a large
and complex gold mineralizing system that is largely untested with
drilling" commented Robert Boyd, President and CEO of Endurance. "The
extensive soil anomalies, a large untested IP chargeability anomaly
between the South Zone and North Zone discoveries indicates that
additional exploration is required to discover the postulated higher
grade feeder structures at the North Zone and to fully explain the
average grade and width of the South Zone discovery. We look forward to
planning for a 2017 exploration program at Elephant that will expand on
these discoveries."

South Zone - The South Zone drill hole EL 16-15 (Az 055 Dip-45)
which underlies the western portion of the South Zone soil anomaly,
intersected a wide oxidized and disrupted zone which includes multiple
areas of faulting, brecciation and clay gouge. Only about 68% of the
core was recovered for the entire 114 m length of the drill hole EL
16-15. The best assay results from this drilling include an
intersection of 0.52 gpt Au over 3.04 m which includes 1.13 gpt Au over
1.06 m. This intersection is associated with one of the zones of clay
gouge breccia and fault rubble and 24% of the core was not recovered
through this interval suggesting possible loss of oxidized
mineralization.

The South Zone drill hole EL 16-16 (Az 235 Dip-45) is located on
the east side of the South Zone soil anomaly 249 m north west of EL
16-14 and intersected primarily syenomonzonite, minor diorite, with
veinlet zones throughout its entire length with some inliers of altered
sediments. The best assay results from this drilling include
intersection of 0.59 gpt Au over 2.44 m and 0.48 gpt Au over 2.44 m.
These intersections are associated with minor pyrite and arsenopyrite
associated with a quartz veinlet zone in syenomonzonite and a clay
gouge zone in silicified and carbonate altered diorite and sediments.
It is now interpreted that this hole was collared too far to the west
to intersect the interpreted northwestern strike extension of the EL
16-14 South Zone discovery.

Expansion of Property - The Elephant Mountain Property was
expanded through the staking of three additional Alaska state mineral
claims in September 2016.

Future Plans - A program of geophysics, soil geochemistry and
diamond drilling will commence the planning stages over year end. Drill
holes EL 16-14A/B and EL 16-16 have only been selectively sampled based
on visual arsenopyrite and/or stibnite mineralization. As part of the
winter phase of the program, further splitting and sampling of these
drill holes may be undertaken to evaluate unsampled zones of vein stock
work and low-suphide silicification.

ENDURANCE GOLD CORPORATION
Robert T. Boyd
FOR FURTHER INFORMATION, PLEASE CONTACT
Endurance Gold Corporation
(604) 682-2707, info@endurancegold.com
www.endurancegold.com

Robert T. Boyd, P.Geo. is a qualified person as defined in
National Instrument 43-101 and supervised the compilation of the
information forming the basis for this release. The drill intersections
in this release may not represent the true width of the intersection.
The split drill core samples from this program were analyzed at ALS
Minerals using Au-AA23, Au-GRA21 ()10 g/t), and ME-MS61L. No assays for
antimony or arsenic were completed on samples with values exceeding
10,000 ppm. Confirmation standards were inserted within sample
shipments by Endurance as well as ALS Minerals inserted standards with
each shipment analyzed.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
news release. This news release may contain forward looking statements
based on assumptions and judgments of management regarding future
events or results that may prove to be inaccurate as a result of
factors beyond its control, and actual results may differ materially
from the expected results

TSX Venture closing price for EDG-V
Date: 2016/12/02
Closing Price: 0.07

TEL: (604) 682-2707
FAX: (604) 681-0902  ENDURANCE GOLD CORP
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1634200013TS11634200702-05391220161208