Source	MARKET NEWS
Date	12/14/2016
Time	08:26:28 AM

Company	 Oceanus Resources Corporation
Title	Intersects 110 Meters of 0.79 g/t Gold Equivalen





    CDNX Symbol: OCN











Press Release





Intersects 110 Meters of 0.79 g/t Gold Equivalent Consisting of 0.6g/t Gold 
and 14.5 g/t Silver at its El Tigre Property in Sonora,Mexico --->@NEWS 
RELEASE
OCEANUS RESOURCES CORPORATION ("OCN-V")
- Intersects 110 Meters of 0.79 g/t Gold Equivalent Consisting of
- 0.6 g/t Gold and 14.5 g/t Silver at its El Tigre Property in
- Sonora, Mexico

Oceanus Resources Corporation ("Oceanus" or the 'Company') reports
additional assay results from the ongoing diamond drilling program on its
100% owned El Tigre Property in Sonora, Mexico. Highlights from the
drilling include the following:
* Hole ET-16-108 ' 110 meters of 0.79 g/t gold equivalent consisting of 0.6
g/t gold and 14.5 g/t silver; including 16 meters of 1.69 g/t gold
equivalent consisting of 0.82 g/t gold and 64.7 g/t silver.

* Hole ET-16-109 ' 20.4 meters of 3.23 g/t gold equivalent consisting of
0.4 g/t gold and 212 g/t silver; including 4 meters of 13.9 g/t gold
equivalent consisting of 0.82 g/t gold and 981.2 g/t silver.

* Hole ET-16-104 ' 115.9 meters of 0.58 g/t gold equivalent consisting of
0.43 g/t gold and 11.4 g/t silver; including 67 meters of 0.81 g/t gold
equivalent consisting of 0.56 g/t gold and 18.3 g/t silver.

The true width has not been calculated for the intercepts, but true width
is generally estimated at 75-90% of drilled width. Drill assays were
composited by length-weighted averaging into intersections using a 0.2 g/t
gold equivalent cut-off grade. The gold equivalent ratio is based on a
gold-to-silver price ratio of 75:1.

Oceanus has now completed 35 holes totaling 6,467 meters of HQ size core.
Results from the first 16 drill holes were announced in the Oceanus News
Releases dated September 14, 2016 and October 18, 2016. Today's news
release provides the results for an additional 11 drill holes. The purpose
of the drilling program is to determine the full extent of the
mineralization in the hanging wall and footwall of the deposit, to confirm
the geological continuity of the mineralization and to test the oxidized
zone to a vertical depth of 200 meters.

Oceanus has geological crews mapping and prospecting to the north and south
of the historical mine workings to define the extensions of the vein /
alteration systems in both directions. Oceanus has hired Geofisica TMC,
S.A. de C.V. to carry out an orientation geophysical survey on the El Tigre
deposit during December, 2016. The survey will consist of 3 traverse lines
totalling 6 line kilometers of induced polarization survey to define the
resistivity and chargeability properties over the historical workings.

Glenn Jessome, President and CEO of Oceanus, commented: 'These drill
results continue to exhibit wide oxidized zones of precious metals
mineralization that outcrop at surface, further supporting our hypothesis
that El Tigre could be another significant bulk tonnage project in the
Sierra Madre Occidental in Mexico. The two drill rigs operating at El Tigre
will continue to move north and south along the 1.6 km strike length over
the old El Tigre mine during the first quarter of 2017 as the Company works
to complete an updated NI 43-101 compliant resource estimate in 2017.'

//st
The following table provides details of the significant intersections for
the 11 drill holes. The holes were drilled between Sections 4500N and
38000N in the central portion of the 1.6 kilometer long deposit:



Drill Section Hole ID Comment    From     To       Length   Au    Ag    AuEq
(meters) (meters) (meters) (g/t) (g/t)(g/t)
ET-16-099     3800               21.9     36.8     14.9     0.76  12.4  0.92
and        50.4     70.5     20.2     0.22  20.3  0.49
and        80.4     98.6     18.3     0.36  92.3  1.60
including  81.0     86.2     5.2      0.74 292.6  4.64
OPEN STOPE 98.6     104.7    6.1      El Tigre Vein
and        104.7    119.4    14.7     0.10  12.0  0.26
ET-16-100     3875               3.8      28.1     24.3     0.60  11.0  0.74
and        36.5     40.5     4.0      0.62  4.1   0.67
and        46.5     52.0     5.5      0.32  4.2   0.37
and        66.7     100.1    33.4     0.33  26.1  0.68
OPEN STOPE 93.7     97.5     3.8      El Tigre Vein
including  97.5     98.8     1.3      0.30  476.0 6.64
and        115.1    122.1    7.0      0.20  19.1  0.45
ET-16-101     4500               41.5     62.0     20.6     0.59  3.9   0.64
and        72.0     95.3     23.3     0.80  6.7   0.89
and        112.2    119.0    6.8      0.52  2.9   0.56
and        136.8    138.4    1.6      1.08  3.8   1.13
OPEN STOPE 201.6    202.9    1.3      Seitz Kelly Vein
and        202.9    218.0    15.2     0.15  25.4  0.49
ET-16-102     4375               15.5     32.5     17.0     0.38  2.7   0.41
and        39.9     57.5     17.7     0.28  6.8   0.37
and        78.0     92.0     14.1     0.32  0.8   0.33
ET-16-103     4375               57.7     88.4     30.7     0.44  5.8   0.52
OPEN STOPE 79.0     82.4     3.4      El Tigre Vein
and        153.2    164.0    10.8     0.60  1.1   0.61
OPEN STOPE 170.5    173.0    2.5      Seitz Kelly Vein
and        173.0    179.6    6.6      0.65  60.8  1.46
including  173.0    174.5    1.5      0.10  256.4 3.52
ET-16-104     4125               22.6     138.5    115.9    0.43  11.4  0.58
including  35.8     102.8    67.0     0.56  18.3  0.81
including  54.0     70.7     16.8     0.63  48.8  1.28
95.3     98.2     2.9      5.01  10.1  5.15
Drill Section Hole ID Comment    From     To       Length   Au    Ag    AuEq
(meters) (meters) (meters) (g/t) (g/t)(g/t)
ET-16-105     4325               14.5     93.5     79.0     0.54  10.6  0.68
including  41.5     58.5     17.0     0.64  29.4  1.04
including  54.2     58.5     4.4      0.84  79.5  1.90
including  81.0     93.5     12.5     1.25  3.1   1.29
and        114.7    121.9    7.3      0.69  1.3   0.71
ET-16-106     4275               0.0      54.9     54.9     0.30  14.4  0.49
including  32.3     42.3     10.0     0.45  42.8  1.02
OPEN STOPE 49.0     51.5     2.5      El Tigre Vein
and        64.5     66.0     1.5      2.35  4.2   2.41
ET-16-107     4225               2.3      9.5      7.2      0.62  3.3   0.67
and        18.3     81.9     63.7     0.36  34.9  0.83
including  19.4     30.6     11.2     0.67  33.3  1.11
including  59.5     65.9     6.5      1.04  129.9 2.77
including  71.1     74.4     3.4      0.27  117.0 1.83
and        93.9     95.7     1.8      0.76  0.9   0.77
and        101.9    120.7    18.8     0.54  6.9   0.64
including  104.4    111.0    6.7      0.80  16.2  1.02
ET-16-108     4175               42.7     152.7    110.0    0.60  14.5  0.79
including  49.9     55.0     5.1      2.16  3.1   2.20
including  74.1     86.0     11.9     1.11  7.1   1.20
including  102.5    118.5    16.0     0.82  64.7  1.69
OPEN STOPE 108.2    109.0    0.8      El Tigre Vein
including  136.5    144.0    7.5      1.20  2.6   1.23
ET-16-109     4025               111.9    140.7    28.8     0.70  3.1   0.75
including  117.2    124.2    7.0      1.57  4.4   1.63
and        160.9    181.3    20.4     0.40  212.0 3.23
including  163.6    167.6    4.0      0.82 981.2 13.90
including  163.6    164.3    0.7     2.12 2964.5 41.65
and        196.5    199.9    3.3      0.30  6.0   0.38
and        210.9    215.0    4.1      0.19  14.2  0.38
Notes:
(1) True width has not been calculated for each individual intercept, but
true width is generally estimated at 75-90% of drilled width. Metallurgical
recoveries and net smelter returns are assumed to be 100%
(2) Gold Equivalent ratio based on gold to silver price ratio of 75:1
Ag:Au.
The following table provides the drill hole locations for the Oceanus drill
holes completed subsequent to the last news release dated October 18, 2016:

Hole ID   Northing Easting Elevation Azimuth Dip Length
(meters)
ET-16-101 3384500  671055  2074.0    90      -45 239.0
ET-16-102 3384375  671140  2007.0    90      -45 150.3
ET-16-103 3384375  671121  1976.0    90      -45 212.65
ET-16-104 3384125  671145  1986.0    90      -45 138.45
ET-16-105 3384325  671121  1976.0    90      -45 129.6
ET-16-106 3384275  671130  1959.0    90      -55 160.1
ET-16-107 3384225  671108  1944.0    90      -45 150.65
ET-16-108 3384175  671086  1935.0    90      -45 180.95
ET-16-109 3384025  671035  1925.0    90      -50 254.45
ET-16-110 3384025  671115  1930.0    90      -45 169.1
ET-16-111 3384975  670858  1819.0    90      -45 252.05
ET-16-112 3383750  671130  1942.0    90      -45 244.5
ET-16-113 3384800  670902  1954.0    90      -45 224.65
ET-16-114 3383850  670900  1814.0    90      -45 342.45
ET-16-115 3384500  670898  2049.0    90      -45 313.05
ET-16-116 3384425  671144  2027.0    90      -45 177.75

Lab Preparation and Assay



//et

The diamond drill core (HQ size) is geologically logged, photographed and
marked for sampling. When the sample lengths are determined the full core
is sawn with a diamond blade core saw with one-third of the core being
bagged and tagged for assay. The remaining two-thirds portion is returned
to the core trays for storage and/or for metallurgical test work.

The sealed and tagged sample bags are transported to the ActLabs facility
in Zacatecas, Mexico. ActLabs crushes the samples and prepares 200-300 gram
pulp samples with ninety percent passing Tyler 150 mesh (106'm).The pulps
are assayed for gold using a 50 gram charge by fire assay (Code 1A2-50) and
over limits greater than 10 grams per tonne are re-assayed using a
gravimetric finish (Code 1A3-50). Silver and multi-element analysis is
completed using total digestion (Code 1F2 Total Digestion ICP).

Quality Assurance / Quality Control and Data Verification

Quality assurance and quality control ("QA/QC") procedures monitor the
chain-of-custody of the samples and includes the systematic insertion and
monitoring of appropriate reference materials (certified standards, blanks
and duplicates) into the sample strings. The results of the assaying of the
QA/QC material included in each batch are tracked to ensure the integrity
of the assay data. All results stated in this announcement have passed
Oceanus' QA/QC protocols.

Qualified Person

David R. Duncan, P. Geo., V.P. Exploration of the Company, is the Qualified
Person for Oceanus as defined under National Instrument 43-101. Mr. Duncan
has reviewed and approved the scientific and technical information in this
press release and has reviewed the Technical Report.

About Oceanus Resources Corporation

Oceanus Resources Corporation is a gold exploration company operating in
Mexico. Oceanus is managed by a team of mine finders with extensive
experience in exploring and developing large hydrothermal gold projects in
Mexico. Oceanus is currently drilling and exploring the El Tigre Property
in the Sierra Madre Occidental.

CAUTIONARY STATEMENT:
Neither TSX Venture Exchange nor its Regulation Services Provider (as that
term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.

This News Release includes certain 'forward-looking statements'. All
statements other than statements of historical fact included in this
release, including, without limitation, statements regarding potential
mineralization, resources and reserves, the ability to convert inferred
resources to indicated resources, the ability to complete future drilling
programs and infill sampling, the ability to extend resource blocks, the
similarity of mineralization at El Tigre to the Ocampo mine, exploration
results, and future plans and objectives of Oceanus, are forward-looking
statements that involve various risks and uncertainties. Forward-looking
statements are frequently characterized by words such as 'may', 'is
expected to', 'anticipates', 'estimates', 'intends', 'plans', 'projection',
'could', 'vision', 'goals', 'objective' and 'outlook' and other similar
words. Although Oceanus believes the expectations expressed in such
forward-looking statements are based on reasonable assumptions, there can
be no assurance that such statements will prove to be accurate and actual
results and future events could differ materially from those anticipated in
such statements. Important factors that could cause actual results to
differ materially from Oceanus's expectations include risks and
uncertainties related to exploration, development, operations, commodity
prices and global financial volatility, risk and uncertainties of operating
in a foreign jurisdiction as well as additional risks described from time
to time in the filings made by Oceanus with securities regulators.

Glenn Jessome
President and CEO
902 492 0298
jessome@oceanusresources.ca
______________________________________
_______________________________________________
TSX Venture closing price for OCN-V
Date: 2016/12/13
Closing Price: 0.21
____________________________________________________________
(c)2016 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1634800035TS11634801290-08245620161214