Source	MARKET NEWS
Date	01/08/2018
Time	07:09:13 AM

Company	 Canamex Gold Corp.
Title	Updated PEA: 
NPV5 of $CAD 88.4 Million or $CAD 1





    CDNX Symbol: CSQ











Press Release




[200/News Release]CSQVCANAMEX GOLD CORPJAN 08 2018  07:04 AMUpdated PEA: 
NPV5 of $CAD 88.4 Million or $CAD 1.44 Per Share --->@NEWS RELEASE
CANAMEX GOLD CORP ("CSQ-V")
- Updated PEA: NPV5 of $CAD 88.4 Million or $CAD 1.44 Per Share

Canamex Gold Corp. (the "Company") is pleased to announce the
positive results of the Updated Preliminary Economic Assessment ("PEA")
on the 100% owned Bruner Gold Development Project, located in Nye
County, Nevada. The PEA was prepared by Welsh Hagen Associates (WHA) of
Reno, Nevada in accordance with the requirements of Canadian National
Instrument 43-101 "Standards of Disclosure for Mineral Projects" ("NI
43-101").

Highlights of the Updated PEA



- After-tax net present value at 5% discount rate (NPV5) $US 69.6
million ($CAD 88.4 million) or $CAD 1.44 per share (based on 61,365,676
shares currently on issue).

- The updated PEA adds 93,000 ounces of indicated resources of
gold and 826,000 ounces of indicated resources of silver to the
resources referenced in the 2016 PEA.

- Low pay-back period of nominally 1.65 years at $US 1,280/oz.
gold.

- Attractive after-tax IRR of 31% at $US 1280/oz gold price and
51.5% at $US 1,500/oz gold.

- Average annual production of 42,500 oz gold, and 44,250 oz
silver.

- 10-year operation, including a 2-year tail of gold and silver
recovery after mining.

- Average annual cash cost of $US 577/oz. for the first two years
and $US 872/oz. thereafter for an average cash cost of $US 796/oz.

- Low initial capital expenditures of $US 37.81 million, including
contingency of $ US 4.8 million, not including $US 6.8 million of
working capital.

- Contract mining with room for significant improvement on mining
costs with owner operated equipment and detailed scheduling of mining
costs between the three proposed pits.

- Facility siting and first two years of production entirely on
patented claims to allow for a streamlined permitting process for the
Phase 1 production scenario.

- Oxide heap leach processing with 90% recovery of gold on single
stage crushed material and 75% recovery of gold on run of mine (ROM)
material.

- The reported NI43-101 resources remain open in multiple
directions and are amenable to expansion with additional drilling.



Comments by Management

Greg Hahn, President and Chief Operating Officer of the Company
stated: "Completion of this updated PEA significantly advances the
Bruner Gold Project. This updated PEA extends the life of the
conceptual mine life from six to eight years and adds 93,000 ounces of
indicated resources of gold and 826,000 ounces of indicated resources
of silver to the resources referenced in the previous 2016 PEA. It also
tightens the capital and operating cost estimates by reference to
recently experienced actual costs on another gold development project
in Nevada. I believe we will be able to move the Bruner Gold Project
forward into permitting and development on the strength of this
positive PEA. The project includes the fundamental elements we consider
important to investors when building a mine, including low capital and
operating costs, and an attractive rate of return in the current price
environment. We can now move ahead with permitting and engineering the
project for development."

The Company cautions that the PEA is preliminary in nature in that
it includes some Inferred Mineral Resources which are considered too
speculative geologically to have the economic considerations applied to
them that would enable them to be characterized as mineral reserves,
and there is no certainty that the PEA will be realized. Mineral
resources that are not mineral reserves do not have demonstrated
economic viability. Dollar references are in US dollars. The exchange
rate used is 1.27 CAD to USD.

Financial Analysis

The PEA base case uses a gold price of $1,280/oz. and generates an
after-tax net present value (NPV5) of $US 69.6 million, after-tax IRR
of 31.0%, and an average annual after-tax net cash flow from operations
of $US 14.4 million for the ten years of gold recovery. The PEA results
are disclosed on an after-tax basis, and take into account the Nevada
Net Proceeds Tax, and federal and state income taxes after allowance
for accelerated depreciation of initial and sustaining capital, and
depletion allowance, but without allowance for depreciation of capital
investment to date. Project break-even (nil IRR) is reached at a gold
price of $US 958/oz, although the first two years of operation have a
break-even gold price of $849/oz. The mine production schedule is
developed such that a decision whether to proceed with the higher cost
Penelas pit development can be made based upon prevailing gold price at
the time, after the first two years of production and payback of
initial capital, and sufficient net cash flow is generated to pay for
the pre-stripping of the Penelas deposit.

Table 1: After-Tax Economic Sensitivity

//st

----------------------------------------------------------
|                        |Base           |Upside         |
|                        |Case$1,280/oz. |Case$1,500/oz. |
|                        |gold           |gold           |
|--------------------------------------------------------|
|IRR                     |31.0%          |51.5%          |
|--------------------------------------------------------|
|NPV@5% Discount Rate    |US$69.6 million|US$114 million |
|--------------------------------------------------------|
|Average Annual Cash Flow|US$14.4 million|US$19.7 million|
|--------------------------------------------------------|
|Average                 |$484/oz.       |$704/oz.       |
|Operational             |               |               |
|Margin                  |               |               |
|--------------------------------------------------------|
|Payback Period          |~1.65 year     |~1.25 year     |
----------------------------------------------------------

//et

Mining and Processing

The Bruner Gold Project PEA was prepared as an open pit mining
project. Contractor mining is assumed, using an average of current
contractor mining rates for similar sized projects in Nevada. There is
considerable room for improvement of the unit mining costs by properly
engineering and quantifying haul road distances and grades and
considering owner operated mining in further studies. Material grading
greater than 0.192 gpt gold will be crushed in a single stage jaw
crusher and conveyed onto the leach pad. Material grading between 0.117
and 0.192 gpt gold will be truck dumped on the leach pad and leached
run-of-mine (ROM). Crushed material will be processed at a rate of
approximately 7500 tonnes per day and conveyed onto a conventional heap
leach pad, with solution reporting to an adsorption-desorption recovery
(ADR) carbon plant producing a gold-silver dore product. Recoveries
used in the PEA include 90% on gold for single-stage crushed material,
75% on gold for ROM material, and only 10% on silver for all material
processed. Dore will be approximately 50:50 gold and silver. Over the
mine life, production will total approximately 21.755 million tonnes of
material at a gold grade of 0.56 gpt for a total payable of 349,300 oz.
of gold and 363,400 ounces of silver. Leached material will require 2
lbs/ton lime for pH adjustment and 0.2 lbs/ton sodium cyanide
consumption. The conceptual production schedule is as follows:

Table 2: Conceptual Production and Processing Summary

//st

-----------------------------------------------------------------
|Year|Tonnes |Gold |Contained|Recovered|Silver|Contained|Recd   |
|    |       |Grade|         |         |Grade |         |       |
|    |----------------------------------------------------------|
|    |(000's)|(gpt)|Gold     |Gold     |Grade |Silver   |Silver |
|    |       |     |(oz)     |(oz)     |      |(oz)     |(oz)   |
|---------------------------------------------------------------|
|1   |3,224  |0.501|51,936   |39,350   |4.87  |504,538  |42,920 |
|---------------------------------------------------------------|
|2   |3,279  |0.601|63,341   |50,850   |8.19  |863,161  |73,400 |
|---------------------------------------------------------------|
|3   |2,444  |0.445|34,948   |35,120   |3.55  |279,084  |31,290 |
|---------------------------------------------------------------|
|4   |2,877  |0.475|43,943   |41,110   |3.9   |360,307  |43,500 |
|---------------------------------------------------------------|
|5   |2,852  |0.549|50,339   |43,720   |5.05  |462,604  |43,540 |
|---------------------------------------------------------------|
|6   |2,839  |0.465|42,471   |38,230   |5.91  |539,441  |51,210 |
|---------------------------------------------------------------|
|7   |2,822  |0.645|58,563   |51,850   |4.68  |424,741  |43,070 |
|---------------------------------------------------------------|
|8   |1,417  |0.975|44,414   |39,810   |4.38  |199,635  |25,090 |
|---------------------------------------------------------------|
|9   |0      |    |        |5,260    |     |        |6,380  |
|---------------------------------------------------------------|
|10  |0      |    |        |4,000    |     |        |3,000  |
|---------------------------------------------------------------|
|   |      |    |        |        |     |        |      |
|---------------------------------------------------------------|
|LoM |21,755 |0.558|389,955  |349,300  |5.19  |3,633,511|363,400|
-----------------------------------------------------------------

//et

Note: Numbers in the table have been rounded to reflect the
accuracy of the estimate and may not sum due to rounding.

Capital and Operating Costs

Initial capital is estimated at $US 37.81 million, including $US
4.8 million for contingencies, but not including $US 8.1 million in
reclamation expenses, or $US 6.8 million for working capital.
Additional capital expenses such as a heap leach pad expansion and
pre-stripping of the Penelas pit bring the total LOM capital required
to $US 51.8 million. The PEA assumes contractor mining with the
contractor providing all mining equipment, maintenance, fuel and
explosives. Operating costs were estimated based on process design
criteria, current contractor mining rates at similar sized projects in
Nevada, grid power available from NV Energy's 60Kv line located in
Gabbs. All costs are in Q4 2017 dollars. Average cash costs are
$577/oz. for the first two years of operation and $872/oz, thereafter.
Break-even gold prices are $849/oz and $1012/oz respectively, or
$958/oz life-of-mine.

Table 3: Capital Cost Summary

//st

---------------------------------------------------------------------
|Capital Items (US$)              |Initial Capital|SustainingCapital|
|-------------------------------------------------------------------|
|Mine                             |$ 5.71 million |$11.2 million    |
|-------------------------------------------------------------------|
|Admin, Infrastructure, Processing|$21.11 million |$ 1.75 million   |
|-------------------------------------------------------------------|
|Indirect (includes EPCM,         |$              |$2.73 million    |
|contingency, owner costs)        |10.99          |                 |
|                                 |million        |                 |
|-------------------------------------------------------------------|
|Salvage                          |               |($1.7 million)   |
|-------------------------------------------------------------------|
|Total Capital Cost               |$37.81 million |$13.98 million   |
---------------------------------------------------------------------

//et

Table 4: Operating Cost Summary

//st

----------------------------------------------------
|                  |         |                     |
|--------------------------------------------------|
|                  |Cost per |Cost per payable     |
|                  |tonne    |ounceproduced (net of|
|                  |processed|silver)              |
|--------------------------------------------------|
|Mining            |$8.80    |$548                 |
|--------------------------------------------------|
|Processing        |$2.63    |$164                 |
|and Heap          |         |                     |
|Leach             |         |                     |
|--------------------------------------------------|
|G&A + Reclamation |$1.35    |$84                  |
|--------------------------------------------------|
|Total Cash Cost(1)|$12.78   |$796                 |
|--------------------------------------------------|
|All-In Cost(2)    |$15.16   |$944                 |
----------------------------------------------------

//et

Note 1: Cash cost is calculated by dividing total life-of-mine
production costs by total ounces produced. Note 2: All-in cost is
calculated by dividing the sum of all capital, operating, and royalty
and reclamation costs by total ounces produced.

Permitting & Property Location

The Bruner Project in Nye County, Central Nevada, is located on
both patented lands and on public lands managed by the Bureau of Land
Management (BLM) Carson City Office. The BLM and the Nevada Division of
Environmental Protection (NDEP) will be the primary regulatory agencies
responsible for ensuring environmental protection as the Bruner Project
progresses through permitting and approval processes.

While the project manager has had preliminary discussions with
both agencies regarding an initial mine development plan on the
project, formal Mining Plans of Operations have not been submitted yet,
and baseline studies to support permit applications have not yet
commenced. The Company expects that baseline studies to support an
Environmental Assessment will commence in the spring of 2018, and
permit applications will be prepared during 2018. All other applicable
State and Local permits will also be applied for in due course. It is
anticipated that permitting for the project will take approximately 18
months to complete. The Company has already secured approval from the
State of Nevada for adequate water rights necessary to conduct mining
activities. The approved water rights will be sufficient for
life-of-mine operations.

The Bruner Project is located within the Walker Lane gold trend.
The nearest mines are the Rawhide Mine located approximately 30 miles
to the west which was operated by Kennecott Minerals and produced in
excess of 1.7 million ounces of gold and 17 million ounces of silver
between 1980 and 2005, and the Paradise Peak Mine, located about 30
miles to the south, which was operated by FMC and produced in excess of
1.5 million ounces of gold and 20 million ounces of silver between
1980-2000. Canamex cautions that historical production from the statednearby 
mines has not been verified by the QP is not necessarily
indicative of the mineralization on the Bruner Project property.

Resource Estimate

The NI 43-101 compliant resource estimate included in the PEA was
performed by Randy Martin, SME-RM and is built upon prior work in 2015
by William Tanaka, FAusIMM and by Randy Martin, SME-RM as part of the
2016 original PEA, and is comprised only of gold resources that fall
within the boundaries of conceptual pits with engineered ramps and
smoothed walls. Grade models for all three resource areas HRA, Penelas,
and Paymaster were all re-created to reflect additional drilling
completed in all three areas since the original PEA in 2016. The
Resource has been updated to reflect the additional drilling and
refinements in relevant economic parameters.

Table 5: Mineral Resource Statement

Table is available at
https://www.thenewswire.com/archives/k1vFjDMa-updated-pea-npv5-of-cad-884-m
illion-or-cad-144-per-share.html



Table Notes:



- The Mineral Resource estimates were prepared in conformity with
CIM "Estimation of Mineral Resource and Mineral Reserves Best
Practices" guidelines and are reported in accordance with the Canadian
Securities Administrators NI 43-101.

- Mineral Resources are not Mineral Reserves and do not have
demonstrated economic viability. There is no certainty that all or any
part of the Mineral Resources estimated will be converted into Mineral
Reserves.

- Resources stated as contained within a potentially economic
minable open pit design with engineered ramps and smoothed walls;
economic cut-off grade parameters are: $1,250/oz Au and $15/oz Ag, 90%
gold recovery for crushed material, 10% silver recovery, $2.70/tonne
unit mining cost $4.23/tonne

- processing + G&A+ reclamation cost, 55-degree inter-ramp pit
slopes. Resources are reported using a 0.006 oz/t (0.192 gpt Au equiv.)
gold cut-off grade for crush material, and a 0.004 oz/t (0.117 gpt Au
equiv.) gold cut-off grade for crush material above internal breakeven
but below external breakeven cut-off.

- "gpt" means grams per metric tonne, "opt" means ounces per short
ton, "oz" means ounce(s), "IRR" means Internal Rate of Return.

- Numbers in the table have been rounded to reflect the accuracy
of the estimate and may not sum due to rounding. Tonnages have been
rounded to nearest 50 k-tonnes. Grades have been rounded to nearest
0.01 gpt. Contained ounces have been rounded to nearest K-oz.

- HRA Resource is based on designed pit for $1350 Au Price Cone
Shell.

- Penelas Resource is based on designed pit for $1350 Au Price
Cone Shell.

- Paymaster Resource is based on designed pit for $1350 Au Price
Cone Shell.

- External Breakeven Cut-off is the cut-off where value of metal
recovered equals the cost of mining and processing.

- Internal Breakeven Cut-off is the cut-off where value of metal
recovered equals the cost of processing.

Further Optimization, Cost Reductions and Project Potential

The Company believes there are opportunities to further improve
the economics of the Bruner Gold Project through continued exploration,
refinement of the resource model using deterministic constraints,
reductions in mining costs through detailed engineering and owner
operated mining, further drilling within gaps in the data in the
Penelas pit area, and possible pre-split blasting to increase pit
slopes and minimize waste mining, and potential increases in silver
extraction through further metallurgical testing. Metallurgical test
work will continue during the feasibility and permitting progresses.

RECOMMENDATIONS

WHA recommends the following work based on the positive results of
the PEA:




- Additional drilling to improve the confidence of the inferred
resources to indicated resources, and to test the open extensions of
the current resources.

- Additional infill drilling in the Paymaster zone surrounding the
current underground workings, and infill drilling in the core and in
the deeper Penelas mineralized zone.

- Column leach tests on large diameter core from the Paymaster and
Penelas resource areas.

- Commencement of permitting with the State of Nevada and the US
BLM.

- Engineering sufficient to support at least a pre-feasibility
study to develop the project as outlined in this PEA.

- Perfection of the water rights granted by the State of Nevada to
secure them for development.

This recommended work program is expected to cost approximately
US$3.5 million.

Qualified Persons

John Welsh, P.E., Rusty Hufford, P.E. (SME-RM), Carl Nesbitt,
(SME-RM), Doug Willis (CPG) and Randy Martin (SME-RM) are the Qualified
Persons as defined under NI 43-101 representing Welsh Hagen Associates
and have reviewed the contents of this press release for accuracy of
the technical and economic information presented. The report titled "NI
43-101 Technical Report on the Bruner Gold Project Updated Preliminary
Economic Assessment, Nye County, Nevada, USA" with an effective date of
December 26, 2017 has been prepared by Welsh Hagen Associates, an
independent geological consulting firm with a local office in Reno,
Nevada. This report will be available on SEDAR (www.sedar.com) within
45 days.

The technical contents of this news release have been reviewed and
approved by Gregory A. Hahn, President and COO of Canamex Gold
Corporation, CPG#7122, a Qualified Person as defined by Canadian
Securities Administrator National Instrument 43-101 "Standards of
Disclosure for Mineral Projects".

About the Company

Canamex Gold Corp. (TSX-V: CSQ) (OTCBB: CNMXF) (FSE: CX6) is
engaged in fast-tracking toward development of the Bruner Gold
Development Project in the prolific gold jurisdiction of Nye County,
Nevada. The region is home to several producing and past-producing
mines along the Walker Lane Trend. Canamex completed a positive
Preliminary Economic Assessment (PEA) on the Bruner Gold Development
Project in 2016. Based on additional drilling conducted on the
property, the company completed an updated PEA in 2018, which
significantly advances the project. The after-tax net present value at
5% discount rate (NPV5) is $US 69.6 million ($CAD 88.4 million) or $CAD
1.44 per share (based on 61,365,676 shares currently on issue). Canamex
is now moving the Bruner Gold Project forward into permitting and
development on the strength of this positive updated PEA. The second
asset is the Silverton Gold property, a gold exploration project, in
Nevada, which has geological similarities to the Long Canyon gold
deposit in Nevada, being mined by Newmont Mining. Canamex has signed
Agreements with Harmonychain AS, for Ethereum Blockchain Smart Contract
Tokens for Gold and Silver, as an alternative means of raising capital,
potentially without equity dilution. The Agreements secure the
exclusive rights to 6 (Six) Ethereum Token domain names, ticker codes,
and associated smart contracts, for Gold and Silver, if any of them
have been successfully completed by 31st December 2018. Further
information is available at http://canamexgold.com

ON BEHALF OF THE BOARD

David Vincent
Chief Executive Officer and Director

david.vincent@canamexgold.com

Mike Stark
Chairman of the Board
Contact: (604) 833-4278
mike.stark@canamexgold.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

CAUTIONARY NOTE TO US INVESTORS REGARDING RESOURCE ESTIMATION

Canamex Gold prepares its resource estimates in accordance with
standards of the Canadian Institute of Mining, Metallurgy and Petroleum
referred to in Canadian National Instrument 43-101 (NI 43-101). These
standards are different from the standards generally permitted in
reports filed with the SEC. Under NI 43-101, Canamex Resources reports
measured, indicated and inferred resources, measurements, which are
generally not permitted in filings made with the SEC. The estimation of
measured resources and indicated resources involve greater uncertainty
as to their existence and economic feasibility than the estimation of
proven and probable reserves. U.S. investors are cautioned not to
assume that any part of measured or indicated resources will ever be
converted into economically mineable reserves. The estimation of
inferred resources involves far greater uncertainty as to their
existence and economic viability than the estimation of other
categories of resources.

CAUTION CONCERNING FORWARD-LOOKING STATEMENTS

This news release includes certain forward-looking statements or
information. All statements other than statements of historical fact
included in this release are forward-looking statements that involve
various risks and uncertainties. Forward-looking statements in this
news release include statements in relation to the timing, cost and
other aspects of the planned 2018 program on the Bruner property; the
potential for development of the mineral resources; the potential
mineralization and geological merits of the Bruner property; and other
future plans, objectives or expectations of the Company. There can be
no assurance that such statements will prove to be accurate and actual
results and future events could differ materially from those
anticipated in such statements. Important factors that could cause
actual results to differ materially from the Company's plans or
expectations include the risk that actual results of current and
planned exploration activities, including the results of the Company's
2018 drilling program(s) on the Bruner property, will not be consistent
with the Company's expectations; the geology, grade and continuity of
any mineral deposits and the risk of unexpected variations in mineral
resources, grade and/or recovery rates; fluctuating metals prices;
possibility of accidents, equipment breakdowns and delays during
exploration; exploration cost overruns or unanticipated costs and
expenses; uncertainties involved in the interpretation of drilling
results and geological tests; availability of capital and financing
required to continue the Company's future exploration programs and
preparation of geological reports and studies; delays in the
preparation of geological reports and studies; the metallurgical
characteristics of mineralization contained within the Bruner property
are yet to be fully determined; general economic, market or business
conditions; competition and loss of key employees; regulatory changes
and restrictions including in relation to required permits for
exploration activities (including drilling permits) and environmental
liability; timeliness of government or regulatory approvals; and other
risks detailed herein and from time to time in the filings made by the
Company with securities regulators. In connection with the
forward-looking information contained in this news release, the Company
has made numerous assumptions, including that the Company's 2018
programs will proceed as planned and within budget. The Company
expressly disclaims any intention or obligation to update or revise any
forward-looking statements whether as a result of new information,
future events or otherwise, except as otherwise required by applicable
securities legislation.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1800700041TS11800701266-07041320180108


[200/News Release]CSQVCANAMEX GOLD CORPJAN 08 2018  07:04 AMUpdated PEA: 
NPV5 of $CAD 88.4 Million or $CAD 1.44 Per Share --->@NEWS RELEASE
CANAMEX GOLD CORP ("CSQ-V")
- Updated PEA: NPV5 of $CAD 88.4 Million or $CAD 1.44 Per Share

Canamex Gold Corp. (the "Company") is pleased to announce the
positive results of the Updated Preliminary Economic Assessment ("PEA")
on the 100% owned Bruner Gold Development Project, located in Nye
County, Nevada. The PEA was prepared by Welsh Hagen Associates (WHA) of
Reno, Nevada in accordance with the requirements of Canadian National
Instrument 43-101 "Standards of Disclosure for Mineral Projects" ("NI
43-101").

Highlights of the Updated PEA



- After-tax net present value at 5% discount rate (NPV5) $US 69.6
million ($CAD 88.4 million) or $CAD 1.44 per share (based on 61,365,676
shares currently on issue).

- The updated PEA adds 93,000 ounces of indicated resources of
gold and 826,000 ounces of indicated resources of silver to the
resources referenced in the 2016 PEA.

- Low pay-back period of nominally 1.65 years at $US 1,280/oz.
gold.

- Attractive after-tax IRR of 31% at $US 1280/oz gold price and
51.5% at $US 1,500/oz gold.

- Average annual production of 42,500 oz gold, and 44,250 oz
silver.

- 10-year operation, including a 2-year tail of gold and silver
recovery after mining.

- Average annual cash cost of $US 577/oz. for the first two years
and $US 872/oz. thereafter for an average cash cost of $US 796/oz.

- Low initial capital expenditures of $US 37.81 million, including
contingency of $ US 4.8 million, not including $US 6.8 million of
working capital.

- Contract mining with room for significant improvement on mining
costs with owner operated equipment and detailed scheduling of mining
costs between the three proposed pits.

- Facility siting and first two years of production entirely on
patented claims to allow for a streamlined permitting process for the
Phase 1 production scenario.

- Oxide heap leach processing with 90% recovery of gold on single
stage crushed material and 75% recovery of gold on run of mine (ROM)
material.

- The reported NI43-101 resources remain open in multiple
directions and are amenable to expansion with additional drilling.



Comments by Management

Greg Hahn, President and Chief Operating Officer of the Company
stated: "Completion of this updated PEA significantly advances the
Bruner Gold Project. This updated PEA extends the life of the
conceptual mine life from six to eight years and adds 93,000 ounces of
indicated resources of gold and 826,000 ounces of indicated resources
of silver to the resources referenced in the previous 2016 PEA. It also
tightens the capital and operating cost estimates by reference to
recently experienced actual costs on another gold development project
in Nevada. I believe we will be able to move the Bruner Gold Project
forward into permitting and development on the strength of this
positive PEA. The project includes the fundamental elements we consider
important to investors when building a mine, including low capital and
operating costs, and an attractive rate of return in the current price
environment. We can now move ahead with permitting and engineering the
project for development."

The Company cautions that the PEA is preliminary in nature in that
it includes some Inferred Mineral Resources which are considered too
speculative geologically to have the economic considerations applied to
them that would enable them to be characterized as mineral reserves,
and there is no certainty that the PEA will be realized. Mineral
resources that are not mineral reserves do not have demonstrated
economic viability. Dollar references are in US dollars. The exchange
rate used is 1.27 CAD to USD.

Financial Analysis

The PEA base case uses a gold price of $1,280/oz. and generates an
after-tax net present value (NPV5) of $US 69.6 million, after-tax IRR
of 31.0%, and an average annual after-tax net cash flow from operations
of $US 14.4 million for the ten years of gold recovery. The PEA results
are disclosed on an after-tax basis, and take into account the Nevada
Net Proceeds Tax, and federal and state income taxes after allowance
for accelerated depreciation of initial and sustaining capital, and
depletion allowance, but without allowance for depreciation of capital
investment to date. Project break-even (nil IRR) is reached at a gold
price of $US 958/oz, although the first two years of operation have a
break-even gold price of $849/oz. The mine production schedule is
developed such that a decision whether to proceed with the higher cost
Penelas pit development can be made based upon prevailing gold price at
the time, after the first two years of production and payback of
initial capital, and sufficient net cash flow is generated to pay for
the pre-stripping of the Penelas deposit.

Table 1: After-Tax Economic Sensitivity

//st

----------------------------------------------------------
|                        |Base           |Upside         |
|                        |Case$1,280/oz. |Case$1,500/oz. |
|                        |gold           |gold           |
|--------------------------------------------------------|
|IRR                     |31.0%          |51.5%          |
|--------------------------------------------------------|
|NPV@5% Discount Rate    |US$69.6 million|US$114 million |
|--------------------------------------------------------|
|Average Annual Cash Flow|US$14.4 million|US$19.7 million|
|--------------------------------------------------------|
|Average                 |$484/oz.       |$704/oz.       |
|Operational             |               |               |
|Margin                  |               |               |
|--------------------------------------------------------|
|Payback Period          |~1.65 year     |~1.25 year     |
----------------------------------------------------------

//et

Mining and Processing

The Bruner Gold Project PEA was prepared as an open pit mining
project. Contractor mining is assumed, using an average of current
contractor mining rates for similar sized projects in Nevada. There is
considerable room for improvement of the unit mining costs by properly
engineering and quantifying haul road distances and grades and
considering owner operated mining in further studies. Material grading
greater than 0.192 gpt gold will be crushed in a single stage jaw
crusher and conveyed onto the leach pad. Material grading between 0.117
and 0.192 gpt gold will be truck dumped on the leach pad and leached
run-of-mine (ROM). Crushed material will be processed at a rate of
approximately 7500 tonnes per day and conveyed onto a conventional heap
leach pad, with solution reporting to an adsorption-desorption recovery
(ADR) carbon plant producing a gold-silver dore product. Recoveries
used in the PEA include 90% on gold for single-stage crushed material,
75% on gold for ROM material, and only 10% on silver for all material
processed. Dore will be approximately 50:50 gold and silver. Over the
mine life, production will total approximately 21.755 million tonnes of
material at a gold grade of 0.56 gpt for a total payable of 349,300 oz.
of gold and 363,400 ounces of silver. Leached material will require 2
lbs/ton lime for pH adjustment and 0.2 lbs/ton sodium cyanide
consumption. The conceptual production schedule is as follows:

Table 2: Conceptual Production and Processing Summary

//st

-----------------------------------------------------------------
|Year|Tonnes |Gold |Contained|Recovered|Silver|Contained|Recd   |
|    |       |Grade|         |         |Grade |         |       |
|    |----------------------------------------------------------|
|    |(000's)|(gpt)|Gold     |Gold     |Grade |Silver   |Silver |
|    |       |     |(oz)     |(oz)     |      |(oz)     |(oz)   |
|---------------------------------------------------------------|
|1   |3,224  |0.501|51,936   |39,350   |4.87  |504,538  |42,920 |
|---------------------------------------------------------------|
|2   |3,279  |0.601|63,341   |50,850   |8.19  |863,161  |73,400 |
|---------------------------------------------------------------|
|3   |2,444  |0.445|34,948   |35,120   |3.55  |279,084  |31,290 |
|---------------------------------------------------------------|
|4   |2,877  |0.475|43,943   |41,110   |3.9   |360,307  |43,500 |
|---------------------------------------------------------------|
|5   |2,852  |0.549|50,339   |43,720   |5.05  |462,604  |43,540 |
|---------------------------------------------------------------|
|6   |2,839  |0.465|42,471   |38,230   |5.91  |539,441  |51,210 |
|---------------------------------------------------------------|
|7   |2,822  |0.645|58,563   |51,850   |4.68  |424,741  |43,070 |
|---------------------------------------------------------------|
|8   |1,417  |0.975|44,414   |39,810   |4.38  |199,635  |25,090 |
|---------------------------------------------------------------|
|9   |0      |    |        |5,260    |     |        |6,380  |
|---------------------------------------------------------------|
|10  |0      |    |        |4,000    |     |        |3,000  |
|---------------------------------------------------------------|
|   |      |    |        |        |     |        |      |
|---------------------------------------------------------------|
|LoM |21,755 |0.558|389,955  |349,300  |5.19  |3,633,511|363,400|
-----------------------------------------------------------------

//et

Note: Numbers in the table have been rounded to reflect the
accuracy of the estimate and may not sum due to rounding.

Capital and Operating Costs

Initial capital is estimated at $US 37.81 million, including $US
4.8 million for contingencies, but not including $US 8.1 million in
reclamation expenses, or $US 6.8 million for working capital.
Additional capital expenses such as a heap leach pad expansion and
pre-stripping of the Penelas pit bring the total LOM capital required
to $US 51.8 million. The PEA assumes contractor mining with the
contractor providing all mining equipment, maintenance, fuel and
explosives. Operating costs were estimated based on process design
criteria, current contractor mining rates at similar sized projects in
Nevada, grid power available from NV Energy's 60Kv line located in
Gabbs. All costs are in Q4 2017 dollars. Average cash costs are
$577/oz. for the first two years of operation and $872/oz, thereafter.
Break-even gold prices are $849/oz and $1012/oz respectively, or
$958/oz life-of-mine.

Table 3: Capital Cost Summary

//st

---------------------------------------------------------------------
|Capital Items (US$)              |Initial Capital|SustainingCapital|
|-------------------------------------------------------------------|
|Mine                             |$ 5.71 million |$11.2 million    |
|-------------------------------------------------------------------|
|Admin, Infrastructure, Processing|$21.11 million |$ 1.75 million   |
|-------------------------------------------------------------------|
|Indirect (includes EPCM,         |$              |$2.73 million    |
|contingency, owner costs)        |10.99          |                 |
|                                 |million        |                 |
|-------------------------------------------------------------------|
|Salvage                          |               |($1.7 million)   |
|-------------------------------------------------------------------|
|Total Capital Cost               |$37.81 million |$13.98 million   |
---------------------------------------------------------------------

//et

Table 4: Operating Cost Summary

//st

----------------------------------------------------
|                  |         |                     |
|--------------------------------------------------|
|                  |Cost per |Cost per payable     |
|                  |tonne    |ounceproduced (net of|
|                  |processed|silver)              |
|--------------------------------------------------|
|Mining            |$8.80    |$548                 |
|--------------------------------------------------|
|Processing        |$2.63    |$164                 |
|and Heap          |         |                     |
|Leach             |         |                     |
|--------------------------------------------------|
|G&A + Reclamation |$1.35    |$84                  |
|--------------------------------------------------|
|Total Cash Cost(1)|$12.78   |$796                 |
|--------------------------------------------------|
|All-In Cost(2)    |$15.16   |$944                 |
----------------------------------------------------

//et

Note 1: Cash cost is calculated by dividing total life-of-mine
production costs by total ounces produced. Note 2: All-in cost is
calculated by dividing the sum of all capital, operating, and royalty
and reclamation costs by total ounces produced.

Permitting & Property Location

The Bruner Project in Nye County, Central Nevada, is located on
both patented lands and on public lands managed by the Bureau of Land
Management (BLM) Carson City Office. The BLM and the Nevada Division of
Environmental Protection (NDEP) will be the primary regulatory agencies
responsible for ensuring environmental protection as the Bruner Project
progresses through permitting and approval processes.

While the project manager has had preliminary discussions with
both agencies regarding an initial mine development plan on the
project, formal Mining Plans of Operations have not been submitted yet,
and baseline studies to support permit applications have not yet
commenced. The Company expects that baseline studies to support an
Environmental Assessment will commence in the spring of 2018, and
permit applications will be prepared during 2018. All other applicable
State and Local permits will also be applied for in due course. It is
anticipated that permitting for the project will take approximately 18
months to complete. The Company has already secured approval from the
State of Nevada for adequate water rights necessary to conduct mining
activities. The approved water rights will be sufficient for
life-of-mine operations.

The Bruner Project is located within the Walker Lane gold trend.
The nearest mines are the Rawhide Mine located approximately 30 miles
to the west which was operated by Kennecott Minerals and produced in
excess of 1.7 million ounces of gold and 17 million ounces of silver
between 1980 and 2005, and the Paradise Peak Mine, located about 30
miles to the south, which was operated by FMC and produced in excess of
1.5 million ounces of gold and 20 million ounces of silver between
1980-2000. Canamex cautions that historical production from the statednearby 
mines has not been verified by the QP is not necessarily
indicative of the mineralization on the Bruner Project property.

Resource Estimate

The NI 43-101 compliant resource estimate included in the PEA was
performed by Randy Martin, SME-RM and is built upon prior work in 2015
by William Tanaka, FAusIMM and by Randy Martin, SME-RM as part of the
2016 original PEA, and is comprised only of gold resources that fall
within the boundaries of conceptual pits with engineered ramps and
smoothed walls. Grade models for all three resource areas HRA, Penelas,
and Paymaster were all re-created to reflect additional drilling
completed in all three areas since the original PEA in 2016. The
Resource has been updated to reflect the additional drilling and
refinements in relevant economic parameters.

Table 5: Mineral Resource Statement

Table is available at
https://www.thenewswire.com/archives/k1vFjDMa-updated-pea-npv5-of-cad-884-m
illion-or-cad-144-per-share.html



Table Notes:



- The Mineral Resource estimates were prepared in conformity with
CIM "Estimation of Mineral Resource and Mineral Reserves Best
Practices" guidelines and are reported in accordance with the Canadian
Securities Administrators NI 43-101.

- Mineral Resources are not Mineral Reserves and do not have
demonstrated economic viability. There is no certainty that all or any
part of the Mineral Resources estimated will be converted into Mineral
Reserves.

- Resources stated as contained within a potentially economic
minable open pit design with engineered ramps and smoothed walls;
economic cut-off grade parameters are: $1,250/oz Au and $15/oz Ag, 90%
gold recovery for crushed material, 10% silver recovery, $2.70/tonne
unit mining cost $4.23/tonne

- processing + G&A+ reclamation cost, 55-degree inter-ramp pit
slopes. Resources are reported using a 0.006 oz/t (0.192 gpt Au equiv.)
gold cut-off grade for crush material, and a 0.004 oz/t (0.117 gpt Au
equiv.) gold cut-off grade for crush material above internal breakeven
but below external breakeven cut-off.

- "gpt" means grams per metric tonne, "opt" means ounces per short
ton, "oz" means ounce(s), "IRR" means Internal Rate of Return.

- Numbers in the table have been rounded to reflect the accuracy
of the estimate and may not sum due to rounding. Tonnages have been
rounded to nearest 50 k-tonnes. Grades have been rounded to nearest
0.01 gpt. Contained ounces have been rounded to nearest K-oz.

- HRA Resource is based on designed pit for $1350 Au Price Cone
Shell.

- Penelas Resource is based on designed pit for $1350 Au Price
Cone Shell.

- Paymaster Resource is based on designed pit for $1350 Au Price
Cone Shell.

- External Breakeven Cut-off is the cut-off where value of metal
recovered equals the cost of mining and processing.

- Internal Breakeven Cut-off is the cut-off where value of metal
recovered equals the cost of processing.

Further Optimization, Cost Reductions and Project Potential

The Company believes there are opportunities to further improve
the economics of the Bruner Gold Project through continued exploration,
refinement of the resource model using deterministic constraints,
reductions in mining costs through detailed engineering and owner
operated mining, further drilling within gaps in the data in the
Penelas pit area, and possible pre-split blasting to increase pit
slopes and minimize waste mining, and potential increases in silver
extraction through further metallurgical testing. Metallurgical test
work will continue during the feasibility and permitting progresses.

RECOMMENDATIONS

WHA recommends the following work based on the positive results of
the PEA:




- Additional drilling to improve the confidence of the inferred
resources to indicated resources, and to test the open extensions of
the current resources.

- Additional infill drilling in the Paymaster zone surrounding the
current underground workings, and infill drilling in the core and in
the deeper Penelas mineralized zone.

- Column leach tests on large diameter core from the Paymaster and
Penelas resource areas.

- Commencement of permitting with the State of Nevada and the US
BLM.

- Engineering sufficient to support at least a pre-feasibility
study to develop the project as outlined in this PEA.

- Perfection of the water rights granted by the State of Nevada to
secure them for development.

This recommended work program is expected to cost approximately
US$3.5 million.

Qualified Persons

John Welsh, P.E., Rusty Hufford, P.E. (SME-RM), Carl Nesbitt,
(SME-RM), Doug Willis (CPG) and Randy Martin (SME-RM) are the Qualified
Persons as defined under NI 43-101 representing Welsh Hagen Associates
and have reviewed the contents of this press release for accuracy of
the technical and economic information presented. The report titled "NI
43-101 Technical Report on the Bruner Gold Project Updated Preliminary
Economic Assessment, Nye County, Nevada, USA" with an effective date of
December 26, 2017 has been prepared by Welsh Hagen Associates, an
independent geological consulting firm with a local office in Reno,
Nevada. This report will be available on SEDAR (www.sedar.com) within
45 days.

The technical contents of this news release have been reviewed and
approved by Gregory A. Hahn, President and COO of Canamex Gold
Corporation, CPG#7122, a Qualified Person as defined by Canadian
Securities Administrator National Instrument 43-101 "Standards of
Disclosure for Mineral Projects".

About the Company

Canamex Gold Corp. (TSX-V: CSQ) (OTCBB: CNMXF) (FSE: CX6) is
engaged in fast-tracking toward development of the Bruner Gold
Development Project in the prolific gold jurisdiction of Nye County,
Nevada. The region is home to several producing and past-producing
mines along the Walker Lane Trend. Canamex completed a positive
Preliminary Economic Assessment (PEA) on the Bruner Gold Development
Project in 2016. Based on additional drilling conducted on the
property, the company completed an updated PEA in 2018, which
significantly advances the project. The after-tax net present value at
5% discount rate (NPV5) is $US 69.6 million ($CAD 88.4 million) or $CAD
1.44 per share (based on 61,365,676 shares currently on issue). Canamex
is now moving the Bruner Gold Project forward into permitting and
development on the strength of this positive updated PEA. The second
asset is the Silverton Gold property, a gold exploration project, in
Nevada, which has geological similarities to the Long Canyon gold
deposit in Nevada, being mined by Newmont Mining. Canamex has signed
Agreements with Harmonychain AS, for Ethereum Blockchain Smart Contract
Tokens for Gold and Silver, as an alternative means of raising capital,
potentially without equity dilution. The Agreements secure the
exclusive rights to 6 (Six) Ethereum Token domain names, ticker codes,
and associated smart contracts, for Gold and Silver, if any of them
have been successfully completed by 31st December 2018. Further
information is available at http://canamexgold.com

ON BEHALF OF THE BOARD

David Vincent
Chief Executive Officer and Director

david.vincent@canamexgold.com

Mike Stark
Chairman of the Board
Contact: (604) 833-4278
mike.stark@canamexgold.com

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

CAUTIONARY NOTE TO US INVESTORS REGARDING RESOURCE ESTIMATION

Canamex Gold prepares its resource estimates in accordance with
standards of the Canadian Institute of Mining, Metallurgy and Petroleum
referred to in Canadian National Instrument 43-101 (NI 43-101). These
standards are different from the standards generally permitted in
reports filed with the SEC. Under NI 43-101, Canamex Resources reports
measured, indicated and inferred resources, measurements, which are
generally not permitted in filings made with the SEC. The estimation of
measured resources and indicated resources involve greater uncertainty
as to their existence and economic feasibility than the estimation of
proven and probable reserves. U.S. investors are cautioned not to
assume that any part of measured or indicated resources will ever be
converted into economically mineable reserves. The estimation of
inferred resources involves far greater uncertainty as to their
existence and economic viability than the estimation of other
categories of resources.

CAUTION CONCERNING FORWARD-LOOKING STATEMENTS

This news release includes certain forward-looking statements or
information. All statements other than statements of historical fact
included in this release are forward-looking statements that involve
various risks and uncertainties. Forward-looking statements in this
news release include statements in relation to the timing, cost and
other aspects of the planned 2018 program on the Bruner property; the
potential for development of the mineral resources; the potential
mineralization and geological merits of the Bruner property; and other
future plans, objectives or expectations of the Company. There can be
no assurance that such statements will prove to be accurate and actual
results and future events could differ materially from those
anticipated in such statements. Important factors that could cause
actual results to differ materially from the Company's plans or
expectations include the risk that actual results of current and
planned exploration activities, including the results of the Company's
2018 drilling program(s) on the Bruner property, will not be consistent
with the Company's expectations; the geology, grade and continuity of
any mineral deposits and the risk of unexpected variations in mineral
resources, grade and/or recovery rates; fluctuating metals prices;
possibility of accidents, equipment breakdowns and delays during
exploration; exploration cost overruns or unanticipated costs and
expenses; uncertainties involved in the interpretation of drilling
results and geological tests; availability of capital and financing
required to continue the Company's future exploration programs and
preparation of geological reports and studies; delays in the
preparation of geological reports and studies; the metallurgical
characteristics of mineralization contained within the Bruner property
are yet to be fully determined; general economic, market or business
conditions; competition and loss of key employees; regulatory changes
and restrictions including in relation to required permits for
exploration activities (including drilling permits) and environmental
liability; timeliness of government or regulatory approvals; and other
risks detailed herein and from time to time in the filings made by the
Company with securities regulators. In connection with the
forward-looking information contained in this news release, the Company
has made numerous assumptions, including that the Company's 2018
programs will proceed as planned and within budget. The Company
expressly disclaims any intention or obligation to update or revise any
forward-looking statements whether as a result of new information,
future events or otherwise, except as otherwise required by applicable
securities legislation.
____________________________________________________________
(c)2018 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1800700041TS11800701266-07041320180108