Source	Marketwire
Date	02/12/2013
Time	06:00:10 AM

Company	 INTERNATIONAL SAMUEL EXPLORATION CORP.
Title	International Samuel Exploration Corp.: 4.28 % Copper, 4 g/t Gold at Frog 
Property





    CDNX Symbol: ISS











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRE


FOR: International Samuel Exploration Corp.

TSX VENTURE SYMBOL: ISS

February 12, 2013

International Samuel Exploration Corp.: 4.28 % Copper, 4 g/t Gold at Frog 
Property


VANCOUVER, BRITISH COLUMBIA--(Marketwire - Feb. 12, 2013) - International 
Samuel Exploration Corp. (TSX VENTURE:ISS) (the "Company") is pleased to 
announce an exploration update from the 2012 exploration program on the 
company's 100% owned, 32,164.59 hectare, Frog Property. The Frog Property is 
located approximately 170 kilometres east-southeast of Dease Lake, British 
Columbia.

The 2012 Frog Property exploration program consisted of a multi-phase approach 
including: regional reconnaissance, detailed prospecting, detailed petrologic 
analysis of the outcrop and subcrop mineralization.

The detailed petrographic analysis was conducted for all the rock samples 
collected in the 2012 program. This analysis was two-fold, firstly using 25X 
and 50X hand lenses, 50-220X zoom digital USB scope feeding images directly 
into a computer to obtain lithology, structure, alteration, mineralization, 
mineral assemblages and mineral sequences. And secondly, fourteen samples were 
selected for further thin section petrologic study.

The petrographic analysis identified three alteration assemblages on the Frog 
Property:

/T/

--  The first and most common alteration assemblage, the property's main
assemblage, is biotite-magnetite-pyrite/marcasite +/- chlorite-epidote,
which occurs throughout the non-pervasive silica +/- clay flooding.

--  The second alteration assemblage on the property includes magnetite
replacement of hornblende and amphiboles in the granitoids. This
alteration appears to be both property-wide and does extend outside the
property boundary.

--  A third alteration assemblage found is muscovite-pyrite/marcasite-
magnetite +/- chlorite-epidote. This alteration apparently has a very
limited range, both vertically and horizontally, and is seen in only a
few samples.

/T/

Forex Prospect

The Forex Prospect on the Frog Property has 6 km x 4.6 km aerial extent, with 
copper-silver-gold and overlapping molybdenum-rhenium with anomaly. Of the 430 
rock samples collected, 101 of them returned copper values of 0.1% or higher. 
Nine samples within the area returned copper values above 1% with gold grades 
ranging 0.5 to 4 g/t. Sample 129606 was a grab from talus and was strongly 
mineralized, containing 4.28% copper and 4 g/t gold.

28 of the widely spaced samples on the Forex Prospect had elevated molybdenum 
values of 101 ppm to 4270 ppm, with an average of 724 ppm. The molybdenum 
values appear to be associated with rhenium; the rhenium values range from 0.04 
ppm to 1.245 ppm, with an average for the same 29 samples.

Technical information in this news release has been reviewed by Derrick 
Strickland P.Geo., a qualified person as defined in NI 43-101.

ON BEHALF OF THE BOARD OF DIRECTORS

Conrad Swanson, President

- 30 -

CONTACT INFO:

International Samuel Exploration Corp.
Conrad Swanson
President
604-718-5454 or Toll Free: 888-500-4587
info@internationalsamuel.com
www.internationalsamuel.com

The TSX Venture Exchange has not reviewed and does not accept responsibility 
for the adequacy or accuracy of the content of this news release.

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

MWDisclaimer
If you no longer want to receive announcements from us, please do 
not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=406583648