Source	MARKET NEWS
Date	02/27/2013
Time	05:28:08 AM

Company	 Standard Graphite Corporation
Title	Achieves 
Positive Metallurgical Results Obtained





    CDNX Symbol: SGH











Press Release	





STANDARD GRAPHITE CORP ("SGH-V")
- Achieves Positive Metallurgical Results Obtained On Mousseau
- East Graphite

Standard Graphite Corp. (the "Company") is pleased to report the
positive results from the ongoing metallurgical tests performed by SGS
Lakefield on sections of drill core from the first diamond drill program on
its flagship Mousseau East Deposit.

Standard initiated metallurgical beneficiation testing at SGS Mineral
Services in Lakefield, Ontario to characterize the graphite present on the
main portion of the historical deposit. The testing was done through Locked
Cycle Tests ("LCT"). These consist in a series of mechanical operations
including crushing and grinding to liberate the graphite from the matrix
followed by sieving and sorting and assaying of the different fractions to
characterize particle size and purity.

Three (3) runs have now been completed on composite drill core samples
from the main Mousseau East Deposit. The tests were carried out by
gradually increasing the polishing time from 30, 45 and 60 minutes in each
sample to evaluate its effects on the final product. The final treatment
produced a concentrate with a purity approximating 95% for all large and
medium size fractions. The results from the last run (60 minutes) are
presented below:

//st
Preliminary graphite distribution & recovery results
Mousseau East Project

Mesh size                Weight fraction (%)    Cg (%)
+48                                      7.0      94.5
+80                                     14.5      95.3
+150                                    21.9      94.9
+200                                    14.1      94.4
-200                                    42.5      81.9

//et

Chris Bogart, President & CEO comments: "We are extremely pleased with
these initial results having achieved a commercial product using standard
processing methods. Results can be expected to improve further by
optimizing and customizing the processing to our material". The three year
average value of this blend of graphite concentrates is ~$1400/tonne. This
has been calculated using the average of prices tracked by Industrial
Minerals using their FCL, CIF European port $/tonne price for medium to
large flake graphite concentrate."

SGS Mineral Services also estimated that the rejects would not require
post-treatment since they contain sufficient carbonate minerals to buffer
any potential acid generating reactions. This testing of the acid
generating potential of the rejects is crucial to determine the processing
involved during operations. Consequently, the rejects at Mousseau East
would require no additional treatment or separation thereby reducing
overall costs and environmental hazards.

Fieldwork is expected to resume during the second quarter of 2013 with
follow-up diamond drilling on its Mousseau East project aimed at better
defining and expanding the historical resource en-route to a N1 43-101
resource.

Antoine Fournier P. Geo., manages Standard's exploration and
development programs and is the Qualified Person as defined by National
Instrument 43-101. He supervised the preparation of the technical
information in this release.

About SGS Minerals Services

SGS Minerals Services was founded over half a century ago and is an
industry leader in a full range of metallurgical services including the
development of bankable flow sheets and pilot plant programs. Its
metallurgists, hydro-metallurgists and chemical engineers are experienced
in all the major physical and chemical separation processes utilized in the
recovery of metals and minerals contained in ore bodies around the world.

About Standard Graphite

Standard Graphite Corp is focused exclusively on the exploration and
development of a large portfolio of flake graphite properties in Canada.
The company is rapidly positioning itself as North America's premier
pure-play graphite exploration company and it controls 100% interest in 13
highly prospective graphite properties within known graphite districts in
both Quebec and Ontario. An aggressive 2012 exploration strategy has
commenced and will be implemented by a geologic team with the pedigree of a
previous world-class graphite discovery.

ON BEHALF OF THE BOARD
Chris Bogart, President & CEO

Cautionary Statement:

The foregoing information may contain forward-looking statements
relating to the future performance of Standard Graphite Corp.
Forward-looking statements, specifically those concerned with future
performance are subject to certain risks and uncertainties, and actual
results may differ materially. These risks and uncertainties are detailed
from time to time in Standard Graphite Corp.'s filings with the appropriate
securities commissions.

Neither the TSX Venture Exchange nor its Regulation Services Provider
(as that term is defined in the policies of the TSX Venture Exchange)
accepts responsibility for the adequacy or accuracy of this release.

TSX Venture closing price for SGH-V
Date: 2013/02/26
Closing Price: 0.16

TEL:  (604) 683-2509  Chris Bogart, President & CEO
FAX:  (604) 683-2506
EMAIL:  info@standardgraphite.com
____________________________________________________________
(c)2013 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1305700008TS11305700727-05253420130227