Source	Marketwire
Date	02/04/2014
Time	06:33:25 AM

Company	 AMEX EXPLORATION INC.
Title	New Gold-Bearing Horizon Identified at Amex's Perron Property, Abitibi





    CDNX Symbol: AMX











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Amex Exploration Inc.

TSX VENTURE SYMBOL: AMX

February 4, 2014

New Gold-Bearing Horizon Identified at Amex's Perron Property, Abitibi


MONTREAL, QUEBEC--(Marketwired - Feb. 4, 2014) - Amex Exploration Inc. (TSX 
VENTURE:AMX) ("Amex" or the "Corporation") is very pleased to announce that a 
new gold-bearing horizon has been identified following a first phase of 
drilling on Amex's Perron property executed under the option agreement with 
Agnico Eagle Mines Ltd ("AEM"; see press release of June 21st, 2013 for details 
on the option agreement terms and conditions).

This horizon, that has been intersected and recognized in 9 drill holes up to 
now, has an average width of about 15 to 20 meters (up to 80 meters) with gold 
values that range from 0.20 to 0.90 g/t (see table 1). The best result is from 
hole 163-13-002, with an intercept of 22,5 meters at 0,93 g/t Au including 1,5 
meters at 7,58 g/t Au. Geologically, this horizon is typically composed of high 
sericite and silica bearing rhyolitic volcanics associated with pyrite and, 
occasionally, with visible gold (VG). This stratigraphic horizon has been 
followed over a minimum strike length of 400 meters and to a depth of 400 
meters below surface and it is open in all directions.

Table 1: New identified gold-bearing horizon drill intersects.

/T/

--  PE-2013-02 : about 0.5 g/t Au over 15 m
--  PE-2013-01 : about 0.4 g/t Au over 20 m
--  163-13-003A : about 0.5 g/t Au over 15 m
--  PE-2011-04 : about 0.9 g/t Au over 7.7 m
--  PE-2000-65b-ext : about 0.2 g/t Au over 10.5 m
--  163-13-001 : about 0.2 g/t Au over 20 m
--  163-13-002 : about 0.9 g/t Au over 22.5 m
--  PE-1999-51p : about 0.2 g/t Au over 86.8 m
--  PE-2000-63 : about 0.3 g/t Au over 14.9 m

Note: gold values per intersect are an approximation based on partial
results from 2013 drilling and should be taken as a general reference.

/T/

This new horizon is located at the top of a rhyolitic unit (Rhyolite 6a), just 
under another rhyolitic unit that is lithogeochemically quite different 
(Rhyolite 7) within the Beaupre bloc (as recently identified by Barret et al., 
2013, "Report on the Burntbush-Normetal Volcanic Belt, ONT-QC", OGS, MR-Data 
299). This anomalous gold-bearing stratigraphic interval could correspond to an 
accumulation zone for fertile hydrothermal fluids located on top of Rhyolite 6a 
and trapped under the Rhyolite 7 that could have potentially acted as a 'cap 
rock'. Taking into account the extensive lateral extension of this anomalous 
gold-bearing horizon located at the upper part of t Rhyolite 6a, it should be 
considered as an exploration target for the next phase of work, considering 
also that a recent isotopic study on Rhyolite 6a is suggesting a similar age to 
the footwall unit of the nearby Normetal Mine (approx. 2725 Ma; Barrett et al., 
2013).

Table 2 : Results from AEM 2013 drilling.

/T/

----------------------------------------------------------------------------
Length
Hole                From      to     (m) Au (ppm) Ag (ppm) Cu (ppm) Zn (ppm)
----------------------------------------------------------------------------
163-13-001         485,5   492,9     7,4     0,31     0,10       12       21
----------------------------------------------------------------------------
497,0   507,0    10,0     0,26     0,10        3       16
----------------------------------------------------------------------------
567,0   568,0     1,0     2,27     1,50       44      354
----------------------------------------------------------------------------
715,5   724,5     9,0     0,75     0,25       13       40
----------------------------------------------------------------------------
incl.            715,5   717,0     1,5     2,85     0,20        4       31
----------------------------------------------------------------------------
751,5   753,0     1,5     5,32     0,90       33      231
----------------------------------------------------------------------------
793,5   795,0     1,5     1,31     0,60        7       16
----------------------------------------------------------------------------
799,5   808,5     9,0     0,17     0,52        7      118
----------------------------------------------------------------------------
163-13-002         258,0   280,5    22,5     0,93     0,10        3       47
----------------------------------------------------------------------------
incl.            262,5   264,0     1,5     7,58     0,10        3       81
----------------------------------------------------------------------------
and incl.        279,0   280,5     1,5     1,10     0,10        2       88
----------------------------------------------------------------------------
295,5   297,0     1,5     1,76     0,70        3       55
----------------------------------------------------------------------------
459,0   469,5    10,5     0,22     0,73       39      350
----------------------------------------------------------------------------
475,8   486,5    10,7     0,20     0,35       25      468
----------------------------------------------------------------------------
163-13-003A        290,5   292,0     1,5     1,08     0,10        4       28
----------------------------------------------------------------------------
317,5   326,5     9,0     1,80     0,12       17      149
----------------------------------------------------------------------------
incl.            319,8   321,1     1,3    10,80     0,10       16      788
----------------------------------------------------------------------------
571,3   579,0     7,7     0,41     0,19       20       45
----------------------------------------------------------------------------
incl.            576,5   577,5     1,0     1,98     0,30       51       35
----------------------------------------------------------------------------
632,5   633,5     1,0     2,66     1,10       22       58
----------------------------------------------------------------------------
PE-2000-65b-ext    466,5   472,5     6,0     0,44     0,22       34      108
----------------------------------------------------------------------------
478,5   480,0     1,5     1,33     0,10       70       36
----------------------------------------------------------------------------
505,5   507,0     1,5     8,80     1,70      225    1 055
----------------------------------------------------------------------------
586,5   588,0     1,5     2,39     0,90       14      514
----------------------------------------------------------------------------
Note: 5 drill holes totalling 2735 meters have been drilled by AEM in late
2013. Hole 163-13-003 was stopped early due to deviation and was 'redrilled'
at the same location with hole 163-13-003A. Hole PE-2000-65b-ext is a hole
that was previously drilled by Amex and deepened by AEM. Geochemical
analysis was executed by ALS Chemex Laboratories in Val d'Or under AEM QA/QC
program and supervision.

/T/

In addition to this major highlight from this drilling campaign, it is also now 
interpreted that the high grade polymetallic gold-rich sulphide mineralization 
intersected by Amex in its discovery hole PE-2013-03 (see press release of 
March 4th 2013) is potentially located in close relationship with a synvolcanic 
fault that could be genetically related to the encountered alteration and 
mineralization. The identification of such an environment for hole PE-2013-03 
is coherent with a typical VMS (volcanogenic massive sulphide ) deposit of the 
DBL (Dumagami-LaRonde-Bousquet) gold-rich deposits type of the Quebec Abitibi 
greenstone Belt.

Jacques Trottier, PhD, President and CEO of Amex Exploration comments, "We are 
very pleased with Agnico Eagle's work done so far on our Perron Property. From 
their work and expertise, various gold target types have been identified and 
should be further tested in a follow-up exploration program still to be 
confirmed and announced. We look forward seeing Agnico Eagle to resume 
exploration work as soon as possible in 2014."

Table 3: Amex 2013 drilling results completed with additional and re-sampling 
done by AEM.

/T/

----------------------------------------------------------------------------
Length
Hole                From      To     (m) Au (ppm) Ag (ppm) Cu (ppm) Zn (ppm)
----------------------------------------------------------------------------
PE-2013-01          70,6    72,0     1,4     4,98        -        -        -
----------------------------------------------------------------------------
81,0    85,5     4,5     0,27     0,07        2       99
----------------------------------------------------------------------------
139,5   141,0     1,5     2,56     0,10        2      252
----------------------------------------------------------------------------
151,1   160,1     9,0     4,99     0,04        2       15
----------------------------------------------------------------------------
incl.            156,1   156,6     0,5    81,84        -        -        -
----------------------------------------------------------------------------
and incl.        156,6   157,3     0,7     4,74        -        -        -
----------------------------------------------------------------------------
181,5   201,2    19,7     0,41     0,06        2       27
----------------------------------------------------------------------------
400,9   401,2     0,3     0,04     1,70       89   33 400
----------------------------------------------------------------------------
405,5   405,8     0,4     0,18     6,70      412  100 500
----------------------------------------------------------------------------
407,2   408,2     1,0     1,13        -        -        -
----------------------------------------------------------------------------
467,6   475,5     7,9     0,26     0,12        9       46
----------------------------------------------------------------------------
incl.            469,2   470,2     1,0     1,25     0,40       37       51
----------------------------------------------------------------------------
481,3   481,8     0,5     1,98        -        -        -
----------------------------------------------------------------------------
PE-2013-02          15,0    40,2    25,2     0,26     0,08        2       19
----------------------------------------------------------------------------
incl.             34,6    40,2     5,6     0,68     0,21        4       41
----------------------------------------------------------------------------
40,5    47,9     7,4     0,45        -        -        -
----------------------------------------------------------------------------
PE-2013-03         197,1   198,6     1,5     5,14        -        -        -
----------------------------------------------------------------------------
362,7   363,0     0,3    12,70        -        -        -
----------------------------------------------------------------------------
363,2   363,8     0,6     1,93        -        -        -
----------------------------------------------------------------------------
375,8   417,2    41,4     2,19    11,51      742    8 516
----------------------------------------------------------------------------
incl.            375,8   376,3     0,5     5,80    17,50      987   44 000
----------------------------------------------------------------------------
and incl.        381,0   381,5     0,5     6,89     6,50      558    9 500
----------------------------------------------------------------------------
and incl.        388,0   391,0     3,0     3,96     8,22    1 030    3 384
----------------------------------------------------------------------------
and incl.        402,0   417,2    15,2     3,84    22,81    1 039   14 187
----------------------------------------------------------------------------
and incl.        410,5   412,5     2,0    19,07   101,82    3 765   50 250
----------------------------------------------------------------------------
450,1   457,6     7,5     1,50    18,35    2 532    1 228
----------------------------------------------------------------------------
465,7   476,2    10,5     1,13    15,20    1 360   17 985
----------------------------------------------------------------------------
PE-2013-04         123,0   124,5     1,5     1,07     0,10        8       16
----------------------------------------------------------------------------
128,2   128,8     0,6     1,37        -        -        -
----------------------------------------------------------------------------
181,7   182,9     1,2     1,26     0,10        2       26
----------------------------------------------------------------------------
206,3   216,6    10,3     0,84     0,12        7       71
----------------------------------------------------------------------------
incl.            206,3   206,7     0,4     2,53        -        -        -
----------------------------------------------------------------------------
and incl.        207,7   208,5     0,8     1,49     0,40       10      163
----------------------------------------------------------------------------
and incl.        210,9   211,2     0,3    12,93        -        -        -
----------------------------------------------------------------------------
and incl.        214,2   214,7     0,5     2,20        -        -        -
----------------------------------------------------------------------------
232,5   234,0     1,5     1,18     0,20        -        5
----------------------------------------------------------------------------
278,6   280,1     1,5     1,45     0,50        2      156
----------------------------------------------------------------------------
307,5   309,0     1,5     1,82     0,20        5       86
----------------------------------------------------------------------------
324,9   329,7     4,8     0,94     0,21        6       69
----------------------------------------------------------------------------
incl.            328,8   329,7     0,9     3,39        -        -        -
----------------------------------------------------------------------------
352,0   363,5    11,5     0,50     0,01        1        
5----------------------------------------------------------------------------
incl.            358,5   359,5     1,0     2,51        -        -        -
----------------------------------------------------------------------------

/T/

Amex Exploration Inc. is a junior mining exploration company listed on the TSX 
Venture Exchange whose primary objective is to develop and bring into 
production viable gold and base metal deposits. Jacques Trottier, PhD Geol, 
Qualified Person as defined by Canadian N43-101 has approved the technical 
information reported in this news release.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Amex Exploration Inc.
Jacques Trottier
514-866-8209
Fax: 514-866-8096

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=465785145