Source	Marketwire
Date	02/18/2014
Time	09:10:10 AM

Company	 EXCELSIOR MINING CORP.
Title	Excelsior Files Prefeasibility Study for Gunnison





    CDNX Symbol: MIN











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Excelsior Mining Corp.

TSX VENTURE SYMBOL: MIN
OTCQX SYMBOL: EXMGF
FRANKFURT SYMBOL: 3XS

February 18, 2014

Excelsior Files Prefeasibility Study for Gunnison


PHOENIX, ARIZONA--(Marketwired - Feb. 18, 2014) - Excelsior Mining Corp. (TSX 
VENTURE:MIN)(FRANKFURT:3XS)(OTCQX:EXMGF) ("Excelsior" or the "Company") is 
pleased to announce that it has filed a National Instrument ("NI") 43-101 
Technical Report dated February 18, 2014 on SEDAR at www.sedar.com. The Report 
is with respect to Excelsior's Prefeasibility Study ("PFS") on the Gunnison 
Copper Project in southern Arizona; the results of which were originally 
announced in a January 17, 2014 news release. The final results of the PFS are 
presented below in this news release. Some of the final results differ from the 
results set out in the January 17, 2014 press release, but the variance is less 
than 1% unless otherwise noted below. Results of the PFS disclosed in this news 
release are in USD and pre-tax (except where otherwise indicated).

Prefeasibility Study Results

Highlights of the North Star Gunnison Copper Project PFS "Acid Plant" option 
include:

/T/

--  Pre-tax Net Present Value ("NPV") of $1.24 billion (after-tax $0.824
billion) at a 7.5% discount rate (using a copper price of $2.75/lb);
--  Pre-tax Internal Rate of Return ("IRR") of 59.7% (after-tax 44.7%);
--  Pre-tax payback period of 1.8 years (after-tax 2.4 years);
--  Initial estimated capital cost (excluding sustaining capital) of $284.84
million;
--  Average life-of-mine operating costs of US$0.69 per pound;
--  Other costs of $0.13 per pound, including Royalties of $0.029 per pound;
--  Annual production rate of 110 million pounds of copper for the first 14
years, then declining for a 20 year mine life, with a total of 1.682
billion pounds of copper produced over the life of the mine.

/T/

Financial Analysis

As highlighted in the tables below, the PFS demonstrates robust project 
economics in both the "Acid Plant" and "Non-Acid Plant" scenarios, with the 
Acid Plant option adding an additional $173.8 million to the project pre-tax 
NPV. Based on an initial annual production rate of 110 million pounds, the PFS 
indicates that including an Acid Plant as a component of the project, generates 
a pre-tax NPV of $1.24 billion, at a cash flow discount rate of 7.5%. The 
pre-tax IRR for this option is 59.7% with a payback period of 1.8 years. On an 
after-tax basis, the PFS shows an NPV7.5 of $824.17 million, IRR of 44.7% and a 
payback period of 2.4 years.

Without an Acid Plant, the project still has a significant pre-tax NPV7.5 of 
$1.06 billion and an IRR of 61.3%, (after-tax NPV7.5 of $720.4 million and an 
IRR of 46.1%). The after-tax analysis is based on a number of assumptions which 
will be fully set out in the Report. The level of accuracy of the PFS is 
considered to be +/-20%.

Both scenarios used the following parameters over the 20 year life of the 
project:

/T/

--  copper selling price of $2.75 per pound,
--  total copper recovery of approximately 47% (based on a combination of
metallurgical recovery and sweep efficiency),
--  average of 8.14 pounds of acid consumed for every pound of copper
produced,
--  acid price of $45.47/ton for the Acid Plant option and $125/ton for the
Non-Acid Plant option,
--  state tax rate of 6.97%, and
--  a federal tax rate of 35%.

----------------------------------------------------------------------------
PRE-TAX                                      Acid Plant      Non-Acid Plant
----------------------------------------------------------------------------
IRR                                               59.7%               61.4%
----------------------------------------------------------------------------
Payback (years)                                     1.8                 1.5
----------------------------------------
NPV (million $)
----------------------------------------
Discount Rate
0%            2,368.4             1,956.0
5%            1,522.7             1,293.0
7.5%            1,236.8             1,063.0
10%            1,012.5               880.0
----------------------------------------------------------------------------



----------------------------------------------------------------------------
AFTER-TAX                                    Acid Plant      Non-Acid Plant
----------------------------------------------------------------------------
IRR                                                44.7%               46.1%
----------------------------------------------------------------------------
Payback (years)                                     2.4                 2.0
----------------------------------------------------------------------------
NPV (million $)
Discount Rate
----------------------------------------
0%            1,616.1             1,354.9
5%            1,025.8               885.5
7.5%              824.2               720.4
10%              665.2               588.2
----------------------------------------------------------------------------

/T/

Total initial capital expenditures for the "Acid Plant" option (including 
contingency) are estimated at $284.84 million. Sustaining capital, which 
includes the acid plant built in year three, water treatment facilities and 
production wellfield are estimated at $598.8million. Net closure costs are 
estimated at $52.65 million(1). For the "Non-Acid Plant" option, total initial 
capital expenditures (including contingency) are estimated at $284.84 million. 
Sustaining capital, which includes the water treatment facilities and 
production wellfield are estimated at $525.2 million. Net closure costs are 
estimated at $45.2 million(2).

The PFS assumes a copper selling price of $2.75/lb. Average life-of-mine 
operating direct cash costs are estimated at $0.69/lb for the "Acid Plant" 
option and $0.98/lb for the "Non-Acid Plant" option.

/T/

----------------------------------------------------------------------------
Acid Plant          Non-Acid Plant
----------------------------------------------------------------------------
Copper Cathode sold (MMlb)                     1,682                   1,682
Copper Price ($/lb)                             2.75                    2.75
Gross Revenue (million $)                    4,625.9                 4,625.9
----------------------------------------------------------------------------
Operating Costs              (million $)     Cost/lb (million $)     Cost/lb
Production (Wellfield)       447.8        0.27       935.5        0.56
SXEW    360.8(3)        0.21    372.8(4)        0.22
Water Treatment Plant       199.7        0.12       199.7        0.12
G&A       147.3        0.09       147.3        0.09
Direct Operating Cash Costs      1,155.6        0.69     1,655.2        0.98
Royalties                           48.3        0.03        48.3        0.03
Other Production Expenses       169.9(5)        0.10    156.4(6)        0.09
----------------------------------------------------------------------------
Initial Capital Costs        (million $)     Cost/lb (million $)     Cost/lb
Production (Wellfield)        75.3        0.04        75.3        0.04
SXEW + Infrastructure       186.3        0.11       186.3        0.11
Owners Costs        23.2        0.01        23.2        0.01
Sub-total Initial Capital
Costs                             284.8        0.17       284.8        0.17
------------------------------------------------
Sustaining Capital Costs     (million $)     Cost/lb (million $)     Cost/lb
Production (Wellfield)       440.7        0.26       440.7        0.26
Plant + Infrastructure    158.1(7)        0.10     84.6(8)        0.05
------------------------------------------------
Sub-total Sustaining Capital
Costs                             598.8        0.36       525.2        0.31
----------------------------------------------------------------------------
Taxes                              752.3        0.45       601.1        0.36
----------------------------------------------------------------------------

/T/

Noted Variances:

/T/

----------------------------------------------------------------------------
(1)18.3% Increase  (2)6.9% Increase   (3)1.4% Increase   (4)1.4% Increase
----------------------------------------------------------------------------
(5)5% Increase     (6)1.9% Increase   (7)2.5% Increase   (8)4.5% Increase
----------------------------------------------------------------------------

/T/

Project Summary

The Gunnison Copper Project is located in a remote section of Cochise County 
about 65 miles east of Tucson, Arizona in the Johnson Camp Mining District. The 
property is within the copper porphyry belt of Arizona.

Technical Report and Qualified Person

The PFS Report was prepared under the supervision of Conrad Huss, P.E. of M3 
Engineering & Technology Corporation, Tucson, Arizona, who is a qualified 
person that is independent of the Company. The Report also received 
contributions from the following additional qualified persons, who are also 
independent of the Company:

/T/

--  Dr. Ronald J. Roman of Leach, Inc., Tucson, Arizona (metallurgy and
leaching recovery).
--  Peter Lenton, P.E. of Haley & Aldrich, Phoenix, Arizona (hydrology,
extraction methods, production schedule).
--  Thomas L. Drielick, P.E. of M3 Engineering & Technology Corporation,
Tucson, Arizona (SX-EW treatment and related facilities).
--  Mr. Herb Welhener, MMSA-QPM, of IMC of Tucson, Arizona (geology, mineral
resource and reserve).

/T/

Each of the qualified persons has reviewed and approved the technical 
information contained in this news release that is relevant to his area of 
responsibility and verified the data underlying such technical information.

Engagement of Investor Relations Consultant

Excelsior also announces that Liolios Group, Inc. ("Liolios") has been engaged 
to support the Company's investor relations activities.

Terms of Engagement

During the term of the agreement with Liolios, Liolios will collaborate with 
Company management on a non-exclusive basis to provide services which will 
include, but not be limited to, the development, implementation and maintenance 
of an on-going stock market support system aimed at increasing investor 
awareness of the Company's activities and to stimulate investor awareness in 
the Company. Liolios will disseminate public information about the Company to 
key investment professionals and private parties, and as well to Liolios's 
existing database of business associates and investment professionals in both 
the United States of America and Canada. In addition to the ongoing 
communication and introduction of the company to key members of the financial 
brokerage and investment community, they will conduct periodic conference 
calls, identify investor conferences which may be of interest to the Company, 
and arrange group or individual meetings with portfolio managers, analysts, 
stockbrokers, and other investment professionals.

As compensation for the services provided under the agreement, the Company 
agrees to pay fees of up to US$8,000 per month to Liolios, and the Company has 
sufficient cash in its treasury to pay the fees for Liolios services. The 
agreement with Liolios shall be automatically renewed on a month to month basis 
unless either party provides thirty days' notice of termination to the other 
party. The Liolios' engagement is subject to acceptance by the TSX Venture 
Exchange.

Liolios is independent of the Company, does not hold any securities of the 
Company and does not have any direct or indirect interest in the Company. 
Liolios and it principals do not engage in market making activities and the 
firm will restrict its services to public relations and investor relations 
consulting. Liolios will provide its services from its offices located in 
Newport Beach, New York and Toronto.

About Liolios Group

Liolios Group is a highly selective and comprehensive investor relations firm 
specializing in micro to mid-cap companies. The firm aims to deliver superior 
performance in corporate messaging and positioning, investor awareness, analyst 
and financial press coverage and capital attraction. Founded in 1999 by J. 
Scott Liolios, Liolios Group executives have extensive experience in financial 
and investments and represent clients in a wide range of industries, including 
life sciences/healthcare, consumer/internet retail, business services, digital, 
media/software, clean technology, technology, natural resources and special 
situations. For more information about Liolios Group, visit www.liolios.com.

About Excelsior

Excelsior is a mineral exploration and development company that is advancing 
the Gunnison Copper Project. The Excelsior management team consists of 
experienced professionals with proven track records of advancing mining 
projects into production.

Further information about the Gunnison Copper Project can be found in the 
technical report filed on SEDAR at www.sedar.com entitled: "Gunnison Copper 
Project, NI 43-101 Technical Report, Prefeasibility Study" dated February 14, 
2014.

For more information on Excelsior, please visit our website at 
www.excelsiormining.com.

ON BEHALF OF THE EXCELSIOR BOARD

/T/

"Stephen Twyerould"
President & CEO

/T/

Cautionary Note Regarding Forward-Looking Information
This news release contains "forward-looking information" concerning anticipated 
developments and events that may occur in the future. Forward looking 
information contained in this news release includes, but is not limited to, 
statements with respect to: (i) the estimation of mineral resources and mineral 
reserves; (ii) the robust economics, potential returns associated with the 
Gunnison Project, (iii) the technical viability of the Gunnison Project; (iv) 
the market and future price of copper; (v) expected infrastructure 
requirements; (vi) the results of the PFS including statements about future 
production, future operating and capital costs, the projected IRR, NPV, payback 
period, construction timelines, permit timelines and production timelines for 
the Gunnison Project, (vii) expected acid consumption rates; and (viii) the 
ability to mine the Gunnison Project using in-situ recovery mining techniques.

In certain cases, forward-looking information can be identified by the use of 
words such as "plans", "expects" or "does not expect", "is expected", "budget", 
"scheduled", "estimates", "forecasts", "intends", "anticipates" or "does not 
anticipate", or "believes", or variations of such words and phrases or state 
that certain actions, events or results "may", "could", "would", "might" or 
"will be taken", "occur" or "be achieved" suggesting future outcomes, or other 
expectations, beliefs, plans, objectives, assumptions, intentions or statements 
about future events or performance. Forward-looking information contained in 
this news release is based on certain factors and assumptions regarding, among 
other things, the estimation of mineral resources and mineral reserves, the 
realization of resource and reserve estimates, copper and other metal prices, 
the timing and amount of future exploration and development expenditures, the 
estimation of initial and sustaining capital requirements, the estimation of 
labour and operating costs, the availability of necessary financing and 
materials to continue to explore and develop the Gunnison Project in the short 
and long-term, the progress of exploration and development activities, the 
receipt of necessary regulatory approvals, the completion of the permitting 
process, the estimation of insurance coverage, and assumptions with respect to 
currency fluctuations, environmental risks, title disputes or claims, and other 
similar matters. While the Company considers these assumptions to be reasonable 
based on information currently available to it, they may prove to be incorrect.

Forward looking information involves known and unknown risks, uncertainties and 
other factors which may cause the actual results, performance or achievements 
of the Company to be materially different from any future results, performance 
or achievements expressed or implied by the forward-looking information. Such 
factors include risks inherent in the exploration and development of mineral 
deposits, including risks relating to changes in project parameters as plans 
continue to be redefined including the possibility that mining operations may 
not commence at the Gunnison Project, risks relating to variations in mineral 
resources and reserves, grade or recovery rates resulting from current 
exploration and development activities, risks relating to the ability to access 
infrastructure, risks relating to changes in copper and other commodity prices 
and the worldwide demand for and supply of copper and related products, risks 
related to increased competition in the market for copper and related products 
and in the mining industry generally, risks related to current global financial 
conditions, uncertainties inherent in the estimation of mineral resources, 
access and supply risks, reliance on key personnel, operational risks inherent 
in the conduct of mining activities, including the risk of accidents, labour 
disputes, increases in capital and operating costs and the risk of delays or 
increased costs that might be encountered during the development process, 
regulatory risks, including risks relating to the acquisition of the necessary 
licenses and permits, financing, capitalization and liquidity risks, including 
the risk that the financing necessary to fund the exploration and development 
activities at the Gunnison Project may not be available on satisfactory terms, 
or at all, risks related to disputes concerning property titles and interest, 
environmental risks and the additional risks identified in the "Risk Factors" 
section of the Company's reports and filings with applicable Canadian 
securities regulators.

Although the Company has attempted to identify important factors that could 
cause actual actions, events or results to differ materially from those 
described in forward-looking information, there may be other factors that cause 
actions, events or results not to be as anticipated, estimated or intended. 
Accordingly, readers should not place undue reliance on forward-looking 
information. The forward-looking information is made as of the date of this 
news release. Except as required by applicable securities laws, the Company 
does not undertake any obligation to publicly update or revise any 
forward-looking information.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release, and no securities 
regulatory authority has either approved or disapproved of the contents of this 
release.

- 30 -

CONTACT INFO:

Excelsior Mining Corp.
JJ Jennex, Vice President, Corporate Affairs
604-681-8030 x240
info@excelsiormining.com
www.excelsiormining.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=467737919