Source	MARKET NEWS
Date	02/26/2014
Time	06:36:17 AM

Company	 Mirasol Resources Ltd.
Title	Expands 
Targets at Atlas High sulphidation Silve





    CDNX Symbol: MRZ











Press Release	





MIRASOL RESOURCES LTD ("MRZ-V;MRZLF-0")
- Expands Targets at Atlas High-sulphidation Silver-Gold Project
- in the Gorbea Belt, Chile

Mirasol Resources Ltd. is pleased to report encouraging silver and
gold assay results from a recent project-wide rock chip sampling
program at its 100%-owned Atlas high-sulphidation epithermal precious
metal project, in the Gorbea Belt, Chile. These samples have returned
assays of up to 2.91 g/t Au and 2,470.0 g/t Ag from float and outcrop,
highlighting a number of new gold and silver targets and significantly
expanding the recognized area of surface mineralization at the Atlas
project.

The Gorbea Belt (Figure 1) is Mirasol's new strategic area-play
for high-sulphidation epithermal gold and silver mineralization in
Chile.  The Gorbea Belt is located in the prolifically mineralized
Miocene-age volcanic arc, and is situated approximately 150 km north of
the Maricunga Belt which contains two major gold and silver mines
(Maricunga Mine and La Coipa), and five large-scale gold and copper
deposits.

Mirasol's Atlas and Titan projects are the most advanced of the
Company's nine 100%-owned precious metals properties (Figure1) in the
Gorbea Belt. At Titan, Mirasol recently reported encouraging oxide gold
results from the near-surface in the first round of drilling (see news
release of November 25, 2013).  Atlas and Titan have the logistical
advantage of being located only eight km apart with good access via a
well-travelled gravel road, which will benefit exploration and
potential future development.

At Atlas, Mirasol applied a combination of short-wave infrared
alteration-vectoring, trace-element gridding and detailed remote
sensing to focus this season's field exploration into the more
prospective areas of the +25 sq km alteration system. A total of 1,020
rock chip samples were collected from October to December 2013, during
ground reconnaissance of these areas.  Combined with last season's
sampling, these samples give Mirasol a rock chip data base with an
impressive 3,032 assay points across the project; however, large areas
of the project are covered by late syn-mineral to post-mineral flow
domes and lavas, as well as scree and soil, which could conceal
additional mineralized areas.

Preliminary analysis of the Atlas rock chip database (Figure 2)
shows widespread anomalous gold and silver mineralization across the
project. To date, five discrete prospect areas have been identified
where surface outcrop or float samples assayed higher than 1 g/t gold
and/or contained silver greater than 60 g/t.

Assay results from this season's sampling have increased the areal
extent of the AGZ (Atlas Gold Zone) and ASZ (Atlas Silver Zone)
prospects where Mirasol previously reported encouraging gold and silver
channel results from an initial trenching program (see news release of
September 16, 2013).  This season's assays include silicified float
from ASZ assaying up to 0.189 g/t Au and 492.0 g/t Ag. Higher grade
assays from new target areas include float samples of brecciated and
vuggy silica assaying 2.91 g/t Au and 24.3 g/t Ag from an area located
1.5 km to the southwest of the ASZ.  In the northern extent of the
project area, 3 km northeast of the AGZ, silicified float returned
assays up to 0.02 g/t Au and 2,470.0 g/t Ag.

Information gathered to date at Atlas, including publicly
available radiometric age-dates of alteration, demonstrate that Atlas
is a large-scale, early Miocene-age silver and gold- enriched
high-sulphidation epithermal system.  The combination of the age of
mineralization, the silver-enriched character and the high-sulphidation
style of mineralization, show strong geological similarities* to
Kinross Gold's La Coipa silver - gold mine, located at the northern end
of the Maricunga gold belt, which has historic production and remaining
resources totaling** approximately 2.75 million oz gold and 128 million
oz silver.

Surface exploration continues to upgrade the Atlas silver and gold
project, where exploration has now identified multiple exploration
targets, and appears to outline a series of mineralized trends up to 3
km in length. Mirasol's field teams have initiated follow-up sampling
of the new target areas in order to prioritize targets for potential
trenching and/or electrical geophysical surveys.

Through the process of open ground staking and an earn-in JV
agreement with a private Chilean company (see news release of June 26,
2013), Mirasol Resources has expanded the claims it is exploring to
over 40,000 hectares in the Gorbea Belt and surrounding areas.

Mirasol plans to initiate third party field reviews of its Gorbea
Belt projects with the objective of identifying a strategic joint
venture partner to accelerate exploration of its Gorbea Belt package of
precious metal projects.

Stephen C. Nano, Vice President of Exploration for Mirasol, is the
Qualified Person under NI 43-101 who has prepared and approves the
technical content of this news release.

*Analog that has similar geological characteristics (age of
mineralization / type of mineralization / style and potentially the
grade of mineralization).  This may be used to suggest exploration
prospectivity but does not give any guarantee that exploration could
identify any resource or a resource of similar size of scale to the
original mine.

**Indicative total only. Should only be used as an indication of
the pre-mining global metal contained in the La Coipa district.

Quality Assurance/Quality Control:

Exploration at the Titan and Atlas Projects and the Gorbea belt is
supervised by Stephen C. Nano, Vice President of Exploration, who is
the Qualified Person under NI 43-101, and Timothy Heenan, Exploration
Manager. All technical information for the Company's projects is
obtained and reported under a formal quality assurance and quality
control (QA/QC) program.  All rock chip, stream sediment and drill
samples are collected under the supervision of Company geologists in
accordance with standard industry practice.  Samples are dispatched to
an ISO 9001:2000-accredited laboratory in Chile for analysis.  All rock
chip, stream sediment and drill samples are submitted to the Laboratory
with independently sourced, accredited standard and blanks and where
appropriate duplicate samples to facilitate monitoring of laboratory
performance.  Certified Results are examined by an independent
qualified consultant to ensure laboratory performance meets required
standards.

Neither the TSX Venture Exchange nor its Regulation Services
Provider (as that term is defined in the policies of the TSX Venture
Exchange) accepts responsibility for the adequacy or accuracy of this
release.

SOURCE  Mirasol Resources Ltd.
TSX Venture closing price for MRZ-V
Date: 2014/02/25
Closing Price: 1.63

TEL:  (604) 602-9989   Mary L. Little, President and CEO
EMAIL:  contact@mirasolresources.com
WEBSITE:  www.mirasolresources.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1405600023TS11405601176-06340020140226