Source	Marketwire
Date	02/19/2014
Time	06:00:20 AM

Company	 HUDSON RESOURCES INC.
Title	Hudson Updates Alumina Development Program at Its White Mountain 
Anorthosite Project in Greenland





    CDNX Symbol: HUD











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Hudson Resources Inc.

TSX VENTURE SYMBOL: HUD
OTCQX SYMBOL: HUDRF

February 19, 2014

Hudson Updates Alumina Development Program at Its White Mountain Anorthosite 
Project in Greenland


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Feb. 19, 2014) - HUDSON RESOURCES 
INC. (the "Company") (TSX VENTURE:HUD)(OTCQX:HUDRF) is pleased to announce 
updated results for its alumina (aluminum oxide) development program on the 
calcium feldspar anorthosite from its White Mountain Project in Greenland. The 
objective of this phase of testwork is to produce smelter grade alumina (SGA) 
that meets both the chemical purity and physical specifications required by the 
aluminum industry.

Hudson, under the supervision of Hudson's consulting metallurgist, John Goode, 
P. Eng., has now generated a number of alumina samples at SGS Lakefield's 
laboratory facilities in Ontario. The process involves three key stages, 1) 
leaching the anorthosite in hydrochloric acid ("HCl"); 2) sparging the leach 
solution with HCl gas to form aluminum chloride hexahydrate ("ACH") crystals; 
and 3) calcining the ACH at high temperature to remove the water and chlorine 
to regenerate the HCl for recycle and to produce the final SGA.

Critical to producing a marketable SGA product is ensuring that the physical 
properties match or exceed the required specifications from the aluminum 
industry, which requires two tonnes of alumina to produce one tonne of aluminum 
metal. Two key criteria are:

/T/

--  The percent of alpha phase alumina typically needs to average less than
7.5%, and;
--  The crystal surface area of the alumina particles (measured by a test
with the acronym "BET"), needs to be between 60 and 80 square metres per
gram.

/T/

Meeting these parameters is very challenging when using non-traditional 
(non-bauxite) ore as the feed material. Hudson has managed to meet or exceed 
these key parameters in part due to the unique nature of the White Mountain 
anorthosite and its high solubility.

Through extensive testwork, Hudson has now defined a preliminary flowsheet and 
operating parameters that produce an alumina product with a BET of 74 m2/g and 
a very low alpha content of 1.7%. The BET and alpha-alumina tests were 
conducted at McGill University's Department of Mining and Material Engineering. 
The determination of alpha alumina content used the Australian standard method 
(AS 2879.3 - 2010) for testing metallurgical alumina.

James Tuer, Hudson's President, stated, "These results are a very significant 
step in the development of a flowsheet to produce smelter grade alumina from 
our anorthosite. Based on discussions with key industry players, we know that 
generating alumina using an HCl leaching method has proven difficult from a 
physical property perspective. Generally, it is relatively straightforward to 
meet the chemical purity specifications for SGA. However, meeting the physical 
parameters such as BET, low alpha alumina, and larger, stronger particles has 
remained elusive. We believe that our success to date has been due to the 
unique nature of the White Mountain anorthosite. As previously reported, we 
have utilized and improved upon existing, unpatented aluminum chloride 
production processes and we do not require any new technologies to produce a 
high quality product."

Metallurgical testwork is ongoing and an economic model is being developed to 
further evaluate the potential of White Mountain anorthosite as a new source of 
alumina. Currently almost all alumina is produced from bauxite using the Bayer 
process, which produces 2 tonnes of waste for every tonne of ore. Hudson 
believes the White Mountain project will have several saleable byproducts and 
will not produce significant tailings. Hudson has signed confidentiality 
agreements with several companies interested in the alumina project.

The White Mountain Anorthosite project is 100% owned by Hudson. The anorthosite 
has three potential high-value applications which are being investigated, as 
follows:

/T/

1.  A new source of feedstock to the high end fiberglass (E-glass) industry;
2.  A new source of alumina to supply aluminum smelters
3.  A new source of filler material. Fillers are extensively used by the
plastics, paints and paper industries

/T/

The company is rapidly advancing the E-Glass project with several Letters of 
Intent in place. The planned bulk sample test with a major fiberglass producer 
is commencing later this month. The environmental and social impact assessments 
and technical study are near completion and the plan is to submit them to the 
Greenland Government within the next few months as part of Hudson's application 
for a mining permit.

Hudson remains well financed with approximately $2.5 million in working capital.

John R. Goode is the Qualified Person, as defined by National Instrument 
43-101, who reviewed the preparation of the scientific and technical 
metallurgical information in this press release.

ON BEHALF OF THE BOARD OF DIRECTORS

James Tuer, President

Forward-Looking Statements

This news release includes certain forward-looking statements or information. 
All statements other than statements of historical fact included in this news 
release, including, without limitation, statements regarding plans for the 
completion of a financing and the intended terms and use of proceeds thereof, 
and other future plans and objectives of the Company are forward-looking 
statements that involve various risks and uncertainties. There can be no 
assurance that such statements will prove to be accurate and actual results and 
future events could differ materially from those anticipated in such 
statements. Important factors that could cause actual results to differ 
materially from the Company's plans or expectations include market prices, 
general economic, market or business conditions, regulatory changes, timeliness 
of government or regulatory approvals and other risks detailed herein and from 
time to time in the filings made by the Company with securities regulators. The 
Company expressly disclaims any intention or obligation to update or revise any 
forward-looking statements whether as a result of new information, future 
events or otherwise except as otherwise required by applicable securities 
legislation.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Hudson Resources Inc.
James Tuer
President
604-628-5002 or 604-688-3415
Fax: (604) 688-3452
tuer@hudsonresources.ca
www.hudsonresources.ca

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=467985660