Source	MARKET NEWS
Date	02/20/2014
Time	06:49:24 AM

Company	 Revolver Resources Inc.
Title	First 
Assay Results Of Its Summit B Drilling Cam





    CDNX Symbol: RZ











Press Release	





REVOLVER RESOURCES INC ("RZ-V")
- First Assay Results Of Its Summit B Drilling Campaign

Revolver Resources Inc. ("Revolver") is releasing the assay results
of the first two of its three diamond drill holes program on its Summit
B property. The 1,394 hectare (3,446 acre) Summit B property is located
in the Iskut area of northwestern British Columbia, Canada, and is
contiguous with Colorado Resources Ltd.'s ("Colorado") North Rok
copper-gold property (the "North Rok Property").

The Company is pleased to announce the preliminary assay
results of two DDH (SUMB-02 and SUMB-05), distanced by 1 km, revealing
several intersections of copper mineralization associated with
quartz-carbonate veins and fracture filling. Best results produced
intercepts of 6.3m @ 0.43 wt. % Cu (SUMB-02), 1.2 m @ 0.18 wt. % Cu and
0.3 m @ 0.25 wt. % Cu (SUMB-05)(The lengths of the intervals do not
represent true stratigraphic lengths). The drill holes intersected a
folded, fractured and sheared assemblage of Permian basic-intermediate
volcanic rocks interstratified with thin shale, phyllite, schist and
siltsone layers. A significant number of pyritechalcopyrite-bearing
quartz-carbonate (calcite-ankerite-dolomite) veins were encountered
throughout the core with numerous pyritechalcopyrite fracture and
fault-fillings especially at depth greater than 200 m.

The copper mineralization is associated with the core of a 2 km
x 500 m NW-oriented high-chargeability/low resistivity anomaly bounded
by NW-striking high angle faults (see Revolver Resources press release
of November 8, 2013). Cu-bearing zones extend in a northwesterly
direction for at least 1 km, whereas an arsenic-copper-gold-rich system
is exposed at the periphery of the anomaly, especially on the
southeastern segment of the property. Harsh winter conditions, rugged
terrain and the difficulty to obtain water prevented the investigation
of this area. However, Revolver Resources still holds a drilling permit
for at least four additional holes and expects to resume its drilling
campaign on the Au-rich zone in the early summer months.

Says Michel Boily, geo, PhD, President of Revolver Resources,
"The preliminary drilling campaign on the Summit B property is very
promising and indicates that copper mineralization extends for at least
1 km and is found in association with fractures, shears and
quartz-carbonate veins at the core of an important chargeability
anomaly. The three exploratory drillholes leave us with a better
understanding of the geology, structure and distribution of base and
precious metal mineralization. Revolver Resources will renew its
exploration activities in the early summer by targeting gold-rich zones
inaccessible during the winter season."

Revolver commissioned Black Hawk Diamond Drilling Ltd. for the
drilling operations. UTM Exploration Services from Smithers, BC
perfomed the on-site management of drilling operations, core logging
and core sampling. UTM established a strict protocol for the QA/QC
program including the insertion of standards, blanks and duplicates
into the sampling procedure. Assays were performed at the AGAT
Laboratories using aqua regia digestion with ICP/ICP-MS finish for Cu
and other metals and fire assay with ICP-OES finish for Au.

The Company still waits the assay results of hole SUMB-03.

Technical information in this news release has been prepared
and/or revised by Michel Boily, geo, PhD. who is qualified person as
defined in NI 43-101.

For further information on Revolver please visit our website at
www.revolverresources.com.

ON BEHALF OF THE BOARD OF DIRECTORS

Michel Boily, geo, PhD., President

NEITHER TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICE
PROVIDER (AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE
EXCHANGE) ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS
RELEASE.

TSX Venture closing price for RZ-V
Date: 2014/02/19
Closing Price: 0.07

TEL:  778 331 2025   Revolver Resources Inc.
WEBSITE:  www.revolverresources.com
____________________________________________________________
(c)2014 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1405000026TS11405001302-06472520140220