Source	Marketwire
Date	02/20/2014
Time	06:30:12 AM

Company	 REVOLVER RESOURCES INC.
Title	Revolver Resources Unveils First Assay Results of Its Summit B Drilling 
Campaign





    CDNX Symbol: RZ











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Revolver Resources Inc.

TSX VENTURE SYMBOL: RZ

February 20, 2014

Revolver Resources Unveils First Assay Results of Its Summit B Drilling Campaign


VANCOUVER, BRITISH COLUMBIA--(Marketwired - Feb. 20, 2014) - Revolver Resources 
Inc. ("Revolver") (TSX VENTURE:RZ) is releasing the assay results of the first 
two of its three diamond drill holes program on its Summit B property. The 
1,394 hectare (3,446 acre) Summit B property is located in the Iskut area of 
northwestern British Columbia, Canada, and is contiguous with Colorado 
Resources Ltd.'s ("Colorado") North Rok copper-gold property (the "North Rok 
Property").

The Company is pleased to announce the preliminary assay results of two DDH 
(SUMB-02 and SUMB-05), distanced by 1 km, revealing several intersections of 
copper mineralization associated with quartz-carbonate veins and fracture 
filling. Best results produced intercepts of 6.3 m @ 0.43 wt. % Cu (SUMB-02), 
1.2 m @ 0.18 wt. % Cu and 0.3 m @ 0.25 wt. % Cu (SUMB-05) (The lengths of the 
intervals do not represent true stratigraphic lengths). The drill holes 
intersected a folded, fractured and sheared assemblage of Permian 
basic-intermediate volcanic rocks interstratified with thin shale, phyllite, 
schist and siltsone layers. A significant number of 
pyrite+/-chalcopyrite-bearing quartz-carbonate (calcite-ankerite-dolomite) 
veins were encountered throughout the core with numerous pyrite+/-chalcopyrite 
fracture and fault-fillings especially at depth greater than 200 m.

The copper mineralization is associated with the core of a 2 km x 500 m 
NW-oriented high-chargeability/low resistivity anomaly bounded by NW-striking 
high angle faults (see Revolver Resources press release of November 8, 2013). 
Cu-bearing zones extend in a northwesterly direction for at least 1 km, whereas 
an arsenic-copper-gold-rich system is exposed at the periphery of the anomaly, 
especially on the southeastern segment of the property. Harsh winter 
conditions, rugged terrain and the difficulty to obtain water prevented the 
investigation of this area. However, Revolver Resources still holds a drilling 
permit for at least four additional holes and expects to resume its drilling 
campaign on the Au-rich zone in the early summer months.

Says Michel Boily, geo, PhD, President of Revolver Resources, "The preliminary 
drilling campaign on the Summit B property is very promising and indicates that 
copper mineralization extends for at least 1 km and is found in association 
with fractures, shears and quartz-carbonate veins at the core of an important 
chargeability anomaly. The three exploratory drillholes leave us with a better 
understanding of the geology, structure and distribution of base and precious 
metal mineralization. Revolver Resources will renew its exploration activities 
in the early summer by targeting gold-rich zones inaccessible during the winter 
season."

Revolver commissioned Black Hawk Diamond Drilling Ltd. for the drilling 
operations. UTM Exploration Services from Smithers, BC perfomed the on-site 
management of drilling operations, core logging and core sampling. UTM 
established a strict protocol for the QA/QC program including the insertion of 
standards, blanks and duplicates into the sampling procedure. Assays were 
performed at the AGAT Laboratories using aqua regia digestion with ICP/ICP-MS 
finish for Cu and other metals and fire assay with ICP-OES finish for Au.

The Company still waits the assay results of hole SUMB-03.

Technical information in this news release has been prepared and/or revised by 
Michel Boily, geo, PhD. who is qualified person as defined in NI 43-101.

For further information on Revolver please visit our website at 
www.revolverresources.com.

ON BEHALF OF THE BOARD OF DIRECTORS

Michel Boily, geo, PhD., President

NEITHER TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICE PROVIDER (AS THAT TERM 
IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE) ACCEPTS RESPONSIBILITY 
FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

- 30 -

CONTACT INFO:

Revolver Resources Inc.
778 331 2025
www.revolverresources.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=468348159