Source	CANADA NEWSWIRE
Date	02/27/2014
Time	04:05:12 AM

Company	 Kivalliq Energy Corporation
Title	Kivalliq Announces Additional Positive Results from Metallurgical Tests
and Radiometric Ore Sorting Study





    CDNX Symbol: KIV











Press Release	




" BC-KIV-MetallurgyResults   02-27 2100
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Kivalliq Announces Additional Positive Results from Metallurgical Tests
and Radiometric Ore Sorting Study@

VANCOUVER, Feb. 27, 2014 /CNW/ - Kivalliq Energy Corporation ("Kivalliq",
TSX-V: KIV) today provided a project update for Kivalliq's 340,268 acre
Angilak Property located in Nunavut Territory, Canada. This release summarizes
ongoing results from metallurgical and beneficiation testing performed on Lac
50 Trend uranium mineralization, including locked cycle alkaline leach tests,
yellowcake precipitation, and a radiometric ore sorting study.
Kivalliq's CEO Jim Paterson stated: "Our team continues to advance and
de-risk the Angilak Property by evaluating potential uranium extraction and
processing options. The combination of high uranium recoveries and low reagent
consumption will have a positive impact on project economics. In addition, the
radiometric sorting study demonstrated the potential to remove more than 50%
of the waste rock prior to milling."
Key Point Summary of Metallurgical and Beneficiation Testing
--  Locked cycle leach tests confirmed the ability to recycle 100%
of the primary alkaline leach reagents;
--  Low consumption of ancillary reagents was demonstrated;
--  >95% uranium recovery in 48 hour leach cycle;
--  Low impurity yellowcake product meets ASTM C976-13 standard
specifications;
--  Radiometric ore sorting showed potential to reduce dilution
with up to 96.7% uranium recovered from 49.2% of the sample
mass.
For Angilak Property data, tables, maps and figures please see:
http://kivalliqenergy.com/uranium/archive/
Locked Cycle Leaching Test and Yellowcake Precipitation
In 2013, the Saskatchewan Research Council ("SRC") in Saskatoon, SK,
Canada commenced locked cycle alkaline leach testing on drill core samples
from Kivalliq's Lac 50 Trend uranium deposits. These tests were designed to
simulate continuous leaching operations, optimize processing conditions to
remove impurities and determine dosage of reagents required. A final
yellowcake product was also produced to confirm low impurity levels
demonstrated by preliminary testing disclosed in Kivalliq's news release of
February 28, 2013.
"Results from ongoing metallurgical work at Lac 50 are very encouraging,"
stated Chuck Edwards, Director, Metallurgy at AMEC Americas Limited. "Initial
locked cycle alkaline leach tests have confirmed that a proposed alkaline
leach circuit for Lac 50 mineralization will require low levels of reagent
consumption, resulting in positive cost implications on future plant
operations."
The locked cycle alkaline leaching tests show that after an initial
charge of sodium carbonate and sodium bicarbonate these reagents can be
recycled. Any additional leach reagent needed can be produced onsite by
capturing the carbon dioxide extracted from exhaust gases of diesel generators
typical in mining operations. After initial start up, sodium hydroxide and
lime are the only alkaline reagents that the alkaline leaching process will
consume.
An 8.7 kilogram composite sample derived from 49 drill core pulp rejects
from 12 Lac 50 and J4 Zone drill holes was submitted to SRC for locked cycle
leach tests. A total of 21 cycles were conducted at 70oC, 50% pulp density,
300 kPa of oxygen gas for up to 48 hours. Fresh alkaline solution, containing
50 g/L sodium carbonate and 20 g/L sodium bicarbonate, was only used in the
first cycle to start the process. The other 20 cycles were performed in the
recycled alkaline solutions after sodium diuranate precipitation and
carbonation. Lime, as a calcium hydroxide solution, was used to precipitate
and remove sulfate and other impurities. To reduce consumption of sodium
hydroxide, lime was also used to remove excess sodium bicarbonate from the
leach solution. The sodium hydroxide consumption rate was determined to be
16.9 kg/tonne while the consumption rate for lime was 7.6 kg/tonne. After
sodium diuranate precipitation, excessive sodium hydroxide in the recycled
barren solution was carbonated to produce sodium carbonate and sodium
bicarbonate by introducing carbon dioxide gas.
The process conditions of leaching, impurity removal, sodium diuranate
precipitation, and carbonation achieved high uranium leaching recovery (>95%
in 48 hours), effective lime precipitation impurity removal with low uranium
loss (<0.1%), high uranium recovery in the sodium diuranate precipitate
(99.6%), and consistent solution regeneration for recycling.
Low Impurity Yellowcake Production
Sodium diuranate produced from each leach cycle was combined, dissolved
in sulphuric acid, and precipitated as a single representative ammonium
diuranate yellowcake final product. The final uranium peroxide yellowcake
product was analyzed at SRC for uranium and impurities. The results compared
with Impurity Maximum Concentration Limits from ASTM C976-13 Standard
Specification for Uranium Concentrate are shown in Table 1. The yellowcake
produced contains 70.0% uranium and low impurity levels. Boron and magnesium
are marginally higher than penalty levels but significantly below reject
levels. All impurities assayed meet ASTM C976-13 standards. The conditions for
uranium peroxide yellowcake production are not yet optimized and will be the
focus of future testing.
Radiometric Ore Sorting Test
On September 13, 2013, Kivalliq released encouraging radiometric
characterization results from a Preliminary Ore Sorting Investigation
undertaken by TOMRA Sorting Inc. ("TOMRA") of Surrey, BC, Canada. As follow up
to this work, Kivalliq engaged TOMRA to undertake further radiometric ore
sorting tests on 222.7 kilograms of half-split NQ core collected from Lac 50
Trend resource drilling.
The results from these most recent tests demonstrate a 96.7% cumulative
uranium recovery in a mass recovery of 49.2% (i.e. 50.8% of the rock mass is
rejected with a 3.3% loss of uranium) The testing also shows a 94.1%
cumulative uranium recovery with a marked drop in mass recovery at 15.9% (i.e.
84.1% mass rejected with 5.9% loss of uranium). The testing reflects the
high-grade uranium characteristics at Lac 50 where the majority of uranium
mineralization occurs as disseminations and veins of massive pitchblende
within the carbonate and hematite alteration zone comprising the Lac 50 Trend
inferred resource.
"We are very pleased with the ongoing success of radiometric ore sorting
studies. The substantial upgrading of uranium through sorting could have
significant positive impacts on future mining and milling operations," stated
Jeff Ward, President of Kivalliq Energy. "Kivalliq will conduct further
testing on additional composites of Lac 50 Trend uranium mineralization to
further refine and confirm repeatability of these excellent results."
Kivalliq provided TOMRA with a 222.7 kilogram composite sample from 4
drill holes, comprised of 46.4% "Mineralized Zone" and 53.6% barren wall rock
"Waste", to determine the removal of internal dilution and dilution introduced
through mining. The composite had a head grade of 0.21% uranium which included
103.4 kilograms of half split drill core from Lac 50 Zone and J4 Zone
mineralization grading 0.45% uranium; and 119.3 kilograms of barren wall rock
waste. TOMRA screened the composite material into four size fractions: (1)
+25mm; (2) +20mm -25mm; (3) +12mm -20mm; and (4) -12mm "fines". The samples
were scanned and sorted using a bench top radiometric unit configured to
simulate a full-scale radiometric sorter (short integration recovery). Using
the correlation between measured gamma counts and uranium grade from the
September 2013 characterization study, the individual rock fragments in each
size fraction were classified into 11 different radiometric groups (1 (equal 
sign) barren
& 11 (equal sign) highest grade). No sorting was performed on the -12mm "fine" 
fraction
which was only 0.6% of the sample mass. The sorted sample groups were sent to
SRC for Total Digestion ICP analysis. The recovery curves for the combined
Mineralized Zone and Waste - All Size Fractions (no fines) including
concentrate and tails grades are shown in Figure 1. The data for Figure 1 is
included in Table 2.

TABLE 1. Impurity Analysis of Kivalliq Yellowcake Product ASTM C976-13a

__________________________________________________________________
|   Specifications  |        ASTM C967-13       |Kivalliqre(Mass%, |
|                   |   (Mass%, Uranium Basis)  |  Uranium Basis)  |
|___________________|___________________________|__________________|
|       Component   |Limit without|Limit without|Yellowcake Product|
|                   |   Penalty   |  Rejection  |                  |
|___________________|_____________|_____________|__________________|
|Uranium (U)        |       N/A   |   65% min.  |           70%    |
|___________________|_____________|_____________|__________________|
|Arsenic (As)       |      0.05%  |      0.1%   |        0.0016%   |
|___________________|_____________|_____________|__________________|
|Boron (B)          |     0.005%  |      0.1%   |         0.008%   |
|___________________|_____________|_____________|__________________|
|Calcium (Ca)       |      0.05%  |        1%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Carbonate (CO3)    |      0.2%   |      0.5%   |         0.04%    |
|___________________|_____________|_____________|__________________|
|Chromium (Cr)      |       N/A   |       N/A   |       <0.0001%   |
|___________________|_____________|_____________|__________________|
|Fluoride (F)       |      0.01%  |      0.1%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Halides (Br, Cl, I)|      0.05%  |      0.1%   |        <0.002%   |
|___________________|_____________|_____________|__________________|
|Iron (Fe)          |      0.15%  |        1%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Lead (Pb)          |       N/A   |       N/A   |       <0.0001%   |
|___________________|_____________|_____________|__________________|
|Magnesium (Mg)     |      0.02%  |      0.5%   |         0.05%    |
|___________________|_____________|_____________|__________________|
|Moisture (H2O)     |        2%   |        5%   |          0.2%    |
|___________________|_____________|_____________|__________________|
|Molybdenum (Mo)    |      0.1%   |      0.3%   |         0.003%   |
|___________________|_____________|_____________|__________________|
|Phosphorus (PO4)   |      0.1%   |      0.7%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Potassium (K)      |      0.2%   |        3%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Selenium (Se)      |       N/A   |       N/A   |        <0.001%   |
|___________________|_____________|_____________|__________________|
|Silica (SiO2)      |      0.5%   |      2.5%   |         0.07%    |
|___________________|_____________|_____________|__________________|
|Silver (Ag)        |       N/A   |       N/A   |        <0.001%   |
|___________________|_____________|_____________|__________________|
|Sodium (Na)        |        1%   |      7.5%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Sulfur (S)         |        1%   |        4%   |         0.16%    |
|___________________|_____________|_____________|__________________|
|Thorium            |      0.1%   |      2.5%   |       <0.0001%   |
|___________________|_____________|_____________|__________________|
|Titanium           |      0.01%  |      0.05%  |         0.009%   |
|___________________|_____________|_____________|__________________|
|234U               |   56 µg/gU  |   62 µg/gU  |      55.2 µg/gU  |
|___________________|_____________|_____________|__________________|
|Vanadium (V)       |      0.06%  |      0.3%   |         0.003%   |
|___________________|_____________|_____________|__________________|
|Zirconium (Zr)     |      0.01%  |      0.1%   |        <0.001%   |
|___________________|_____________|_____________|__________________|

FIGURE 1. TOMRA Radiometric Ore Sorting Results - Mineralized Zone &
Waste (All size fractions - no fines)
http://files.newswire.ca/1209/KivaliqFig1.pdf

TABLE 2. TOMRA Radiometric Ore Sorting Results - Mineralized Zone & Waste
(All size fractions - no fines)

______________________________________________________________
|     Set Points     |Mass Pull to|Cumulative|Concentrate|Tails|
|(counts/mass/second)|Concentrate | Recovery |   Grade   |Grade|
|                    |  (Mass %)  |  (U %)   |   (U %)   |(U %)|
|____________________|____________|__________|___________|_____|
|            250     |      1.1%  |   28.3%  |    5.37%  |0.15%|
|____________________|____________|__________|___________|_____|
|            100     |      3.5%  |   86.9%  |    5.20%  |0.03%|
|____________________|____________|__________|___________|_____|
|             80     |      3.7%  |   87.0%  |    4.93%  |0.03%|
|____________________|____________|__________|___________|_____|
|             40     |      5.1%  |   88.0%  |    3.59%  |0.03%|
|____________________|____________|__________|___________|_____|
|             20     |      8.5%  |   91.4%  |    2.26%  |0.02%|
|____________________|____________|__________|___________|_____|
|             10     |     15.9%  |   94.1%  |    1.24%  |0.01%|
|____________________|____________|__________|___________|_____|
|              1     |     49.2%  |   96.7%  |    0.41%  |0.01%|
|____________________|____________|__________|___________|_____|

QA/QC
The SRC facility operates in accordance with ISO/IEC 17025:2005
(CAN-P-4E), General Requirements for the Competence of Mineral Testing and
Calibration laboratories and is accredited by the Standards Council of Canada.
Samples are analyzed by SRC's ICP-OES multi-element ICP1 assay method and
results are reported in parts per million (ppm). 1 ppm (equal sign) 1g/tonne; 
10,000 ppm
(equal sign) 1%. ICP U assays in ppm can be converted to % U3O8 as follows: % 
U3O8 (equal sign) ppm
U x 0.01179
TOMRA (formerly Commodas Ultrasort and Terra Vision) are leaders in the
specialized field of sensor-based sorting technology for the mining industry.
Experience from 15 test facilities worldwide have led to significant advancesin 
automated material identification and sorting for the mining and mineral
processing industries.
Jeff Ward, P.Geo, President of Kivalliq and a Qualified Person for
Kivalliq, has reviewed and approved the scientific and technical information
contained in this release. For disclosure related to the inferred resource for
the Lac 50 Trend uranium deposit, please refer to Kivalliq's news release of
March 1, 2013.
About Kivalliq Energy Corporation
Kivalliq Energy Corporation (TSX-V: KIV) is a Vancouver-based uranium
exploration company holding Canada's highest-grade uranium resource outside of
Saskatchewan's Athabasca Basin. Its flagship project, the 340,268 acre Angilak
Property in Nunavut Territory, hosts the Lac 50 Trend with a NI 43-101
Inferred Resource of 2,831,000 tonnes grading 0.69% U3O8, totaling 43.3
million pounds U3O8. Kivalliq's comprehensive exploration programs continue to
advance the Lac 50 Trend and demonstrate the "District Scale" potential of the
Angilak Property.
Kivalliq's team of northern exploration specialists have forged strong
relationships with sophisticated resource sector investors and Angilak
Property partner Nunavut Tunngavik Inc. ("NTI"). Kivalliq was the first
company to sign a comprehensive agreement to explore for urani

" BC-KIV-MetallurgyResults   02-27 2100
News release via Canada NewsWire, Vancouver 604-669-7764 -ME-

Attention Business  Editors:
^Kivalliq Announces Additional Positive Results from Metallurgical Tests
and Radiometric Ore Sorting Study@

VANCOUVER, Feb. 27, 2014 /CNW/ - Kivalliq Energy Corporation ("Kivalliq",
TSX-V: KIV) today provided a project update for Kivalliq's 340,268 acre
Angilak Property located in Nunavut Territory, Canada. This release summarizes
ongoing results from metallurgical and beneficiation testing performed on Lac
50 Trend uranium mineralization, including locked cycle alkaline leach tests,
yellowcake precipitation, and a radiometric ore sorting study.
Kivalliq's CEO Jim Paterson stated: "Our team continues to advance and
de-risk the Angilak Property by evaluating potential uranium extraction and
processing options. The combination of high uranium recoveries and low reagent
consumption will have a positive impact on project economics. In addition, the
radiometric sorting study demonstrated the potential to remove more than 50%
of the waste rock prior to milling."
Key Point Summary of Metallurgical and Beneficiation Testing
--  Locked cycle leach tests confirmed the ability to recycle 100%
of the primary alkaline leach reagents;
--  Low consumption of ancillary reagents was demonstrated;
--  >95% uranium recovery in 48 hour leach cycle;
--  Low impurity yellowcake product meets ASTM C976-13 standard
specifications;
--  Radiometric ore sorting showed potential to reduce dilution
with up to 96.7% uranium recovered from 49.2% of the sample
mass.
For Angilak Property data, tables, maps and figures please see:
http://kivalliqenergy.com/uranium/archive/
Locked Cycle Leaching Test and Yellowcake Precipitation
In 2013, the Saskatchewan Research Council ("SRC") in Saskatoon, SK,
Canada commenced locked cycle alkaline leach testing on drill core samples
from Kivalliq's Lac 50 Trend uranium deposits. These tests were designed to
simulate continuous leaching operations, optimize processing conditions to
remove impurities and determine dosage of reagents required. A final
yellowcake product was also produced to confirm low impurity levels
demonstrated by preliminary testing disclosed in Kivalliq's news release of
February 28, 2013.
"Results from ongoing metallurgical work at Lac 50 are very encouraging,"
stated Chuck Edwards, Director, Metallurgy at AMEC Americas Limited. "Initial
locked cycle alkaline leach tests have confirmed that a proposed alkaline
leach circuit for Lac 50 mineralization will require low levels of reagent
consumption, resulting in positive cost implications on future plant
operations."
The locked cycle alkaline leaching tests show that after an initial
charge of sodium carbonate and sodium bicarbonate these reagents can be
recycled. Any additional leach reagent needed can be produced onsite by
capturing the carbon dioxide extracted from exhaust gases of diesel generators
typical in mining operations. After initial start up, sodium hydroxide and
lime are the only alkaline reagents that the alkaline leaching process will
consume.
An 8.7 kilogram composite sample derived from 49 drill core pulp rejects
from 12 Lac 50 and J4 Zone drill holes was submitted to SRC for locked cycle
leach tests. A total of 21 cycles were conducted at 70oC, 50% pulp density,
300 kPa of oxygen gas for up to 48 hours. Fresh alkaline solution, containing
50 g/L sodium carbonate and 20 g/L sodium bicarbonate, was only used in the
first cycle to start the process. The other 20 cycles were performed in the
recycled alkaline solutions after sodium diuranate precipitation and
carbonation. Lime, as a calcium hydroxide solution, was used to precipitate
and remove sulfate and other impurities. To reduce consumption of sodium
hydroxide, lime was also used to remove excess sodium bicarbonate from the
leach solution. The sodium hydroxide consumption rate was determined to be
16.9 kg/tonne while the consumption rate for lime was 7.6 kg/tonne. After
sodium diuranate precipitation, excessive sodium hydroxide in the recycled
barren solution was carbonated to produce sodium carbonate and sodium
bicarbonate by introducing carbon dioxide gas.
The process conditions of leaching, impurity removal, sodium diuranate
precipitation, and carbonation achieved high uranium leaching recovery (>95%
in 48 hours), effective lime precipitation impurity removal with low uranium
loss (<0.1%), high uranium recovery in the sodium diuranate precipitate
(99.6%), and consistent solution regeneration for recycling.
Low Impurity Yellowcake Production
Sodium diuranate produced from each leach cycle was combined, dissolved
in sulphuric acid, and precipitated as a single representative ammonium
diuranate yellowcake final product. The final uranium peroxide yellowcake
product was analyzed at SRC for uranium and impurities. The results compared
with Impurity Maximum Concentration Limits from ASTM C976-13 Standard
Specification for Uranium Concentrate are shown in Table 1. The yellowcake
produced contains 70.0% uranium and low impurity levels. Boron and magnesium
are marginally higher than penalty levels but significantly below reject
levels. All impurities assayed meet ASTM C976-13 standards. The conditions for
uranium peroxide yellowcake production are not yet optimized and will be the
focus of future testing.
Radiometric Ore Sorting Test
On September 13, 2013, Kivalliq released encouraging radiometric
characterization results from a Preliminary Ore Sorting Investigation
undertaken by TOMRA Sorting Inc. ("TOMRA") of Surrey, BC, Canada. As follow up
to this work, Kivalliq engaged TOMRA to undertake further radiometric ore
sorting tests on 222.7 kilograms of half-split NQ core collected from Lac 50
Trend resource drilling.
The results from these most recent tests demonstrate a 96.7% cumulative
uranium recovery in a mass recovery of 49.2% (i.e. 50.8% of the rock mass is
rejected with a 3.3% loss of uranium) The testing also shows a 94.1%
cumulative uranium recovery with a marked drop in mass recovery at 15.9% (i.e.
84.1% mass rejected with 5.9% loss of uranium). The testing reflects the
high-grade uranium characteristics at Lac 50 where the majority of uranium
mineralization occurs as disseminations and veins of massive pitchblende
within the carbonate and hematite alteration zone comprising the Lac 50 Trend
inferred resource.
"We are very pleased with the ongoing success of radiometric ore sorting
studies. The substantial upgrading of uranium through sorting could have
significant positive impacts on future mining and milling operations," stated
Jeff Ward, President of Kivalliq Energy. "Kivalliq will conduct further
testing on additional composites of Lac 50 Trend uranium mineralization to
further refine and confirm repeatability of these excellent results."
Kivalliq provided TOMRA with a 222.7 kilogram composite sample from 4
drill holes, comprised of 46.4% "Mineralized Zone" and 53.6% barren wall rock
"Waste", to determine the removal of internal dilution and dilution introduced
through mining. The composite had a head grade of 0.21% uranium which included
103.4 kilograms of half split drill core from Lac 50 Zone and J4 Zone
mineralization grading 0.45% uranium; and 119.3 kilograms of barren wall rock
waste. TOMRA screened the composite material into four size fractions: (1)
+25mm; (2) +20mm -25mm; (3) +12mm -20mm; and (4) -12mm "fines". The samples
were scanned and sorted using a bench top radiometric unit configured to
simulate a full-scale radiometric sorter (short integration recovery). Using
the correlation between measured gamma counts and uranium grade from the
September 2013 characterization study, the individual rock fragments in each
size fraction were classified into 11 different radiometric groups (1 (equal 
sign) barren
& 11 (equal sign) highest grade). No sorting was performed on the -12mm "fine" 
fraction
which was only 0.6% of the sample mass. The sorted sample groups were sent to
SRC for Total Digestion ICP analysis. The recovery curves for the combined
Mineralized Zone and Waste - All Size Fractions (no fines) including
concentrate and tails grades are shown in Figure 1. The data for Figure 1 is
included in Table 2.

TABLE 1. Impurity Analysis of Kivalliq Yellowcake Product ASTM C976-13a

__________________________________________________________________
|   Specifications  |        ASTM C967-13       |Kivalliqre(Mass%, |
|                   |   (Mass%, Uranium Basis)  |  Uranium Basis)  |
|___________________|___________________________|__________________|
|       Component   |Limit without|Limit without|Yellowcake Product|
|                   |   Penalty   |  Rejection  |                  |
|___________________|_____________|_____________|__________________|
|Uranium (U)        |       N/A   |   65% min.  |           70%    |
|___________________|_____________|_____________|__________________|
|Arsenic (As)       |      0.05%  |      0.1%   |        0.0016%   |
|___________________|_____________|_____________|__________________|
|Boron (B)          |     0.005%  |      0.1%   |         0.008%   |
|___________________|_____________|_____________|__________________|
|Calcium (Ca)       |      0.05%  |        1%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Carbonate (CO3)    |      0.2%   |      0.5%   |         0.04%    |
|___________________|_____________|_____________|__________________|
|Chromium (Cr)      |       N/A   |       N/A   |       <0.0001%   |
|___________________|_____________|_____________|__________________|
|Fluoride (F)       |      0.01%  |      0.1%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Halides (Br, Cl, I)|      0.05%  |      0.1%   |        <0.002%   |
|___________________|_____________|_____________|__________________|
|Iron (Fe)          |      0.15%  |        1%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Lead (Pb)          |       N/A   |       N/A   |       <0.0001%   |
|___________________|_____________|_____________|__________________|
|Magnesium (Mg)     |      0.02%  |      0.5%   |         0.05%    |
|___________________|_____________|_____________|__________________|
|Moisture (H2O)     |        2%   |        5%   |          0.2%    |
|___________________|_____________|_____________|__________________|
|Molybdenum (Mo)    |      0.1%   |      0.3%   |         0.003%   |
|___________________|_____________|_____________|__________________|
|Phosphorus (PO4)   |      0.1%   |      0.7%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Potassium (K)      |      0.2%   |        3%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Selenium (Se)      |       N/A   |       N/A   |        <0.001%   |
|___________________|_____________|_____________|__________________|
|Silica (SiO2)      |      0.5%   |      2.5%   |         0.07%    |
|___________________|_____________|_____________|__________________|
|Silver (Ag)        |       N/A   |       N/A   |        <0.001%   |
|___________________|_____________|_____________|__________________|
|Sodium (Na)        |        1%   |      7.5%   |         <0.01%   |
|___________________|_____________|_____________|__________________|
|Sulfur (S)         |        1%   |        4%   |         0.16%    |
|___________________|_____________|_____________|__________________|
|Thorium            |      0.1%   |      2.5%   |       <0.0001%   |
|___________________|_____________|_____________|__________________|
|Titanium           |      0.01%  |      0.05%  |         0.009%   |
|___________________|_____________|_____________|__________________|
|234U               |   56 µg/gU  |   62 µg/gU  |      55.2 µg/gU  |
|___________________|_____________|_____________|__________________|
|Vanadium (V)       |      0.06%  |      0.3%   |         0.003%   |
|___________________|_____________|_____________|__________________|
|Zirconium (Zr)     |      0.01%  |      0.1%   |        <0.001%   |
|___________________|_____________|_____________|__________________|

FIGURE 1. TOMRA Radiometric Ore Sorting Results - Mineralized Zone &
Waste (All size fractions - no fines)
http://files.newswire.ca/1209/KivaliqFig1.pdf

TABLE 2. TOMRA Radiometric Ore Sorting Results - Mineralized Zone & Waste
(All size fractions - no fines)

______________________________________________________________
|     Set Points     |Mass Pull to|Cumulative|Concentrate|Tails|
|(counts/mass/second)|Concentrate | Recovery |   Grade   |Grade|
|                    |  (Mass %)  |  (U %)   |   (U %)   |(U %)|
|____________________|____________|__________|___________|_____|
|            250     |      1.1%  |   28.3%  |    5.37%  |0.15%|
|____________________|____________|__________|___________|_____|
|            100     |      3.5%  |   86.9%  |    5.20%  |0.03%|
|____________________|____________|__________|___________|_____|
|             80     |      3.7%  |   87.0%  |    4.93%  |0.03%|
|____________________|____________|__________|___________|_____|
|             40     |      5.1%  |   88.0%  |    3.59%  |0.03%|
|____________________|____________|__________|___________|_____|
|             20     |      8.5%  |   91.4%  |    2.26%  |0.02%|
|____________________|____________|__________|___________|_____|
|             10     |     15.9%  |   94.1%  |    1.24%  |0.01%|
|____________________|____________|__________|___________|_____|
|              1     |     49.2%  |   96.7%  |    0.41%  |0.01%|
|____________________|____________|__________|___________|_____|

QA/QC
The SRC facility operates in accordance with ISO/IEC 17025:2005
(CAN-P-4E), General Requirements for the Competence of Mineral Testing and
Calibration laboratories and is accredited by the Standards Council of Canada.
Samples are analyzed by SRC's ICP-OES multi-element ICP1 assay method and
results are reported in parts per million (ppm). 1 ppm (equal sign) 1g/tonne; 
10,000 ppm
(equal sign) 1%. ICP U assays in ppm can be converted to % U3O8 as follows: % 
U3O8 (equal sign) ppm
U x 0.01179
TOMRA (formerly Commodas Ultrasort and Terra Vision) are leaders in the
specialized field of sensor-based sorting technology for the mining industry.
Experience from 15 test facilities worldwide have led to significant advancesin 
automated material identification and sorting for the mining and mineral
processing industries.
Jeff Ward, P.Geo, President of Kivalliq and a Qualified Person for
Kivalliq, has reviewed and approved the scientific and technical information
contained in this release. For disclosure related to the inferred resource for
the Lac 50 Trend uranium deposit, please refer to Kivalliq's news release of
March 1, 2013.
About Kivalliq Energy Corporation
Kivalliq Energy Corporation (TSX-V: KIV) is a Vancouver-based uranium
exploration company holding Canada's highest-grade uranium resource outside of
Saskatchewan's Athabasca Basin. Its flagship project, the 340,268 acre Angilak
Property in Nunavut Territory, hosts the Lac 50 Trend with a NI 43-101
Inferred Resource of 2,831,000 tonnes grading 0.69% U3O8, totaling 43.3
million pounds U3O8. Kivalliq's comprehensive exploration programs continue to
advance the Lac 50 Trend and demonstrate the "District Scale" potential of the
Angilak Property.
Kivalliq's team of northern exploration specialists have forged strong
relationships with sophisticated resource sector investors and Angilak
Property partner Nunavut Tunngavik Inc. ("NTI"). Kivalliq was the first
company to sign a comprehensive agreement to explore for uranium on Inuit
Owned Lands in Nunavut Territory, Canada and is committed to building
shareholder value while adhering to high levels of environmental and safety
standards and proactive local community engagement.
On behalf of the Board of Directors
"Jim Paterson" James R. Paterson, CEO Kivalliq Energy Corporation
Kivalliq Energy Corporation is a member of the Aurora Mineral Resource
Group of companies, for more information please visit www.auroraresource.com.
Neither the TSX Venture Exchange nor its Regulation Services Provider (as
that term is defined in the policies of the TSX Venture Exchange) accepts
responsibility for the adequacy or accuracy of this release.
Certain disclosures in this release constitute forward-looking statements
that are subject to numerous risks, uncertainties and other factors relating
to Kivalliq's operations as a mineral exploration company that may cause
future results to differ materially from those expressed or implied in such
forward-looking statements, including risks as to the completion of the plans
and projects. Readers are cautioned not to place undue reliance on
forward-looking statements. Other than as required by applicable securities
legislation, Kivalliq expressly disclaims any intention or obligation to
update or revise any forward-looking statements whether as a result of new
information, future events, or otherwise.
Cautionary Note concerning estimates of Inferred Resources:
This news release uses the term "inferred resources". Inferred resources
have a great amount of uncertainty as to their existence, and great
uncertainty as to their economic and legal feasibility. It cannot be assumed
that all or any part of an Inferred Mineral Resource will ever be upgraded to
a higher category. Kivalliq advises U.S. investors that while this term is
recognized and required by Canadian regulations, the U.S. Securities and
Exchange Commission does not recognize it. U.S. investors are cautioned not to
assume that part or all of an inferred resource exists, or is economically or
legally mineable.

SOURCE Kivalliq Energy Corporation



To view this news release in HTML formatting, please use the following URL:
http://www.newswire.ca/en/releases/archive/February2014/27/c7612.html

PDF available at:
http://stream1.newswire.ca/media/2014/02/27/20140227_C7612_DOC_EN_37182.pdf

-0-                           02/27/2014
/For further information:
For further information about, Kivalliq Energy Corporation or this news
release, please visit our website at www.kivalliqenergy.com or contact
Investor Relations toll free at 1.888.331.2269, at 604.646.4527, or by email
at info(at)kivalliqenergy.com
/
(KIV.)

CO:  Kivalliq Energy Corporation
ST:  British Columbia
IN:  OIL MNG
SU:  DSC

-30-