Source	Marketwire
Date	02/28/2014
Time	07:09:54 AM

Company	 DIOS EXPLORATION INC.
Title	Fall-Winter Work on DIOS 33 Carats Gold





    CDNX Symbol: DOS











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: DIOS Exploration Inc.

TSX VENTURE SYMBOL: DOS

February 28, 2014

Fall-Winter Work on DIOS 33 Carats Gold


MONTREAL, QUEBEC--(Marketwired - Feb. 28, 2014) - Prospecting, geological 
mapping and soil sampling by helicopter over the last two years by DIOS 
EXPLORATION  (TSX VENTURE:DOS) delineated a highly prospective area for gold 
within a felsic intrusive, at the head of a gold-in-till dispersal train on 
wholly-owned 33 CARATS project, along road 167 north of the town of 
Chibougamau, Quebec, 40 km south of the Renard diamond deposit and 6 km 
northwest of the Eastmain Mine gold deposit (1.0 million tons grading 15.3 g/t 
Au, 15.1 g/t Ag and 0.27% Cu). DIOS' Bohier tonalite hosts numerous 
porphyry-type gold-silver-copper-bismuth showings associated with a magnetic 
low. The head of the gold glacial train points to the low magnetic anomaly 
within the Bohier tonalite (a 3.5 by 1.5 km area). First gold-bearing tonalite 
outcrops were discovered in summer 2012. The property is cut by the Eastmain 
River and hosts numerous shallow lakes. It is poorly exposed, with large areas 
without outcrops covered by swamps, muskegs and creeks. Typical mineralization 
within tonalite consists of disseminated/stringer pyrite-chalcopyrite 
associated with 1-5% biotite-magnetite and/or quartz stringers/veinlets.

With recent road access this Fall, a first drill program was undertaken to 
locate the source of some mineralized boulder trains and to drill-test some 
surface showings within the Bohier tonalite on dry ground accessible from the 
road. A total of nine exploratory diamond drill holes totaling 1332 m were 
completed on 33 CARATS SOUTH claims. The drill program specifically targeted 
weak to high magnetic lineaments within the magnetic low. Drilling was divided 
into two parts, with a two km area between the two remaining untested due to 
lack of access, focusing first on the northern part of the low magnetic anomaly 
within the tonalite, where 10 metric intervals greater than 100 ppb Au were 
intersected in three different holes: 13-01, 03 & 04. The best cut returned 
1.14 g/t Au, 2 g/t Ag & 0.12% Cu over 3.0 m (210.35-204.35 m) in hole 13-01. 
Wide zones of potassic (biotite- potassic feldspars) and propylitic (epidote) 
alteration were intersected in holes 13-01 & 03. The second part of the drill 
program targeted the Shower Cap area some two km to the south, located at the 
southern limit of the low magnetic anomaly. Hole 13-07 was drilled directly 
underneath the Shower Cap showing to a total depth of 111 m and returned 3 
intervals greater than 1.0 g/t Au: 1.38 g/t Au, 1.7 g/t Ag & 0.15% Cu over 0.5 
m (19.00-19.50 m), 1.09 g/t Au, 1.2 g/t Ag & 0.13% Cu over 1.5 m (25.25-26.75 
m) and 1.3 g/t Au over 1.0 m (100.00-101.00 m).

Best results from the drill program are as follows:

-1,14 g/t Au; 2,0 g/t Ag; 0,124% Cu; 25 g/t Bi/ 3,0 meters (hole 13-01; 
201,35-204,35m);

-0,322 g/tAu /7,75 m (hole 07; 19,00-26,75 m) including 1,375 g/t Au; 1,7 g/t 
Ag; 0,15% Cu/0,50m (19,00-19,50 m), 1,085 g/t Au; 0,87 g/t Ag; 0,09% Cu/1,50 m 
(25,25-26,75 m) and 1,295 g/t Au /1,00 meters (100-101m).

-0,184 g/t Au /11 meters (hole 13-04; 91,50-102,50 m) including 0,97 g/t Au/ 
1meter (91,50-92,50 m) and 0,9 g/t Au / 1 meter (101,50-102,50 m).

They are all associated with biotitized-silicified-sulfurized (cpy-py) 
tonalitic zones adjacent to feldspar-phyric intermediate dykes.

Extensive porphyry-type alteration zones was observed within the tonalite. 
Biotitization (potassic alteration) is particularly well-developed and appears 
to be coincidental with a 2000 x 250 meter moderate magnetic (vertical 
gradient) lineament within the non to weakly magnetic tonalite (3500 x 
1500-2000 m). The magnetic biotite-alteration consists of 10-30% disseminated 
(mm-cm) and/or fractured-filling. Potassic-feldspar alteration, 
hematitization-epidotization, and +/-carbonation (propylitic alteration) zones 
are also present in the northern portion of the weakly magnetic tonalite.

http://diosexplo.com/images/2013DDH.gif

Let us recall the Bohier tonalite hosts numerous showings associated with 
porphyry-type mineralization in outcrops (up to 4.93 g/t Au, 6.8 g/t Ag & 
0.477% Cu) and in metric boulders (up to 7.76 g/t Au, 17.8 g/t Ag & 1.5%). A 
two km long area within the heart of the magnetic low could not be drill tested 
this fall. During the drill campaign, further prospecting & geological mapping 
was also conducted in the vicinities of the drilling sites.

About 100 m west of Shower Cap, a metric tonalite boulder returned this year 
7.63 g/t Au, 16.5 g/t Ag, 0.64% Cu & 72 g/t Bi. Some 500 m west of Shower Cap, 
another similar mineralized boulder (found in 2012) returned 6.11 g/t Au, 3.7 
g/t Ag, 0.35% Cu. Mineralization comprises disseminated traces-1% PY-CPY-MC 
associated with 2% (mm up to 4 cm wide) quartz veins, hosted within a 
moderately silicified non-magnetic tonalite. The presence of these boulders 
indicates that a 500 x 500 m area located north of Shower Cap between drill 
holes 13-07 & 13-08 remains highly prospective. The whole area is 
non-outcropping and covered with swamps.

About 100 m south of drill holes 13-01 & 02, a metric boulder returned this 
year 5.62 g/t Au, 7,3g/t Ag, 1,48% Cu, 4g/t Bi & 94 ppm Mo within a silicified 
tonalite. The source of this boulder is under a swampy area that was not tested 
during the 2013 drill campaign because of the field conditions. Another metric 
boulder located approximately 350 m south graded 7.33 g/t Au, 14.5 g/t Ag, 
0.63% Cu & 74 g/t Bi. Mineralization consisting of 5-15% PY-PO and tr-1% CPY-MC 
occurs within a sheared, strongly biotitized and magnetic zone located at the 
contact with a fine to medium grained feldspar phyric intermediate intrusive 
(dyke?). The source of this boulder remains unknown.

From 37 new rock samples, best results follow :

2013 Prospecting Assay Results above 100 ppb Au

/T/

UTM x                    UTM y         Rock       Au       Ag    Cu       Bi
(Nad 27 18U)       (Nad 27 18u)         type    (ppm)   (ppm)    (%)   (ppm)
Boulder   692304        5803154     Tonalite     7,63    16,5   0,76      19
Boulder   691689        5805638     Tonalite     5,62     7,3   1,48       4
Boulder   692201        5801910     Tonalite     1,68    10,5   0,73       7
Outcrop   692484        5803170     Tonalite     1,10     0,3   0,01       5
Outcrop   692240        5802126     Tonalite     0,70       0   0,00       6
Outcrop   692698        5802611     Tonalite     0,61     0,6   0,11       2
Outcrop   692698        5802611     Tonalite     0,54     0,6   0,11       5
Outcrop   692698        5802611     Tonalite     0,54     0,4   0,11       0
Outcrop   692698        5802611     Tonalite     0,47     0,9   0,19       2
Outcrop   692698        5802611     Tonalite     0,32     0,2   0,03       2
Outcrop   692709        5802568 Granodiorite     0,25     0,2   0,04       0
Outcrop   692715        5802610     Tonalite     0,22     1,4   0,02       0


See maps : http://diosexplo.com/images/Prospection20112013.gif

http://diosexplo.com/images/33Carats2014Targets.jpg

/T/

Future drilling top priority-targets include:

1-eastern contact between tonalite and granodiorite marked by a N-S moderate 
magnetic lineament (gradient) located up-ice of mineralized (5,62; 6,59 and 
7,33 g/t Au) tonalite glacial boulders; some weak humus gold anomalies (98,5 
percentils) are present.

2-intersection of dioritic breccia (only observed as abundant metric glacial 
boulders) with E-W magnetic lineament;

3-up-ice area of JD glacial float train (grading up to 3,18 g/t Au) 
intersecting the same E-W magnetic lineament associated with diorite breccia;

4-western N-S oriented contact between the main magnetic and non-magnetic 
tonalite; numerous humus copper anomalies (98,5 percentil) are coincidental 
with the contact; including 131 000 ppb Cu.

5-possible extent of the northern biotite-alteration zone and its intersection 
with the magnetic tonalite (top priority target, coincident with spectrometric 
potassic anomaly).

Future work includes completing a grid and geophysical induced-polarization 
survey on the northern portion of the weakly magnetic tonalite where holes 1 to 
6 intersected more intense alterations associated with disseminated sulphides 
(pyrite-chalcopyrite) and magnetite. Coincidental i.p. (induced polarization) 
conductors with magnetic lineaments will define priority drill targets. The E-W 
magnetic lineament associated with dioritic breccia and mineralized tonalitic 
floats also warrant being test-drilled.

Whole rock analysis and geological studies completed this winter indicate the 
Bohier tonalite belongs to the high silica leucotonalite suite (calk-alkaline) 
associated with a deformation zone, alteration and mineralization. Major and 
trace elements suggest geochemistry and geology (apart from thorium) similar to 
that of the Mooshla pluton in Abitibi (which is spatially associated with five 
gold deposits).

The length and significant values of the gold glacial train leading to the 
auriferous Bohier tonalite are comparable to the Au33 West gold glacial 
dispersal train and another major gold train of the James Bay area, such is 
suggested from internal and proprietary data from DIOS. The geological team at 
DIOS is of the opinion that the source of such a major long gold train with 
many values above 2 g/t gold and above 1 g/t gold in till (heavy mineral 
concentrates) suggests a very significant gold source.

Usual industry standard quality control was implemented for prospecting samples 
and core samples, generally 1 m long core samples split in two sent to ALS 
CHEMEX for gold assaying (AA23). This release was prepared by M.J. Girard, 
M.Sc. Geo, a 43-101 Q P.

Neither the TSX Venture Exchange nor its Regulation Services Provider (as that 
term is defined in the policies of the TSX Venture Exchange) accepts 
responsibility for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Marie-Jose Girard
President & CEO
mjgirard@diosexplo.com
(514) 923-9123
www.diosexplo.com

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: DRM - MINING DRILLING RESULTS

If you no longer want to receive announcements from us, please do not reply to 
this e-mail.
Instead simply click http://marketwire.com/mw/fmu.jsp?id=469730210