Source	MARKET NEWS
Date	02/24/2015
Time	05:47:54 AM

Company	 Coastal Gold Corp.
Title	Files NI 43 
101 Technical Report For High Grade





    CDNX Symbol: COD











Press Release	





COASTAL GOLD CORP ("COD-V")
- Files NI 43-101 Technical Report For High Grade Mineral
- Resource At Hope Brook Gold Project, Newfoundland

COASTAL GOLD CORP. (the "Company") has filed a National Instrument
43-101 ("NI 43-101") technical report related to its press release
issued on January 12, 2015 announcing an update to the high grade
mineral resource estimate for the Hope Brook Gold Project in southwest
Newfoundland.

The independent technical report, entitled "2015 Mineral Resource
Estimate, Technical Report Hope Brook Gold Project, Newfoundland and
Labrador, Canada" (the "Technical Report"), dated January 12th, 2015,
was prepared for Coastal Gold by Mercator Geological Services Limited.
The Technical Report is available under the Company's profile on SEDAR
at www.sedar.com and on the Company's website at www.coastalgold.ca.

Dr. Bill Pearson, P.Geo., President & CEO of Coastal Gold,
commented: "The new resource model provides a more accurate basis for
determining the potential for underground development. The grade of the
indicated resource has increased to 4.77 g Au/t compared to the
previous estimate of 4.43 g Au/t (see press release June 3, 2014). The
new resource is designed to consider the potential of mining the entire
deposit from underground using the existing access. In addition,
underground development would facilitate follow-up drilling on
potential high grade target areas and deposit extensions already
identified from our previous surface drilling, including Hole HB11-023
which intersected 11.4 g Au/t over a true width of 20.9 metres." (see
press release dated April 27, 2011 and Figure 1).

The NI 43-101 high grade mineral resources on the Company's Hope
Brook Gold Project, as reported in the press release issued on January
12th, 2015, are estimated to contain 844,000 indicated ounces of gold
and 110,000 inferred ounces of gold using a 3.0 g Au/t cut-off as set
out in Table 1 below.

//st
Table 1: High Grade Underground Mineral Resource Estimate for Gold at
3.0 g Au/t Cut-off, Hope Brook Gold Project as at Jan 12, 2015

Resource Category  Tonnes(Rounded)  Gold Grade(g Au/t)            Gold(Oz)
Indicated                5,500,000                4.77             844,000
Inferred                   836,000                4.11             110,000
//et

Notes pertaining to the January 12, 2015 Mineral Resource Estimate
Statement:

Mineral resources are estimated in conformance with the CIM
Mineral Resource definitions referred to in NI 43-101 Standards of
Disclosure for Mineral Projects. Michael Cullen, P. Geo., Chief
Geologist at Mercator Geological Services Limited and an Independent
Qualified Person as defined under NI 43-101, supervised, and is
responsible for, the mineral resource estimate presented in this press
release.

Gold grades were interpolated separately within High Grade and Low
Grade gold domains. Gold assays within the High Grade domains were
capped at 50 g Au/t within a 50m search restriction and 20 g Au/t
outside the 50m search restriction. Low Grade domain assays were capped
at 15 g Au/t within a 50m search restriction and 3.00 g Au/t outside
the 50m search restriction.

Rock density factors used in the previous NI 43-101 resource
estimate were retained in the current model and reflect a total of
3,650 determinations by Coastal Gold. The average value for each
modeled domain was applied to the block model. Densities were confirmed
for the earlier resource estimate by testing of representative core
samples by G&T Metallurgical Services, a division of ALS Metallurgy.

As in the previous estimate, detailed geological logging and
sectional interpretations by Coastal Gold led to development of
three-dimensional domain models based mainly on assay results and
partially on lithological controls. The wire-framing resulted in a high
grade envelope (approximately 2.5 g Au/t cut-off grade) within a lower
grade silicic domain (between 0.5 g to 1.0 Au/t cut-off grade) that
encompasses the bulk of the mineralization. The wire-framed solids
defining these domains were locally modified by Mercator from those
used in the previous estimate to better reflect 2013 drill hole gold
grade intercepts and to minimize internal dilution within the domains
where possible. The original domains were used in the variography
studies and in development of grade interpolation constraints. A
footwall pyrite domain and a hanging wall argillic alteration domain
were also wire-framed previously to enable interpolation of local areas
of mineralization but these do not contribute mineralized material to
the current resource.

The mineralization is cut by a series of mafic dikes that could
not be individually wire-framed. In a manner reflecting that used in
the previous resource estimate, a mafic dike block model was created
and calibrated with available surface and historical underground
geological information. The mafic model was updated by Mercator for use
in the current resource estimate. Mafic dike material in the current
resource model at the 3 g Au/t cutoff level, in terms of block model
volume, is estimated at 18% in the Mine Zone and 0% in the 240 Zone.

The assay composite interval used for grade interpolation was 1.5
metres. Grade capping was applied prior to compositing.

A 3D geological block model was generated using Geovia-Surpac Ver.
6.6.1(r) software. The block model matrix size is 10 metres (X) by 3
metres (Y) by 5 metres (Z). This was a reduction in size from the
previous model (10 metres by 5 metres by 5 metres) to improve
selectivity of potential underground mining areas. Ordinary kriging was
used for grade interpolation in all domains, with inverse distance and
nearest neighbour check models. Following the example of the previous
resource model, interpolation was carried out in multiple passes with
increasing search ellipsoid dimensions. Resource classification for all
models was based primarily on the pass number followed by an adjustment
to the class model, based on the distance to the closest sample and
kriged variance. Local confirmation of the historical stope model by
2012 and 2013 Coastal Gold drilling was used to support presence of
indicated resource blocks in the immediate area surrounding the
digitally modelled stopes

Copper is not included in the current resource estimate but was
reported previously by Coastal Gold as an exploration target as defined
under NI43-101 and the CIM Standards.

The reported mineral resources are considered to have reasonable
prospects of economic extraction. This reflects consideration of
comparable deposits, an 86% recovery factor based on new metallurgical
testing results and historical plant performance data, and a gold price
of US$1200 per ounce, which is below the three year moving average
price. No open pit constraining shell contributed to the current model
and all resources only reflect underground mining potential. The
deepest level developed in the historical mine is approximately 350
metres below surface.

The rounding of tonnes as required by NI 43-101 reporting
guidelines may result in apparent differences between tonnes, grade and
contained ounces.

The quantity and grade of reported inferred mineral resources in
this estimation are uncertain in nature and there has been insufficient
exploration to define these inferred mineral resources as indicated or
measured mineral resources and it is uncertain if further exploration
will result in upgrading them to indicated or measured mineral
resources.

Mineral resources that are not mineral reserves do not have
demonstrated economic viability. The estimate of mineral resources may
be materially affected by environment, permitting, legal, title,
taxation, sociopolitical, marketing, or other relevant issues.

Qualified Persons

Michael Cullen, P. Geo., Chief Geologist with Mercator Geological
Services Limited, who is independent of the Company and a qualified
person as defined under NI43-101, supervised and is responsible for the
mineral resource estimate presented in this press release. Mr. Cullen
has reviewed and approved the scientific and technical content of the
news release. Dr. Bill Pearson, P.Geo., President & CEO of Coastal
Gold, a Qualified Person as defined by NI 43-101, has also reviewed and
approved the scientific and technical content of this news release.

ABOUT COASTAL GOLD

Coastal Gold is a Canadian mineral exploration company listed on
the TSX Venture Exchange under the symbol "COD". Coastal Gold's
flagship property is the Hope Brook Gold Project located in
southwestern Newfoundland, which has previously disclosed totals of
19.9 million tonnes at 1.93 g Au/t for 1,239,000 ounces of indicated
mineral resources and 1.3 million tonnes at 3.22 g Au/t for 138,000
ounces of inferred mineral resources. This previous mineral resource
includes the newly defined high grade underground resource of 5,500,000
tonnes grading 4.77 g Au/t containing 844,000 ounces gold in the
indicated category and 836,000 tonnes grading 4.11 g Au/t containing
110,000 ounces gold in the inferred category. In addition, there are
previously disclosed inferred mineral resources in the tailings of 4.9
million tonnes at 0.85 g Au/t and 0.09% copper containing 134,500
ounces of gold and 9.5 million pounds of copper. For further details on
the previously disclosed resource, see the Technical Report titled 2013
Mineral Resource Estimate Technical Report Hope Brook Gold Project
dated December 4th, 2013 and for further details on the high grade
resource please see the Technical Report titled Mineral Resource
Estimate Technical Report Hope Brook Gold Project dated January 12,
2015.

Cautionary Note Regarding Forward-looking Information

This press release contains "forward-looking information" within
the meaning of applicable Canadian securities legislation.
Forward-looking information includes, but is not limited to, statements
regarding the estimation of mineral resources. Generally,
forward-looking information can be identified by the use of
forward-looking terminology such as "plans", "expects" or "does not
expect", "is expected", "budget", "scheduled", "estimates",
"forecasts", "intends", "anticipates" or "does not anticipate", or
"believes", or variations of such words and phrases or state that
certain actions, events or results "may", "could", "would", "might" or
"will be taken", "occur" or "be achieved". Forward-looking information
is subject to known and unknown risks, uncertainties and other factors
that may cause the actual results, level of activity, performance or
achievements of the Company to be materially different from those
expressed or implied by such forward-looking information, including but
not limited to: general business, economic, competitive, political and
social uncertainties; the actual results of current exploration
activities; future prices of mineral prices; failure of plant,
equipment or processes to operate as anticipated; accidents, labour
disputes and shortages and other risks of the mining industry. Although
the Company has attempted to identify important factors that could
cause actual results to differ materially from those contained in
forward-looking information, there may be other factors that cause
results not to be as anticipated, estimated or intended. There can be
no assurance that such information will prove to be accurate, as actual
results and future events could differ materially from those
anticipated in such statements. Accordingly, readers should not place
undue reliance on forward-looking information. The Company does not
undertake to update any forward-looking information, except in
accordance with applicable securities laws.

NEITHER TSX VENTURE EXCHANGE NOR ITS REGULATION SERVICES PROVIDER
(AS THAT TERM IS DEFINED IN THE POLICIES OF THE TSX VENTURE EXCHANGE)
ACCEPTS RESPONSIBILITY FOR THE ADEQUACY OR ACCURACY OF THIS RELEASE.

To view accompanying Figure 1, visit the following link:
http://media3.marketwire.com/docs/Fig1_HopeBrookGoldProject.jpg

TSX Venture closing price for COD-V
Date: 2015/02/19
Closing Price: 0.02

TEL:  416-861-5899  Rob Hopkins, Manager, Investor Relations
Coastal Gold Corp.
EMAIL:  info@coastalgold.ca
INTERNET:  www.coastalgold.ca
____________________________________________________________
(c)2015 Market News Publishing Inc.  All rights reserved.
Toronto:(416)366-8881   Vancouver:(604)689-1101   Fax:(604)689-1106

1505400003TS11505400804-05464820150224