Source	Marketwire
Date	02/24/2015
Time	12:39:56 PM

Company	 UNIGOLD INC.
Title	Unigold Announces Updated Mineral Resource Estimate for the Candelones 
Extension Deposit in the Dominican Republic





    CDNX Symbol: UGD











Press Release	




NEWS RELEASE TRANSMITTED BY MARKETWIRED


FOR: Unigold Inc.

TSX VENTURE SYMBOL: UGD

February 24, 2015

Unigold Announces Updated Mineral Resource Estimate for the Candelones 
Extension Deposit in the Dominican Republic


TORONTO, ONTARIO--(Marketwired - Feb. 24, 2015) - Unigold Inc. ("Unigold" or 
"the Company") (TSX VENTURE:UGD) is pleased to report an updated mineral 
resource estimate for its 100% owned Candelones Extension deposit, part of the 
Company's wholly owned, 22,600 hectare Neita Concession in the Dominican 
Republic.

The updated mineral resource estimate considers underground exploitation of the 
Candelones Extension deposit, focusing on high grade gold/copper mineralization 
that occurs as multiple, flat lying to moderately south dipping, sub-parallel 
lenses, ranging from 3.0 to 6.0 metres in thickness, The high grade lenses lie 
within the larger mineralized envelope of lower grade gold / copper 
mineralization that was the focal point of the initial mineral resource 
estimate for the Candelones Project that was reported in November, 2013 (UGD PR 
No 2013-22).

February 20, 2015 Mineral Resource Estimate Summary (at a 3.5 g/t Au cut-off 
grade):

/T/

Inferred   5,274,000 tonnes averaging   5.27 g/t Au;   894,000 ozs Au;
0.35 % Cu;     41,175,000 lbs Cu

/T/

Mineral resources which are not mineral reserves do not have demonstrated 
economic viability. At the present time, Micon does not believe that the 
mineral resource estimate is materially affected by environmental, permitting, 
legal, title, taxation, socio-political, marketing or other relevant issues.

The updated mineral resource was estimated by Mr. W. Lewis, P.Geo., and Mr. A. 
San Martin, MAusIMM (CP) of Micon International Limited ("Micon"), a Toronto 
based consulting company, independent of Unigold. Mr. Lewis and Mr. San Martin 
meet the requirements of a "qualified person" as established by the Canadian 
Institute of Mining, Metallurgy and Petroleum (CIM) Definition Standards for 
Mineral Resources and Mineral Reserves (May, 2014) ("the CIM Standards"). The 
estimate is based on a long term gold price of US$ 1,200 per ounce, a long term 
copper price of $3.00 per pound and an economic cut-off grade of 3.50 g/t gold.

Joseph Del Campo, interim President and CEO of Unigold notes: "The updated 
mineral resource estimate represents a first step in our evaluation of the 
viability of a small to mid-sized underground mine and mill complex at the 
Candelones Extension deposit where initial drilling has identified higher grade 
lenses of gold and copper mineralization within the larger, lower grade, near 
surface resource established in November, 2013. The Company believes that 
should the economic and technical viability be established underground 
development offers significant advantages to the initial near surface 
development model; specifically in terms of reduced capital costs, reduced 
permitting complexity and a reduced development timeline."

Summary of Estimation Methodology

Messrs. Lewis and San Martin of Micon completed a site visit to the Candelones 
Project in May, 2013, to review the Company's drilling, logging, sampling, 
chain of custody, quality assurance, electronic database and data management 
procedures. During the site visit, Micon collected independent samples to 
confirm Unigold's sampling results. Micon advises that their due diligence 
review failed to identify any significant errors or omissions that would 
materially affect the mineral resource estimate and further note that the 
results of their independent sampling are consistent with the sample results 
provided by Unigold.

Micon received the final drilling data for the Candelones Project (315 drill 
holes and over 48,000 individual sample intervals) and completed statistical 
and geostatistical analyses of the data set. Micon verified the data according 
to industry accepted best practices. Micon also reviewed the quality assurance 
and quality control procedures utilized by Unigold in collecting the drill data 
and confirms that the data was collected according to industry accepted best 
practices.

Micon notes that the drilling at the Candelones Extension was completed on 
sections that were spaced on approximate 100 metre intervals with individual 
drill holes spaced at 100 metres along each section line (Ref. Figure 1 plan 
view and Figure 2 sectional view).

Micon received, reviewed and where warranted, edited the company's updated 
geological interpretation of the Candelones Extension Zone. The updated 
interpretation established multiple (up to seven) sub-parallel, flat lying to 
shallow south dipping lenses of mineralization on each interpreted section 
(Ref. Figure 2). The individual zones from each section were joined to generate 
a three dimensional solid for each zone. The individual assay results for each 
mineralized lens were identified on each section. The assay data for each lens 
was statistically evaluated to establish a grade cap for each mineralized zone. 
However due to the number of samples in each mineralized zone an overall grade 
cap of 33.50 g/t Au was used for the mineral resource estimate. The capped 
grade data was then used to interpolate gold and copper grades for each lens 
independently.

Micon utilized an ordinary Kriging interpolation method and verified the grade 
interpolation utilizing industry standard methods and procedures, including 
alternate interpolation methods. Micon then reported the mineral resource at 
various grade ranges and recommended a 3.5 g/t Au cut-off grade to report the 
updated mineral resource estimate.

Micon has classified the resource estimate as an inferred mineral resource, 
consistent with the Canadian Institute of Mining, Metallurgy and Petroleum's 
May 10, 2014 Definition Standards for Mineral Resources and Mineral Reserves.

A Technical Report supporting the mineral resource estimate disclosed herein is 
currently in progress.

To view Figure 1 and Figure 2 accompanying this press release, please visit the 
following link: http://media3.marketwire.com/docs/993676.pdf

The Effective Date of the Mineral Resource Estimate disclosed herein is 
February 20, 2015.

The mineral resource estimate disclosed herein has been prepared by Mr. William 
J. Lewis, (P.Geo.) and Mr. Alan J. San Martin, MAusIMM (CP) of Micon, both of 
whom are "qualified persons" as defined by National Instrument NI 43-101. Both 
are independent of Unigold Inc. Micon has not identified any legal, political, 
environmental or other risks that could materially affect the potential 
development of the mineral resource estimate presented.

The mineral resource estimate is reported above an estimated economic cut-off 
grade equal to 3.5 g/t gold that was established using the following key 
economic assumptions:

/T/

Long term gold price                    $1,200 per ounce
Long term copper price                  $3.00 per pound
Mining costs (underground)              $80.00 per tonne
Processing costs                        $17.50 per tonne ore
G&A costs                               $5.00 per tonne ore
TCs and RCs                             $10.00 per tonne concentrate
Gold recovery                           84%
Copper recovery                         84%

/T/

Mineral resources which are not mineral reserves do not have demonstrated 
economic viability.

QA/QC

Diamond drilling at the Candelones Project included both HQ and NQ diameter 
core for sampling. Holes were typically started with larger diameter HQ core 
and the hole diameter is reduced to NQ at depth. Samples are logged, split by 
wet diamond saw, and half sent for assaying with the other half stored on site. 
Sample lengths typically average 1 m, but vary by geological boundaries. 
Continuous chip samples from trenches are typically 3 m to 5 m in length. QA/QC 
included inserting certified standards and blanks into the sample stream at 
industry standard intervals. Samples are prepped by ACME Analytical Labs in the 
Dominican Republic, with assaying performed through ACME's laboratory in 
Santiago, Chile. Analytical procedures include a 36-element ICP-ES analysis 
(1E) and a 50 g FA AA finish for gold (G6-50).

W. Lewis, P.Geo., and A. San Martin, AusIMM (CP), both employed by Micon 
International Limited, were the "qualified persons" supervising the mineral 
resource estimate. Both are independent of Unigold and both have reviewed the 
contents of this press release.

Wes Hanson, P.Geo., Chief Operating Officer of Unigold, has reviewed and 
approved the contents of this press release.

About Unigold Inc. - Discovering Gold in the Caribbean

Unigold is a Canadian based mineral exploration company traded on the TSX 
Venture Exchange under the symbol UGD, focused primarily on exploring and 
developing its gold assets in the Dominican Republic.

For Further Information please visit www.unigoldinc.com.

Forward-looking Statements

Certain statements contained in this document, including statements regarding 
events and financial trends that may affect our future operating results, 
financial position and cash flows, may constitute forward-looking statements 
within the meaning of the federal securities laws. These statements are based 
on our assumptions and estimates and are subject to risk and uncertainties. You 
can identify these forward-looking statements by the use of words like 
"strategy", "expects", "plans", "believes", "will", "estimates", "intends", 
"projects", "goals", "targets", and other words of similar meaning. You can 
also identify them by the fact that they do not relate strictly to historical 
or current facts. We wish to caution you that such statements contained are 
just predictions or opinions and that actual events or results may differ 
materially. The forward-looking statements contained in this document are made 
as of the date hereof and we assume no obligation to update the forward-looking 
statements, or to update the reasons why actual results could differ materially 
from those projected in the forward-looking statements. Where applicable, we 
claim the protection of the safe harbour for forward-looking statements 
provided by the (United States) Private Securities Litigation Reform Act of 
1995.

Neither TSX Venture Exchange nor its Regulation Services Provider (as that term 
is defined in the policies of the TSX Venture Exchange) accepts responsibility 
for the adequacy or accuracy of this release.

- 30 -

CONTACT INFO:

Mr. Joseph Del Campo, CPA, CMA
President & CEO
jdelcampo@unigoldinc.com
(416) 866-8157

INDUSTRY: Manufacturing and Production - Mining and Metals
SUBJECT: MEX - MINING EXPLORATION UPDATE

----------------------------------------------
Suite 900, 25 York Street, Toronto, ON M5J 2V5
Toll Free:888-299-0338
Phone: 416-362-0885
info@marketwired.com
----------------------------------------------
If you no longer want to receive 
announcements from us, please do not reply to this e-mail.
Instead simply click 
http://marketwire.com/mw/fmu.jsp?id=517663428